## Slide 1: IP address allocation issues for large scale permanent connection networks
Yoshihiro OBATA
Internet Research Institute, Inc.
JAPAN

## Slide 2: Challenges
Permanent
Scale
Speed
Technology

## Slide 3: Permanent
Pre-assignment for entire infrastructure is required including customer access port = Difficulty in on-demand assignment
Usage of customer access ports  Required number of assignment
Number of customer access ports = Number of customers = Required number of assignment

## Slide 4: Scale
Large scale assignment is required for nation wide permanent connection network
  Example: 10% of Internet customer base in Japan=1 million users
  More than 35% of users are on-line in case of permanent access network
  Inefficiency in address assignment in case of nation wide coverage

## Slide 5: Speed
Fast expansion of permanent access service
  Variety of media: CATV, Wireless, xDSL
  User’s current payment for dial up gives good rationale to switch to permanent connection service
Large scale investment
  Bubble in US and Asian market

## Slide 6: Technology
PPP over Ethernet
  Large scale equipment
    Capacity of 100,000 in one box
  Requires dual assignment of IP address
    PPP underlying infrastructure
      Global address may be required in case where PPP and IP are mixed in the same infrastructure
    PPP network
Use of DHCP may not scale up when a network sees rapid unbalanced growth in number of customers, which requires frequent renumbering

## Slide 7: Other Problems
RFC 2050 and RIR’s regulations assumes dial up access or medium scale permanent access by corporate or academic users
  Number of dial up ports = Number of potential PPP sessions??
  Rapid expansion of assignment window is required

## Slide 8: Proposal
Feedback to the community by APNIC from the experimental allocation of A class block to CATV Internet by ARIN
Establishment of study group in APNIC for IP address allocation to permanent connection consumer network
Establishment of similar study group in NIRs and LIRs
Subjects for study
  Experimental assignment to catch up with technology and market requirement
  Requirement of change in RFC 2050
  Requirement for new rules for IRs