## Slide 1: APNIC Open Address Policy Meeting
Special Interest Group Session
March 2nd, Korea, Seoul

## Slide 2: Problem Definition
Should APNIC make allocations from network 61 /8 on a regular basis as part of its total address pool?

## Slide 3: Motivation and Background
Motivation
  Estimate 2 years of remaining ‘C’ space
    21.9% (7 /8s) remains free from the ‘C’ space
    62.7% (79 /8s) remains free from the ‘A’ space
Background
  April 1997
    IANA allocated each registry a /8 from the ‘A’ space
  June 1997 (AMM)
    APNIC would allocate from 61/8 on a trial basis similar to RIPE NCC trial for 62/8

## Slide 4: Current Status
ARIN (63/8)
  Allocations from 63/8 were made to larger members and no experiments were conducted
  In September 1999, ARIN started to allocate from 64/8 (with minimum allocation of a /20)
RIPE NCC (62/8)
  After the trial ended (Dec 1997), RIPE NCC continued to make allocations of class A address space on normal basis

## Slide 5: Current Status
APNIC (61/8)
  Only 1 member volunteered to receive an allocation from 61/8
  Due to lack of resources, APNIC did not actively promote trial from 61/8 in 1997
  Since October 1999, allocations from 61/8 have been made to members in China, India, Hong Kong, Australia, Singapore and Philippines

## Slide 6: Current Status
Network Allocations from 61, 62 and 63

## Slide 7: Current Status
Network announcements in global routing table

## Slide 8: Current Status
Breakdown Of Network Assignment from Network 61

## Slide 9: Discussion
Feedback from APNIC members
  Classful filtering by some ISPs
    network unreachable in some parts of the Internet
    Solution
      contact the individual ISPs and request them to modify their filters
  Old classful equipment or routing protocol
    Solution
      Upgrade software or hardware
      All new equipment now supports CIDR

## Slide 10: Recommendations
Feedback from RIRs and APNIC Members
  Include 61/8 as part of total address range
  Make allocations on a regular and ongoing basis to APNIC members
Recommended implementation
  Announcement via mailing lists (NANOG, APNIC, RIPE-list etc) and web site
  Class ‘A’ allocations commence in June 2000