## Slide 1
Intelligent Optical Networking Evolving the Core Towards Enhanced Service Delivery
Chair:
Scott Larson
Director of Marketing, Strategic Programs
Sycamore Networks

## Slide 2
Optical Wave Services
Scott Beaudoin
Senior Technologist, Transport and Data Services CTO
Williams Communications

## Slide 3
Optical Internet Infrastructure of Thrunet
Hyang-Ah Kim
Internet Engineering Team
Thrunet

## Slide 4
Network Modeling for the Intelligent Optical Network
Wade Rubinstein
Director, Professional Services
Sycamore Networks

## Slide 5: Williams Optical Wave Service
Scott Beaudoin
Sr. Technologist, Transport and Data Services CTO, Williams Communications

## Slide 6: Objectives
The Waves of the Future: Where “waves” fit into Williams Network
A Well Engineered Physical Plant
What is a “Wave”
What are the Applications for “Waves”
Competitive Advantages
Questions

## Slide 7
A Well Engineered Network
Williams
Network In-Service Plan
POPs/ATM Switches
New Network Build
Retained WilTel Network
Date
1999
2000
Notes: The Williams Network exceeds the scale of any network prior to 1997, already more than doubling the capacity of the 11,000 mile network retained from the WilTel sale.
By the end of 2000, Williams will have added a total of 22,000 new miles of high density fiber networks with the latest technology and the most efficient network design.

## Slide 8
WILLIAMS NETWORK
Engineered For Security
Notes: There are times to be polite, and there are times to be direct.
Most fiber optic networks are constructed along highway and railroad rights of way, which are marked with polite signs that say: “Please call before you dig.”
The Williams Network is being constructed primarily along natural gas and petroleum pipeline rights of way, which which are protected from casual traffic and marked with signs that basically say “Dig here and you could die.”
This right of way advantage translates into increased reliability and lower cost of construction and maintenance.

## Slide 9: Engineered For Security
Unlike traditional networks, Williams buries our conduit 42” deep.
Even through bedrock, Williams conduit is a minimum of 18” deep.
Williams
Traditional
Notes: Williams is burying conduit 42” deep, significantly deeper than other Networks. Even through bedrock Williams saw cuts to a minimum of 18” deep. In addition, Williams also protects the fiber conduit trench at road crossings with steel. These measures reduce the chance of incidental fiber cuts.

## Slide 10: Engineered For Data Integrity
Traditional Network
Williams Network
Amplification every 40 miles creates tighter data integrity.
Amplification every 60 miles creates loss of data integrity.
Distance is the Nemesis of DWDM Technology

## Slide 11
WILLIAMS NETWORK
TRADITIONAL NETWORK
FUTURE WILLIAMS NETWORK
OPTICAL DISTANCE
BANDWIDTH
20 Gb
40 Gb
60 Gb
80 Gb
100 Gb
400 Gb
Engineered For Long-Term Economics
Notes: The Williams Network is being constructed with 40-mile optical spacing which we believe is a competitive advantage.
Most other fiber optic networks are being built with 60-mile optical spacing. Intuitively, this sounds like a more cost effective approach.
Williams has challenged that conventional wisdom.
We know from working with the physicists designing the next generation of optical networking equipment, that closer spacing will result in future exponential gains in fiber capacity. This means a single fiber with 40-mile spacing will be capable of transporting as much as 400 gigabytes per second. This is an order of magnitude which will not be available to other networks with 60-mile spacing.
So, while our closer spacing results in a linear increase in initial construction and equipment expense, it will produce exponential gains in network capacity.

## Slide 12
<footer>
SAN FRANCISCO
NEW YORK
Engineered For Reliability
Notes: The Traditional SONET Ring Architecture
Highly Reliable
Redundancy Protection
Strands Assets
Inefficient Utilization of Capacity
Complex Interlocking Ring Design
Time Consuming (avg 18 mos) to Build and Expand
Expensive to Own and Operate
In the traditional SONET ring network, circuits are built by traversing one or multiple rings in sequence. (Because SONET rings were originally intended for Metropolitan Area Networks and are limited to 1200 miles total distance at least 5 rings are required to cross the country.) Protection is provided through redundant rings.
However, this architecture can cause bandwidth in any ring to be stranded and lost. This not only affects nationwide circuit building but also limits the availability of bandwidth within that particular ring.

## Slide 13: Ring Inefficiencies
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
ADM
Bottlenecks due to low drop capacity
Wasted protection capacity

## Slide 14: Engineered For Reliability and Performance
<footer>
San Francisco
New York
Notes: Williams Intelligent Linear Mesh SONET Architecture
Highly Reliable
Redundancy Protection
No Stranded Assets
Maximum Utilization of Capacity
Sophisticated Mesh Design Provides Intelligence & Options
Shorter Time to Build and Expand
Low Cost to Own and Operate
In the Williams Network, circuits are built through the most efficient path across the network and the restorable optical network provides redundancy protection through multiple diverse routing. This architecture allows the maximum efficiency of the available circuit inventory to be achieved.

## Slide 15: Efficient Network Design
End-to-end provisioning
OADM
SONET Switch
ADM
ADM
SONET Switch
SONET Switch
SONET Switch
ADM
ADM
ADM
ADM
ADM
ADM
ADM
OADM
OADM
Shared protection capacity
Optical ADMs for smaller sites
SONET switches at high bandwidth junctions

## Slide 16: Optical Network Infrastructure View
LONG HAUL
METRO BACKBONE
METRO ACCESS
TRANSOCEANIC
ENTERPRISE

## Slide 17: What is an Optical Wave?
An optical wave is a transponder-based service which provides unprotected, concatenated, customized bandwidth primarily for data traffic and allows data carriers requiring low restoration rates to provide protection switching using their own equipment.
Wave 1
Wave 2
Wave 3
Wave 4
Wave 1
Wave 2
Wave 3
Wave 4

## Slide 18: Transponder based
W
W
Transponder
W
P
Traditional

## Slide 19: Transparent OC-48c Wave
  Customers define
  service type
Pass the k bytes through
No interference from different vendor
ATM
Frame
IP
OR
OR
DWDM
Waves
Transponders
Interoperable

## Slide 20: Protection Switching
From core to edge
Protection Switching moves from the core to the edges
Protection done by customer instead of network provider

## Slide 21: What are the Applications for Waves?
Complete SONET rings
Complete diverse routes
ATM, Frame Relay or IP over Waves

## Slide 22: Complete SONET Rings
Customer’s SONET Automatic Protection Switching (APS) can be used

## Slide 23: Complete Diverse Routes
Wave

## Slide 24: ATM, Frame Relay or IP Over Waves
Frame Relay
Interconnect ATM switches and IP routers with OC48 interfaces

## Slide 25: How Customers Connect to Waves
Customers connect to waves by Co-locating or through fiber-interconnects
The transponder is the demarcation point

## Slide 26: How is Waves Different?
Customer
Dark
Fiber
Wave
Dim Fiber
Capacity
Fiber
Optronics
Network
Management
Transponder
Network Provider
Service Types
ATM/IP/Frame
E
q
u
i
p
m
e
n
t

## Slide 27: Quality of Service in the Optical Network
The Williams Network will offer three levels of QoS
GOLD
SILVER
BRONZE
  SONET ring protocols (50 ms)
  Mesh reroute restoration (< 10 sec)
  Unprotected circuits

## Slide 28: Optical Virtual Private Network
OC-48 IP Router
OC-48 IP Router
OC-48 DWDM
OC-48 DWDM
OC-48 DWDM
OC-48 DWDM
OC-48 DWDM
Williams Optical Network

## Slide 29
Others
WHAT IS GOING ON IN THERE?
DON’T WORRY I’M IN CHARGE
I CAN SEE CLEARLY NOW...
Engineered For Carriers
Notes: Williams CNMS (Customer Network Management System) gives the carrier unmatched capability to see and control their network elements within the Williams Network.

## Slide 30: Benefit of ‘wave’
Many entrants don’t want to own the physical layer
  Their expertise is ATM or IP networks
  Don’t want the hassles of route surveillance
  Need capacity to complete their own networks

## Slide 31: What are our Competitive Advantages?
First to market
Full service provider
V&H mile pricing as opposed to route mile pricing
Short-term (1-9 years) contracts
Web-based management system
Notes: First to Market: Williams’ early entry will provide a first mover advantage.
Full Service: Williams offers a full range of products from dark fiber to capacity and provides the ability to migrate from one service to the other.
Short term (1-5 years) service deals:Sustains customer relationship by providing high service value rather than inflexible contractual commitment.
Web-based management system: Allows customers to manage their network.
Decreased Provisioning Time: Due to transponder equipment on the network, the service turn-up time for increasing bandwidth for existing customers, can be reduced.
Vendor Selection: Provides existing customers’ bandwidth on demand.
Williams linear network: Williams linear Network can accommodate technology growth and changes in waves.
Wholesale strategy: Williams wholesale strategy allows us to serve customers and not compete against them.

## Slide 32
Questions?