## Slide 1: Optical Internet Infrastructure of Thrunet
Hyang-Ah Kim
APRICOT2000, Seoul
Korea Thrunet

## Slide 2
I. Who is Thrunet?
II. Facts of the Internet
III. Transport Options
IV. Cost
VI. Case Study: Thrunet IP Network
VII. Conclusion
Agenda

## Slide 3: Korea Thrunet Co., Ltd
Who is Thrunet
  a Korean leading data communications and information service carrier
Foundation
  incorporated in 1996 by 102 first class enterprises in the country
Major Business Area
  Closed circuit network leasing service (CCNW)
    By employing a KEPCO’s fiber backbone network together, Thrunet leases the closed circuit network of 100% optical cable line for hi-quality of multimedia data transmission
  Thrunet Service
    Thrunet provides the ultra-fast internet access service through the cable TV network (HFC) first in the country.
  Portal Service

## Slide 4: Advent of High Speed Internet
Increasing demand for bandwidth
Continued Growth
in the Internet
Growth in IP data traffic
Advance in Internet Technology
New vendor/product
High Speed Internet !
Customer
Business
Carrier
More bandwidth
More multimedia

## Slide 5: Trend in the Network Traffic
Internet data as the dominant traffic type
  Internet booming
  Future applications
Dramatic growth in IP traffic
  Double every 6 months
Service Integration over IP
  IP telephony
  Settop box
Relative
Load
30
25
20
15
10
5
0
1990
1995
2000
2005
Data Is 23x
Voice Traffic
Data
Data Is 5x
Voice Traffic
Voice
Year
[Source: Electronicast, 1998]

## Slide 6: Characteristics of Internet Traffic
Connectionless Network
  50msec restoral myth
Fractal or Bursty Nature of Data
  With fractal bandwidth reserved bandwidth channels causes more congestion than one shared channel of equivalent bandwidth
Asymmetric Tx/Rx
  The extreme imbalances between Tx/RX (up to 16:1)
Predominant Computer-to-computer Traffic
  Insensitive to jitter and delay, but extremely fractal
  Extremely asymmetric & growing exponentially
  Usually many-to-many communications; QoS is hard.
Server Bound Congestion
  Server performance, DNS, routing tables, etc.

## Slide 7: Advance in Network Technology
Rapid Pace of Optical Technology
  Point-to-Point Transmission
  DWDM, CWDM Technology
  Optical ADM
  OXC
Advanced Routers/Switches
  High Speed Interface
    Gigabit Ethernet, 10Gigabit Ethernet, 2.5~160Gbps Interface
  High Speed Switching
    40Gbps~64Tbps Internal Switching Fabric
  High Performance Routing and Service
    QoS routing, Multicast, Mobile IP

## Slide 8: Choice of Network Architecture
IP Network
WDM
SONET
ATM
IP
Lower cost and operation
More reliability
WDM
SONET
IP
WDM
IP

## Slide 9: ATM
Advantages
  Aggregation of different traffic type
  Significant savings in overall bandwidth
  Easy solution to VPNs and classes of service for data
  Incredible degree of flexibility in network engineering/design
But,
  Overwhelming service type in future : Internet data
  Advent of very high speed routers
  Packet segmentation and reassembly (SAR) overhead
  Loss of bandwidth due to SVC setup time
  Complexity
  High cost
  Need a network optimized for the Internet data delivery
  Deliver the remaining services on top of an IP network

## Slide 10: SONET/SDH
Advantages
  Sophisticated link management in the SONET/SDH layer
    Powerful restoral property (less than 50msec)
    Synchronous component  more robust
  Very high efficiency – over 98%
But,
  Optimized for the traditional voice traffic
    Balanced Tx/Rx
    Framing based on 8kHz voice synchronized time sample
  Alternate solutions to the link management
    Protection and restoral capabilities of IP
    GPS technology
  Loss of bandwidth Utilization
    Working & protection fibers
  High cost of transponder and regeneration equipment

## Slide 11: IP over Optical
Advantages
  Optimized network for data service
    No SAR processing
  Scalable architecture
    WDM technology + Fast evolution of IP router
  More reliability
    The fewer equipment, the less points of problems
  More efficient use of bandwidth
    Statistical multiplexing
    Use of protection fibers
  Lower equipment cost
    Fewer platforms, fewer conversions, technology integration
  Lower operations cost
    Less to manage, flexible bandwidth

## Slide 12: ATM, SONET functions to IP layer
Speed
  Manufacturers are about to release routers which can route IP packets at wire speed up to 40 Gbps per port.
Traffic engineering/Class of services
  The technologies such as MPLS may provide traffic engineering capability at the IP layer.
Synchronization
  GPS
  More tolerant IP technology to timing faults
Restoral capacity
  Support from WDM layer
  Inherent self-healing feature of IP

## Slide 13: Optical and LAN Convergence
LAN/Campus
MAN
WAN
- Seamless connection to MAN and
WAN through same frame
protocol and transmission
technology desired
- 802.3 10Gbps
standards work
- 10G/s market emerging
in campus backbone
- High speed transport
for MAN/LAN
- Proven photonic
technology for WDM
and OC-192

## Slide 14: 10 Gigabit Ethernet
10 Gigabit Ethernet provides a universal Link
  Layer2: Frame forwarding, QoS, protection, multicast
  Layer1: Header integrity, payload integrity, frame delineation, efficient line coding, signal trace, protection, FEC
  Layer0: Physical connectivity
IP
Media
Access
Control
Physical
Coding
Optics
10Gigabit
Ethernet
Estimated Schedule
  June 2000 Market momentum starts to build.
  March 2001 First 10Gigabit Ethernet products appears on the market
  January 2002 Completion of IEEE 10Gigabit Ethernet standard

## Slide 15: Case Study: Thrunet Optical Internet
Evolution of Thrunet IP Backbone
Metropolitan Area Network
Wide Area Network
Connection with Other Networks
Plan for 2000

## Slide 16: Evolution of Thrunet IP Backbone
1st generation: Classical network
  FDDI connecting small number of SO’s
  Issues: High speed network for different services
2nd generation: Hybrid network
  ATM and routers to connect SO’s
  Issues: performance, speed, complexity of ATM
3rd generation: Optical Internet
  Phase 1: Gigabit Ethernet in metropolitan area (1998-1999)
  Phase 2: Gigabps wide area network (1999)
  Phase 3: Wavelength Division Multiplexing fiber system (2000)
Thrunet is providing high-speed Internet services
at low cost by deploying its 3rd generation network!

## Slide 17: Metropolitan Area Network
To Thrunet WAN
IP over Gigabit Ethernet over WDM
Current bottleneck is the headend system.
Headends are connected with Gigabit interfaces

## Slide 18: Wide Area Network
IP over Gigabit Ethernet over WDM
Currently, WAN interconnects 4 Regional Data Centers.

## Slide 19: Connection to Other Networks
DIX
KT-IX
Thrunet
AS9277
NCA
AS3608
Hanaro
AS9318
KTNet
AS7557
DreamLine
AS9457
AUNet
AS7620
HanQ
AS4660
NetsGo
AS4792
Nextel
AS4745
Hitel
AS5051
Shinbiro
AS4670
Kornet
AS4766
Dacom
AS3786
International Link
Inet
AS3976
Nowcom
AS4669
Edunet
AS9455
KREN
AS2563
LG internet
AS7561
Unitel
AS6619
Content Providers
100M
1G
1G
1G
1G
100M
100M
100M
100M
100M
Content Providers
100M
100M
100M
100M
Nowcom
AS4669
Dreamline
AS4745
Unitel
AS6619
Elimnet
AS4663
Kotis-net
AS7562
Shinbiro
AS4670
KINX
TIX

## Slide 20: 2000 Plan of Thrunet
Traffic Volume & Number of Subscribers from Major Cities
Assumptions
  Ring architecture connecting Seoul, Taegu, and Pusan
  Seoul as the only connection point to other networks
  No consideration of bandwidth saving by web caching

## Slide 21: Conclusions
Data growth will bring about dramatic changes in transport.
IP over Optical provides the new data-optimized solution. Remaining services can be delivered on top of IP layer or on the other wavelengths of WDM.
Thrunet is providing simple-to-manage and high bandwidth services with great magnitude of cost savings.