## Slide 1
Notes: 1

## Slide 2: Network Modeling for the Intelligent Optical Network
Wade Rubinstein
Director, Professional Services
Sycamore Networks
“wade.rubinstein@sycamorenet.com”

## Slide 3: Agenda
Intelligent Optical Networking Defined
The Planning Objectives
Design Processes

## Slide 4: Intelligent Optical Networking
Transforming the optical network
  Flexible foundation for the rapid delivery of high speed bandwidth and new services
  Simplified infrastructure -- minimizes costly electrical/optical conversions
  Scales easily, enables just-in-time investment
  Supports multiple topologies
    Backbone mesh
    Interoffice & access rings
    Linear with optical add/drop
Notes: Intelligent optical networking not only addresses the challenge of scaling the existing public infrastructure as data continues its exponential growth, but it also presents the architects of new data-centric networks with a viable, state-of-the-art solution. With Intelligent optical networking, the core optical network is transformed from a static transmission medium to an intelligent and flexible foundation for delivering bandwidth more quickly and efficiently, and at a lower cost.
(translation)

## Slide 5: Intelligent Optical Networking
Services are delivered over networked lightpaths
  Easy to turn up -- easy to tear down
    Fixed or flexible services
    End-to-end service management
  Targeted at services at speeds of 100 Mbps and above
    STM-n/OC-n
    Gigabit Ethernet
Intelligent Optical
Network
DS0
E1
E3
STM-1
STM-4
STM-16
STM-64
E
FE
GE
10GE

## Slide 6: Components of the Intelligent Optical Network
Large Region
Small Region/Access
Backbone
MANAGEMENT
SWITCHING
ACCESS
TRANSPORT

## Slide 7
Software Intelligence, Enabling Services
Optical routing and signaling
  Provides the foundation for network intelligence
  Industry standard protocol implementation
Intelligent grooming of sub-rate circuits
  STM-1/STS-3,STM-4/STS-12,STM-16/STS-48 grooming support
  “Express trunks” provide network efficiency
Local and network level protection
  Support for Path, Span and Line protection
  Protection options 1+1, 1:1, 1:n, Pre-emptable Traffic

## Slide 8
Intelligent Optical Routing & Signaling
Routing: Open Shortest Path First (OSPF)
  Link-state routing protocol
  Distributed database of switching nodes, their interconnect trunks, and control channels
  Provisions circuits and routes/reroutes traffic
  Enables network protection
  Virtual private network (VPN) support
Signaling: Label Distribution Protocol (LDP)
  Used to set up circuits, hop-by-hop, as they are provisioned
  LDP queries OSPF for the optimal route, and verifies that resources are available prior to circuit set-up

## Slide 9: Network Planning Objectives
Multi-layer network optimization
  Circuits
  Wavelengths
  Fiber
  Conduit
Service level planning
  Failure analysis
  Availability analysis
  Protection and restoration simulation
Strategic network planning
  Business case analysis (new service ROI analysis)
  Capacity planning

## Slide 10
Fundamentals of Network Design Problem
A telecommunications network is a connected set of
  Nodes
    where traffic begins / ends
    and where traffic can be routed through
  Links
    of a given capacity, length, cost, medium, etc…
    connect the nodes together and carry the traffic between them
  Lightpaths
    Traffic demand to be set up between nodes
    End-to-end routing and protection

## Slide 11
Traffic is loaded onto two links
Node must determine routing and have “cross-connect” capacity
Lightpath loaded onto a single direct link

## Slide 12
Sample Network Modeling Architecture

## Slide 13: Logical Network Design
Goal: Determine the minimum cost wavelength plan for a given set of demands and a physical network.
Inputs: Physical network topology, end-to-end demands, equipment specifications, availability requirements, network element and link costs
Outputs: demand routes, link wavelength requirements, link capacities, equipment requirements

## Slide 14: Physical Network Design
Goal: Find the minimum-cost, optical-network design.
Inputs: Physical topology, fiber specifications, wavelength routes, equipment specifications, span engineering rules.
Outputs: Network element requirements, Fiber count requirements.

## Slide 15
Multi-layer Network
The duct layer: physical fibers
The real topology of the network
Tributary layer:
155 & 622 Mbit/s links
routing and grooming
Wavelength layer:
2.5 Gibts/s Links
routing
STM-1/OC-3 layer
generates traffic demands for the STM-16/OC-48 layer
STM-16/OC-48 layer specifies cost/price details for a logical link

## Slide 16
Layer Options
Duct layer
STM-16 (transport)
Optical (DWDM)
STM-4
STM-1

## Slide 17
Network Layers & Grooming
First bundling : Containers (switched at Transport depots)
Second Bundling: Transport ships (switched at ports)
Containers

## Slide 18
Network Protection Options
Network topology optimization
  Produce the “lowest-cost” network
  Guarantee traffic demands are met
  Account for path diversity
Protection
    1 + 1 End-to-end diversity
      if required taking into account information on the underlying fibre-paths in the physical ducts
    or “Shared” (1:N) protection
      pre-calculated diverse paths

## Slide 19
Network Restoration
Main Path
Restoration Path
Main Path
Failure 1
Failure 2
Protection capacity for both demands

## Slide 20: Summary
Advanced routing and signaling enable the Intelligent Optical Network
Multiple Network Design and Planning Processes are a Necessity For:
  Network optimization
  Service Level Planning
  Strategic Network Planning
Multi-layer Design Methodology is Required
  Physical Layer - Fiber, Network Elements
  Logical Layer - Lightpaths