## Slide 1: Multiprotocol Lambda Switching: MPLS for Optics
Mark I. Williams
APRICOT 2000
Seoul, Feb 28-Mar 02, 2000

## Slide 2: MPLS for Optics
Optical Opportunities
Layer Problems
Solution Motivations
L1/L2/L3 Integration
Solutions for Existing SDH/TDM
OXC Solutions
Multilayer Services
Issues

## Slide 3: Optical Opportunities
Smart 
IP
MPLS
ATM
FR
TDM
Voice
IP
Optical bandwidth capability growing rapidly, so is IP traffic demand.
  Exploit optical capabilities for IP esp. high bandwidth
Opportunity to consolidate separate optical network and packet network with MPLS.
  Reduce equipment and maintenance costs.
Improve existing optical services by applying IP routing and switching capabilities to optical network.
  Fast creation of lease line service.
Exploit optical bypass capabilities for IP tandem traffic.

## Slide 4: Layered View
L1, L2, and L3 each have a service, data (forwarding), and control.
Restoration and protection mechanisms are also present at each layer.
Service
ATM UNI connection oriented
Forwarding
Label switching
Control
PNNI, PVC
call control
Best effort IP connectionless
Hop-by-hop IP connectionless
IP Routing (OSFP)
ARP
Fixed b/w transparent bit service
Electrical cross connect
Optical cross connect
Patch panel
Mux/demux
Protection
L1
L2
L3

## Slide 5: Layer Dependence
Hop in SONET path
L1
Fiber link
L0
SONET path (e.g., OC12c)
ATM link
L2
ATM VC
L3
Router-router link
IP connectionless path
L4
TCP session
A given layer can use the service of an underlying layer for its connection.
Services offered at each layer rely on characteristics of layer below.
Layer n usually adds functionality/value not present at layer n-1.

## Slide 6: Layering Problems
Lots of boxes -> higher cost, more complexity to manage.
  If an organization owns several layers, it is complex to manage the logical topologies.
  If an organization doesn’t own a layer beneath it, it may be subject to unknown risks of that service provider.
Resolution protocols are needed.
  Address resolution protocols from one layer’s address to another.
  Service mappings between layers.

## Slide 7: Layering Problems
Amplification of failure.
  Failure of a link at one layer can affect many connections in the layer above.
Reliability functions may overlap.
  Cost of higher layer services may reflect cost of reliability functions at lower layers which aren’t really needed because adequate reliability may be present at the higher layer.

## Slide 8: Motivation - L2/L3 Unified Control
MPLS and IP control subsumes L2 control in order to leverage L2 forwarding advantages.
Service
ATM UNI connection oriented
Forwarding
Label switching
Control
call control
Best effort IP connectionless
Hop-by-hop IP connectionless
IP Routing (OSFP)
MPLS LDP
Fixed b/w transparent bit service
Electrical cross connect
Optical cross connect
Patch panel
Mux/demux
Protection
L1
L2
L3

## Slide 9: Motivation - L2/L3 Integration
Alignment of L2 and L3 topologies.
  No L2 addressing (e.g., NSAP) needed which simplifies control by eliminating address resolution.
  Can reduce number of boxes needed if LSR combines routing and switching hardware, thus simplifying network management.
  Can reduce effect failure amplification of L2 link failure on L3 links.
MPLS is a common L2 control function.
  By defining labels that consider NBMA and broadcast types, L2 media interworking is much simpler.
  Basic SVC capability is provided using the same protocol for various L2.
Enable use of non-shortest paths.

## Slide 10: Motivation - Fast L1 Failure Detection
When a physical link that is carrying multiple L1 paths fails, each endpoint of all the paths knows about the failure through physical detection methods specific to the cross connect technology.
Fast Detection: Channel endpoints learns of failure quickly.
Scalable Detection: All affected channels are informed.
All channel endpoints are notified

## Slide 11: Review - L3 IP Forwarding
L3 Forwarding takes IP packets and does a lookup on the destination IP address in an IP Forwarding table. A successful lookup results in an identifier for an outgoing link on which to place the packet. This is repeated at each router.
R1
R2
R3
R4
•
•
•
•
•
•
•
•
•
•
•
•
IP prefixes
Next hop
lookup
to link A
lookup
IP packet
to link B
A
B
R1 table
R2 table
R4 table
IP packet to R4
C
D

## Slide 12: Review - MPLS Forwarding
LSP defined over links A, C, and D (R1 - R2 - R3 - R4)
Packet arriving at R1 destined for R4 is handled by L3 forwarding and placed on an LSP. At R2 and R3, it is handled by L2 forwarding (I.e., switching).
R1
R2
R3
R4
•
•
•
•
•
•
•
•
•
•
•
•
L3 Forwarding table for R1
IP packet to R4
lookup
to LSP
Labeled IP packet
A
B
•
•
•
•
R2 label table
L3 Forwarding table for R2
L3 Forwarding table for R4
•
•
•
•
R3 label table
•
•
•
•
R4 label table
Label lookup
Label swap
Label lookup and swap
C
D
•
•
•
•
L3 Forwarding table for R3

## Slide 13: Unified Layers
Extend L2/L3 integration concepts downward for simplicity and potentially cost reduced network elements.
IP control subsumes L1/0 control in order to leverage L1/0 forwarding advantages.
  Use IP control to replace L1 protection for L2 and L3 services.
Retain L1 and L0 control functions where needed.
Service
ATM UNI connection oriented
Forwarding
Label switching
Control
Best effort IP connectionless
Hop-by-hop IP connectionless
IP Routing (OSFP)
MPLS LDP
Fixed b/w transparent bit service
Electrical cross connect
Optical cross connect
Patch panel
Mux/demux
L1
L2
L3
call control

## Slide 14: L1/L2/L3 Switch
Define a switch that is a Label Switching Router linked with an L1 multiplexor/demultiplexor and cross connect. For example:
  an IP router and a SONET ADM
  an IP router and a TDM cross connect
For every physical link, allocate one or more channels to connect the LSRs on either end of link.
LSR
L1 Cross Connect
Physical Topology
Logical Topology

## Slide 15: L1/L2/L3 Solution for Existing SDH/TDM
Physical Topology
Router Topology
R1
R2
R3
R4
R6
R5
R1
R2
R3
R4
R6
R5
ADM
ADM
ADM
ADM
ADM
ADM
R7
R8
R7
R8
TDM
TDM
Define an IP network with many interconnected L1/L2/L3 switches.
No L1 restoration mechanisms are needed or assumed (e.g., SONET restoral).
L3/L2/L1 topologies are aligned. All router-router links are now one physical hop and routers view the physical topology.
This network differs from networks where L1 and L2 are separated in that no L1 paths (series of cross connected channels) are used as router-router links.

## Slide 16: L1 cut-through path
LSP = L1 Path
LSRs are configured with LSPs which correspond to L1 paths.
L1 cut-through - Extends the concept of an L2 cut-through (use of L2 path for IP data flows).
Analogous to L2 cut-through paths in existing L2/L3 protocols (e.g., NHRP, MPOA).
The L1 cut-through or path, is an end-to-end path established with L1 cross connects.
  Could use existing methods to create L1 path.

## Slide 17: L1 Cut-through Forwarding for L3 Service
Packet from R8 to R5 is sent to L1 cut-through and does not perform label swapping or lookup at intermediate switches.
•
•
•
•
•
•
•
•
L3 Forwarding table for R8
IP packet to R4
lookup
Labeled IP packet
•
•
•
•
R7 label table
L3 Forwarding table for R7
Label lookup
R1
R2
R3
R4
R6
R5
R7
R8
R7 cross connect
R8 cross connect
•
•
•
•
•
•
•
•
R6 label table
L3 Forwarding table for R6
R6 cross connect
R5 cross connect
•
•
•
•
•
•
•
•
R5 label table
L3 Forwarding table for R5

## Slide 18: L1 Link Failure
When a physical link that is carrying multiple L1 cut-through paths fails, each endpoint of all the paths knows about the failure through physical detection methods specific to the cross connect technology.
Fast Detection: Channel endpoints learns of failure quickly.
Scalable Detection: All affected channels are informed.
  Many L1 Cut-through Ingress and Egress nodes are informed.

## Slide 19: L1 Link Failure
Fast recovery of IP Forwarding under physical link failure.
  Upon failure of a physical link, all L1 cut-through endpoints are notified by physical detection methods.
  The MPLS entity managing LSPs is notified of LSP failures which correspond to L1 cut-through path failure.
  Backup procedures are then executed to restore IP Forwarding.
  The router can then adjust the affected next hop fields for the destination IP prefixes with other valid routes if they exist.
This action can take place sooner than the L3 routing protocol reaction to the failed link because the detection method is based on L1 physical layer detection that spans multiple cross connects.

## Slide 20: Example of Fast Detection on Failure
If link R7-R6 fails, R8 immediately detects the failure of L1 cut-through R8-R7-R6-R5
Next hop entries which use the affected L1 cut-through can be updated to not use the cut-through.
  Could for example, replace with L3 connectionless next hop. That is, just send packets to R7 at L3.
•
•
•
•
L3 Forwarding table for R8
IP packet to R4
lookup
R1
R2
R3
R4
R6
R5
R7
R8
Update next hop entry to stop using cut-through.

## Slide 21: Applicability/Observations
Solves fast LSP failure detection and scaling of failure notification.
Enables fast LSP restoration independent of L3 IGP convergence.
Flexible Backup - could backup onto fixed bandwidth path (like full SONET protection) or onto L2 MPLS LSPs (stat muxed).
Not as scaleable as L2 LSPs, but probably good for an IP core.
  E.g., 192 STS-1 on an OC192 link vs 1000s of VCs on an ATM interface.
  But, don’t discount future technology with finer b/w granularity.

## Slide 22: Applicability/Observations
No LSP signaling protocol changes are needed.
Could use with timeslot fabrics (TDM, SONET) and/or wavelength fabrics (DWDM cross connects).

## Slide 23: L1/L2/L3 Solution for OXCs
L1/L2/L3 Integration and Control of L1/L0 Cross Connect
  Use L3 control to create L1 paths.
  Extend MPLS to treat SONETchannels, TDM timeslots, and s as labels.
SONET Channel routing
  Use ER-LDP signaling to setup L1 paths.
 Routing
  Use ER-LDP signaling to setup L0 paths.

## Slide 24: L1/L2/L3 Solution for OXCs
L1/L2/L3 Advantages
  Network management simplicity.
  Switch cost reduction (one switch instead of router/ATM/SONET boxes).
  Unified control plane with known characteristics (OSPF).
  Independent of ring or mesh L1 networks of today.

## Slide 25: MPLS for  Switching
<draft-awduche-te-optical-01.txt> presented at IETF46
Draft describes “an approach to the design of control planes for optical cross connects, which leverages existing control plane techniques developed for MPLS Traffic Engineering”.
Trend: evolution of existing optical networks (ITU, ANSI, OIF) with switchable OXC.
Similarities between LSRs and OXCs
  LSR dataplane switching fabric  OXC switching
  LSR control plane functions  OXC control plane functions
  Explicit LSP optical trail

## Slide 26: MPLS for  Switching
“ If the OXC is a wavelength routing switch, then the physical fiber between a pair of OXCs would represent a single link in the OTN network topology. Individual wavelengths or channels would be analogous to labels.”
Suggests a uniform control plane for all layers and that this be the MPLS Traffic Engineering Control Plane

## Slide 27: Distributed Multi-Protocol Lambda Switching (using OADM ring)
OADM
OADM
OADMs
mapping
port
n
to wavelength

under control of
optical network controller
Central Office
Location
OADM

1

1

1

1

2

3
Central Office
Location
Central Office Location
Central Office
Location
OADM
OADM

1

2

3

4
Optical
Network
Controller
DCC
Traffic
Engineering
Application
IP/MPLS Signalling

Routing/Allocation
Statistics Collection
Light-path
Signalling
Integrated-knowledge
of Network and Optical
Layer Connectivity
Used by permission from John Hopkins, Fujitsu

## Slide 28: Unified Control plane
IP Routing and MPLS now used across all layers
Applications can use MPLS LDP APIs to provide different services.
Assumes cross connects can be controlled by signaling.
Service
ATM UNI connection oriented
Forwarding
Label switching
Control
Best effort IP connectionless
Hop-by-hop IP connectionless
IP Routing (OSFP)
MPLS LDP for L1/2 “labels”
Fixed b/w transparent bit service
Electrical cross connect
Optical cross connect
L1
L2
L3
L1 API
L2 API
ATMCall control
SONET Path set up
 Path set up
L3 API
IP FECs

## Slide 29: Restoration and Optimization
Restoration of L1 paths after physical link failure.
  Upon failure of a physical link, all L1 paths are notified by physical detection methods.
  Pre-defined backup L1 path could be used (old-style protection 1:1 or 1:N)
  Or, new backup L1 path could be signaled (slower timescale)
  Same applies to L0 paths
Variable restoration service
  Can backup an LSP onto another LSP which has less guaranteed resources. E.g., backup a fixed bandwidth L1 LSP with a UBR-type L2 LSP. This provides cost advantages and resource efficiency at the expense of guaranteed restoration characteristics.

## Slide 30: Layer Specific LSPs
Definition: a “Layer Specific LSP” is an LSP which only uses one type of layer in each of its hops.
  L0 LSP - a  path
  L1 LSP - an STS path
  L2 LSP - current definition of an LSP
  ATM LSP - an LSP that only uses ATM links
Could use Traffic Engineering control plane to create Layer Specific LSPs
  Constraint based routing could be used to select paths which only used links that supported a requested label type.

## Slide 31: Service Interfaces
Integrated L0/L1/L2/L3 switch can offer services at each layer.
  Layer n traffic can use layer 0..n LSP.
  Layer n traffic can be protected using layer (n+1) for degraded service.
MPLS used to setup LSPs at each layer.
OSPF + CR-LDP
IP Forwarding
ATM UNI
FR-UNI
Circuit app
Path app
IP hop-by-hop path
L2 LSP
L1 LSP
L2 LSP
L1 LSP
L1 LSP
L0 LSP
L0 LSP
IP service
ATM service
FR service
Leased line service
path service
L3
L2
L1
L0
API
Control Protocol
Notes: Various services can be provided to external customers using the same L0/L1/L2/L3 network.
IP Service could be provided using normal IP hop-by-hop connectionless means, or by MPLS LSPs at different layers.
  Optical startups are essentially trying to do IP over L0 LSPs
ATM and FR service require that the API provide call services. These are not provided by MPLS because MPLS only provides connection service. Call service functionality would include:
  Address resolution (NSAP -> IP, or X.121 -> IP)
  Handling call parameters like accounting.
  Connection management (PVC, SPVC, SVC type connection service)

## Slide 32: References
D. Awduche, Y. Rekhter, J. Drake, R. Coltun, “Multi-Protocol Lambda Switching”, Internet-Draft, Work in Progress, <draft-awduche-mpls-te-optical-1.txt>, Jan. 2000
D. Basak, D. Awduche, J. Drake, “Multiprotocol Lambda Switching Issues”, Internet-Draft, Work in Progress, <draft-basak-mpls-oxc-issues-00.txt, Jan. 2000
S. Shew, “Fast Restoration of MPLS Label Swiched Paths”, Internet-Draft, Work in Progress, <draft-shew-lsp-restoration-00.txt>, October 1999