## Slide 1: Overview of Multicast Deployment

## Slide 2: Multicast Past
Flood and Prune
DVMRP/PIM DM - global RIP
Mbone
Virtual network tunneled over unicast Internet
Not scaleable
Third party resource dependencies
Difficult to manage and support

## Slide 3: Multicast Present
MBGP
Explicit Join - PIM Sparse Mode
MSDP
Native Multicast Topology
Scales better
Attempt to resolve chicken and egg problem
Experiment in static address allocation
MIX (Multicast Exchanges)

## Slide 4: MBGP
RFC 2283
Replaces topology discovery aspect of DVMRP
Brings with it all the administrative policy control of BGP
rtr1#sh ip b sum
BGP router identifier 204.212.44.129, local AS number 65000
BGP table version is 1203950, main routing table version 1203950
67686 network entries and 135169 paths using 11160882 bytes of memory
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
129.250.16.125 4 2914 340238 2665 1203950 0 0 1d20h 67481
rtr1#sh ip mbgp sum
BGP router identifier 204.212.44.129, local AS number 65000
MBGP table version is 300278
7773 network entries and 14967 paths using 1261701 bytes of memory
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
129.250.16.125 4 2914 340270 2666 300278 0 0 1d20h 7192

## Slide 5: MSDP
draft-ietf-msdp-spec-02.txt
Allows PIM Sparse Mode domains to talk to each other
MSDP peers exchange SA (Source Active) messages with each other to inform each other of sources within its domain
Borrows heavily from BGP protocol design
Resolves third party resource dependency issues
Enables anycast RP

## Slide 6: Anycast RP
draft-ietf-mboned-anycast-rp-04.txt
Within a PIM domain, can deploy more than one RP per group range
Sources and Receives use topologically closest RP (based on unicast routing metrics)
Provides fast convergence in case of RP failure
Provides load sharing for the RPs
Uses MSDP to share source info. Between the RPs

## Slide 7: Anycast RP Example
RP
RP
RP
AS 234
MSDP
MSDP
MSDP
Src
Src
Src
Rec
Rec
Rec
10.0.0.1
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.3
192.168.0.2

## Slide 8: Moving Forward
Beyond MBGP/MSDP/PIM SM
  PIM Express/Single Source PIM
  BGMP/MASC
MPLS/TE

## Slide 9: Beyond MBGP/MSDP/PIM SM
Shortcomings of MBGP/PIM SM/MSDP Model
  Lots of Join/Prune state in the network scales poorly when dealing with extremely large number of (> 100,000) groups
  MSDP SA flooding mechanism doesn’t scale well with extremely large number of groups
  Causes traffic concentration at the RPs
  Combination of mechanisms are complex to manage
Not a problem today, but should be addressed now to continue scaling for tomorrow

## Slide 10: PIM Express/Single Source PIM
Uses PIM SM and IGMPv3
If last hop router knows source, PIM (S,G) joins can be sent directly without using the RP rooted shared tree.
Works for Inter-domain case much like MSDP currently does, although without SA flooding

## Slide 11: Current MBGP/MSDP/PIM SM Model
Receiver
Last Hop Rtr
First Hop Rtr
RP
Source
Join
Data
Prune
MSDP
IGMP (*,G)
PIM (*,G)
PIM (S,G)

## Slide 12: Single Source PIM
Receiver
Last Hop Rtr
First Hop Rtr
RP
Join
Data
IGMP (S,G)
PIM (S,G)

## Slide 13: Pros and Cons of Single Source PIM
Pros
  Interoperates with existing MSDP/PIM SM model
  Reduces state required for multicast forwarding
  Simplifies multicast management and debugging for 90% of applications
  Uses mechanisms proven to work in Inter-domain case
  Prevents traffic concentration at the RPs
  IGMPv3 support in Windows 2000 SP1(?)
Cons
  Need Host OS support for IGMPv3 and API changes
  Need IGMPv3 support in routers, DSLAMs and switches
  Need changes to routers with directly connected hosts

## Slide 14: BGMP
BGMP (Border Gateway Multicast Protocol)
  Uses shared tree between PIM domains
    Bi-directional trees
    Joins sent toward root PIM domain
  Single root domain per group
    Each domain assigns multicast group addresses
    MASC is the currently proposed group address assignment mechanism
  Needs changes to existing MBGP implementations
    Group addresses need to be carried in MBGP

## Slide 15: MASC
MASC (Multicast Address Set-Claim)
  Hierarchical assignment of group addresses
    Top of hierarchy is at peering points
    Provides for aggregation in multicast group addresses
    Dynamic mechanism at top level allows for address collision resolution
  Addresses are allocated with lifetime
    Address allocation must be renewed
    May not receive same space at renewal time
    Reclamation of space at renewal time is possible
    Permits reallocation of space

## Slide 16: Why MPLS/TE for Multicast?
Allows for finer granularity traffic engineering than possible with IGP metric manipulation
Optimizes existing bandwidth in a network, aka constraint based routing/forwarding
Makes it possible to implement different class of service for multicast traffic
May make billing for multicast easier by making available finer granularity of traffic accounting

## Slide 17: How to TE for Multicast using MPLS
There are multiple ways to construct label switched paths for multicast
  Using event triggers
    intercepting PIM join/prune messages
    topology (multicast routing table) changes
    traffic driven (multicast forwarding cache changes)
  constraint based via administratively weighted links
  RP placement based tree constructing based on user/traffic classification
  use MASC/BGMP to influence tree construction

## Slide 18: Some of the Challenges with using MPLS/TE for Multicast
Multicast is more dynamic, which makes LSP engineering more challenging
Multicast label switched path construction would be dependent on multicast tree branching, which makes constraint definition for multicast LSPs more challenging
Coexistence of SPT and shared tree requires intelligence in constructing multicast LSPs
Increases the degree of complexity of operating a multicast supported network
Pricing multicast is challenging, and pricing different class of service for multicast is….

## Slide 19: Alternatives to MPLS/TE
maintaining separate topology and link cost for multicast, using some of the work currently going on in IGP working groups such as ISIS
running separate IGPs for unicast and multicast
disabling multicast on select interfaces
manual manipulation of unicast routing table that PIM uses for multicast tree construction

## Slide 20: Work in Progress
draft-farinacci-multicast-tagsw-01.txt
draft-farinacci-multicast-label-part-00.txt
draft-ooms-mpls-multicast-01.txt
draft-acharya-ipsofacto-mpls-mcast-00.txt