## Slide 1: Virtual Private Networks
Bruce Case Network Consultant
InterNetworking Systems, Service Provider Networks
bcase@lucent.com

## Slide 2: VPN - Definition
A class of network services that use public or shared network resources to emulate the characteristics of a private network
They use shared facilities and equipment
Are (partly) managed, engineered and operated by a public network operator
Are comparable to private network solutions in performance, reliability, security and Quality of Service (QoS)

## Slide 3: Privacy and Security
Traffic Isolation
  Virtual mean many (potentially competing) customer s using the same network
  Closed User Groups
  Data must be kept private
  Private and Overlapping IP Address Space must be Isolated
Trust
  There is a Trust relationship between the Service Provider and the customer
  Trust can vary according to the data type
  Oddly Enough - Trust has Never been an issue until VPNs implemented with IP technologies came into being

## Slide 4: Implementation: Past, Present and Future
Leased Lines
  Extremely high margin
  Very predictable Network Behavior
  Highly Bandwidth intensive
  Very Difficult to Provision
Layer Two Technologies: Frame Relay and ATM
  USD$10 Billion (and growing) service industry Worldwide
  Very Predictable Network Behavior
  Difficult to Provision

## Slide 5: Implementation: Past, Present and Future (Con’t)
IP and Tunneling (IPIP, IPSec, GRE, etc)
  IP’s Greatest Strengths
    Everyone talks to Everyone
    Automatic Provisioning
  Tunneling schemes do not scale
    Very difficult to provision
    do not carry routing protocols (OSPF, RIP, etc)
    Routing Processor Intensive
  Only applicable to Small Enterprise Do-It-Yourself implementations or when the customer does not Trust the Service Provider

## Slide 6: Implementation: Past, Present and Future (Con’t)
MPLS
  Adds some predictability to IP WAN networks by guaranteeing network path
  Enables Traffic Isolation and Closed User Groups (Standards still being defined)
  Maintains IP’s Strength of Automatic Provisioning
    Adds the ability to provision non-optimal paths for best effort traffic

## Slide 7: Implementation: The Real World
Configuration Issues
  Only MPLS offers Automatic Provisioning of services
    can still provision path as desired
  All Other technologies must provision each path
    The N Squared Problem
QoS
  Only ATM, and to some extent, Frame Relay CIR, Offer QoS
  MPLS does NOT have
    Minimum/Maximum Bandwidth Guarantees
    Traffic Policing
    Latency and Jitter guarantees
      Prevented by Variable length packets
Obviously, a mixture of MPLS and ATM technologies are the best path to a Service Oriented VPN

## Slide 8: The Expensive part VS. the Easy part
Profit
Margin
Service Provider Value
Access
Closed User
Groups
Leased/Managed CPE
Integrated Internet Access
SLA with minimum
bandwidth guarantees
IP Telephony
Managed Security
Consulting & Integration
Applications Design
Vertical Applications
Web Hosting Service
Collaboration Services
Electronic Billing
Extranets
}
The Expensive Part
{
The Easy Part

## Slide 9: Thank You!
Bruce Case Network Consultant
InterNetworking Systems, Service Provider Networks
bcase@lucent.com