## Slide 1: Internet Protocol Voice

## Slide 2: Internet Protocol Voice
Voice quality indistinguishable from the telephone network
Call setup times indistinguishable from the telephone network
No additional customer equipment required
No change in user behavior patterns required
Leverages silicon economics
IP Voice…

## Slide 3: Key Concepts Major Communication Networks
IP NETWORK
SS7
NETWORK
TELEPHONE
NETWORK
IP Voice…

## Slide 4: Key Concepts Digital Circuit Switch
Integrated functionality
Proprietary code
Proprietary service development
IP Voice…

## Slide 5: Key Concepts SS7 Enabled Softswitch
Distributed functionality
Open platforms
Open interfaces enable new services
Overflow to PSTN when quality is unacceptable
IP Voice…

## Slide 6: Capital Cost Comparison Cost Per Ports For 32,256 Ports (U.S. Dollars)
Call Control Server 27.72
Route Server 2.78
SS-7 Gateway .10
DSO Cross Connect 23.25
Total 53.91
Single Integrated Purchase
Total $95.00
Softswitch
Circuit Switch
Source: Level 3 Estimates
IP Voice…

## Slide 7: Capital Cost Comparison
Time To Double
Performance Per Dollar
(mo)
Currently a distributed softswitch costs 40% to 45% less than an equivalent circuit switch
Given relative price-performance improvement rates, softswitches will be much less expensive over time
Distributed components with open interfaces will spur development of new applications
IP Voice…
Circuit Switch 80
Softswitch 20

## Slide 8: Voice Quality Factors Public Telephone Quality
Latency (delay two-way) Less than 250 msec
Call setup delay 1 to 3 seconds
Signal loss Less than 0.5 dB
Packet loss 1 in 10,000
Speech Quality Less than 2.0 ITU PSQM Score
IP Voice…

## Slide 9: Actual Quality Measurements
Latency (delay two-way) 200 ms 120 ms
Call setup delay 3 seconds 2 seconds
Signal loss ~ 0 dB ~ 0 dB
Packet loss 1 in 1,000,000 N/A
Speech Quality 1.1 PSQM 1.1 PSQM
IP Voice…
Softswitched
Circuit Switched

## Slide 10
(3) Voice for Facilities Based Resellers
1
2
3
4
5
Level 3 Enhanced all-IP-based Network
1. Customer routes call to nearest Level 3 Gateway via one of the multiple
connectivity options
2. SS7 signaling path is routed through the Level 3 Softswitch to the local telephone
company servicing the called party
3. Call is converted to an IP format and routed to a Level 3 Gateway near the called party
4. Level 3 converts call back to a traditional switched format and routes it to the local telephone company
5. Local telephone company routes call to called party

## Slide 11
Global IP Network
Self Healing SONET/SHD rings
Multi-conduit fiber optic network (WDM)
All IP, no circuit switching
21 international city networks
50 U.S. city networks
Transatlantic and transpacific cable

## Slide 12: Summary
IP Voice works today
Softswitch architecture assures PSTN quality today
IP Voice is less expensive today and improving faster than PSTN
Tomorrow, IP Voice will be better quality than PSTN, have more features and be far less expensive
IP Voice…