## Slide 1: APNIC Open Address Policy Meeting
Special Interest Group Session
APNIC Reverse DNS in Operation
March 2nd, Korea, Seoul

## Slide 2: What is Reverse DNS?
What is ‘Reverse DNS’?
  Forward DNS maps names to numbers
    whois.apnic.net  203.37.255.97
  Reverse DNS maps numbers to names
    203.37.255.97  whois.apnic.net

## Slide 3: IN-ADDR.arpa
Hierarchy of IP addresses
  Use in-addr.arpa domain
    INverse ADDRess
  IP address is written L to R
    203.37.255.97
  Reversed in in-addr.arpa hierarchy
    97.255.37.203.in-addr.arpa

## Slide 4: IN-ADDR.arpa
whois
61 203 210 211..
63.62.61.in-addr.arpa
Root DNS (‘.’)
edu
com
arpa
ph
net
apnic
in-addr
Mapping numbers to names - ‘reverse DNS’
62
63

## Slide 5: SOA Record
63.62.61.in-addr.arpa IN SOA
machine.that.is.primary.NS myself.my.address (
2000030201 ; SOA Serial Number
; YYYY MM DD XX
3H ; Refresh time
30M ; Retry time
2W ; expiry
12H ) ; minimum Time To Live (TTL)

## Slide 6: NS Records
; Still in ‘63.62.61.in-addr.arpa’
IN NS ns1.my.forward.domain.
; See RFC 1035
IN NS ns2.my.forward.domain.
; At least two nameservers
IN NS ns.some.faraway.site.
; See RFC 2182 - backup in
; case your site is down

## Slide 7: PTR Records
; PTR records ‘point’ an IP to a hostname
; In current $ORIGIN, 63.62.61.in-addr.arpa
1 IN PTR router.my.forward.domain.
; IP address 61.62.63.1
2 IN PTR mail.my.forward.domain.
; IP address 61.62.63.2
; …
254 IN PTR last.machine.in.subnet.

## Slide 8: Always Remember the Dot.
Forgetting the trailing dots is bad
  BIND appends the current domain ($ORIGIN) to a record without a trailing dot
Zone file entry
3 IN PTR machine.no.dot
$ host 61.62.63.3
3.63.62.61.IN-ADDR.ARPA domain name pointer
machine.no.dot.63.62.61.in-addr.arpa

## Slide 9: Good Books for DNS
Images copied from http://www.ora.com/ and Copyright O’Reilly and Associates

## Slide 10: Tell the World About It
Reverse delegation are not automatically setup as part of an IP allocation
    Request form
  http://www.apnic.net/db/domain.html
    Verifies configuration, adds to APNIC database, creates in-addr.arpa domain object in WHOIS database

## Slide 11: The Form

## Slide 12: Filling out the Form
Domain:
63.62.61.in-addr.arpa
Descr:
Country:
Admin-c:
Tech-c:
Zone-c:
Server and Office subnet
KR
(APNIC) NIC-HDL
(APNIC) NIC-HDL
(APNIC) NIC-HDL
nserver:
Ns1.my.forward.domain
ns2.my.forward.domain
ns.some.faraway.site

## Slide 13: Filling out the Form (cont)
remarks:
Any other remarks (optional)
notify:
Mnt-by:
password:
mnt-lower:
Database emails this if object changes
Maintainer-object
password-for-above
Same-as-mnt-by
Your E-mail:
Source:
Myself@my.address
APNIC

## Slide 14: ERR: Nameserver mismatch

## Slide 15: Request sent to APNIC

## Slide 16: Successful Update

## Slide 17: When are changes active?
Zone files rebuilt from database every morning (Mon-Fri) at 10am
(10am, UTC +1000)
Changes after 10am Friday not visible until 10am Monday
ns.apnic.net automatically reloads zone files if required
dns-admin@apnic.net for requesting human assistance

## Slide 18: Questions?