## Slide 1: Quality of Service (QoS) Technical Overview

## Slide 2: What is QoS?
Quality of Service - a set of performance attributes associated with a service
The performance of IP packet flows through networks
QOS Metrics
  Availability
  delay (latency)
  delay variation (jitter)
  throughput (average and peak rates)
  packet loss

## Slide 3: QoS, Who Cares?
QoS is the way to implement premium “business class” IP services over the Internet (businesses don’t think the internet is reliable)
QoS allows carriers to offer premium services to business customers based on SLAs (Service Level Agreements) resulting in higher revenues
Allows service providers to safely over-subscribe their network resources without compromising premium services or multi-media performance
QoS is the key technology that will allow large scale deployment of VOIP and Video over IP, services that many believe can only be achieved over ATM connection oriented virtual circuits (layer 8 = religion)

## Slide 4: The Need for QoS
The carrier edge aggregates and mediates QoS between thousands of subscribers at the entrance to the public network
Notes: The characteristics of internet traffic are evolving once again. While the expansion of data traffic continues unabated a new challenge has been added, convergence. Traditional voice carriers are rushing to move their voice traffic on to the internet while multimedia content providers add real time information like voice and video into the IP arena.
Increased bandwidth for LANs and new broadband access services such as xDSL and Cable networking are delivering the capacity needed to support new applications. Improved optical technologies like DWDM are providing the added capacity needed in the core of the Internet. However, increases in network bandwidth alone do not deliver the guaranteed quality of service and high reliability demanded by critical applications.
The emergence of time sensitive applications like Voice over IP and Video over IP have introduced a requirement to provide service better than the “Best Effort” delivery traditionally provided by IP.
A secondary driver behind Quality of Service is a business need for service providers to differentiate themselves from their competitors. If all any service provider offers is “Best Effort” service why should a potential customer choose one over another.
Quality of Service (QoS) refers to the ability of network equipment to differentiate data streams and apply various queuing policies on the data to offer customers differentiated services for time sensitive packets. Quality of Service is in essence a bandwidth management function ensuring that enough resources are allocated to support time sensitive applications and shield them from the bursty nature of the typical data traffic.
Service Level Agreements between the customer and the Service Provider provide monetary penalties if end-to-end performance metrics are not met while providing a commodity for the Service Provider to sell at premium prices.
Internet
Traditional Data Traffic

## Slide 5: QoS Prerequisites
Wire speed forwarding at routers/switches
  The edge switch must have sufficient processing power to process packets at full wire-rate while also performing classification, rate policing, and statistics harvesting for billing with no degradation in performance
Carrier class reliability
Advanced routing protocols to quickly recover from node or link failures
End-to-end behaviors (PHBs such as Diff Serv) which implies good queuing and scheduling algorithms on each router/switch
Good network design

## Slide 6: QoS Components
Separating traffic into queues according to classification
A policy manager that implements SLAs (Service Level Agreements) using QoS, used to configure routers and switches
Diff Serv and Int Serv
Traffic marking, policing, and shaping on ingress
Filtering traffic for security or mapping to VPNs
Active output queue management
Packet discard algorithms (RED, WRED, SRTCM, TRTCM) to prevent congestion and enforce traffic priorities
Traffic shaping to a rate on egress
ATM CoS mapping and layer 3 IP AF (Assured Forwarding)
Guaranteed minimum bandwidth, CAR (Committed Access Rate)

## Slide 7: QOS Terminology
Tail Drop
  Drops arriving packets when buffers in queue are full, can lead to network meltdown due to TCP global synchronization
RED = Random Early Discard
  Queuing algorithm for congestion avoidance that randomly discards packets from queues in an attempt to prevent TCP retransmits simultaneously on all flows
WRED = Weighted Random Early Discard
  A variant of RED that attempts to weight queues for random early discard
TCM = Tri-Color Marker
  Marks packets either green, yellow or red depending on whether they conform to rate variables
DSCP = Diff Serv Code Point
  Defined by RFC 2597 and 2598, 6 bit patterns in the DS field

## Slide 8: QoS - Queuing and Scheduling
FIFO - First In First Out queuing, definitely not compatible with QoS since high priority packets can get stuck behind low priority packets
Strict priority scheduling - services higher priority queue whenever there are packets present, can lead to starvation of lower priority queues
Fair Queuing or Round Robin Scheduling (RR) - services all queues within a traffic class round robin assuring that all queues get equal treatment
Weighted Fair Queuing (WFQ) - queue is serviced based on a weight proportional to the bandwidth allocated to it
Class Based Queuing (CBQ) - different queues used for each traffic class
Hierarchical Class Based Queuing - Classes have sub-classes, forming a hierarchical tree. A sub-class might share bandwidth with other sub-classes in the same higher level class

## Slide 9: QoS Architectures
Diff-Serv (Differentiated Services)
  Per Hop Behaviors (PHBs) based on network-wide traffic classes
  Flows are classified at the edge router based on rules, and are aggregated into traffic classes, allowing scalability
  Diff Serv uses the IP header TOS byte (first 6 bits), which is renamed the DS field
  Initially Diff Serv only defines two values for the DS field, DE (default) = 000000 = best effort, and EF (Expedited Forwarding) = 101110 = low latency, low jitter PHB, AF defines other DSCP values
Int-Serv (Integrated Services)
  Defined by RFC 1633 (RSVP)
  RSVP requires resource reservation at each hop end-to-end for each IP packet flow, as well as end-to-end signaling along nodes in the path
  This architecture does not scale well and breaks down when domain boundaries are crossed
  Int Serv appears to be best suited to the edge of the network where IP flows can be managed at the CPE or Edge Router and then mapped onto Diff Serv or MPLS LSPs

## Slide 10: End-to-End QoS
ISP-B
ISP-C
ISP-D
ISP-A
Notes: In order for true Quality of Service to be realized the policies must be enforced from end-end throughout the internet. Customer, Service provider, and carrier business models are all factors – end-to-end service cannot be reasonably provided until all providers have QoS Service level Agreements (SLAs) at each peering point. Also customers will demand statistics and metrics to prove they are receiving high QoS levels.
Not only must we insure that enforceable agreements are negotiated between a number of core ISPs it is equally important that client applications have the ability to ensure QoS forwarding on their local network segments.
Good QoS design must move the majority of control functions as close to the applications as possible. Ideally core routers will have a limited set of packet forwarding rules optimized to enable wire line throughput.

## Slide 11: DiffServ Standard Code Points
Expedited Forwarding (EF)
  A Single DS Code Point
  Minimizes Delay and Jitter
  Provide Highest level QoS
  Out of Profile Traffic is Dropped
Assured Forwarding (AF)
  Four Classes of Service with three drop precedence per Class
  Twelve DS Code Points
  Out of Profile Traffic may be demoted
Notes: Differentiated Services uses the eight bit Type of Service in the IP datagram header to mark DiffServ service criteria. RFC 2474 defines a six bit DS Code Point utilizing the space formerly used for ToS, (first 6 bits).
Expedited Forwarding (EF) will provide low delay low jitter service for real time applications like voice and video. The DS Code Point defined in RFC 2598 for EF is
Codepoint 101110
Assured Forwarding as described in RFC 2597 provides four classes of IP forwarding service for “Better then Best Effort” routing. The four classes, each with three drop preference levels, provides for extremely flexible policy building within a DiffServ Domain.
Class 1 Class 2 Class 3 Class 4
Low Drop Prec | 001010 | 010010 | 011010 | 100010 |
Medium Drop Prec | 001100 | 010100 | 011100 | 100100 |
High Drop Prec | 001110 | 010110 | 011110 | 100110 |
The RFCs define only these thirteen code points out of the sixty four available for DiffServ. This leaves lots of flexibility for experimentation and proprietary implementations.

## Slide 12: End to End and Top to Bottom
ISP-B
ISP-C
ISP-D
ISP-A
Presentation
Application
Session
Transport
Network
Data Link
Physical
Top-to-Bottom QoS
End-to-End QoS
802 SBM
RSVP
RSVP
DiffServ and MPLS
QoS
Enabled
Application
RSVP
DiffServ
SBM
QoS API
802 SBM
Presentation
Application
Session
Transport
Network
Data Link
Physical
Notes: There are a variety of tools being implemented today to provide IP Quality of Service. The current consensus it that there will be no one “Silver Bullet” application that will clear all the hurdles and solve all of the problems associated with QoS, different tools will be used in different network segments.
RSVP/Intserv -- Int-Serv, Integrated Services and it’s signaling protocol the Resource Reservation Protocol RSVP can provide truly end to end, top to bottom QoS service. QoS enabled transmitting applications send a transmission spec to receiving clients who respond with a reservation request which essentially reserves bandwidth hop by hop through the network for the session. This is difficult to implement in the Core Internet and does not scale up.
802 SBM -- An outgrowth of the IEEE 802.1p, 802.1Q and 802.1D standards, Subnet Bandwidth Management protocol is used to provide QoS support on 802.x LANs (Ethernet, Token Ring, FDDI,etc.) The protocol provides functionality for a Requestor Module to request service levels from a Bandwidth Allocator on the local segment. The protocol is not bound to a particular QoS method, the specs are written using RSVP for an example of possible mappings, but it will work with the older ST-II protocol as well.
MPLS - Multi Protocol Label Switching, as the name implies, is not really an IP QoS tool at all. It is a traffic engineering tool that permits a packet to be classified at the ingress point of a network, in this example an ISPs core network, and provided with a twenty bit label that will define the next hop interface the data will traverse. At the next hop router the label is stripped off, looked up in a table, and used to choose a new label and next hop interface. The result is improved network performance because only the MPLS label needs to be looked up and overall treatment of traffic is decided at ingress to the MPLS network.

## Slide 13: Differentiated Services Network Components
Edge Device
MF Classification
DSCP Marking
Flow Policing
Traffic Conditioning
MPLS Tagging
Core Routers
BA Classification
Per Hop Behaviors
Policy
Manager
Customer
Network
Notes: There are three key components in the DiffServ architecture, the Edge Device, Behavior Aggregates, and the Policy. The QoS development work for the ERX is focused primarily on implementing Edge Router functionality.
The Edge Device is the first place in the domain that DiffServ rules are put into effect. The edge device can be the originating workstation of an IP Datagram, or many hops into a packets path. The border router connecting to a separate DiffServ Domain will always be an Edge Device.
The Edge Device is responsible for doing Multi Field Classification of incoming packets. MF classification typically include the IP Source/Destination address, TCP/UDP Source and Destination Ports, the Protocol field in the datagram header, and the IP Type of Service field or DS-Field. Other fields can be examined but these are the most common. The traffic is compared to some listed attributes and if it matches the Edge Device will Mark the appropriate DS Code Point in the IP Datagram header.
Marking is used to assign the traffic flow to a Behavior Aggregate (BA). The BA will define the treatment of the packet by routers within the local DS Domain. A BA defines how all traffic sharing some common characteristics will be treated.
Once the MF Classifier has identified and marked the packet for the appropriate service type the policing function kicks in. Since the point is to sell differentiated service levels the policing functions ensures that customers get what they pay for and pay for what they get.
The edge device is also responsible for implementing the Per Hop Behavior associated with Behavior Aggregates. Per Hop Behaviors are essentially queuing policies that define how much of the available bandwidth is allocated to each of the various Behavior Aggregates.

## Slide 14: Differentiated Services Network Components
Edge Device
MF Classification
DSCP Marking
Flow Policing
Traffic Conditioning
Core Routers
BA Classification
Per Hop Behaviors
Policy
Manager
(PDP)
Customer
Network
Peer
DiffServ
Domain
PEP
PEP
Notes: BA Classifiers are the core routers in a DiffServ Domain. The classification function is limited to examining the DS Field (TOS Byte) in the IP Datagram header and then applying the appropriate Per Hop Behavior. Core routers need to forward traffic and should not be burdened with complicated classification/policing functions.
Policy -- The Diff-Serv Policy is the overall set of rules that define Diff-Serv operation within the domain. The overall policy framework consists of two elements, the Policy Decision Point (PDP) and the Policy Enforcement Point (PEP). The Policy Decision Point, here shown as a generic Policy Manager, is responsible for storing and disseminating the Diff-Serv policies. It may be co-located within the PEP or in a remote server and may provide only static policy definition or may respond dynamically to event driven policy requests from the PEP. The connection shown here is a TCP communication channel running a signaling protocol called Common Open Policy Services (COPS).
The PEP classifies, polices, and marks datagrams to enforce a domain’s Diff-Serv Policy.
Metering is also a requirement of a DiffServ Policy. In order to ensure that Service Level Agreements are fulfilled traffic aggregates will be metered in the PEP and PDP to assure policy compliance.

## Slide 15: Differentiated Services & Convergence
<footer>Unisphere Solutions
MPLS Overview – 1-11-00 - <number>
LER
LER
MPLS
Network
Ingress
Egress
LER
LER
LSR
LSR
LSR
LSR
LER
FEC - a group of packets that are forwarded the same way
  Packets are mapped to FECs which are then mapped to LSPs
  LSPs have different capabilities to handle different traffic types
Mapping FECs with different traffic types to traffic engineered LSPs enables convergence of voice, video, & data with differentiation of service
Notes: Forwarding Equivalence Classes (FECs) are mapped onto LSPs. Initially, a FEC is based upon IP destination address. So all traffic heading to the same destination can be mapped into the same FEC which is then mapped onto the same LSP. However, traffic engineering allows traffic heading for the same destination address to be in different FECs depending upon things such as traffic type, delay characteristics, or even based upon the application that was used to generate the traffic (e.g., FTP). The classification process at the edge of the network determines which FEC a particular packet belongs to. By enabling traffic engineering to be utilized in an IP network, MPLS resolves the other two problems facing the service provider community: namely, convergence and service differentiation.

## Slide 16: MPLS and QoS/CoS
Traffic engineered LSPs determines QoS for the LSP
Mapping packets to FECs and then to LSPs determines path through the network and Class of Service (CoS) for the “flow”
Packets can be mapped to FECs via different criteria
  Traditional shortest path routing algorithms (defacto)
  Use of DiffServ byte in IP header
  Application of policy and traffic engineering (bandwidth, delay)
  Further examination of IP packet contents to application layer
Notes: See previous slide for explanation.

## Slide 17: Configuration Options

## Slide 18: Policy Manager
CLACL
DB
Classifier
Access
Control List
RLP
DB
Rate
Limit
Profile
TC
DB
Traffic
Class
Policy
DB
Policy
INTERFACES
Notes: Policy manager will provide the CLI interface to build data bases which can be drawn from to implement a Policy. Each data base will contain traffic specifications individually specified. These data bases are global in nature. When building a Policy the user specifies input from one or more of these data bases. The policy is then applied to an interface.

## Slide 19: Policy Manager

## Slide 20: Policy Lists and clacls

## Slide 21: Policy Actions
Set Next IP Interface
Set IP Next-Hop Address
Packet Filtering
Set Traffic Class
Set IP ToS
Set Rate Limit Profile

## Slide 22: Policy Routing
Policy routing allows users to create access lists to determine how data will be sent through the router
T3
T3
If IP_ADDR = 192.168.23.0 0.0.0.255
then
Forward out ATM 4/0.1
192.168.23.39
192.168.23.25
192.168.23.47
192.168.23.75
192.32.48.243
140.250.10.98
200.204.97.65
ATM 4/0.1
Notes: This is not a QoS service per se, but is a service that can provide QoS by diverting designated customer traffic flows to links that are provisioned for a given QoS. The ERX can classify packets such that flows from a given customer interface are routed to a designated logical interface or IP Address.
Policies are ordered lists of access lists and associated policy actions. Packets that match an access list in a policy have the specified action applied to them. Policies are defined but they are not enabled until they are attached to an IP interface. Packets received on an IP interface have the attached policy applied to them.
Policy actions include:
1. Set Next IP Interface - Packets are routed out the specified IP interface, even if their IP Destination Address would have indicated another forwarding route.
2. Set IP Next-Hop Address - Packets are forwarded towards the specified IP address, even if their IP Destination Address would have indicated another forwarding route. The specified IP address can be local or many hops away. The router forwards the packet just as if the IP Destination Address were the IP Next Hop Address.
3. Packet Filtering - Packets matching the access-list are dropped. Note that since the RX supports IP SA validation independently of packet filtering, there is no need to explicitly configure filters to implement anti-spoofing
4. Set Traffic Class - Packets matching the access list are assigned to the specified traffic class.
5. Set IP ToS - Packets matching the access list are stamped with the specified ToS.
6. Set Rate Limit Profile - Packets matching the access list are processed through a token bucket pair. The rate limit profile specifies whether to mark or drop packets that are in excess of the rate limits.

## Slide 23: Classifier
CT3
T1 28
T1 2
T1 1
T1 2/1
IP #1
T1 2/2
IP #2
T1 2/3
IP #3
.
.
.
Rule set #1
Rule set #2
Rule set #1
Rule sets can be applied to either ingress or egress traffic on an interface
Notes: The classifier FPGA supports the notion of rules and rule sets. A rule is a match clause based on fields of an IP header. A two-field rule matches on a range of IP SAs and a range of IP DAs. For example, a two-field rule can specify a match if the packet SA is in subnet 192.168/16 AND the packet DA is in subnet 10/24. A five-field rule specifies ranges for the typical five fields of the IP header – the IP protocol, IP SA and DA, and TCP/UDP source port and destination point.
Rules are combined into rule sets. The ERX ingress processor supports rule sets of up to 32 five-field rules, or rule sets of up to 64 two-field rules. The FPGA supports up to 8000 rule sets per line card. Rule sets are assigned one to an IP interface. A single rule set can be shared across many interfaces, but each interface can have just one rule set attached to it.

## Slide 24: Classifier Example
CT3
5/0
T1 28
T1 2
T1 1
5/0:2/1
IP #1
5/0:2/2
IP #2
5/0:2/3
IP #3
.
.
.
Rule Set #1
1. If DA = x, place data in GOLD
2. If DA = y, place data in BRONZE
3. If DA = z place data in BE
Rule set #2
Rule set #1
Rule Set #2
1. If SA = a, send data out 4/0.1
2. If DA = z, place data in BE
3. If DA = z and SA = a send data out 3/1:1/1
Rule set #1
Notes: In this example we show how rule sets can be applied at the IP interface level on a given line card to control the flow of data into or out of the box.
In this example we have a CT3 line card in which we have defined various T1 subchannels. For the second T1 subchannel we have group the DS0s into three subinterfaces, each with their own IP interface.
On IP Interfaces #1 and #3 we have implemented the same rule set which classifies various incoming data streams based on the destination address of the data into either the GOLD, BRONZE, or BEST EFFORT traffic classes. This will allow us to set up differentiated services for each traffic class.
On IP Interface #2 we have implemented a unique rule set that forwards data to specific outgoing ports based on the combination of source and destination addresses, as well as classifying some of the data as part of the BEST EFFORT traffic class.
A specific line card can support up to 8000 rule sets. Each IP interface can only support one rule set. A single rule set can be used on more than one IP interface, for example the rule set on IP interfaces #1 and #3. For a multiport card the total rule sets supported (8000) would be split across all of the ports.

## Slide 25: QoS Services - Per Customer Fairness
The RX has the ability to stop aggressive customers from starving lower load customers for bandwidth
Core
CPE
Over aggressive customers will fill their buffers and drop packets while lower load customers will be able to send data without an issue
Each interface has its
own set of data buffers
Process works the same on both ingress to the core, and egress from the core
RX
Edge
Packets
Dropped
Notes: The RX supports 10,000 queues per line card. When aggregating traffic from access interface towards the core, separate queues for each source access interface protect low traffic customers from more aggressive customers. The more aggressive customers will reach their queue limits first and not effect the low traffic customers.
In the core to access direction, the access interface queues provide the same protection – if one customer generates a large burst of traffic from the core, that customer will see packet drops if the burst exceeds his queue size, while other customer queues are still buffering packets.
The buffer management algorithms skew the customer queue lengths based on traffic class, providing deeper buffering to queues that are higher priority. Also the queue lengths vary based on whether the packet memory is lightly or heavily loaded.

## Slide 26: QoS Services - Gold Service
Differentiated service which allocates bandwidth to different data classes based on relative importance of the data
T3
T3
Data queues are
weighted to offer
different levels of
service (SLAs)
Notes: Service Providers may wish to offer differentiated service to a class of packets, such that those applications (packets) are given access to resources (bandwidth, buffers, queues) dedicated for that class. If the provider wishes to offer only a relative differentiation, packets can be scheduled using Weighted Round Robin (WRR) scheduling. A WRR scheduler allocates bandwidth to queues such that out of all queues with traffic presenting, a queue receives a bandwidth share equal to its configured weight, divided by the sum of the weights of all queues with traffic to be scheduled. The RX Edge router scheduler is implemented in hardware, so that there is no software overhead, even as the numbers of queues to be serviced grows to over 10,000.

## Slide 27: Bandwidth Management - The Scheduler
BE
BE
Bronze
Bronze
Gold
Traffic
Class
Level
VC #1
VC #2
Sub
Port
Level
OC3
Port
Level
1
2
4
1
2
1
2
100.224 Mb
50.112 Mb
14.32 Mb
28.64 Mb
57.27 Mb
33.41 Mb
16.70 Mb
Notes: The bandwidth management consists of a hierarchical scheduler with 3 levels of weighting. The top level corresponds to the relative buffer weight associated with queues competing for the same class. The next level corresponds to the relative class weight associated with QoS classes competing for the same interface. The bottom level corresponds to relative interface weights competing for the same port.
Calculation for available bandwidth for VC#1, VC#2: OC3 = 150.336 Mb Total Bandwidth BW = ( (relative weight ) / (sum of weights) ) * AvailableBandwidth
For VC#1 For VC#2 BW = ( ( 2 ) / ( 3) ) * 150.336 BW = ( ( 1 ) / ( 3) ) * 150.336 BW = 100.224 Mb BW = 50.112 Mb
Calculation for available bandwidth for VC#1 and VC#2 QoS Classes:
For VC#1 BWGold = (( 4 ) / ( 7 ))*100.224 BWBronze = (( 2) / ( 7 ))*100.224 BWGold = 57.27 Mb BWBronze = 28.64 Mb
BWBestEffort = (( 1 ) / ( 7 ))*100.224 BWBestEffort = 14.32 Mb
For VC#2 BWBronze = ( ( 2) / ( 3 ) ) * 50.112 BWBestEffort = ( ( 1 ) / ( 3 ) ) * 50.112 BWBronze = 33.41 Mb BWBestEffort = 16.70 Mb

## Slide 28: Scheduler - Packet Processing Example

## Slide 29: Congestion Management
QUEUE - Tri Color Marking with policing
Red
Drop
Threshold
Yellow
Drop
Threshold
Queue
Limit
As egress queue depth reaches first threshold, red packets are dropped, at second threshold red and yellow are dropped, and once queue is full back pressure is applied to ingress queue
Notes: The queuing system uses drop eligibility to do two different types of packet dropping. The simpler form is called dynamic color-based threshold dropping. Each packet queue in the system has two color-based thresholds as well as a queue limit. Green packets are never dropped until the queue limit is reached. Yellow packets are dropped when the yellow threshold is reached. Yellow and Red packets are dropped when the red threshold is reached.
The second form of dropping is Random Early Detection, conforming with the IETF AF PHB. This mechanism is a more TCP-friendly mechanism that does not drop all packets that are drop eligible, but instead randomly drops a deterministic number of drop eligible packets based on a dynamic mechanism based on Averaged Queue Lengths. Details on RED are provided in RFC 2597.
When configuring Bandwidth profile limits for the purpose of marking the data as Red, Green, or Yellow the commands use the terms Committed, Conformed, and Exceeded. Below is the relationship between configuration term and color term:
Configuration: Color:
Committed Green
Conformed Yellow
Exceeded Red

## Slide 30: References
RFC 2267, Network Ingress Filtering: Defeating Denial of Service Attacks which employ IP Source Address Spoofing, P. Ferguson, D. Senie, January 1998
RFC 2474, Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers, K. Nichols, S. Blake, December 1998
RFC2475, An Architecture for Differentiated Services, S. Blake, D. Black, December 1998
RFC 2597, Assured Forwarding PHB Group
RFC 2598, An Expedited Forwarding PHB
draft-ietf-diffserv-af-04.txt, Assured Forwarding PHB Group, J. Heinanen, F Baker, January 1999
draft-heinanen-diffserc-trtcm-00.txt, A Two Rate Three Color Marker, J. Heinanen, R Guerin, March 1999
draft-heinanen-diffserv-srtcm-00.txt, A Single Rate Three Color Marker, J. Heinanen, R, Guerin, March 1999