## Slide 1: Architects of an Internet World
Michael S Cox, CTO
Carrier Data, Asia Pacific
michael.cox@alcatel.com.au
Notes: 1
1
1
2
2
Welcome.
My name is Michael Cox,
I’m the Chief Technology Officer for Alcatel’s Carrier Data Division within Asia Pacific.

## Slide 2
QoS Enterprise and Carrier Interactions
2
APRICOT
000
Notes: Today I would like to give a brief overview on some of the problems and their proposed solutions for providing end-to-end QoS over IP internetworks.
In particular the main focus of this presentation is examining the interaction that will exist between the Enterprise space (consisting of people, applications, roles, terminals and servers) and the Carrier space (consisting of customers, priorities, relationships, sites and their respective SLAs).
I will also touch on the need for inter-carrier bandwidth exchanges and concepts such as negotiating and purchasing megabit-minutes :-)
But before we start ...

## Slide 3: What is QoS?
QoS specifications are typically included as part of an SLA (Service Level Agreement)
QoS specifications vary for each service (SDH, Voice, ATM, IP, …)
in general QoS is many things to many people.
QoS encompasses the specification of a set of objective and subjective parameters relating to an offered service and the subsequent delivery and verification of those parameters.
Notes: 2
2
QoS is also an umbrella term that has been used to refer to collections of technologies, protocols and even specific products.
An SLA is a contract between the consumer and their provider and may include appropriate access, network, service, fault handling and restoral guarantees.
SDH is characterised by (Severely) Errored Seconds ...
Voice by Mean Opinion Scores, Blocking probs ...
ATM services by PCR, MBS, CDV, CLP …
and finally IP by GFR, DiffServ, Latency, Loss, Throughput … upper/lower bounds.
Focus: IP can be specified using LUB and GLB.

## Slide 4: QoS for Data transport
Connection QoS
Packet QoS
Differentiates Connection performance
Parameters define virtual circuit performance
Data is populated within intermediate nodes
Each node implements per-connection queuing
Scales poorly (core nodes require per connection state)
ATMF, IETF RSVP
Differentiates Forwarding performance
Parameters define packet forwarding behaviours
Data is populated within the packets (marking)
Each node implements a set of standard PHBs
Scales well (no core node connection state)
IETF Differentiated Services
Notes: Connection QoS refers to packet behaviours that include: Average cell rate, peak cell rate, maximum burst size, transmission latency, cell delay variation, cell loss probability ...
Proposals such as Stoica et al and Westberg et al implement connection QoS in a slightly different manner. But still suffer from other issues.
Packet QoS better maps to physical implementation. Networks are dimensioned, forwarding engines ingress packets into buffers, perform advanced queue servicing etc.
Packet terms include Weighted Fair Queuing, Priority Queuing, Weighted Random Early Discard etc

## Slide 5: Application Requirements
Interactive realtime applications
  Voice/Video teleconferencing
  Multiplayer gaming systems
  Closed-loop monitoring and control systems
Non-interactive, realtime applications
  Streaming audio/video systems
  Transaction network systems
Non-interactive, non-realtime applications
  File transfer services, Web browsing, e-mail
Applications typically specify connection QoS
Notes: Applications in general fit three broad categories:
Interactive realtime apps require very low latency and and very low delay variation to function optimally.
Non-interactive realtime appls can tolerate larger latencies and delay variations by deploying a de-jitter buffer at the receiver end (typically .1-2 seconds)
Non-realtime apps can tolerate very large latencies and thus large delay variations with no permanent loss of information (greater than 1 second)
Of course these can be further differentiated in terms of performance and cost by adjusting the packet discard probability. Ie. Games etc.
Apps typically specify a Connection QoS requirement.

## Slide 6: Enterprise Requirements
Granularity:
  Guarantees provided to individual micro-flows
  Policies controlled on a per user/app/term basis
Convergence:
  Cost reductions and productivity improvements
Flexibility:
  Extensive array of features and services
Policies:
  Users: Application, Roles, Priority, Time
  Resources: Terminals, Servers, Networks
Notes: Enterprises are typically focused on providing specific users of specific applications on specific terminals a pre-determined quality of service defined in terms of connection QoS parameters.
The applications expect the network to provide the necessary performance characteristics to meet the users defined policy capabilities. This preferably includes a form of busy tone signalling.
Busy tone should only be generated when there are insufficient resources available to support the user or application at that point in time.
RSVP and Integrated Services use explicit resource signalling and reservation to provide this functionality.

## Slide 7: Integrated Services
Defines three modes of operation:
Best Effort Service
  The network promises nothing but does its best to deliver the packets end to end.
Guaranteed Service
  Provides an assurance of throughput, max latency and no discard for conforming packets.
Controlled-Load Service
  Provides a performance level similar to that of an uncongested best effort network for conforming packets.
Notes: The best effort service is the default service and requires no explicit reservations or signalling.
The guaranteed service provides a guaranteed throuput, maximum latency, low loss service. It performs metering and policing at the ingress. Out of profile packets receive BE performance. Applications provide a Tspec and Rspec. Bursts may be optionally shaped to conform.
The controlled load service provides the equivalent of an uncongested best effort service. It provides no latency or delay variation guarantees but will provide low loss services to conforming traffic. It performs shaping and policing at the ingress. Out of profile packets receive BE performance. Only a Tspec is required.

## Slide 8: Provider Requirements
Scalability:
  No connection state within the core
  No connection signalling within the core
Reliability:
  Network redundancy and resiliency to failure
Monitoring:
  Ability to verify and report performance data
Policies:
  Customers: Priority, business relationships
  Products: Differentiated service offerings

## Slide 9: Differentiated Services
Expedited Forwarding
  Egress rate limited priority queueing.
  Minimised end-to-end latency, minimal packet loss.
Assured Forwarding
  Medalist classes - Platinum, Gold, Silver, Bronze.
  Dimensioning can control latency and loss.
Default Best Effort Forwarding
  We are familiar with this one!
Others
  LBE, EF-D, ...
Defines several Per Hob Behaviours (PHBs):
Notes: Differentiated services implement Packet QoS mechanisms directly.
These mechanisms are defined as Per Hob Behaviours (PHBs) and have been generalised by the IETF in Traffic Conditioning Blocks (TCBs).
The current PHBs are EF, AF,

## Slide 10: Architectural Options
Provider
Enterprise
Enterprise
3
DiffServ
This option is unlikely due to the lack of explicit signaling and feedback.
2
RSVP Intserv
DiffServ
RSVP Intserv
This is where we appear to be heading as the best of both worlds.
RSVP Intserv
RSVP Intserv
1
RSVP Intserv
This is where we are now, however there are a number of concerns.

## Slide 11: IntServ End-to-End
Enterprise
Policy Server
WAN Bandwidth
Manager
SLA
Policy Manager
Traffic
Manager
Enterprise
Policy Server
WAN Bandwidth
Mgr
Private
Provider 1
Provider 2
Lines
+ : It works!
+ : Supports per connection QoS signaling to applications
- : Carrier scalability limited due to core state info
- : Requires continuous keepalive checking across core
LAN
LAN
RSVP Intserv
1
RSVP Intserv
RSVP Intserv
Path
Path
Path
Path
Path
Resv
Resv
Resv
Resv
Resv

## Slide 12: IntServ to DiffServ
Enterprise
Policy Server
WAN Bandwidth
Manager
SLA
Policy Manager
Traffic
Manager
Enterprise
Policy Server
WAN Bandwidth
Mgr
Private
Provider 1
Provider 2
Lines
+ : Provides excellent core scalability (minimum state)
+ : Supports per connection QoS signaling to applications
- : Provider requires a complex traffic manager
- : It’s not quite here yet … but almost
LAN
LAN
DiffServ
1
RSVP Intserv
RSVP Intserv
Path
Path
tunneled
Path
Path
Resv
Resv
tunneled
Resv
Resv

## Slide 13: CAC - COPS
Connection Admission Control (CAC)
  The CAC function determines if a specific flow of traffic can be supported across the network
  Once a CAC has approved a flow, traffic shapers, markers, policers and meters are needed to enforce the agreed-to traffic profile.
Common Open Policy Services (COPS)
  COPS is a protocol and an architecture for supporting centralised QoS policies
  COPS populates the network elements with the appropriate TCBs and provides the necessary signaling support.
Policy
Server
Bandwidth
Manager
Provider 1
LAN
LAN
Resv
tunneled
Resv
COPS accepts and installs TCB
Notes: The CAC performs its functioning by keeping a record of current QoS commitments and current network load.
Network performance should never cause a CAC accepted session to degrade below its QoS guarantees. (CAC must not be overly optimistic).
The CAC should never refuse a session that could have been safely accepted and guaranteed. (CAC must not be overly pessimistic).
This provides the familiar “busy tone” concepts of the PSTN.
We can use COPS to provide the CAC signaling.

## Slide 14: Bandwidth Exchanges
Provider 1
Provider 2
Provider a
Provider b
TM
TM
TM
TM
Providers a and b can compete against each other in terms of price and bandwidth by offering Mbm of transit capability from Provider 1 to 2
These advertisements can be dynamically driven from the traffic managers (TM) which can recognise cyclical traffic patterns
A developing area of interest within the standards bodies

## Slide 15: Further Information
Integrated Services
  http://www.ietf.org/html.charters/intserv_charter.html
  RFC 2205: RSVP Version 1
  RFC 2210: Use of RSVP with IntServ
  RFC 2211,2212: Controlled Load and Guaranteed Service
Differentiated Services
  http:// www.ietf.org/html.charters/diffserv_charter.html
  RFC 2474: Definition of DS Code Field
  RFC 2475: Architecture for DiffServices
  RFC 2597,2598: Assured and Expedited Forwarding PHBs
Resource Allocation
  http:// www.ietf.org/html.charters/rap_charter.html
  RFC 2748: Common Open Policy Server Protocol
  RFC 2753: A framework for Policy Admission Control
  RFC 2749: COPS Usage for RSVP
General Information
  http://www.internet2.edu/html/about-i2.html
Visit Alcatel @ http://www.alcatel.com