## Slide 1: Peering in the U.S.
William B. Norton
Chief Technical Liason, Equinix, Inc.
<wbn@equinix.com>
APRICOT
Seoul, Korea

## Slide 2: Peering Decision Tree Agenda
Share Research Paper and Facilitate Peering
  Peering Decision Tree White Paper
  Peering Contact Database
Get Feedback – Document Regional Issues
Notes: I’m here to share information about some research work I’ve done with respect to ISP interconnection. In particular, how and why do ISPs approach peering relationships? What is the mindset of the Peering Coordinator, the one chartered with roles ranging from traffic engineering and analysis to peering negotiation to implementing ISP interconnection? This is the first attempt to document current practices, and one result of interviewing the ISP Peering Coordinators is the Peering Contact Database which I’ll bring up later. Today I’d like to present the information collected to date and see where the observations made in the US are also observable in AP region. I more importantly would like to see how they are differ.

## Slide 3: This is NOT about:
1) Peering Politics, who is evil
2) Religion, content provider peering
3) Who pays, who gets the value
Ground rules:
Remain positive–Goal is to:
Capture the essence of peering process, and
facilitate peering among those seeking peering relationships.
<noone willing to speak up publicly on their peering policy but willing to talk to me…>
Definitions…
Notes: Since peering discussions sometimes get a bit heated, I’d like to highlight some specific non-goals. We won’t highlight peering politics or religious positions such as “Peering is the right way to grow the Internet.” While interesting who pays and who receives value from peering is a complex topic beyond the scope of this narrowly focused research. So during this presentation I will try and keep discussions on track, seeking to document current practices, and see what can be done to facilitate interconnecting those who wish to interconnect.
Now, so we are all speaking the same language, let’s start with some definitions.

## Slide 4: Def: Peering and Transit
Customer vs. Peer - What happens when ISPs peer?
What happens when they buy transit?
Working Def: Transit is the business relationship whereby one ISP
sells access to all destinations in its routing table.
Working Def: Peering is the business relationship whereby ISPs
reciprocally announce reachability to each others’ transit customers.
Peering
USNet
EastNet
WestNet
Peering
Transit
Transit
Transit
Notes: The most important and misapplied terms are peering and transit. Peering is defined as the business relationship by which ISPs exchange routing information about each others customers. The picture shown above shows WestNet announcing reachability to its customers to USNet and visa versa. Same occurs at EastNet announcing yellow customers and receiving announcements to blue. The key is that EastNet and WestNet do not have reachability to each others customers. The fact that USNet peers with both is inconsequential. Only USNet has access to both in this configuration. Transit on the other hand is a business relationship where the transit provider announces its entire routing table to the transit customer. In this way, transit customers of USNet are the only ones who gain access to the entire net diagrammed above. So how can WestNet and EastNet gain access to each others customers?

## Slide 5: Larger Example: Peering & Transit
CompNet
Peering
USNet
EastNet
WestNet
Peering
Transit
Transit
Peering
Transit
Transit
Transit
Transit
Notes: In this slightly more complex example, EastNet and WestNet buy transit from CompNet. By definition, transit provides EastNet and WestNet access to CompNets entire network routing table. In this way, WestNet and EastNet gain access to each others network as well as CompNet’s Red customers. An alternative would be for WestNet and EastNet to seek peering arrangements with each other and CompNet, but that gets us ahead of ourselves.

## Slide 6: Peering Decision Tree Paper
Based on Interviews with 50+ ISP Peering Coordinators revealed…
3 General Phases of Peering:
1) Identification of Potential Peer – the who
2) Initial Contact and Qualification – the why
3) Implementation Discussions – the how
Notes: This research paper focuses on how ISPs think peering relationships; current practices on how they seek, obtain, and implement peering relationships. Interviews with about 50 ISPs highlighted three rough stages of establishing peering. We’ll discuss each one in turn, starting with the motivations and context in which most ISPs operate.

## Slide 7: I. Phase 1: Identification of Peer: Traffic Engineering Data Collection and Analysis
Motivations:
Reduce load on expensive Transit service
Traffic src/dest
Measure or Intuit
Usage-based Billing
2nd Goal: Lower latency
ResultTop 10 list
Part of larger business deal
Seek
interconnection
Transit
$$
Transit
$$
ISP A
ISP B
Transit ISP
Notes: All ISPs start out needing to purchase transit from an upstream ISP. Starting out, one simply cannot connect to all destinations on the Internet, and peering with all ISPs is neither practical nor an overnight activity. So ISPs purchase transit services at a cost that can be quite high. From that point on, most ISPs continue to operate and build out their network infrastructure into new regions. ISPs have articulated several motivations for peering. First, they seek to establish peering relationships to reduce the demand on their expensive transit circuit. How? Two methods: traffic capture and analysis to determine src/dest pairs or intuition. Another motivation is to maximize consumption of bandwidth – this is attractive for those who charge on a consumption basis. By engineering peering you achieve lower latency and by engineering minimize packet loss and therefore maximize the TCP thruput. The end result is that the ISP comes up with a top 10 list of potential peers with supporting traffic data and analysis to warrant peering as beneficial to both ISPs.

## Slide 8: Phase 1: Identification of Potential Peer

## Slide 9: II. Phase 2: Contact & Qualification, Initial Peering Discussion
How to make contact with potential peer ISP?
E-mail person or peering@<ispdomain>.net
Exchange point participant list
Tech-c/admin-c from DNS/ASN registries
Engineering Forums NANOG, IETF, RIPE, etc.
Trade shows: speakers and booth staff
Target ISP sales force
Target ISP NOC

## Slide 10: II. Phase 2: Contact & Qualification, Initial Peering Discussion
Once contact is made…
Sometimes Mutual NDA
Exchange BiLateral Peering Agreement (BLPA)
Traffic Data justification shared
  One basis: Peering iff PeeringCost < TransitSavings?
Requirements Exchange
  (e.g. Must be at n Public Peering Points, xMbps, private peering migration strategy, etc.)
Either Party may walk away…..
If still interested, implementation discussion…

## Slide 11: Phase 2: Contact and Qualification

## Slide 12: III. Phase 3: Implementation Discussions
  How to interconnect?
  Direct Circuit-based Interconnection
  VS.
  Exchange-Based Interconnection
  White Paper available:
  “Interconnection Strategies for ISPs”
  Email request to: <wbn@equinix.com>

## Slide 13: Cost Comparison at n=5
costDCfn()=(n-1)*C/2
C=OC-3 @ $11,400
n=5
costDC=(4)*$11,400/2
costDC=$22,800/mo
costExchfn()=BDC+(n-1)*x/2+Racks
BDC=OC-12 @ $23,000
n=5, 1 Rack@$1500
costExch=$23,000+(4)(200/2)+$1500
costExch=$24,900/mo
More expensive to use Exchange-Based
Interconnection Strategy at n=5. N>5?

## Slide 14: Exchange-based vs. Direct Circuit Interconnection
See http://www.nanog.org/mtg-9905/norton.html for slides
Direct Circuits Model
MUX Big Pipes Model
Dark Fiber Model
For “Interconnection Strategies for ISPs” e-mail wbn@equinix.com

## Slide 15: 9 Exchange Selection Criteria
Telecommunications Access Issues
Deployment Issues (getting in & up)
ISP Current Presences (there yet?)
Operations Issues (restrictions?)
Business Issues (neutrality/alignment)
Cost Issues ($$)
Credibility Issue (backing,attraction) 
Exchange Population (side effect)
Existing vs. Emerging Exchange?

## Slide 16: Value of the Internet Exchange
VExchange
NParticipants
Cost
Of Coming In
(Circuits+
Routers+
StaffTime)
VCapacity
The Exchange Startup Hump
First Carrier(s)
First ISP(s)
First CP(s)
Critical Mass Point (Vexchange=CostExchange)
Large Facility Scaling

## Slide 17: Exchange Environment Evaluation

## Slide 18: IV. Summary
Findings from Interviews
Three phases to peering:
1) Identification of Potential Peers
2) Contact & Qualification
3) Implementation Discussions
9 Selection Criteria for Exchanges
(Vary in relative weighting of criteria)

## Slide 19: Acknowledgements
Thanks to those who helped with the draft: Ren Nowlin (PGExpress/Onyx), Joe Payne (IXC), Dave Diaz (NetRail), Jake Khuon (Frontier GlobalCenter), Patricia Taylor-Dolan (Level 3 Communications), Cathy Wittbrodt (Excite@Home), John Curran (NextLink), Jeff Rizzo and Dan Gisi (Equinix), Tom Ryan (NewEdge), Alex Bligh (GX Network), Steve Meuse (GTE), Aaron Dudek (Sprint)

## Slide 20: Peering Decision Tree

## Slide 21: Peering Contact Database
Initiated at NANOG 17 Peering BOF: Pass the hat
  Handwrite: PeeringEmailTo: peering@<ispdomain>.net if avail
  Handwrite: AS Number
  Cross out stuff you don’t want in spreadsheet
  This process  ISPs Will Peer
wbn will email Excel Spreadsheet to each participant
Method for LINX peering contact info merging?
Peering Whie Paper? E-mail: wbn@equinix.com