## Slide 1
Standard Expectations for Peering Agreements Prepared for APRICOT 2000, Seoul, Korea Lauren F. Nowlin - ren@onyx.net

## Slide 2: Peering
Terminology - NAPs, MAEs, Peering & Transit
Background - Peering Tidbits
Common Peering Philosophy
Common Corporate Concerns
Common Security Concerns
Common Dispute Resolution Methods
Shameless Plug For Regional Traffic Distribution
Reminders To Be Given To Customer Support, Sales & Marketing Regarding Limited Disclosure
Onyx Peering Contacts & Online Documents

## Slide 3: Terminology
‘Network Access Point’ - NAP - $ - local loops(s) Often carrier neutral location to enable many participants to exchange traffic between their respective customers via aggregate circuit(s) to a FDDI, FastEthernet, Gigabit Ethernet,or POS platform. Relatively inexpensive cross-connects between participants are encouraged at modern/emerging NAPs
‘Metropolitan Area Exchange’ - MAE - $ - local loop(s) In 1994 MFS, now WorldCom, won a government bid to create Internet exchange points on the coasts. MFS is the only carrier with access into the facilities. Most MAEs are legacy FDDI and have a poor image due to congestion. ONYX participates on the new ATM platform at 3 locations: East, West & Dallas

## Slide 4: Terminology
‘Autonomous System Number (ASN)’ The unit of routing policy in the modern world of exterior routing. An AS is connected group of one or more IP prefixes run by one or more network operators which has a SINGLE and CLEARLY DEFINED routing policy. Routing policy decisions such as geography, AUP (Acceptable Use Policy) compliance and network topology can influence decisions regarding the use of a single ASN or multiple ASNs.
‘Public Peering’ - $ - port + local loops Uses NAPs/MAEs to carry traffic to networks seen as peers
‘Direct/Private Peering’ - $$ - local loops Enables 2 networks to exchange traffic between their respective customers without port fees via point-to-point circuits

## Slide 5: Terminology
‘Purchased Peering’ - $$$ - reduced port charge + local loops Enables 2 networks to exchange traffic between their respective customers with 1 of the 2 bearing the cost of the interconnection. Consequently, the network with the established traffic would be receiving income & would not be responsible for carrying the traffic end-to-end, as in a transit relationship
‘Purchased Transit’ - $$$$ - port + local loops Purchased transit from an NSP gives ONYX full reachability & connectivity to the Internet. A transit provider would carry ONYX’s traffic to networks not seen as peers or customers. The ‘funnel’

## Slide 6: Tidbits
Peering should imply equivalent value to both networks
Peering was a handshake deal between network operators until 1995 when UUNET decided to charge smaller peers for use of their global network.
Peering is now considered a corporate asset & legal concern
De-peering is awkward and generally worked around
‘Grandfather clauses’ apply to legacy networks that would now need to pay for transit. Today peering is generally settlement free
Some peers require a settlement on traffic that exceeds 2:1 ratio
Smaller peer, at a lesser cost than transit, often purchases first round of direct circuits or cards for the other peer network’s routers in exchange for routes of customer

## Slide 7: Common Peering Philosophy
24 x 7 NOC with trouble ticket capability
Exchange traffic at 2 or more locations
Commit to joint capacity planning if peering is direct
Relationship does not include transit on behalf of peer’s customers
Security concerns should be worked through jointly unless under court order or denial of service attack
Routes should be consistent or will be dampened by peer
SPAM messages should be prevented
Neither party should discuss network of peer with clients or media
Can be a customer of a service if not Internet Access (either free/peering or product/transit)

## Slide 8: Common Corporate Concerns
Non-Disclosure Agreements
  separate document (often more explicit than existing NDA)
  combined in base document
  document tracking
  host/location specifics under non-linked web location
Exchange traffic at 2 or more locations - redundancy
  waived for international locations
  covered via transit in many cases
Security concerns should be worked through jointly unless under court order or denial of service attack
Can be a customer of a service if not Internet Access (either free/peering or product/transit)

## Slide 9: Common Security Concerns
Non-Disclosure Violations
  how would you know if the peer has violated the NDA?
  how do you keep the details out of Sales & Marketing?
Trouble Shooting Outages / Events
  exchange of configuration details
  language, terminology or accessibility barriers often exist
Shared Fabrics and 3rd Party Colocation
  quality of 3rd party remote hands
  details regarding ‘who is there’ or ‘who peers with who’

## Slide 10: Common Dispute Resolution Methods
United Nations Commission on International Trade Law (UNCITRAL)
  global negotiations held in New York, NY
  each peer selects an arbitrator and 3rd selected by UNCITRAL
  proceedings are in English
American Arbitration Association / Governed by State of larger peer
  US bias
  Requires local court jurisdiction
Senior or Executive Staff Intervention
  inexpensive
  larger network generally prevails

## Slide 11
ONYX Networks, Inc.- AS6067 Global Exchange Participation
23 Planned Interconnect Locations
+120 ASNs Exchange Traffic with AS6067
LAX & NYC are direct peers only

## Slide 12: Shouldn’t Discuss Specifics With Customers
Most peering relationships are bound by NDAs
Peering relationships are evolutionary
Not all reasons for peer relationship are black & white
Product vs. Policy - Sell! Once peering is mentioned as an option it is very difficult to sell transit
Regulatory efforts may be underway that are not evident
Aggregate quantities to POPs should be sufficient detail

## Slide 13: Willing to Discuss Under NDA
Fully-executed NDA must be in hand prior to start of conference call. Prefer conference calls with Sales person on the line to prevent finger pointing.
Questions from potential & existing customers can/should be submitted to peering@<whatever>.net - Outages should be documented via noc@<whatever>.net - All mail should be answered with a carbon copy to Sales person
Sales, Marketing, Business Development, Engineering & Peering folks review RFI details to ensure accuracy
Good procedure for capacity planning to ensure high volumes of traffic are well distributed among peers for customers. Communicate.

## Slide 14: Contacts & Documents
Lauren F. Nowlin, Director of Peering & Interconnects, ren@onyx.net
peering@onyx.net - read by several parties
http://www.onyx.net/peering/
General sources
  http://www.data.com/issue/991007/peering.html
  http://www.nanog.org/mtg-9910/peering.html
  http://www.nanog.org/mtg-0002/agenda.html (NAP update links)