## Slide 1: High Speed Router Requirements
Scaling the IP Services Core

## Slide 2: Outline
Introduction
Internet Scaling and the New IP Infrastructure
Requirements and Anatomy of a Next Generation Core Router
Requirements for Market Success
Conclusions

## Slide 3: Next Generation Core Routing
Plummeting cost of raw bandwidth
Continuous improvement in semiconductor development
Rapid growth of the Net
Users and Applications
Fundamental importance of IP

## Slide 4: Router Evolution – Not Just Speed
Connectivity
Reliability
Performance
Intelligence
Scale
1980’s 1990’s
Today
The New IP
Infrastructure
Time

## Slide 5: Next Generation Router Design Goals
Predictable performance characteristics
  Line Rate forwarding under any conditions
  Low and predictable latency
  Class of Service with performance
Interface Rates up to current optical limits
Ability to support wide range of interfaces
System reliability
Support IP Service Provider requirements
  e.g. MPLS, multicast, etc.
Interoperability with installed base

## Slide 6: Anatomy of a Next Generation Router
System and network control
Line rate packet scheduling and forwarding decisions
High speed interface interconnect
Three Balanced Elements
Operating System
Packet Processing
Forwarding Fabric

## Slide 7: A Closer Look at the Anatomy
Route Calculation
Software flexibility
Stability under stress
Complete Interoperability
Forwarding Fabric
I/O card
I/O card
Internet Processor
Routing Operating System
Update
Forwarding table
Forwarding table
Packet Forwarding
ASIC based performance
Integration of features affecting packet flow
Oversized capacity
Balanced fabric throughput and route lookup speed

## Slide 8: The Feature Requirements Curve
Late 1980s
Microprocessor-based packet processing
Internet focused routing O/S
Rate of feature Introduction
1990s
Late 1990s
ASIC-based packet processing
Switch Fabric
Packet Processing
Operating System
General purpose routing O/S

## Slide 9: Routing Operating System Requirements
Focused on provider scale and features
Modular design
  High reliability
  High maintainability
  Aggressive feature introduction
Rich, robust routing protocol implementations
Complete interoperability
Operating system
Protocols
Interface Mgmt
Chassis Mgmt
SNMP
Security
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Many Aspects of Product Success
System Design
  Sufficient capacity and room for growth
  Leading edge but implementable design
Software Credibility
  Interoperability with installed base
  Robustness under Internet-level stress
  Meeting the feature requirements curve
Hardware Expertise
  Leading edge ASIC design and verification
  Complete range of manageable interfaces
Quality manufacturing and support team and processes

## Slide 11: Observations/Conclusions
IP Demand and growth in available bandwidth fuel the need for next generation routers
Requirement is for Speed with robust control, high reliability and capabilities for value-added service delivery
Barriers to market entry are continuously rising

## Slide 12
http://www.juniper.net
Copyright © 2000, Juniper Networks, Inc.