## Slide 1: Computer Telephony Integration
An Overview
Srinivas Mulugu
smulugu@cisco.com

## Slide 2: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 3: CTI Definitions
“ A technology platform that merges voice and data services at the functional level to add tangible benefits to business applications”…
Today, one needs to automation, IN services of the telephony world and databasing applications of the data world…

## Slide 4: CTI: Allied Technologies
Voice recognition
Screen-based Telephony
Video processing
Web-based “Follow-me” applications
Voice compression techniques
Voice Messaging & Voice Mail
Interactive Voice Response Systems
Voice-to-text Applications (&vice-versa)
Fax-to-text Applications (& vice-versa)
Media Processing
Technologies

## Slide 5: CTI: Why Now?
Early 90’s Failed to have Major Influence
What’s Changed?
  Improvements Sftware/Hdware/Standards
  Open Standards Becoming Norm
  Internet: Fast, WW, Pervasive Transport
  Cultural Change in Enterprise
    IT Recognized as Key Weapon
    Move to Outsourcing, Hiring Consultants/SI’s
    More Mobile Workforce
    Emphasis on Team/Comm Up & Down Org.

## Slide 6: CTI: Why now ? (cont’d…)
IP has become THE integration tool
IP Telephony is now recognized & accepted
IVR & Voice-recognition software on networking & IT components
Outsourcing of call center operations
  Customer in US, Company in UK, Call center in Malaysia

## Slide 7: The Problem State
The PSTN network has global, ubiquitous access to devices
Home
Work
Grocery Stores
Convenience Stores
Airplanes
Cars
Restaurants
. . .
The IP network has global, ubiquitous access to data
Customer Info
Product Info
Email
News, weather
and sports
Research Information
Directory Services
. . .
So how do we get the best of both worlds ?
Notes: Telephones are available almost anywhere -- even on the airplane. We all know how to use them, and we all have access.
The Internet has the information we need, including email, business updates and research information. This information cannot be accessed without a PC connected to the Internet -- but what if you’re on the road or in your car?

## Slide 8: Why the Problem Exists
Registry
Services
Voice Msg.
Polling
Click-to-Dial
Directory
Services
FAX Over IP
Unified
Messaging
Web
Conferencing
Web Based
Paging
Voice over IP
Proprietary
HW/SW
IP-Based Enhanced Services
Voice Mail
FAX
E-Mail
Web Access
Notes: The problem is a technical one that centers on the architecture of the PSTN and IP networks, and how companies have chosen to bridge those networks.
Proprietary solutions are expensive, make a service provider a captive to a specific vendor, and don’t allow everyone to take advantage of new technologies.
Bridging telephony and the ‘net is necessary to achieve the enhanced services that solve the problem.

## Slide 9: Moving away from black-boxes…
PROTOCOL GENERATION
PROGRAMMING TOOLS
CALL CONTROL
NETWORK MANAGEMENT
DATABASE SERVICES
REDUNDANCY SERVICES
ACCESS SERVICES
T1/E1
MF/MFC
Tones
Application
Creation
Routing Tables
Software
Libraries
Templates
Scripts
Resource
Management
Live Upgrade
Host Backup
Database
Synchronization
Diagnostics
Alarms
SNMP
Telnet
Multihost
FTP
Security
Log/Trace
Configuration
Host-Based
Application
Notes: ICS is an integrated set of features and tools that operate inside VCO series switches that are designed to simplify programming, facilitate information access, and enhance management and administration without forfeiting flexibility or control. The result is faster time-to-market for your applications and improved system reliability. Unlike other programmable switches that force the host computer to store and manage call states, configuration databases, error processing, and network signaling, ICS lets you off-load some or all of these responsibilities to the switch.
Call Control—With ICS, your application need assume only as much of the call control burden as you determine appropriate.
Programming Tools—ICS provides you with a series of software libraries that perform many common switch functions and can be easily integrated into your software. In addition, the ICS integrated routing tables can be used to perform autonomous switch routing.
Network Management—ICS is built on an SNMP platform. This means that all switch and network events are reported as alarms and are easily accessed by both operators and application software.
Database Services—At the foundation of ICS is a sophisticated set of databases that contain the real-time information necessary to support many ICS functions.
Redundancy Services—With ICS, the redundancy automatically switching upon failure detection—is accomplished transparently to the application software.
Access Services—ICS supports various remote and local access approaches.
Protocol Generation—PC-based software utility for modifying T1/E1, MF/MFC, and tone plans.

## Slide 10: The Solution
Allow ANY existing device to access both the PSTN and IP networks -- making communication possible anywhere, anytime
IP
Notes: A solution is needed that allows people to get to information anywhere, at any time, from any access device -- be it a wireless phone, wireline phone, PC, cellular phone or payphone.

## Slide 11: IP Phone 7960
Professional, Manager -
High or Busy Telephone Traffic
Six Lines - Mix Directory Numbers or Features
Display Area: Calling Information, Feature Access Via “Soft Keys,” Additional Display Area for Value-added Services and Applications
Full Duplex Handsfree
Built-in Headset Connection
10/100 BaseT, 3 Port Switch
Expected timeframe: 2nd Quarter Calendar Year 2000

## Slide 12
IP Phone 7910
Common Areas - Hallway, Break Room, Reception or Office Cubicle
Medium Telephone Traffic
Single Line
Display Area: 2 x 24 Character Based
10BaseT
Message Waiting
Basic Features
Expected timeframe: 2nd Quarter Calendar Year 2000

## Slide 13: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 14: CTI Architectures: First Party CTI
Switch
Server
LAN
“Line Intercept” based approach
to CTI
Telephone
Network

## Slide 15: First Party CTI: Highlights
The integration is based on intercepting the line signaling that would pass between the telephone handset and the telephone switch
The attachment interface between the computer and the line can be RS-232, USB
In some architectures the handset becomes that attachment interface

## Slide 16: First Party CTI: Signaling
The computer generates the same basic signaling set as the handset: On-hook, off-hook, recall, etc.
The POTS interface generates: ringing current, supervisory tones (dial, engaged, etc.) and reversal (to indicate called-party answering)

## Slide 17: First Party CTI: Conclusion
First party CTI is a first generation architecture that essentially attempts to use the computer as a basic telephone unit, and is a primitive attempt to provide the user simultaneous access to voice lines, and data from the same console… there by integrating computer and telephone

## Slide 18: Third Party CTI
Switch
Server
LAN
“Application Programming” based
approach to CTI
Telephone
Network
CTI Link

## Slide 19: CTI Link Examples

## Slide 20: Third Party CTI: Highlights
Third Party CTI evolves from intelligent exchange between computer and the telephone switch through well defined application programming interfaces…
Simple example :
  Open Palm Pilot address book
  Select Bob Berger
  Click on Dial function on CTI pop-up

## Slide 21: CTI Protocol Messages
Functional messages
  Computer to switch: Answer call, Hold call, Make a new call, Toggle the calls, Conference the calls, etc.
  Switch to computer: CLI, DNIS, Run a program, Get data, Save data, etc.
Status messages: Call in progress
Housekeeping messages

## Slide 22: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 23: CTI Components
Networks
APIs
Business Automation Tools / Application Programs
Call Signaling Software

## Slide 24: New-World Services Accelerated by Open Model
Computing
New World
Open Distributed Computing
Centralized Mainframe
Telecommunications
Open Distributed Telecommunications
Central-Office Circuit Switch
Old World

## Slide 25: Web-Enabled Telephony
Conferencing
International LD
Any Internet-enabled
Device
Instant Messaging
Find-Me/Follow-Me
TimeShift

## Slide 26: Client/Server Model with Thinner Clients
Application
Fat
Clients
Application
Services
New World
IP Network
Thinnest
Clients
Translates Telephony DTMF & Voice to IP
Proxy Application Services for Telephony Clients
Thinner
Clients
Browser
Proxy Application Services for Web Clients
V
V
V
LAN Access
Services
Application
Web Application
Servers
Telephony Application
Servers
Application

## Slide 27: Integrating at the Enterprise
Analog Gateway
Call Manager
Voice Mail
FAX
NetMeeting
Client
NetMeeting
Client
Desktop
Digital Gateway
PSTN
Old World
PBX

## Slide 28: Putting “Intelligent Dial Tone” in the Call Path
Intelligent Dial Tone
Systems & Service Management
Unified Messaging
Inbound Call Management
Name Dialing
Personal List Dialing
Return Call from Message
SNMP and Web-Based System Administration
Logging of Call Detail Records
Web-Based Subscriber Administration
Web Access to Personal Distribution Lists,
Preferences, etc.
Telephony and PC Access
Visual and Voice Interfaces
Unified Notification
Streaming of Messages
Reach Me Services
  Multiple Reach Numbers & Schedules
  Paging, Transfer to Attendant
  Delivery to Mailbox
Find Me
Distinctive Brand Dial Tone at Off-hook
How may I help you?
Web Access with Self Provisioning
Directory Services for Community of Interest
Audio Content “Weather”, “Sports”, “Stocks”
Directory and Content Services
Outbound Call Management
Unified
Multimedia
Mailbox

## Slide 29: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 30: CTI: Application Programming Interfaces
IBM: Call path
Novell: TSAPI
Microsoft: TAPI
Sun: JTAPI
Cisco (Summa Four): Assist

## Slide 31: IBM CallPath/400
Based on AS/400 Operating System
API provides a set of procedures that can be invoked by any application program
The underlying AS/400 Operating System performs the requisite actions, like communicating with a telephone switch
Migration to Java in works…

## Slide 32: Novell’s TSAPI
Telephony Services API(TSAPI): A combined effort of Novell & AT&T started in 1992 with AT&T’s Definity PBX
Initial partners included Alcatel, Fujitsu, SDX and others
Based on ECMA standards
Move into TCP/IP from 1996

## Slide 33: Microsoft’s TAPI
Windows access to telephony through a series of DLLs
TAPI1 oriented towards First Party CTI, TAPI2 was more for Third Party
Development of the switch drivers was left to the switch vendors:
  PC-DT from Fujitsu
  Alcatel TAPI interface kit

## Slide 34: SUN’s Javatel & JTAPI
Both First & Third Party CTI supported
Interoperability with TAPI, TSAPI, CallPath, etc. so that the switch drivers written earlier could be re-used (emulation of sorts)
JTAPI defines basic telephony objects, the call model and the methods for telephony functions
Not having direct switch drivers, and the need to invoke them through drivers written for TAPI, TSAPI, etc. causes interoperability issues

## Slide 35: Who was Summa Four…?
A leading provider of programmable switches
Summa’s platforms are used as:
  Service Nodes
  Intelligent Peripherals
  Class 4 Tandem Switches
VCO API well-defined
Notes: Carrier Class Voice Quality on a multiservice packet Network

## Slide 36: Summa Four Programmable switch
In-band signaling (DTMF, MF, MFCR2)
Call-progress analysis
Integrated prompt and record
Digital conferencing
Tone generation
Switch
Matrix
Service
Resources
Intelligent Call Services
Signaling System 7
Network
Interfaces

## Slide 37: Summa Four: Service Resources
Integrated prompt and record card (IPRC)
  Full 64-kbps toll-quality voice
  Scalable sizes ranging from eight–128 prompting ports per card; four–32 record ports per card
  Remote prompt updating over LAN and PCM bus
  Prompt libraries: 16 per switch; 255 prompts per library
  Prompt storage/card: 35 minutes
  PC-based prompt-editing software
Benefits
  Reduces off-board VRU requirements
  Performs routine prompting (such as system greetings, passwords)
  Integrated with VCO API
Notes: Our Integrated Prompt and Record Card (IPRC) allows multiple libraries, prompt updates via download from NFS or the generic, and is scalable from eight to 128 ports. (A competitive product followed from Excel 18 months later, but cannot be updated on the fly, has no recording capability, and uses flash memory, which has limited write-to capacity).
The card provides a high level of voice response unit (VRU) functionality at about a third of the price of what an external VRU costs.
Typically our customers use the IPRC for all their bulk-level voice prompting, such as “please enter your debit card,” or “please enter your mailbox password,” or “you have X amount of time left on your calling card.”

## Slide 38: Summa’s Application Developers
ABNAR-TelSoft
ADC NewNet
AirNet Communications
Alliance Systems
Andros Telecom
Bellcore
Call Sciences
Castel
Cisco/Lightspeed International
Compro Technologies
Comverse Technology
CPT International
Datatronics
Dialogic
Digital Equipment Corp
e-Net
Evolving Systems
Global Interactive Technology Pte Ltd
GTE Telecommunication
IBM
In.Fi.Tel Italia
Info Systems
Infoserve Telecom Corp
INTEC
Intellivoice Communications
Interactive Technology Ltd
Interactive Voice Systems
Keuk Dong Telecom
Lacis Group B.V.
Locus Corporation
Marubeni
MDTelecom
Motorola
National TechTeam
Online Advanced Systems
ODC - A Glenayre Technologies Company
Optex
Prairie Systems
Sixbell
Stratus Computer
SynapSys
Tandem Computers
Trigem Infocom
Unisys
Vicorp
Vocalis Group plc
Voicetek
Worldwide Intelligent Network Systems

## Slide 39: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 40: CTI Standards bodies
Audio/Video Transport (AVT/RTP) Working Group in IETF
  “specify a protocol for real-time transmission of audio and video over UDP and IP multicast”
Enterprise Computer Telephony Forum (ECTF) www.ectf.org
  “ECTF facilitates the development, implementation and acceptance of Computer Telephony solutions by bringing together suppliers, developers, systems integrators and users…”
ECMA Technical recommendations on CTI

## Slide 41: CTI Standards
T.120, H.323 (ITU)
RTP, RSVP (IETF)
R.100, S.100, S.200, S.410, H.100, H.110 (ECTF)

## Slide 42: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 43: ECTI: Sever Configuration

## Slide 44: ECTF Framework

## Slide 45: ECTF Vision

## Slide 46: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 47: Network CTI: The next generation
Making the the transmission network a key component of the CTI
Intelligent call routing: toll-free, time-of-day, day-of-week, workforce-based call allocation
Database-lookup routing: dealer locator, customer-profile based routing
Network Application Managers to become SCPs
Network/IVR integration

## Slide 48: Network CTI Highlights
Network Application Manager uses MIS, CTI, IVR and IN together
Pre-routing
  Based on CLI, DNIS, identify the best resource to handle the call
Post-routing
  gathering information of that call and storing it in the databases
Intelligent call-routing using Network as a resource

## Slide 49: NAM IVR Integration
TCP/IP based, fault tolerant interface
GeoTel peripheral gateway technology
  Fault tolerant wide area link management
  Wide area link bandwidth management
  Data normalization
  Integrated alarm management
Location independence
  IVR “behind” ACD
  IVR “In front” of ACD
  Network IVR
NAM
ICM
Notes: GeoTel Enterprise IVR provides enhanced integration of Interactive Voice Response (IVR) units with the Intelligent CallRouter. Based on business requirements, ICR users can strategically position premises-based IVRs behind or in front of the ACD and/or utilize network-based IVR capabilities. An IVR can act as an ICR routing client; become a managed answering resource; and/or collect call and event data and deliver them to the ICR for use in caller segmentation and reporting.
GeoTel Enterprise IVR allows ICR users to leverage existing IVR investments while achieving higher levels of customer satisfaction. The software’s open interface enables any IVR vendor to provide support.

## Slide 50: Connecting IVRs and Other NAM Resources
Peripheral Gateways adapt external devices to the NAM
Fault-tolerance for both devices and network connections
Heartbeats monitor the state of all connections, active or not
System automatically reconfigures itself to avoid faults
Synch
Synch
Heartbeats
Peripheral Events
Device-specific links

## Slide 51: IVR and VCC

## Slide 52: Shall we take a break…?

## Slide 53: Agenda
CTI : Introduction
Classical CTI Architectures
CTI Components
  Networks
  APIs
CTI Standards
  ECTF Reference Architecture
CTI’s Next Step: Network CTI
Implementation Examples

## Slide 54: So, has anybody done it...
Anyone called a bank and checked their balance on the phone…?
  Pacific National Bank was one of the very first to do it,
  in 1991-93 time-frame using Tandem computers,
  Galaxy ACD and other CTI elements

## Slide 55: Anybody else…?
Nissan USA for debt recovery process
Operator Assistance in PSTN networks; almost all baby Bells
Skynet Car theft prevention, using CTI & GPS
Travel Agents

## Slide 56: Call Centers: Cable & Wireless Australia
Cisco’s Intelligent Call Manager
Nortel’s ACDs
4 call centers
1800 agents
Reduced costs and gave 8% improvement in productivity
80% of calls answered within 12 seconds
Average call-time cut down by 20 seconds
1999 Customer Profile

## Slide 57: Vendors with CTI Solutions/Components
Active Voice
Artisoft
Aspect Telecommunications
Aurora Systems
AVT
Datapoint
Dialogic
Edify
Ericsson
Fujitsu
Genesys
IBM
LG Information and Communications Ltd
Lucent
Microsoft
NEC
Novell
Octel Communications
Philips
Rockwell Telecommunications
Royalblue
Samsung
SAP

## Slide 58
<number>
0445_11F9_c1
© 1998, Cisco Systems, Inc.