## Slide 1: BIND v8
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 2: The New BIND, Version 8.x
Many new features
Some new RRs (resource records)
Better security
Supported by ISC, the Internet Software Consortium
  See http://www.isc.org
Primary developer/maintainer: Paul Vixie, Vixie Enterprises

## Slide 3: New Features
Dynamic Update (RFC 2136)
Change Notification (RFC 1996)
New Resource Records
New syntax for configuration files
  Tool to map from old syntax to new one: src/bin/named/named-bootconf.pl
Infinitely flexible logging
Access lists (per zone) for queries, xfers, updates
More efficient zone transfers
Improved performance for servers with lots of zones
Many bug fixes

## Slide 4: Dynamic Updates
Before, all DNS updates were done to the master files for the zone
Dynamic update allows changes to come across the network
  Updates can add or delete a single RR or set of RRs
  Updates can depend on the existence or nonexistence of a particular RR
  Updates are atomic operations
Fits things like the DHCP server paradigm well
Security tough, held up RFC for ages

## Slide 5: Change Notification
Before, secondaries probed the primary to see if they needed an update (serial number had changed)
  Refresh times were often long to reduce load on primary server
  Left zone incoherent for quite a while
Change notification has the primary notify secondaries when data for the zone has changed
  No longer a polling model
  Asynchronous notification instead (an interrupt)
Makes changes easier
Caching old answers still a problem

## Slide 6: New Resource Records
LOC resource record, for geographic location
  Latitude
  Longitude
  Altitude
  Size
SRV resource record, for service location
  Sort of WKS and MX
  Not closest server
  DNS round robin complicates things
KEY resource record, for security
  Holds public key
SIG resource record, for security
  Holds signature of a set of resource records

## Slide 7: Secure DNS
Clients can verify that they got right data
Uses new KEY and SIG records, private key is kept offline
Uses RSA encryption, problems with export remain
Signed DNS messages are bigger
Secure servers and clients are slower

## Slide 8: New Configuration Language
Jargon changes
  primary name server --> master name server
  secondary name server --> slave server
  cache file --> hints file
Filename changes
  /etc/named.boot --> /etc/named.conf
Language consists of comments and statements

## Slide 9: Config Language Comments
Comments can be C style, C++ style or shell style
# xxx type, one line only
/* xxx */ type, may span multiple lines, cannot be nested
// xxx type, also only one line
; does not begin a comment, instead it ends a statement

## Slide 10: Config Language Statements
acl - defines access control lists of IP addresses and says what they can do
include - includes a file, so zone files can stay neat and tidy
key - specifies key information for authentication
logging - specifies what to log where
options - specifies global configuration options, sets default values
server - per server options
zone - defines a zone

## Slide 11: Example, localhost zone
      // example
      options {
        check-names response warn;
        directory "/var/named";
        recursion yes;
        listen-on { 127.0.0.1; };
      };
      zone "localhost" {
        type master;
        file "inf/localhost";
      };
      zone "0.0.127.in-addr.arpa" {
        type master;
        file "inf/127.0.0";
      };
      zone "." {
        type hint;
        file "inf/cache.db";
      };

## Slide 12: A Longer Example
      options {
      directory "/var/named";
      pid-file "/var/run/named.pid";
      };
      logging {
      category lame-servers { null; };
      category cname { null; };
      };
      zone "isc.org" in {
      type master;
      file "master/isc.org";
      }
      zone "vix.com" in {
      type slave;
      file "slave/vix.com";
      masters { 10.0.0.53; };
      };
      zone "." in {
      type hint;
      file "named.cache";
      };

## Slide 13: Configuration Language Details
Looks like C or gated config file
acl keyword defines the name of an access control list and the IP addresses that it pertains to
Several acl's are pre-defined
  any: allows all hosts
  none: denies all hosts
  localhost: allows the IP addresses of all interfaces on the system
  localnets: allows any host on a network for which system has an interface

## Slide 14: Address List Format
List of IP addresses in various formats
  Dotted decimal notation
  IP prefix in the / notation
  The name of a previously defined address list
A leading ! negates an entry
If negated, access is denied
If not, access is permitted

## Slide 15: Address Lists, cont.
When comparing addresses, the first match is used
  Implies that if you have nested sets of addresses, the more specific must go first
    If 1.2.3/24; is followed by ! 1.2.3.13; 1.2.3.13 is allowed through
    Must use ! 1.2.3.13; followed by 1.2.3/24 to block host 13 but allow other hosts on the 1.2.3/24 net
Address Lists are defined with the acl keyword and used with the topology, allow-query, allow-transfer, and allow-update options

## Slide 16: Global Options
Lots of global options, 31 to be exact
  Location of servers working directory
  Location of binaries
  Location of pid file
  Whether to be a recursive server
  Whether to answer at all (access lists)
    List of hosts allowed to query server, defaults to allow all queries from all hosts
    List of hosts allowed to receive zone transfers, defaults to allow transfers to any host

## Slide 17: More Options
  What to do if name checking fails
    In master zone, defaults to fail: log and reject bad data
    In slave zones, defaults to warn: log but continuing processing
    In responses, defaults to ignore: don't check
  Resource limiting parameters, memory usage, files, stack size
  Where to listen for queries, IP address and port
  Who forwarders are, IP address
  Topology hints re. closeness of servers
  Zone transfer control
    Supports new format that puts multiple answers in one packet, faster, V8 only
    Can limit max time and size for inbound transfers

## Slide 18: Server Specification
Must specify server IP address
Can qualify it with several parameters
  bogus keyword: marks it as bogus, giving out bad data, prevents further queries to it
  transfer-format keyword: allows you to specify one-answer or many-answers
    one-answer is what all BIND 4.x servers use for zone transfers
    many-answers is new BIND 8.x format that is more efficient
  transfers and keys keywords are for future use

## Slide 19: Zone Specification
zone keyword identifies the domain name of the zone and the type of data (IN or HESIOD)
  Defaults to IN if not specified
  Requires type of server specification
    master: formerly primary server
    slave: formerly secondary server
    stub: sort of like a forwarding server, only replicates NS records of master
    hint: formerly cache or root hints
  Master and hint zones require file specification
  Slave and stub zones require masters IP address and may include file specification

## Slide 20: Options for Zones
All types of zone have lots of options that can be specified on a per zone basis
  check-names option to determine what to do with hostnames that break the rules
  allow-updates, allow-query, allow-transfer options to control who can access data from the server
  notify option to allow the master to drive the updates of the slaves

## Slide 21: More Flexible Logging
Standard syslog flexibility includes:
  Facilities to identify program type
  Severity levels to say how important messages are
  Actions to say what to do with the messages
New logging specification allows:
  Channels which name combinations of logging actions and severities
  Categories which identify types of messages to be logged
  As many category/channel pairs as you like to fine tune logging
If none are defined, sensible defaults are used

## Slide 22: Logging Channels
Each channel definition must specify where messages go
  file keyword
    Specifies path name of file
    Can limit the size of the file
    Can specify number of versions (file.1, file.2, file.3, ...)
  syslog keyword: specifies the syslog facility code
  null keyword: to /dev/null, messages are discarded

## Slide 23: Channels, cont.
Each channel can limit the severity of messages it sees
  Default level is info, to change use the severity clause
    Like syslogs severity
    Can apply to files also
Can also influence the format of the messages logged with boolean print modifiers
  print-time keyword includes date and time message was logged
  print-category keyword includes the category of the message
  print-severity keyword includes the serverity code

## Slide 24: Pre-Defined Channels
      channel default_syslog {
      syslog daemon;
      severity info;
      };
Default using syslog, daemon.info
      channel default_debug {
      file "named.run";
      severity dynamic;
      };
Default for debugging, uses SIGUSR1 and SIGUSR2 to adjust debugging level
      channel default_stderr {
      severity info;
      };
Default to stderr
      channel null {
      null;
      };
Default to bit bucket

## Slide 25: Logging Categories
Messages are divided into types called categories
Categories of messages are associated with any number of channels to accomplish the actual logging
Category names must be from this fixed list
  default: catch-all for things that aren't classified yet
  config: high level config file processing
  parser: low level config file processing
  queries: for every query the server receives
  lame-servers: lame delegation messages
  statistics: for stats

## Slide 26: Category Names, cont.
  panic: for internal server errors
  update: for dynamic updates
  ncache: negative caching (cache failures so you don't continually retry down machines)
  xfer-in: zone transfers server is receiving
  xfer-out: zone transfers server is sending
  db: all database operations
  eventlib: debugging info from the event system
  packet: dumps packets received and sent
  notify: the notify protocol

## Slide 27: Category Names, cont.
  cname: messages about pointing to a CNAME
  security: approved and unapproved requests re. acl lists
  os: operating system problems
  insist: internal consistency check failures
  maintenance: periodic maintenance events
  load: zone loading messages
  response-checks: messages like malformed response, invalid RR type, etc.

## Slide 28: Pre-Defined Category Defaults
Some categories have pre-defined default values
  Can be overwritten if you define them
      category panic {
      default_syslog;
      default_stderr;
      };
Category panic
      category eventlib {
      default_debug;
      };
Category eventlib
      category packet {
      default_debug;
      };
Category packet

## Slide 29: The BIND 8.x Distribution
Available from the Internet Software Consortium for anonymous ftp
  ftp://ftp.isc.org/isc/bind/cur - current production version
  ftp://ftp.isc.org/isc/bind/src/testing - latest test release
Contains src, doc, contrib tar.gz files with signatures which unpack into
  src: source code for named, named-xfer, resolver libraries and a few stand alone tools like nslookup and dig
  doc: documentation for both BIND 4.x and BIND 8.x
    Original BOG (Name Server Operation Guide for BIND 4.9)
    HTML descriptions of new stuff
    man pages
    Relevant RFCs
    Porting notes
    FAQ

## Slide 30: BIND 8 Distribution, cont.
  contrib: contains goodies contributed by other folks
    Many focused on Bind 4.9
    Many to ease maintenance
    Many to find configuration errors
    Spotty documentation sometimes
    Some architecture specific (NextStep, OS2)
  Contributions welcome

## Slide 31: Installing BIND 8
Find about 20mb of disk space, an ANSI C compiler (gcc is fine), and Perl
Get the distribution and unpack it
See if your architecture is on the supported list (src/INSTALL document)
  If so, follow the instructions in INSTALL, basically
    make clean
    make depend
    make
    Convert your current boot file with named-bootconf.pl; tune it
    make install
  If not, change to the src/port directory and read on

## Slide 32: Converting named.boot
named-bootconf.pl PERL script to convert named.boot to named.conf
      named-bootconf.pl < named.boot > named.conf
Acts like a filter
Seems to do the right thing
  Preserves comments, uses C++ style
  Doesn't use any of the new features
  Definitely a good start

## Slide 33: BIND References
Newsgroups
  comp.protocols.dns.bind
  comp.protocols.dns.ops
  comp.protocols.dns.std
Mailing lists
  bind-users
    bind-users-request@vix.com
    Gatewayed to dns.bind newsgroup
  namedroppers
    namedroppers-request@internic.net
    Gatewayed to dns.std newsgroup
  bind-workers
    bind-workers-request@vix.com
    Vixie requests "code warriors" only
See also the RFC repositories

## Slide 34: BIND 9
Complete architecture redesign
  Domain name system growth, particularly in very large zones such as .COM
  Protocol enhancements necessary to securely query and update zones
  Protocol enhancements necessary to take advantage of certain architectural features of IP version 6
BIND9 Features
  Scalability
    Thread safe
    Multi-processor scalability
    Support for very large zones
  Security
    Support for DNSSEC
    Support for TSIG
    Auditability (code and operation)
    Firewall support (split DNS)

## Slide 35: More BIND 9 Features
  Portability
  Maintainability
  Protocol enhancements
    IXFR, DDNS, Notify, EDNS(0,1)
    Improved standards conformance
  Operational enhancements
    High availability and reliability
    Support for alternative back end database
  IP version 6 support
    IPv6 resource records (A6, DNAME, etc.)
    Bitstring labels
    APIs

## Slide 36: Squid Web Cache
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 37: Caching
Caching saves objects (web pages) closer to the next requestor than the original
  Costs more disk space and cpu cycles on caching machine
  Costs less network bandwidth and gives user the page with less delay
External web traffic saved
  30% - 40% at typical sites
  60% - 70% at very focused sites
Exponential Growth
  The Internet and the information on it is growing exponentially
  The only way to deal with exponential growth is by replication
  Caching is a dynamic form of replication

## Slide 38: Squid Web Caching Software
History
  Squid is derived from the Harvest project
    ARPA funded research project at the University of Colorado
    Was led by Prof. Mike Schwartz (now at a startup after a stint at @Home)
  Currently supported by NLANR, the National Laboratory for Applied Network Research
    Primary developer/maintainer: Duane Wessels, NLANR
    See http://www.nlanr.net/Squid
Freely available, ftp it from squid.nlanr.net

## Slide 39: What is Squid
Web client cache
  Faster than most commercial caches
Supports several protocols: HTTP, FTP, Gopher, SSL
Caches cooperate in a hierarchy
Likes lots of disk and memory
  Meta data about cached objects kept in memory
  Objects themselves are saved on disk
  Hot objects are also cached in memory

## Slide 40: Why Cache?
Squid motivated by studies on the NSFNet backbone (1993) showing that, at that time, half the packets were ftp and half of that half were duplicates
  Well placed caches would save that bandwidth
  Bandwidth hog is now the web
    65-70% of the packets
    70-75% of the bytes
  Caching assumes that several different people look at the same page
  Assumes pages don't change too often
  Assumes that people don't care where the pages come from as long as they get the right thing

## Slide 41: Problems with Caching
Mostly political, not technical
Laws about who is responsible for content are scary
  Cache contents are controlled dynamically by what users request
  Cannot hold the ISP who owns the machine and provides caching service responsible
Privacy Issues
  Cache operators have lots of demographic data
  Marketeers gold mine of data
Caches need correct headers
  HTTP 1.0 had 2 or 3 "freshness" headers
  HTTP 1.1 has 10 or more of them
  Expensive to maintain

## Slide 42: Problems, cont.
Bean counting, who has the most hits
Sites that sell advertising care about hits
  Is it a hit when a user gets their page from a cache
  How to do the accounting
    See RFC 2227 on hit metering
Dynamic content changes with each fetch
  Little ad blocks that randomly choose an ad for each instance
  Little counters of number of visits to a page
  Company called matchlogic.com has solution with Java accounting script

## Slide 43: Problems, cont.
Finding the right TTL value for objects in the cache
  Units are % of last modify time
  Determines how long objects stay in the cache
  Influenced in one direction by folks to maximize saved bandwidth
    AOL, for example
    ISPs with pricy bandwidth
    Results in stale data
  Influenced in other direction by folks who want every access to go direct to their site
    Microsoft, for example (set to 0)
Results in a conflict between cache managers and content providers
  Need to communicate and cooperate
  Need accurate expire times

## Slide 44: Squid Parts
squid: main server program
dnsserver: domain name system lookup program
ftpget: a program to retrieve FTP data
client: a command-line browser to use for testing or managing squid
ICP: Internet cache protocol to talk to other caches (RFCs 2186, 2187)
Lots of features
  Supports SSL, the secure socket layer
  Has extensive access controls
  Very configurable logging

## Slide 45: Installing Squid
Find about 10mb of disk space and an ANSI C compiler (gcc is fine)
Get the distribution and unpack it
See if your architecture is on the supported list (AIX, FreeBSD, HP-UX, IRIX, Linux, OSF/1, Solaris, SunOS)
If not, try it anyway, send mail to squid-bugs@nlanr.net to report changes if you have problems

## Slide 46: Installing Squid, cont
Follow the instructions in INSTALL, basically
  Run ./configure
    Assumes you install it in /usr/local/squid
    Use --prefix=/other/dir/squid if you put it somewhere else
  make all
    Takes a while (1/2 hour + on a P133 running BSDI)
  make install
    Doesn't do anything dangerous
    All installation is beneath /usr/local/squid
  Localize the config file /usr/local/squid/etc/squid.conf
    See the file QUICKSTART in the distribution for the minimal changes you must make to the sample squid.conf file

## Slide 47: Configuring Squid
Has one configuration file, in the squid/etc directory
  Called squid.conf Shipped with a squid.conf.default file that is extensively commented
Decisions to be made in configuration
  Resource limits
    How much memory will you let squid take (he takes about 3x what you say :-)
    How much disk space do you have for storing pages
  Your caching topology
    Who is your parent, or parents
    Who are your siblings
  Access lists, who can use your cache
    Anyone (not recommended)
    Your own site (definitely)
    Customers if you are an ISP (sure)
    Peers (maybe)

## Slide 48: Squid Configuration, cont.
Mandatory things that must be changed
  cache_swap: the amount of disk you are willing to donate to the cache
  http_access: access control lists to monitor use of your cache
  icp_access: access control lists to monitor other cache's access to you
  cache_mgr: email address of the squid-meister
  cache_effective_user: who the software should run as
    Defaults to user nobody, group nogroup
    Make sure these exist
  visible_hostname: hostname you advertise for the cache
    Use a DNS cname record to make this generic
    Easier in case you want to change hosts

## Slide 49: Other Config Parameters
cache_stoplist pattern: doesn't cache URLs that match pattern
cache_dir: directory where objects will be cached
  Defaults to /usr/local/squid/cache
  Assumes each cache_dir is the same size (version 1.1, will be fixed in 1.2)
cache*log: specifies location of various log files
pid_filename: where to store pid of running process

## Slide 50: Testing and Running Squid
Run it by hand to build and zero out the directory structure where the cached web pages will be stored
  squid -z
    Builds 16 directories under your cache root
    Builds 256 directories under each of them
    Takes a while
Start it by hand and test your web performance
  squid &
  Eventually do this at boot-time in the rc scripts
    Use /usr/local/squid/bin/RunCache
    Put it in the background

## Slide 51: Testing cont.
Test with a browser if you can
  Clear your local .netscape cache
  Configure your browser's network preferences (under proxies)
    By hand in the manual configuration section
    With a proxy.pac file (java script) such as:
      function FindProxyForURL(url, host)
      {
      if (isPlainHostName(host))
      return "DIRECT";
      if (!isResolvable(host))
        return "DIRECT";
      if (url.substring(0, 5) == "http:")
      return "PROXY 205.180.223.3:3128; DIRECT";
      if (url.substring(0, 4) == "ftp:")
        return "PROXY 205.180.223.3:3128; DIRECT";
      return "DIRECT";
      }
  If you don't have a browser, use /usr/local/squid/bin/client

## Slide 52: Monitoring Squid
squid -k reconfigure
  Same as sending squid a HUP signal
  Needed if you edit the config file and want squid to re-read it
squid -k rotate
  Same as sending squid a USR1 signal
  Tells squid to rotate the log files
  Rotates them in place, config file parameter tells how many to keep
The client program
  Can be used to display statistics on the running squid process and the cache
  Parameters are URLish with protocol field = cache_object
  Complete list in squid configuration file comments

## Slide 53: client Program Examples
Assumes that the hostname of the machine running squid is "squid"
client cache_object://squid/info
  Gives lots of information about running cache
    Watch the ratio of page faults to TCP connnections (should be .2 or so)
    Watch LRU Expiration Age, if below 5 days increasing squids disk can help
client cache_object://squid/stats/dns
  Gives stats on squid dns lookup processes
    Watch last dnsserver, if used a lot, configure more servers (dns_children)

## Slide 54: Squid References
Mailing lists, join them by adding -request to the name
  squid-users, general discussions about squid software
  squid-users-digest@nlanr.net, the users list digested daily
  squid-announce@nlanr.net, announcements of new versions
  squid-bugs@nlanr.net, an alias for reporting bugs
  squid@nlanr.net, an alias for sending feedback and ideas
  squid-faq@nlanr.net, an alias for feedback and additions to the FAQ
See also the IETF Internet draft repositories
Lots of info beneath the squid web page: http://www.nlanr.net/Squid

## Slide 55: Caching References
http://ircache.nlanr.net/Cache/reading-list.html
http://ircache.nlanr.net/Cache/Learn/
http://vancouver-webpages.com/CacheNow
http://home.netscape.com/comprod/ \\ announce/dss_prox.html
http://www.microsoft.com/proxy/default.asp (down?)
http://www.w3.org/Daemon/
http://www.netcache.com

## Slide 56: Other Options
Akamai
  If you are an ISP, they locate an Akamai server at your site. Large web sites like Yahoo pay Akamai money to mirror pages on all the distributed Akamai servers. URL magic causes your users to hit your local Akamai server rather than going all the way to the web hosting server.
  They call it their Accelerated Network Program for ISPs. There is no cost to the ISP as long as you are big enough to be worth it.
  http://www.akamai.com/

## Slide 57: Managing Acceptable Use
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 58: Acceptable Use
What is acceptable use
  Your users will try things you never thought of
  Limit possible use to the services you want to support
  Explicitly prohibit uses which are
    illegal
    disruptive
    violation of your upstream contracts
    present liability problems
  Example
    http://www.coop.net/policy/aup.html

## Slide 59: Industry Norms
Typical Prohibitions
  Security compromise
  Security related activity, i.e. hacking
  violating acceptable use of others
  unsolicited commercial email
  forgery or fraudulent activity
  “netiquette” violations
  benefit of any above activity (mail drop)
http://www.labyrinth.com/localhost/survey.html

## Slide 60: What is Spam?
News
  off-topic
  more than 10 groups regardless of content or cross-posting
  not using cross-post
Email (UCE)
  Unsolicited (including “subscriptions” if not validated)
  Commercial
  Volume is irrelevant
  Method of delivery is irrelevant

## Slide 61: Spam
Why Spam?
  10% return!
    (3% for paper) so Marketers love it!
  Cheap! Marketers love it!
  Immediate! Marketers love it!
  90% wasted bandwidth is unacceptable
  expensive - but not to the marketers
  annoying - requires user action

## Slide 62: SPAM Profile
Origin
Patsy
Beneficiary
Recipient
Scapegoat
enticement
Desired
response
blame
Proactive Zone
Reactive Zone
YOU ARE HERE

## Slide 63: Analyzing Spam Headers
Received: (from daemon@localhost) by labyrinth.com (NO SOLICITING) id PAA02925 for <barb.dyker@labyrinth.com>; Thu, 15 May 1997 15:52:13 -0600 (MDT)
From: adsnet@earthlink.net
Received: from mail-gw2.pacbell.net(206.13.28.53) by morass.labyrinth.com via smap (V1.3) id sma002911; Thu May 15 15:51:55 1997
Received: from mail.pacbell.net (hd31-076.hil.compuserve.com [206.175.222.76]) by mail-gw2.pacbell.net (8.8.5/8.7.1) with SMTP id OAA01857; Thu, 15 May 1997 14:49:58 -0700 (PDT)
Received: from mailhostcapelas.net(alt1.capelas.com(208.9.77.65)) by capelas.net
(8.8.5/8.6.5) with SMTP id GAA00254 for <a7@capelas.net>; Tue, 15 Apr 1997 14:00:24 -0600 (EST)
To: a7@capelas.net
Message-ID: <199702170025.GAA08056@capelas.net>
Date: Tue, 15 Apr 97 14:00:24 EST
Subject: Free Subscription
Reply-To: a7@capelas.net
Comments: Authenticated sender is <a7@capelas.net>
RECIPIENT
ORIGIN
PATSY
SCAPEGOAT
BOGUS

## Slide 64: How to deal with Spam
Proactive / Prevention
  filters
    outgoing
    relaying
  policy as deterrent
  education
  ISP new account qualification
Reactive
  filters
    incoming server
    user mail agent
  policy enforcement
  legal recourse
  reporting
  education

## Slide 65: Spam Scapegoats
  Domain or user names used in forgeries - never touched the spam
  Get heat from hasty complainers
  Only recourse is reactive: legal
  Educate spam complainers on how to read mail headers to determine true players

## Slide 66: Legal recourse ineffective
  “So sue me” attitude
  can’t sue everyone
  spam & run
  anonymous spam & run
  lack of jurisdiction: create a law making spam illegal and spammers go to another jurisdiction (including off-shore)
  US unsolicited FAX law proves law is not a deterrent

## Slide 67: Spam Characteristics
Obscure origin
  forged MAIL FROM (!= “From” header)
  HELO != peer name
  Extra forged Received header (EST -0600)
  Relayed through unrelated third-party
  non-existent DNS domain name
  From: and envelope sender don’t match
  To: matches From:
None of these are REQUIRED
More than 50% of Spam has legitimate (not forged) headers

## Slide 68: What we can do:
ORIGIN
  Funnel outgoing mail through a spam throttle SMTP server
  Enforce valid MAIL FROM address including username
  Enforce valid headers - no forgery
  Limit envelope recipient list
  Throttle frequency of SMTP connects
  Content?

## Slide 69
Big I
Mail Relay
Mail Relay
Router
Customers
Internal Network
employees
X
X

## Slide 70: Why bother?
Already spending time, money, and reputation dealing with complaints
Avoid embarrassing public apologies like Zoom, config.sys, and UUNET
New Revenue - charge premium rate for:
  non-relayed SMTP
  filtered incoming mailboxes

## Slide 71: What can we do:
Patsy (relay)
  Require valid envelope addresses
  Disallow relay
    No external recipients from external sessions
    Usally based only on envelope addresses
    Spammers can use ! And % mail syntax to get around this
  Don’t screw up your Received header record keeping (from [validated], by, for)
  Block SMTP sessions from known spam networks and hosts (RBL or private list)

## Slide 72: What can we do: Recipient
Server filters - reject connect/msg
  from known spam hosts (RBL)
  with invalid envelope address
  from known spam address
  to non-local users (no relay)
User filters
  Best approach is to filter all mail except explicitly _to_ known addresses: personal or lists
  Bounce or refile others
  You won’t get Bcc mail anymore
Nothing is 100%

## Slide 73: Resources: Sendmail
Use sendmail v8.9+
  Relay is off by default
  Allows relay only to/from hosts in cw file by default
  Also full relay control
  Has an arbitrary access database which can be fed by RBL
  See FAQ 3.27 for relay exceptions
  See http://www.sendmail.org/m4/anti-spam.html
  Extensible to create your own rejection rules
  http://www.sendmail.org

## Slide 74: Sendmail MC Features
Feature(`relay_entire_domain') $=m
Feature(`relay_local_from')
Feature (`relay_hosts_only') $=R
Feature(`relay_based_on_MX') imperfect, but easier to manage
Feature(`access_db') private blackhole list
Feature(`rbl') http://maps.vix.com/
Feature(`blacklist_recipients') disable users
Feature(`loose_relay_check')
Feature(`accept_unqualified_senders')
Feature(`accept_unresolvable_domains')

## Slide 75: NT Mail servers
All these resources cost money, but they have filters and ways to disallow relaying
  sendmail (www.metainfo.com)
  Post.Office (www.software.com)
  Imail (www.ipswitch.com)

## Slide 76: Mail Client Resources
Outlook has a spam threshold and filters
Eudora has new & improved filters
My Favorite: SpamBeGone! (www.internz.com/SpamBeGone/)
  Intelligent plug-in that learns what you think is spam
  Works with Eudora on Win
  Available as UNIX binary command-line filter adding X-Priority for Solaris, Linux, IRIX, FreeBSD, Amiga

## Slide 77: More Tools
These rely upon lists of known spam senders/recipients
  Spam Exterminator
  Spam Attack Pro
  SpamScan97 (you need to provide your own list)
These help you complain, not necessarily correctly
  Spam Hater
  Spam Cop (spamcop.net)

## Slide 78: Other Resources
Other Tools – most have some level of filtering and/or RBL support
  www.qmail.org/
  Spamshield.conti.nu/
  www.obtuse.com/smtpd.html
General Info
  www.cauce.org/
  www.mids.org/nospam/
  www.sprocket.com/Security/Stopping-UCE.html
  spam.abuse.net/spam/
  thomas.loc.gov/ (to look up legislation to see if it is real)
  www.labyrinth.com/localhost/

## Slide 79: Complaint Forwarding
Address complaints to domain@abuse.net
They maintain a list of complaint addresses - not always abuse@domain
Iff not on list, sends to postmaster@domain
Requires registration
Only downside, bad sites can silently block mail from abuse.net

## Slide 80: Avoiding Being a Target
How you get on Spam lists
  HTML mailto or text with @
  Web Browser preferences
  USENET News postings
  Re-sold opt-in lists, surveys, etc.
  Complaints
  Vacation
How to not get on Spam lists
  Don’t use mailto or @ in html
  Don’t use a browser’s built-in email and don’t put your email in prefs
  Use modified news identity
  Opt-in with a modified identity
  Never complain to the originator

## Slide 81: How to Complain Successfully
Complain to the RIGHT place!
  Parse Received headers TOP->BOTTOM!
  Stop at discontinuity
  verify bogosity of remaining Received lines
  differentiate between the roles played
  identify IP addresses of contributing parties
  traceroute and find ISP nearest to that host, not the host itself
  send POLITE and INFORMATIVE message to their ISP
    Include offending message with FULL HEADERS
    Include your analysis of the parties involved

## Slide 82: Never complain to the Spammer!
They like valid recipient addresses and you just confirmed yours!
Validated addresses are worth MONEY even if they are never used.
They take you off one list and add you to another or sell your validated address.
Vacation programs automatically validates your address – so run them after your spam filters
If you block spam, give a “550 User Unknown” error

## Slide 83: Recommended complaint
I received this spam. Please take appropriate action.
joes.net - origination in your net from X.X.X.X
bobs.net - Bob, you’ve been used - disallow relaying on your server. See www.sendmail.org/antispam.html
billy.net - your web site at THISURL is benefitting from this spam so you are a party to it.
Most of the time you will know more about mail than the folks you complain to. Be helpful and informative rather than derisive.

## Slide 84: Pyramid Schemes
The only spam that is actually illegal in US without question… as long as some part of it uses the USPS.
US Postal Inspection Service
  it’s their job
  print and mail to them
  include whois of players
  http://www.usps.gov/postalinspectors/pyramid.htm

## Slide 85: U S Laws
S.1618 Consumer Anti-Scamming Act of 1998
  DIED! Any email that refers to this law is definitely spam.
Coalition Against Unsolicited Commercial Emaill (CAUCE)
  http://www.cauce.org/legislation.html

## Slide 86: Responsible Bulk Email
True opt-in requires validation
Provide an opt-out when you collect the address
Validate addresses by sending email confirming opt-in
Don’t fall into typical marketing speak
  Why is the person is getting the message?
  Provide any information possible to ensure the recipient doesn’t consider the message to be unsolicited
  Provide a “how’s my driving” address
Have an “abuse” email address that works
Respond to “abuse” email
Register at abuse.net

## Slide 87: ISPs: Preventing other abuses
Filter everything except those activities you endorse
For hourly dialup users filter:
  all incoming SYN (not established) packets
  all outgoing packets except what you endorse
  outgoing SMTP to any relay except your own
More complicated for dedicated/business customers
Always filter at your upstream & downstream borders
  RFC1918
  127/8
  directed-broadcast
  source route

## Slide 88: ISPs: Capitalize on Prevention
99% of users only need these outgoing sessions:
  POP to your POP server
  SMTP to your SMTP relay
  HTTP to anywhere
Charge extra for unrestricted client-side initiations
Provide incoming “security” for free
Charge extra for unrestricted incoming

## Slide 89: Internet Cafes
Special problem of no user identification
Enables Spam and run
Require identification and log customer access
Disable any means of abuse
  remove ALL applications not intended for use
  run browser in “kiosk” mode
  disable client side tools like java
  prevent physical access to I/O, e.g. floppy/cd/serial
  remove system access, e.g. run, ms-dos, explorer

## Slide 90: Monitoring Use
LOG LOG LOG
  mail server
  mail headers
  pop server
  syslog
  radiusd
  router packet filters
  firewalls
  sniffers
  SNMP monitors
Duplicate log entries on a secure system

## Slide 91: Enforcement
Proactive
  preventive measures already discussed
  customer awareness
  know your customers - disallow anonymity
Reactive
  take action on each and every abuse
    notify, educate, and warn or sanction
Sanctions
  warning
  two strikes, you’re out

## Slide 92: Customer Awareness
Most customers are completely ignorant of acceptable use policy and issues
  This is why technical prevention is crucial
  Make AUP readily available
  Refer to AUP often
  Provide introductory training for users
  Identify good practices for marketing and advertising
  Refer to AUP often
  Require customer signature acknowledging sanctions
  Refer to AUP often
  Write a readable AUP

## Slide 93: Writing your AUP
What your AUP should contain
  Why the AUP is necessary
  Where the rules come from
  What makes activities unacceptable and why
  Examples of acceptable uses
  Examples of unacceptable uses
  Possible sanctions
  Recourse
  Authority
  Contact for more information or clarification on specific activities

## Slide 94: Summary
An AUP is the cornerstone of use management
Prevention is the foundation

## Slide 95: Web Server Performance
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 96: Server Performance
Performance Variables
  CPU speed
  Memory
  IO bandwidth
  Bus speed
  Architectural gotchas
  Software
Hard to size web server in advance
  Sizing for 1-2 millions hits/day

## Slide 97: Achieving Balance
Balance very important for overall performance
  Need all aspects of performance to run out of capacity at about the same point
One of the major advantages of UNIX over other web server platforms is that it can be finely measured and tuned
  No mysteries as to how things are architected
  Designed as a multi-user operating system from the start
The most commonly misunderstood web server performance aspect is I/O
  In most cases, more CPU's do not mean more performance
There's no magic performance "crystal ball"
  You have to measure the performance of your actual production system to ascertain bottlenecks

## Slide 98: Basic Balance
The #1 measure of UNIX performance health is how the machine spends its time
The "golden rule" is a 50/50 mix between "user" time and "system time"
  While this doesn't work for all UNIX applications, it's darn good for web servers
A machine which tends to spend more cycles as "user" time may be CPU-bound
A machine which tends to spend more cycles as "system" time is probably I/O-bound or might be virtual memory system
These ratios don't work if the machine suffers from other serious "illness"
  Run-away processes (CPU or memory)
  Lossy network (collisions)
  Disks with bad blocks
Check for general health before comparing user/system ratio

## Slide 99: User/System Ratio examples
  web 4 % vmstat 5
  procs memory page disks faults cpu
  r b w avm fre flt re pi po fr sr s0 s1 in sy cs us sy id
  1 2 0 331940 19432 194 35 24 0 0 2 5 9 223 1005 421 25 13 63
  9 2 0 338552 18652 548 86 51 0 0 0 25 24 509 3317 1113 41 46 13
  0 3 0 335352 20432 288 40 50 0 0 0 27 4 392 2508 1176 22 30 48
  0 2 0 331612 20668 318 87 58 0 0 0 10 22 375 1668 1147 15 25 60
  1 2 0 331060 20884 171 52 40 0 0 0 2 4 317 1294 1010 12 22 67
  43 2 0 329908 20528 293 68 64 0 0 0 0 16 351 1773 1145 21 29 50
  2 2 0 331760 18140 285 41 45 0 0 0 1 6 377 1876 1360 59 34 6
  2 2 0 336168 14844 397 58 57 0 0 0 12 21 384 1774 1150 63 37 0
  web2b % vmstat 5
  procs memory page disks faults cpu
  r b w avm fre flt re pi po fr sr s0 s1 in sy cs us sy id
  1 0 0 151484 107772 102 38 2 0 0 0 22 9 109 156 165 22 15 63
  1 0 0 149888 108540 854 112 7 0 0 0 7 6 917 4951 5802 13 39 48
  1 8 0 151108 108212 509 75 4 0 0 0 32 32 763 3089 3574 8 23 69
  3 0 0 152688 107344 610 44 5 0 0 0 34 11 834 3767 3718 12 28 60
  0 0 0 153276 107344 527 38 3 0 0 0 5 5 841 4176 4174 7 27 66
  1 0 0 148660 107264 432 23 4 0 0 0 7 6 814 4251 3108 11 21 6

## Slide 100: vmstat, cont.
Selected headings
  procs is process states
    r - runnable, should not have spikes
    b - blocked
    w - swapped, if this is non-zero, buy more memory
  cpu is state the cpu is running in
    us - user time, executing your programs instructions
    sy - system time spent on your behalf, usually i/o
    id - idle time, deceptive, it measures when the cpu cannot do anything to move processes forward, might be waiting for disk or network
Sometimes, I/O-bound machines really are in need of more RAM
web2b - I/O bound, 5 million hits/day
  Needs more disk controllers
  Needs more disk arms
  Needs more network interfaces

## Slide 101: Tuning somaxconn - symptoms
On a "good day" (i.e., when IP connectivity to most locations is stable), the web server is happy as a clam
On bad days, users often see "server is down or unreachable" or broken images, even when reachability to their site isn't affected
Machine load average is low
During the "bad" times, "telnet localhost 80" times out
Nameservice is not in use (no reverse lookups for connections)

## Slide 102: Tuning somaxconn
tcpdump(1) of traffic inbound to the web server show that connection requests arrived (SYN) and are acknowledged (SYN-ACK) but open acknowledgement (ACK) isn't received by web server from remote host
"netstat -a -n" shows that a number of connections in SYN_RCVD state
"netstat -a -n | grep tcp | awk '{print $6}' | sort | uniq -c" always shows 5 connections in this state during the bad times, a smaller number in good times
Connections in this state tie up a slot in the "unaccepted socket queue", often referred to as the listen() queue
The size of this queue needs to be adjusted on machines, such as web servers or mail hubs, that have lots of contact with the outside world
Increasing this queue helps deal with SYN flooding attacks

## Slide 103: somaxconn - The Fix
On Solaris, you can adjust the size of this queue with the ndd(1m) command:
      ndd -set /dev/tcp tcp_conn_req_max 32
Under IRIX, modify the value of somaxconn in /var/sysgen/master.d/bsd:
        int somaxconn = 32;
Under BSD/OS, you can declare it as an option in your kernel config file:
        options "SOMAXCONN=32"
Under SunOS, you have to replace/edit uipc_socket.o
  Default somaxconn=5 on SunOS 4.1.3
  For details, see http://www1.islandnet.com/~mark/somaxconn.html
    C program to change uipc_socket.o
    Byte offsets to use adb or an editor to change
    Differences in the od (octal dump) output before and after the fix

## Slide 104: DNS reverse lookups
TURN OFF DNS reverse lookups on your machine (web server) entirely
Even if you have the cycles to do it, mis-configured user sites will introduce false delays
If you need the information from reverse lookups, consider processing the log files on a separate machine to do this (PERL).
  www.statslab.cam.ac.uk/~sret1/analog/ tool for reverse lookups
Also try to do all web access control (.htaccess, access.conf) using IP addresses.
Apache comes with a utility, libresolv, that does it efficiently

## Slide 105: iostat
Measures terminal and disk I/O activity
  Terminals
    tin - number of characters in
    tout - number of characters out
  Disks
    bps or sps - blocks/sectors transferred per second
    tps - transfers per second
    msps - average milliseconds per seek
  tty sd0 sd1 nfs1 nfs2 cpu
  tin tout kps tps serv kps tps serv kps tps serv kps tps serv us sy wt id
  0 0 1 0 21 6 1 34 0 0 0 0 0 0 0 0 0 99
  0 47 0 0 0 18 2 61 0 0 0 0 0 0 0 0 0 100
  0 16 0 0 0 3 0 15 0 0 0 0 0 0 0 0 0 100
  0 16 56 7 226 21 3 48 0 0 0 0 0 0 0 0 1 99
  0 16 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 100
iostat Example, lollipop, Solaris 2.6
  Can use this data to balance disk load across disk arms and controllers

## Slide 106: Another iostat Example
    tty sd0 sd1 sd2 cpu
    tin tout sps tps msps sps tps msps sps tps msps us ni sy in id
    0 62 58 5 12.6 133 9 8.8 136 10 8.8 24 0 13 0 63
    0 14 39 3 18.8 81 8 11.8 336 11 10.6 54 0 32 0 14
    7 48 158 11 11.8 88 7 12.3 126 5 10.3 13 0 24 0 63
    3 83 42 4 10.5 48 3 7.6 93 2 14.4 37 0 32 0 31
    3 39 152 11 14.7 524 38 9.0 318 19 10.4 49 0 43 0 7
    1 26 237 29 13.7 338 28 10.0 98 6 11.0 45 0 39 0 16
    3 37 125 14 14.1 44 7 11.9 101 6 10.2 50 0 45 0 4
Example: web4, BSD/OS
Raid storage for web servers
  Software raid requires CPU and overhead
    Not good for web servers
    Gives reliability
  Hardware raid real win in performance
    There are lots on the market
    Find one that focuses on performance not reliability

## Slide 107: Virtual Adrian
Solaris users can benefit from the efforts of Adrian Cockcroft who documents and improves Solaris performance
Adrian has a book out "System and Performance Tuning: SPARC and Solaris (Sunsoft Press)" that documents many tricks
His "Virtual Adrian" SE performance tool is available on the web from www.sun.com

## Slide 108: Other Kernel Parameters
maxusers determines a number of other kernel parameters:
  Maximum # of processes
  Maximum # of processes per user
  System wide open files limit
  Per-process open files limit
  Maximum # of mbuf clusters
  Proc/pgrp hash table size
Vendors set MAXUSERS at 8, 16 or maybe 32
  Serious web server needs it at 512

## Slide 109: Parameters, cont.
NMBCLUSTERS defines and number of mbuf clusters - defaults to 256.
  Consider changing this to something like 4096
        627/2048 mbufs in use:
        10 mbufs allocated to data
        38 mbufs allocated to packet headers
        184 mbufs allocated to socket structures
        202 mbufs allocated to protocol control blocks
        183 mbufs allocated to routing table entries
        7 mbufs allocated to socket names and addresses
        3 mbufs allocated to interface addresses
        0/28 cluster buffers in use
        284 Kbytes allocated to network (27% in use)
        0 requests for memory denied
        0 requests for memory delayed
        0 calls to protocol drain routines
  Use "netstat -m" to determine if this needs to be changed.
CHILD_MAX controls the maximum number of process children
  Better set this to something like 256

## Slide 110: Hardware Candidates
The hardware upgrade most likely to cause improved performance is adding more RAM
Consider balancing load across disk arms
  RAID
  Separate disk arms for db indexes and data
If possible, dedicate a separate physical disk for log files.
High-speed network interfaces
High-speed disk controllers and busses
Use netstat -i to check for physical network problems.

## Slide 111: Software
Content is often the limiting factor
  Use JPEG for pictures
  Use reduced colorset GIFs for images with just a few colors (less than 32)
Fine tune default settings in server
  keep-alive timeout
    Too long hogs resources, but too short causes too many tcp setups
  proxy timeout

## Slide 112: WAN Performance
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 113: Commercial Platforms
Commercial integrated network management platforms (INMP) provide a nice GUI interface to monitoring data
Many vendor "drop-ins" customize generic platform interface for specific hardware
  CiscoWorks
  Chipcom drop-in
  Many others
Platforms may include capability to notify administrators in case of trouble via email, pager, telephone, etc.
HP's OpenView platform is by far the most mature platform in the industry -- but it still leaves a lot to be desired
All platforms are computing resource intensive -- typically requiring $15K-$20K workstation dedicated to the task

## Slide 114: Freely Available Software
SNMP Packages and Libraries
  CMU (Carnegie Mellon University), good for C developers
  MIT (Massachusetts Institute of Technology) development kit
  Univ of California, Davis has a relatively new SNMP package
  PERL SNMP package by Simon Leinen

## Slide 115: Freely available software - Cont.
NOCOL/NetConsole (Network Operation Center On-Line) - a network monitoring package that runs on Unix platforms and capable of monitoring network and system variables such as ICMP or RPC reachability, RMON variables, nameservers, Ethernet load, port reachability, host performance, SNMP traps, modem line usage, appletalk & novell routes/services, BGP peers, etc.
Scotty - TCL interpreter with extensions for network management; includes tkined, a network editor for drawing maps of network configurations (shipped with BSD/OS)

## Slide 116: The quick, easy, and accurate way
Direct performance measurement through benchmarking
Performance measurement by historical statistics
Performance data gathering and graphing

## Slide 117: Measurement through benchmarking
ttcp is a benchmarking tool for determining TCP and UDP performance between 2 systems.
The program was created at the US Army Ballistics Research Lab (BRL) and is in the public domain (ftp://ftp.sgi.com/sgi/src/ttcp/)
The nice thing about ttcp is that it shows the performance of your end-to-end network, no holes barred
Most basic use
  Receiver: ttcp -r -s
      ttcp-t: buflen=8192, nbuf=2048, align=16384/0, port=5001 tcp -> xor.com
      ttcp-t: socket
      ttcp-t: connect
      ttcp-t: 16777216 bytes in 19.99 real seconds = 819.55 KB/sec +++
      ttcp-t: 2048 I/O calls, msec/call = 10.00, calls/sec = 102.44
      ttcp-t: 0.0user 0.6sys 0:20real 3% 0i+0d 0maxrss 0+0pf 11092+2csw
  Sender: ttcp -t -s host
    -s for the receiver means throw away actual data transferred
    -s for the sender means generate random data to send

## Slide 118: Fancy ttcp
  % ttcp -t -s -l 64 -n 16384 xor.com
  ttcp-t: buflen=64, nbuf=16384, align=16384/0, port=5001 tcp -> xor.com
  ttcp-t: socket
  ttcp-t: connect
  ttcp-t: 1048576 bytes in 1.15 real seconds = 890.73 KB/sec +++
  % ttcp -t -s -l 1024 -n 16384 xor.com
  ttcp-t: buflen=1024, nbuf=16384, align=16384/0, port=5001 tcp -> xor.com
  ttcp-t: socket
  ttcp-t: connect
  ttcp-t: 16777216 bytes in 20.65 real seconds = 793.27 KB/sec +++
    -l specifies the length of the buffers
    -n specifies the number of the buffers

## Slide 119: Measuring Expectations
What performance should we really expect from our WAN?
If it's a dedicated point-to-point circuit, then we should expect to get 92% or better of the purchased bandwidth
  For T1, 1.536Mb/s = .1536MB/s = 153.6KB/s
  153.6KB/s * .92 = 141.31KB/s
If it's a frame-relay circuit, at best we could expect to get 80% of the purchased bandwidth, often 50%
Some line errors in WAN circuits are unavoidable. As a good rule of them, you should expect to see less than 1 error in every 1,000,000 packets for a "clean" line.
Some times, circuits carried on copper like T1s may take a few errors per day
  Designed for voice aggregated over copper, doesn't handle certain kinds of data well (lots of sequential zeros)

## Slide 120: Measurement by history
      Hssi2/0 is up, line protocol is up
      Hardware is cxBus HSSI
      Internet address is 1.2.3.4/30
      MTU 4470 bytes, BW 45045 Kbit, DLY 200 usec, rely 255/255, load 42/255
      Encapsulation HDLC, loopback not set, keepalive set (10 sec)
      Last input 00:00:02, output 00:00:00, output hang never
      Last clearing of "show interface" counters never
      Queueing strategy: fifo
      Output queue 0/40, 7362 drops; input queue 0/75, 1721 drops
      5 minute input rate 5187000 bits/sec, 1519 packets/sec
      5 minute output rate 7590000 bits/sec, 2807 packets/sec
      1624911546 packets input, 2931056137 bytes, 3 no buffer
      Received 508079 broadcasts, 0 runts, 0 giants
      0 parity
      3251 input errors, 31 CRC, 3046 frame, 174 overrun, 0 ignored, 0 abort
      287423330 packets output, 3815049764 bytes, 0 underruns
      0 output errors, 0 applique, 2 interface resets
      0 output buffer failures, 0 output buffers swapped out
      13 carrier transitions
  Input errors are .0002%
  Carrier transitions low

## Slide 121: Measurement by history (cont.)
      Hssi4/0 is up, line protocol is up
      Hardware is cxBus HSSI
      Internet address is 3.4.5.6/30
      MTU 4470 bytes, BW 45045 Kbit, DLY 200 usec, rely 255/255, load 35/255
      Encapsulation HDLC, loopback not set, keepalive set (10 sec)
      Last input 00:00:00, output 00:00:03, output hang never
      Last clearing of "show interface" counters never
      Queueing strategy: fifo
      Output queue 0/40, 0 drops; input queue 1/75, 1727 drops
      5 minute input rate 1551000 bits/sec, 1221 packets/sec
      5 minute output rate 6298000 bits/sec, 1239 packets/sec
      1574691557 packets input, 956588456 bytes, 6 no buffer
      Received 563056 broadcasts, 0 runts, 3174 giants
      0 parity
      3995089 input errors, 13049 CRC, 3978697 frame, 169 overrun, 0 ignored
        0 abort
      2356338480 packets output, 1572466122 bytes, 0 underruns
      0 output errors, 0 applique, 483 interface resets
      0 output buffer failures, 0 output buffers swapped out
      6717 carrier transitions
  Input errors are .25%
  Carrier transitions too high

## Slide 122: Measurement by data gathering
Multi-Router Traffic Grapher (MRTG) is a tool to monitor the traffic load on network-links
MRTG is available under the GNU PUBLIC LICENSE
See the homepage at:
  http://ee-staff.ethz.ch/~oetiker/webtools/mrtg/mrtg.html
Works on most UNIX platforms and Windows NT
Uses Perl for easy customization, and has a highly portable SNMP implementation written entirely in Perl thanks to Simon Leinen. There is no need to install any external SNMP package.

## Slide 123: Other Tools
SiteScope
  From Freshwater software, www.freshtech.com
  Software that monitors, reports, and alerts arbitrary objects including SNMP variables and scripts
SiteSeer
  Also from Freshwater
  Service that monitors, reports, and alerts from outside your network
ServiceMetrics and other services are like SiteSeer
rrdtool: http://ee-staff.ethz.ch/~oetiker/webtools/rrdtool/

## Slide 124: Routing Protocols
APRICOT2000
Seoul, South Korea
Barbara Dijker
barb@netrack.net

## Slide 125: Routing Basics
Two basic choices of routing models
  Static
  Dynamic
Static works, but doesn't scale well and is hard to maintain
We'll talk about dynamic routing today
Routing Protocols are protocols that implement routing algorithms (BGP, OSPF, RIP, etc.).
Routed protocols are transport protocols that are routed over an inter-network (IP, DECnet, IPX, etc.).

## Slide 126: Routing Protocol Families
Two families of distributed routing algorithms:
  Distance Vector
  Link state
All popular network routing protocols are based on one of these
Distance Vector is also sometimes called "Bellman-Ford" routing, after the people that invented the algorithm

## Slide 127: Distance Vector Routing
A distance vector routing protocol requires that each router maintain a list of each possible destination and the distance to each of those destinations
Each router advertises to its neighbors its list of destinations
Each router saves the advertisements most recently received from its neighbors
Each router calculates the shortest path to each destination based on information heard from neighbors

## Slide 128: Link State Routing
A link state routing protocol maintains a list of neighbors, their names, and a list of their links
Each router meets its neighbors and learns their names, and exchanges link state information with them
Each router, having a full graph of the network, computes the shortest path to each destination

## Slide 129: Distance Vector vs. Link State
Distance vector suffers from "count-to-infinity" problem
  Infinity can far away because of timing of synchronous updates
Link state can be complex to calculate
Link state routing makes network topology easier to discover
Troubleshooting a network is easier with link state routing
Link state routing converges more quickly than distance vector

## Slide 130: Autonomous Systems
An Autonomous System (AS) is a group of routers controlled by the same administrative entity
Each AS has an AS number
Protocols which use AS number as part of their route state information require a globally unique AS number for each entity -- you can apply for one from the NIC
Protocols which do not propagate AS information can be assigned AS numbers that are unique within your site
Sometimes, it's easiest to think of an AS as a fun-filled routing club, focused on single routers meeting each other

## Slide 131: RIP
Routing Information Protocol
Distance-vector, interior gateway protocol
Grew out of Xerox XNS (last 70s)
Used by routed on many workstations
Maximum metric of 15
Broadcast routing protocol
Routing updates every 30 seconds
  "I'm a router to network xxx.xxx.xxx.xxx in yy hops"

## Slide 132: RIP - cont.
Convenient solution for LANs. Spoken by:
  Printers
  Hubs
  PCs
  UNIX boxes
If misused, can cause extreme network congestion and chaos
UNIX boxes should always run routed -q to avoid advertising false information
If you must use RIP, use it only to advertise a handful of networks and perhaps a default route

## Slide 133: Debugging RIP
Use a packet sniffer, or run routed -t on a UNIX box...
      % in.routed -t
      RESPONSE from 199.45.198.253.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.10.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.34.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.254.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
What a mess
  Four different gateways all with the same metric
  But not all have the same capability (Sun 3 vs. Sparc Ultra)
When running RIP, it's often a good idea run gated instead of routed on major gateways, artificially weighting metrics

## Slide 134: EIGRP
Enhanced Interior Gateway Routing Protocol
IGRP originally developed by Cisco in mid-1980's to replace RIP
Distance-vector, interior gateway protocol
Uses ASs to identify routing groups
Very handy for all-cisco networks, no so handy for heterogeneous networks
Works well in a WAN environment, can be easily distributed into RIP
Routing updates every 90 seconds
Complex metric includes factors for load, bandwidth, and reliability; varies from 1-255

## Slide 135: OSPF
Open Shortest Path First
Interior gateway, link-state protocol
Also designed as a replacement for RIP
Can balance load across multiple links
Can operate within a hierarchy
Top of hierarchy is an AS
  Uses internal AS#'s, unique within the organization
Each AS is divided into "areas"
Link State information is exchanged by all routers within an area; summarized at borders of areas
OSPF "backbone" (area 0) is responsible for exchanging information between areas

## Slide 136: OSPF - SPF algorithm
The Shortest Path First (SPF) [sometimes called Dijkstra] algorithm is the basis for operation of OSPF
Once interfaces are initialized, a router sends OSPF HELLO to its neighbors
Friendly neighbor routers exchange link state information. Once they're synchronized, they are said to be "adjacent"
Link state information is re-transmitted periodically (say, every 90 minutes) or when a router's state changes
Each router calculates a shortest path tree, with itself as the root. This information is used to generate a routing table
Network segments with more than one router elect a "designated router" which is responsible for maintaining link state information for that segment

## Slide 137: OSPF - cont.
One big feature of OSPF is support of variable-length subnet masks
Currently, gated is the best way to support OSPF on a UNIX box
      router ospf 235
      network 199.45.100.0 0.0.0.255 area 4
      network 199.45.101.0 0.0.0.255 area 0
On a Cisco router, your OSPF clause might look like:
  AS# choosen is 235
  You are willing to speak OSPF to the networks listed
      show ip ospf
      Routing Process "ospf 235" with ID 199.45.141.67
      Supports only single TOS(TOS0) routes
      Number of areas in this router is 1
      Area 1.1.1.1
      Number of interfaces in this area is 1
      Area has no authentication
      SPF algorithm executed 29 times
      Area ranges are
      Link State Update Interval is 0:30:00 and due in 0:23:15
      Link State Age Interval is 0:20:00 and due in 0:03:15

## Slide 138: BGP
Border Gateway Protocol
An Exterior Gateway Protocol, derived from EGP
Distance vector protocol
But transmits a list of AS numbers (real ones assigned by RIR) in path to destination
Designed to detect routing loops
Primarily designed to exchange information between ASs
Four types of messages: Open, Update, Keepalive, Notification
Uses TCP connections between peers
Also requires an AS number
Currently BGP version 4

## Slide 139: BGP Update Packet Contents
Origin
  IGP - learned within AS
  EGP - learned via EGP (obsolete)
  Incomplete - learned some other way
AS path
Next hop
Unreachable (now being used to black hole spammers)
Intra-AS metric (if you are using BGP internally)

## Slide 140: BGP Uses
BGP is commonly used when sharing information with backbone service providers, or between large corporate networks
      router bgp 101
      neighbor 199.45.255.6 remote-as 3404
  You must enable BGP routing, specify a real autonomous system number and the neighbors that will speak BGP to you
BGP then shares routing information with routers in other ASs
  Advertised/accepted routes can be controlled with Access Lists

## Slide 141: Debugging BGP
      > show ip bgp summary
      BGP table version is 13923, main routing table version 13923
      319 network entries (338 paths) using 52992 bytes of memory
      27 BGP path attribute entries using 1920 bytes of memory
      Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State
      144.224.13.5 4 6176 82342 82320 13923 0 0 1w2d
      199.45.132.75 4 3404 81205 80797 13923 0 0 6d07
On a cisco...
  InQ and OutQ fields represent BGP messages exchanged but not yet processed
    If InQ field is ever non-zero, get a bigger router
  State field uses unfortunate defaults
    Blank means neighboring router is up and happy
    Active means its really broken and trying to re-establish things
    Non-blank means neighbor is down or is coming up
  Up/Down field shows time in current state

## Slide 142: Debugging BGP, cont.
      > show ip bgp regexp 4151
      BGP table version is 13923, local router ID is 199.45.255.254
      Status codes: s suppressed, * valid, > best, i - internal
      Origin codes: i - IGP, e - EGP, ? - incomplete
      Network Next Hop Metric LocPrf Weight Path
      * i134.249.0.0 199.45.132.75 0 0 6582 4151 4151 4151 i
      * i151.121.0.0 199.45.132.75 0 0 6582 4151 4151 4151 ?
      * i160.232.0.0 199.45.132.75 0 0 6582 4151 4151 4151 i
      * i162.79.0.0 199.45.132.75 0 0 6582 4151 4151 4151 i
      * i165.221.0.0 199.45.132.75 0 0 6582 4151 4151 4151 ?
      * i192.78.16.0 199.45.132.75 0 0 6582 4151 4151 4151 ?
      * i192.153.14.0 199.45.132.75 0 0 6582 4151 4151 4151 i
      * i198.22.127.0 199.45.132.75 0 0 6582 4151 4151 4151 ?
      * i199.128.0.0/11 199.45.132.75 0 0 6582 4151 4151 4151

## Slide 143: Debugging BGP, cont.
Again, on a Cisco...
  "regexp" clause is like a grep
    Knows ^ for beginning with, eg. ^4151
    Knows $ for ending with, eg. 4151$
    Can glue AS paths together, eg. ^4151_666$ means the AS path starts with AS 4151 and ends with AS 666
Nice BGP tutorial on Cisco's web site (under tech support section)

## Slide 144: Network Crisis Case Studies
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 145: Network Crisis Case Studies
The situations detailed here are all based on real-world network crises.
The names and minor details have been changed to protect the innocent (or the guilty, as the case may be).
In each case, we were called in after local attempts to fix the problems failed.
  Often the fix took 2-3 hours of an expert consultants time after a month of in-house attempts to solve the problem.

## Slide 146: Case #1: FloodDyne Industries
FloodDyne Industries recently moved into a new office building.
Previously, their network was 100% thinnet (10base2).
In their new offices, they installed Level 5 UTP cabling and switched to 100% 10BaseT.
They have approximately 30 hosts on a single Ethernet.
There is one machine (a Sun Sparc 1) that acts as a hub for mail, data, and administrative tasks.
The rest of their network consists of a variety of other hosts, including Macs, PCs, Suns, and SGIs.
The day they moved into the new facilities, the nightmare began.

## Slide 147: The Symptoms
From the moment the new network was brought online, it was apparent that a problem existed.
The first noticeable problem was "NFS server not responding; NFS server OK" being spit out by a number of the cross mounted machines
Then, one engineer noticed that ftp throughput was hovering around 50Kb/sec, well below what a fairly idle Ethernet should be able to handle
Some of the SGIs began spitting out "ec0: late collision" on their console.
  < 512 bits: normal collision
  > 546 bits: OK Ethernet packet
  in between: late collision
A ping across the LAN would result in about 5% lost packets

## Slide 148: The Diagnosis
Since the only aspect that had changed was the network media itself, attention turned to examining the cabling in the walls -- that MUST be the problem!
A number of tests were run, using a tester similar to the Siemon MD-CAT5.
But... all the wall cabling checked out OK.
Next, it was suspected that one of the hosts had been damaged during the move, and it was causing interference on the Ethernet.
Efforts were made to isolate the "broken" host. In particular, netstat and ping were used as tools.

## Slide 149: Diagnosis (cont.)
Excitingly, a candidate "broken" host was found.
From an arbitrary workstation on the network, ping worked fairly reliably (2% or less packet loss) to all hosts on the network except the Sun server.
      % netstat -I le0 -i 5
      input (le0) output
      packets errs packets errs colls
      86676 8982 85686 9240 92
      256 20 240 16 0
      350 40 321 51 2
      179 21 180 10 0
      153 17 128 14 0
netstat on the Sun server showed an unusual number of input and output errors:
Clearly (?), this must be the offending host; its Ethernet interface must be BROKEN.

## Slide 150: Diagnosis (cont.)
A hot stand-by was put in its place.
The problems continued, no better than before.
Finally, someone took a look at the whole picture.
  Cabling in wall has been certified "OK"
  Hosts at ends of cables have been certified "OK"
  What could be in-between?
Silver-satin. 8 conductor silver-satin cable (flat) was used to connect between the wall jack and the hosts
Since the Sun had the most simultaneous transmit and receive traffic, it suffered from the largest amount of cross-talk.
Solution: Use twisted-pair hookup and patch cables in a twisted-pair network!

## Slide 151: Case #2: Ajax Publishing
Ajax Publishing is a publishing house that prints a weekly newsletter about their Coyote Abatement products. This is their sole livelihood, no newsletter, no food on the table.
They have approximately 100 hosts on their network, which consists of two physical 10base5 cables connected by a handful of redundant gateways.
Their network includes everything from the latest-and-greatest from manufacturers like HP and DEC, to some Sun3s, PCs, Macs, and an IBM mainframe.
They have about 80% TCP/IP and about 20% IPX traffic on their network.

## Slide 152: The Problem
They have a proprietary typesetting system that is used to typeset the articles in their newsletter. It too speaks TCP/IP, and is based on PDP 11/34 processors with Excelan Ethernet boards. They plan on replacing this system "real soon now." But for today, this system is mission critical to printing their newsletter.
The crisis is thought to have begun months ago, when users started noticing short "hiccups" on the network when using it for interactive applications.
But starting today, the PDP 11/34s refuse to speak to the rest of the network. HELP!
The two mission-critical hosts that must speak to each other (the PDP and a Sun) are on different networks. So, at first a routing problem is suspected.

## Slide 153: The Problem (cont.)
The site is running "dynamic" routing (RIP) so that if a gateway fails another one will step in.
      % in.routed -t
      RESPONSE from 199.45.198.253.520: (sun 2)
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.10.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.34.520:
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
      RESPONSE from 199.45.198.254.520: (sparc 10)
      dst 0.0.0.0 metric 1
      dst 199.45.197.0 metric 1
What a mess! A variety of gateways all advertise routes to the same net with the same number of hops. But, the gateways are not equivalent: 199.45.198.253 is a Sun-2, and 199.45.198.254 is a Sparc-10.

## Slide 154: The Diagnosis
These folks need to be running gated(8) rather than routed(8) on their gateways, and artificially weighting the paths. This is likely the cause of the "hiccups" users reported earlier.
So, if routing is OK, maybe it's the case that the network is too saturated. Using a PC running LanWatch (from FTP Software), utilization of the network is analyzed. It peaked around 30% with an average of about 9%.
How about we test the PDP?
Moving the Sun near the PDP (don't try it the other way around!), we constructed a network of just the Sun and the PDP. That worked fine.

## Slide 155: Diagnosis (cont.)
So far, we have:
  Verified it's not a routing problem
  Verified the Ethernet is operating at a reasonable utilization level
  Verified that other hosts on the network (except the PDP) are happy
  Verified the PDP is operational
What could it be?
A rather aged member of the network community scratched his head. What had changed recently on our network? he asked.
The young wet-behind-the-ears SA said "well, we've recently upgraded some of the Ethernet cards in the PCs to FASTER ones."
And in fact, that led to a hunch later proven by timing measurements: the new high-performance cards "jump" the settling time between packets to gain an edge. This hopelessly upsets the Excelan cards.
Solution: Bridge the PDP onto a separate segment until it can be replaced.

## Slide 156: Case #3: SynthTree Laboratories
SynthTree Labs is an International company with extensive LAN and WAN needs.
Each office has its own SA staff, and there is no central coordination.
Their traffic mix is about 50% TCP/IP and 50% IPX.
Their company wide-network consists of over 600 hosts, ranging from PCs and X-terminals to mainframes.
Network segments are connected together using bridges and "Ethernet Switches", because "it's so much easier to administer"
Most remote sites are connected (bridged) via 56KB dedicated circuits

## Slide 157: The Problem
The network is only usable about 50% of the work day. For about 2 hours in the morning and 2 hours in the afternoon, the network is claimed by users to "stop" Some days, however, are better than others.
All services are inaccessible -- from printing to email.
Management is furious -- how could this happen?

## Slide 158: The Diagnosis
      % netstat -I le0 -i 5
      input (le0) output
      packets errs packets errs colls
      133 0 59 0 0
      100 0 33 0 30
      159 0 29 0 3
      121 0 28 0 4
      154 0 61 0 0
      108 0 43 0 1
      188 0 75 0 0
      131 0 67 0 52
      192 0 97 0 0
      165 0 73 0 1
      138 0 99 0 0
      107 0 61 0 3
      122 0 33 0 0
      32 0 20 0 17
      103 0 30 0 0
Notice how collisions skyrocket at regular intervals -- approximately every 30 seconds. This is the first clue.

## Slide 159: Diagnosis (cont.)
      14:35:01.589490 bulldozer.xor.com.525 > 192.108.21.255.525: udp 76
      14:35:01.590005 bulldozer.xor.com.525 > 192.108.21.255.525: udp 76
      14:35:01.590340 bulldozer.xor.com.525 > 192.108.21.255.525: udp 76
      14:35:01.790240 phone.xor.com.525 > 192.108.21.0.527: udp 76
      14:35:02.090100 phone.xor.com.525 > 192.108.21.0.527: udp 76
      14:35:02.221030 phone.xor.com.525 > 192.108.21.0.527: udp 76
What could those bursts of collisions be from? tcpdump shows us the actual traffic during those periods:
Broadcast traffic with mis-matched broadcast address
  bulldozer thinks 255
  phone thinks 0
Packet's hardware address is broadcast, but IP doesnt recognize the 0 as broadcast and so forwards the packet, on and on.

## Slide 160: Diagnosis (cont.)
Broadcast traffic! Since the bridges provide no firewall against broadcast traffic, broadcast "storms" are taking over the network
Solution #1: Look around for mis-configured hosts, hosts that do not match the specified broadcast address
Solution #2: Turn off routed, rwhod, and other broadcast generators on everywhere but essential hosts

## Slide 161: Case #4: Web-footed Nation, Inc.
Web-footed Nation, Inc. recently moved their web server from an NT box to a UNIX-based box
Their web traffic has been steadily increasing
They have a SPARC running Solaris 2.5 that acts as their web server. It's a speedy little box, as Solaris goes.
This box is also responsible for services such as email, and anonymous ftp.
They run the Apache web server, so it's gotta be good

## Slide 162: The Symptoms
On a "good day" (i.e., when IP connectivity to most locations is stable), the web server is happy as a clam
On bad days, users often see "server is down or unreachable" or broken images, even when reachability to their site isn't affected
Machine load average is low (less than 0.20)
During the "bad" times, "telnet localhost 80" times out
Nameservice is not in use (no reverse lookups for connections)

## Slide 163: Finding the Cause
tcpdump(1) of traffic inbound to the web server show that connection requests arrived (SYN) and are acknowledged (SYN-ACK) but open acknowledgement (ACK) isn't received by web server from remote host
"netstat -A -n" shows that a number of connections in SYN_RCVD stat.
"netstat -A -n | grep SYN_RCVD | wc -l" always shows 5 connections in this state during the bad times, and a smaller number at other times.
Connections in this state tie up a slot in the "unaccepted socket queue", often referred to as the listen() queue.
The size of this queue needs to be adjusted on machines, such as web servers or mail hubs, that have lots of contact with the outside world

## Slide 164: The Fix
On Solaris, you can adjust the size of this queue with the ndd(1m) command:
      ndd -set /dev/tcp tcp_conn_req_max 32
Under IRIX, modify the value of somaxconn in /var/sysgen/master.d/bsd:
        int somaxconn = 32;
Under BSD/OS, you can declare it as an option in your kernel config file:
        options "SOMAXCONN=32"
Under SunOS, you have to replace/edit uipc_socket.o
      http://www1.islandnet.com/~mark/somaxconn.html
  For details, see
    C program to change uipc_socket.o
    Byte offsets to use adb or an editor to change
    Differences in the od (octal dump) output before and after the fix

## Slide 165: Case #5: AmeriRodent, Inc.
AmeriRodent, Inc. recently moved into a new office building
A rapidly expanding cheese delivery enterprise, they added another 28 desktops to their network following the move
The have primarily Sun servers and NCD xterminals
Customer service representatives run an X-based GUI to assist customers with complaints about late cheese deliveries
X-based GUI interact with a herd of commercial database servers, also attached to the network
Expected response time to user queries is less than 5 seconds

## Slide 166: The Symptoms
Customer service agents report response times are much longer then 5 seconds, sometimes closer to 300. "Worked fine when we were in our old offices!"
Some of the X-terminals appear to "freeze" when starting new applications, sometimes for minutes at a time. "Never did this in the old offices."
Management was so unhappy with network performance, they handed pink slips to all the sys admins and hired an "outsourcing" firm to "fix their network"
Outsourcing firm is still "looking into the cause of the problem"

## Slide 167: The Diagnosis
Logical and physicals maps of network were requested. None exist, or left the company when the sys admin staff was fired.
Performed rough mapping by hand. Network is constructed of a single logical 10baseT Ethernet, with approximately 230 hosts on the segment.
Decided to measure network utilization. Segment is over 80% sustained utilization
  Ethernet knee
  Use netstat -ni to see collision rate
A significant percentage of usage is NFS ... from the X-terminals. Rather than tftp fonts, they mount them via NFS. [explains X-terminal freeze-ups]

## Slide 168: The Fix
Limit workstations on a single segment to 15-20 per segment
For X-terminal fonts don't use NFS with UDP (no congestion avoidance, so is terrible for a congested network)
  Use tftp or NFS over TCP
  Or use a font server if a small group of folks are sharing lots of fonts; can become a bottleneck if too heavily used
Network segments together via a router or a switch, with high bandwidth connections for primary servers (100baseT, etc.).
Avoid hiring "outsourcing" firms who are not familiar with TCP/IP and Ethernet to do network debugging

## Slide 169: Case #6: Green Fountain Labs, Inc.
Green Fountain Labs, Inc. has been on the Internet for over 3 years
Their Internet connection is an important research tool, and provides information about their Fountain-coloring products to potential customers
They have a packet-filtering firewall on their router, together with a software firewall on their UNIX box (including COPS and Crack).
Convinced they've done enough, they weren't too concerned about network security

## Slide 170: The Problem
One day, a user logs in to discover that her home directory is filled with files she didn't put there -- including password files from other machines, etc.
She calls the system administrator, who correctly identifies the problem as a potential security breach. He tells her to change her password right away.
As the days go by, more and more users find strange things lying around. The system administrator notices unusual log messages like "su root succeeded for jsmith" when jsmith is not a sys admin
System administrator goes on vacation. Junior system administrator assigned to watch machine in his absence discovers that the machine is a "hacker nest", with 10 or more unauthorized users on at a time.

## Slide 171: What Happened?
Legitimate user probably logged in from outside world and password as "sniffed"
Since passwords on this machine are "reusable", hacker could log in under that account
Since shadow passwords were not used on this machine, hacker could try to "Crack" password file to find other accounts.
Sys admin hadn't installed vendor security fixes, so hacker could also get root.
Sys admin ignored weekly mail from Crack which indicated problems with some passwords

## Slide 172: ISP Account Management
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 173: Account Management
Adduser Program
  The first job of a Sys Admin is often to write an adduser program to implement user policy:
    who can have an account
    how the account is configured
    what services does the account allow
  But at an ISP, user accounts need to include information to track and bill their usage.
  Discrepancies between what is billed and what is possible in the system configuration means LOST REVENUE.
  Don’t think your customers won’t notice.

## Slide 174: Billing Integration
So you thought billing wasn’t your problem
  Customers are charged for their system usage
  This requires:
    tracking usage
    limiting use to only that which is paid for
    getting usage data into the billing system
  Since most Accounts Receivable managers know nothing about computers, guess who’s job it is to make this work.
  Even after it is setup and working, the Sys Admin must consider impact to billing issue for any system change.

## Slide 175: Billing Example
You’re an ISP that has a terminal server (Livingston Portmaster let’s say) and sells PPP accounts on the portmaster.
  How do you process the portmaster logs to charge customers by the hour for usage?
  How do you disable the features of the portmaster you don’t want your customers accessing, such as the ability to directly telnet from the portmaster command?
  If you use dynamic IP addresses, how do you track reported illicit activities?
  How do you get the usage data from the portmaster into a system to bill it to your clients?
  How do you ensure that sessions aren’t billed twice or not at all?

## Slide 176: Accounts Receivable Software
You need to ask yourself those questions for every service you offer to your customers.
  There are many things you can do to make this much easier for each system.
  You’ll need some databases:
    Central billing account database - one entry per billable customer
    User database - one entry per authorized user
    Services database - one entry per type of service available
  If not integrated databases, then written or at least well-known processes to keep things in sync.
You’ll need COMMERCIAL Accounts Receivable software.

## Slide 177: Accounts Receivable Software
Do not write your own. It’s a bigger job than you think, and it has already been done real accounting professionals. So it’s a waste of your time.
But you may have to in extremely complex custom situations.
Choose AR software with the following capabilities:
  customizable customer records
  import charges from external data files
  export customer database
  balance tracking
  collections reporting

## Slide 178: Customer Database
The Customer database is usually implemented in the AR software.
It must be linked to the User database - to track which user accounts are billed to which customer.
Link is usually by a customer number added to the user database.

## Slide 179: Customer Database
Database Field Examples
  Customer Name
  Billing Address
  Billing Period (monthly, quarterly, annually)
  Special Billing arrangements (discounts)
  Billing method (paper, email, credit card)
  Payment method (check, credit card, electronic draft)
  Account status (active, overdue, suspended, cancelled)
  Activation Date
  Expiration Date if any
  Billing history and/or balance
  Payment history

## Slide 180: Customer Database
Database Field Examples (continued)
  Billing rate plan
  Contact person for bill payment issues
    voice telephone number
    fax number
    email address
  Contact person for administrative issues (like security)
    voice telephone number
    fax number
    email address
  Contact person for specific technical issues: DNS, News, Postmaster

## Slide 181: User Database
This database will correspond to each separately billable item. For example, a PPP user, a special web page, DNS service, etc.
The User database should be used to directly build the system configuration files such as:
  passwd files
  radiusd password files
  DNS named.boot
  http virtual host
  mail aliases file
This will ensure that your configuration files and billing data are kept in sync.

## Slide 182: User Database
The primary key for the User database would be a unique name for each user service.
It should contain any and all definable user-specific service that may ever get billed.
Each record must link to Customer database for billing. This would usually be by including a Customer number in each record.

## Slide 183: User Database
This database will need to have variable fields depending on the type of “user”. For example:
Type = POP
  mailbox name
  password
  pop server name
  user’s full name
Type = MAIL ALIAS
  mail alias name
  mail address

## Slide 184: User Database
Type = UNIX SHELL
  login name
  password
  UID
  home directory
  user’s full name
  shell
  accessible servers

## Slide 185: User Database
Type = PPP
  login name
  password
  authentication options
  PPP options
  accessible terminal servers
  Type = DNS domain
  domain name
  server type (primary or secondary)
  primary server IP address or file name of zone data

## Slide 186: User Database
Type = VIRTUAL WEB HOST
  actual web server name
  virtual server name
  virtual IP address
  document root
  admin email address
  log file location
Type = IP NETWORK NUMBER
  network number
  netmask
  gateway

## Slide 187: User Database
Type = IP HOST NUMBER (static)
  IP address
  host name
Type = MAILING LIST
  mailing list name
  mailing list manager
  public/private
  moderated & moderator
  description file
  list of recipients

## Slide 188: Putting it all together
Now write adduser.
Prompt for customer name/number
Check existence and status
Prompt for user name
Verify unique/available
Prompt for user type and other information
Verify input
Write to User database

## Slide 189: System Configuration Files
Generate system configuration files from User database and customer database (don’t enable a user for a customer that is suspended or cancelled).
Do this regularly (like every night via cron).
This approach ensures one source of data to avoid synchronization problems.
This will require custom software. Use PERL.
Write custom software for user services - like changing passwords.
This solves the problem of limiting use to only that which is billed/paid.

## Slide 190: Services Database
This may also be part of the AR software.
You need one entry for each “type” of user account.
Some types may have multiple service charges, eg.
  virtual web host hits
  virtual web host disk space
For each service you need:
  base rate (minimum charge)
  maximum charge
  unit rate
  discount scale
  any special algorithm

## Slide 191: Tools
Everything you write should have a web interface
Use good tools
Apache + SSLeay + mod_perl + fastcgi
Mysql
PERL

## Slide 192: Usage Tracking
Reduce or eliminate this issue by billing flat monthly rates not dependent upon usage.
Some services can’t pay for themselves at what the market will bear in flat rates.
Usage tracking depends on service implementation.
Will require custom software to convert system logs into useful billing entries.
Must correlate log entries with User database

## Slide 193: Usage Tracking
Problems:
  time calculations and conversions (time zones, daylight savings time, time representation)
  correlating start & stop events
  correlating start & stop events over file checkpoints
  correlating special service access points (toll free modems, high speed modems)
  usage data volume and reduction
  usage data archival
  non-discrete usage (like disk space)
  conversion to billing system format
  log location distribution

## Slide 194: Usage Tracking
Collect and reduce your data daily to reduce volume.
Store reduced data on a centralized and reliable disk system.
Locate together the resources that are charged similarly, e.g. toll free modems all on one terminal server.
Run sanity checks on the data, e.g. it is impossible for a connection to last more than 86400 seconds in one day.
This data is also important for management to view trends in customer use.

## Slide 195: Summary
Try to use a commercial AR package
Use a centralized database of user service settings
Use centralized database to build system configurations
Collect usage data to one location.
Learn PERL so you can make all this work

## Slide 196: ISP Security
APRICOT2000
Seoul, South Korea
Barb Dijker
barb@netrack.net

## Slide 197: Security
The Internet is not a friendly place
  Unique to ISPs:
    your users are your enemy
    your users are your revenue
  You must protect your users’/customers’ data from
    the outside world
    each other
  You must protect your staff systems & data from
    the outside world
    your users/customers
    each other
  This is a big job

## Slide 198: Avenues of Attack
Three popular avenues of attacks:
  external probes and exploitation
    done by those who don’t have user access
    exploits vulnerabilities in socket services to gain access
    may use information gained from snooping to gain access
  internal exploitation
    done by those who have user access
    exploits system configuration or software vulnerabilities
  passive snooping
    done by those who have network access
    gathers information for future attacks

## Slide 199: Limit Customer Access
To both protect the customers and to protect against them, limit their access.
If you provide UNIX shell accounts:
  use restricted shells (chroot or menu driven)
  make OS filesystems read only
  disallow executables and setuid files (noexec, nosuid) on all filesystems except the OS
  disable read access on files that could be used for exploitation
  use shadow passwords
  provide defaults for file permissions, umask, etc.

## Slide 200: A Key to the City
Simple software programs are available to gain root access from a normal user account - no technical experience required.
Giving a normal user account on a UNIX machine to a stranger is practically like giving them the root password.
Do not provide UNIX shell accounts to any one without:
  validated and authentic identification
  documenting identification
  validating contact information (address, phone)
  contract signature

## Slide 201: Beware of Restricted Accounts
A restricted or menu-based access mechanism may not be as foolproof as you might expect.
Don’t assume it does what it claims to.
Try to break it.
Best case scenario:
  Limit user access to systems which provide no special privileges

## Slide 202: Don’t lose your own visibility
A “hacker” will usually first replace these files:
  /bin/login: to provide a back door or collect passwords
  /bin/ps: to hide programs being run
  /bin/ls: to hide files
Keep a valid vendor distribution copy of those programs handy ON A HARDWARE READ ONLY DEVICE (like a floppy) for regular bit-by-bit comparisons and monitoring system activity.
Keep other detailed monitoring tools handy, like ‘lsof’, in a place a hacker may not look. (not under /usr)

## Slide 203: Firewalls
User systems need almost full access to the Internet, but not completely.
Setup a firewall, as you would for a private company, that disallows typical spoofing accesses from outside while allowing your customers full access.
Separate your staff systems and data on a completely separate internal LAN.
Put a BIG and STRONG firewall between your staff systems and your customer systems.
Limit outgoing access to limit liability and acceptable use abuses.

## Slide 204: Firewalls – Suggested Config
Disable source routing
Disable distribution of packets to broadcast address
Incoming Filters
  deny source addresses inside your networks
  deny source addresses of localhost (127)
  deny source addresses of RFC1597
  allow established session packets
  allow specific services to specific hosts only
  maybe let ping through
  deny ALL else
Notes: <number>
<footer>
<header>
<date/time>
and RFC1918

## Slide 205: Firewalls (cont.)
Adding outgoing filters in addition to incoming filters on the same interface dramatically reduces performance
Put outgoing filters on interior ports and incoming filters on exterior ports
Outgoing Filters
  allow access to specific services such as web, FTP, gopher, DNS
  deny ALL else
  notice SMTP is not in the allow list
What you disallow limits what your customers can do and thus prevents participation in certain sorts of security attacks
This protects your liability and reduces the likelihood of being involved in complaints or legal action.

## Slide 206: Customer vs. Staff Systems
Customer may be able to snoop your LAN that hosts customer access services: terminal servers, routers, customer shell systems, web servers, etc.
Assume they can and do.
Assume your customers are doing so to access your staff systems - the ones with the account and billing databases, master configuration files, etc.
Encrypt all data between staff and customer LANS.
Staff should use ssh or something similar.
PROTECT YOUR ACCOUNT DATABASES!

## Slide 207: Don’t forget “insider” attacks
Most security breaches are accomplished from the “inside”.
That means by your own employees.
What do they have to gain?
  notoriety with friends & peers
  free access for friends & relatives
  access to customer data & systems
ISPs are more vulnerable to this problem than most companies because of the concentration of customer data and fast growing demand for skilled employees.

## Slide 208: Prevent “insider” attacks
Screen prospective employees carefully.
Have a strong and enforced policy of no tolerance for overstepping authority and privileges.
Implement ways to limit privileged access such as sudo and customized interfaces to configuration files.
Reduce incentives by providing free services to immediate family of staff with limitations.
Educate staff regarding appropriate use of privileged access to customer data.
Be alert to staff needs - don’t foster retribution.

## Slide 209: A firewall isn’t enough
A firewall doesn’t stop social engineering attacks.
New vulnerabilities are discovered regularly.
Each system on your networks requires a complete security analysis.
  Turn off all unused service ports
  Ensure all used services are secure
  Do not use NIS or NFS
  Use smap or something else secure for mail
  Keep systems patched for security vulnerabilities
  DO NOT USE LINUX or any other free OS

## Slide 210: Security Resources
COAST http://www.cs.purdue.edu/coast/archive
CERT http://www.cert.org
TAMU ftp://www.tamu.edu/pub/security
FWTK Firewall Toolkit, http://www.tis.com/
ISS Internet Security Scanner
TIGER checks host vulnerabilities like COPS
Tripwire Detects file changes

## Slide 211: Security Mailing Lists
CERT
  limited disclosure
  announcements only - no discussion
  cert-advisory-request@cert.org
Bugtraq
  full disclosure
  discussion and dissection of bugs
  also gets CERT announcements
  send “subscribe bugtraq” to listserv@netspace.org
NT Security
  send "subscribe ntsecurity" to majordomo@iss.net