## Slide 1: Introduction to Network Management and ISP Fundamentals
Miguel A.L. Paraz
IPhil Communications Network, Inc.

## Slide 2: Open Content
While the material is copyrighted by the author, permission is granted to present it again or make derived works as long as credit is given.

## Slide 3: Part 1
What is All About

## Slide 4: Tips and Tricks Workshop
I am not “teaching”, instead we are sharing each others’ experiences
Put Best Current Practices into Application
Focus on the technical/architectural issues, and not details

## Slide 5: Assumptions for this Session
Existing start-up or medium scale ISP, or,
Design or start-up phase

## Slide 6: Prerequisites
Already familiar with the different components of what make up an ISP
Nevertheless, feel free to ask questions anytime and go “off-topic”

## Slide 7: Network Management?
An ISP is an IP Network, and we will discuss how to manage it properly as a whole
However, to manage, we must build and sustain it properly

## Slide 8: ISP Fundamentals?
We will discuss how to build on your existing knowledge

## Slide 9: Let’s start with some input?
Let me know what your expectations are so we can all learn something

## Slide 10: Solution-Independent
This workshop is not particular to any vendor, product or methodology
However, the presentor is biased towards those he has actual experience with.

## Slide 11: Why run an ISP at all?
Tie-up with Content Production business
Tie-up with real-life “Brick and Mortar” business
Architecture will depend on these

## Slide 12: How do you want to run it?
Build and operate everything?
Outsource? (From whom?)
Mixture?

## Slide 13: Part 2
IP Architecture

## Slide 14: Routing and Access
IP Level Management
  Routing and Switching
Can be divided:
  Core Network - your “backbone” if you have multiple locations
  Distribution to the customer

## Slide 15: Selecting an Upstream
Almost all Asia-Pacific ISP's have an upstream
Very few have “Tier 1” provider status in the US (defaultless)

## Slide 16: Selecting a foreign upstream provider
Usually a “high bandwidth” country like US, Japan, Singapore.
  Take circuit costs into consideration, US link is just as effective/cheap in many cases.
Foreign upstream providers (except colo facilities) are usually telcos.

## Slide 17: International connection method
Fiber
  More expensive per Megabit, lower latency, required for VoIP and sensitive VPN apps
Satellite
  Cheaper per Megabit, higher latency
Mixture

## Slide 18: Selecting a local upstream provider
Telco
  Pros
    tight integration with communications facilities
    easy upgrades of bandwidth
  Cons
    No telco diversity
    May be weak in applications and value-added services

## Slide 19: Selecting a local upstream provider (2)
Other ISP
  Pros
    Not tied down to one telco
  Cons
    May be harder to get local and international lines

## Slide 20: Colocate?
You can colocate equipment at providers which either:
  sell bandwidth, or,
  allow interconnection with bandwidth providers and peers
You have fine control over bandwidth management and routing policy.

## Slide 21: But Colocate?
Can make troubleshooting telco problems more difficult, than an “all-in” solution

## Slide 22: Bandwidth Management
Customers are now asking for Committed (International) Bandwidth
Upstream QoS - queueing
Edge QoS - traffic shaping
Overprovisioning - can you afford it?

## Slide 23: Non-Op: Competition with Provider
Regardless, be sure that you are not competing (directly) with your provider!

## Slide 24: Do you want to multihome?
Eliminate points of failure.
Use different telcos going to different ISP's
However, it is tricky to use multihoming to add up the effective bandwidth!

## Slide 25: Considerations in running BGP
Need BGP know-how (APRICOT: ISP Clinic, and meet the Routing Gurus)
  Incorrect BGP setup can lead to disaster! Blackholes, route flap...
Need AS number

## Slide 26: Considerations in getting own address space
Some providers might not allow you to announce their space separately (“punching a hole” in the routing tables)
No providers will let you use their space if you terminate their service.
However, you need to be a certain size (check with APNIC)

## Slide 27: BGP Peering with customers
Gives customer more choices (unless you want to prevent them?)
Customers must also know BGP configuration
You have to protect yourself from customer misconfiguration

## Slide 28: Peering with "public" exchange points
For AP ISP's, depending on the country’s structure, you can save costly international bandwidth
Bilateral peering - you can select what routes to send to which peers
Multilateral - your routes are sent to all, though you can filter inbound

## Slide 29: Private peering with other ISP's
Is always bilateral peering
Is used for high-volume peers or critical since QoS on exchange points is at a lower quality

## Slide 30: Knowing bandwidth and peering requirements
Traffic analysis is important so you know where your packets are coming from and going
Set acceptable levels on your lines to protect against spikes/bursts/surges in traffic

## Slide 31: BGP Route filtering
Set policies on incoming and outgoing routes
Don’t make yourself a transit AS by mistake
Need a routing database to make this scalable with large numbers of peers

## Slide 32: IP ingress filtering
Define what packets can be received from a client or peer
Helps prevent Denial of Service attacks (flooding) and catches incorrect configuration (broadcast packets, packets that should exit another customer downstream)

## Slide 33: IP ingress filtering
Prevents IP Spoofing, with packets coming in that pretend to be coming from the internal network
RFC 2267, now an IETF Best Current Practice
Disadvantage - can eat up router CPU, apply wisely

## Slide 34: Port Filtering
Can prevent DoS attacks, exploits for ports
Usually applied at the edge and with customer consent, since the ISP’s job is to route packets

## Slide 35: Routing Protocol Software
Cisco IOS
  Most popular, de-facto “reference implementation” for BGP, proprietary
Gated
  Commercial with older source code releases available, licensed by vendors (e.g. Lucent GRF)

## Slide 36: Routing Protocol Software (2)
Zebra
  Free software, open development. Stable BGP, not-so-stable OSPF at the moment
How do you combine them?

## Slide 37: Dialup services
Still the most common customer access method
In many AP cities, the only choice for consumers
Dialup LAN service

## Slide 38: Dialup provisioning
Single-line
  cheap lines, modems and remote access servers - even PCs will do
  does not scale to large numbers, does not support V.90

## Slide 39: Dialup provisioning (2)
Channelized
  expensive lines and RAS - router quality
  can possibly interface with telco at the switching (such as SS7) level for advanced services

## Slide 40: RADIUS
Allows multiple RAS to authenticate against one or more servers
Some servers support “realms” (username@domain) which permit proxying to another service provider for roaming

## Slide 41: Global Roaming
Peer-to-peer roaming requires peer-to-peer arrangements, and a full mesh for a full roaming setup
Speaker from Global Roaming Service Provider

## Slide 42: Telco/ISP interaction phases:
In the Beginning - Telco provides raw async service, ISP provides IP dial-in and transit
  Back when Telcos did not know about the Internet
Telco provides channelized trunks

## Slide 43: Telco/ISP interaction phases:
Telco handles channels directly, routes the IP connection to ISP (bulk dialup service)
Telco provides complete IP service, the ISP is just a value-added reseller

## Slide 44: Cable and DSL
Commonly known as “Broadband”
Watch out, these might eat up more bandwidth than is available for AP ISPs

## Slide 45: Monitoring Tools
Commercial Packages and Network Management Systems (NMS)
Freely available “mainstays”
  NOCOL “NOC ONline” Monitoring System
  MRTG Multi Router Traffic Grapher

## Slide 46: Part 3
Application Architecture

## Slide 47: Applications
Applications complement IP
  Without applications, we just transport bits from one place to another
Centralized versus Distributed Services
  Can choose for a geographical dispersed service

## Slide 48: Platforms
Simplify as: Commercial Unix vs Free Unix vs Windows
Do not have to use only one
Lots of subjective inputs here

## Slide 49: What Platform are you Using?
Specific: IPhil uses mostly Linux, a little BSD for specific functions
Opinion: Linux has more available software (free and proprietary), and is easier to learn

## Slide 50: DNS
Application closest to the IP routing layer (L3.5?)
Must never go down, or else you will “disappear” off the Internet

## Slide 51: DNS Design
Nameserver synchronization
  Especially if you are handling large numbers of zones, configurations can go out of sync
  Watch out for SOA serial numbers!
Offsite Backup
  Preferable so that you don’t “disappear” if all your lines go down
  Backup DNS providers are coming out

## Slide 52: DNS Design (2)
Dead zone removal
  Set a policy that customer zones will be removed if they are no longer authoritative, or if the master is dead
  This speeds up nameserver loading especially with dead masters

## Slide 53: DNS Design (3)
Reverse DNS - in-addr.arpa
  Is not commonly practiced within APNIC networks (APRICOT: see the BOF)
  Is necessary to give “identity” to your networks, and makes it easier to track abuse
  Personal preference: if you want to hide the identity, just make dummy entries that resolve.

## Slide 54: DNS Design (4)
Restricting recursive lookups
  Lessens your server load, but makes it harder for others to debug problems by “digging” against you
Restricting zone transfers
  Prevents attackers from learning your network structure, if your zones are “revealing”, but your backup nameservers must manually notify you if their IP address changes

## Slide 55: Common DNS Errors
Lame servers and delegations
Incorrect use of CNAME

## Slide 56: DNS Implementations
Internet Software Consortium (ISC) BIND - de facto standard
DENTS <http://www.dents.org>
Dan Bernstein’s tools <http://cr.yp.to>

## Slide 57: E-Mail
Small-scale mail delivery works “out of the box”
Choosing an MTA - what features are needed the most?
Web-based E-Mail Solutions
  Free solutions

## Slide 58: Mail Retrieval
Shell - do you still have shell users?
POP - still the most common
IMAP - might eat up space in the ISP environment
  OK for the enterprise

## Slide 59: Building Large-Scale E-Mail
Separate mail routing from delivery, inbound from outbound
“One large domain” vs multiple subdomains
Mailing list management
How much mailbox space should you allocate?
  Quotas

## Slide 60: Preventing Mail Abuse
Usually theft of service aka “spam”
MTA tools such as filtering
DNS Verification
DNS-based abuse prevention systems

## Slide 61: Common E-Mail Errors
Incorrect From: address, unresolvable
Forwarding Loops
Running out of delivery or queuing space
Running out of CPU/memory - can it handle DoS?

## Slide 62: E-Mail Implementations
sendmail.org/.com
qmail/qmail POP
postfix
qpopper
University of Washington imap + pop

## Slide 63: Web Caching
Important for AP ISP’s who wish to save bandwidth
By experience, at least 30% can be saved

## Slide 64: Caching Design
Caching can be geographically distributed
Determining disk space requirements
  Empirical rule of thumb (thanks to squid mailing list) - keep 3 days worth of traffic

## Slide 65: Transparent Caching
Can be considered as “tampering” with the TCP connection
Causes problems with end-user browsers who don’t “know” there’s a cache and do not act correctly
Caching system must be fail-safe since users can’t “turn off” the proxy setting

## Slide 66: Transparent Caching (2)
Router or switch can catch the connection by TCP port, or an L4 switch can actually look at the URLs and do load balancing.
Web Cache Coordination Protocol increases the fail-safe ability

## Slide 67: Cache-Augmentation Services
FTP Mirror Finders can redirect FTP access to a local mirror or a close one network-wise
Satellite-based cache push can increase hit rate by prefetching

## Slide 68: Caching Implementations
Free Software (squid)
Proprietary Software (Inktomi...)
Appliances (NetApp, Cisco Cache Engine, Cacheflow...)

## Slide 69: Web Serving
Easy to serve static content
More complex to create apps or host customer apps with CGI, dynamic web pages, databases and the like

## Slide 70: Offsite high-bandwidth mirrors
Many AP web servers are in the US for better connectivity, but it is easier to maintain application engines locally
A live mirror/accelerator can handle this transparently

## Slide 71: Content Delivery Networks
Acceleration is now taken to a commercial level by Content Delivery Network providers who push content to globally distributed servers and provide a means for browsers to select the best one.

## Slide 72: Web Serving Implementations
Apache + extensions (mod_perl, PHP, Java servlets, SSL...)
Microsoft IIS
Lotus Notes + Domino

## Slide 73: Part 4
Looking at a Higher Level

## Slide 74: Applications
Becoming an Application Service Provider
Hosting Commercial off-the-shelf Software
Hosting Customized Applications

## Slide 75: E-Commerce Applications
Higher level of system security needed
  encrypted communications not enough!
Settlement issues for Consumers
Business-to-Business (B2B)

## Slide 76: Programming
Needed to implement custom application services
Systems Development Languages
  C/C++ for Unix-level coding
Scripting Languages
  Perl for System Administration and Web Applications

## Slide 77: Servicing Colocated Customers
Colocating single servers
Handling diverse customer equipment - routers, switches, and server farms
Building a high-grade Data Center
IP and Telco bandwidth requirements
Security considerations

## Slide 78: Security
Depends on enforceable policies
Need regular auditing of procedures - can be traced to human factors

## Slide 79: Security Problems
Intrusions/Break-Ins
  Keeping software up-to-date - almost all are host-based
Denial of Service - don’t need break ins
  Combination of IP and Application policies
Theft of Service
  E-Mail spam prevention
  “smurfing” and other ICMP attacks

## Slide 80: Security Problems (2)
Theft of Information
  “Sniffing” critical information, or usernames/passwords used to break into other locations

## Slide 81: Quality of Service
Is your service "IP Dial Tone" quality? “Carrier Class”?
Managing your bandwidth charges
Committing bandwidth vs Overprovisioning

## Slide 82: Service Level Agreements
How many “9’s”? 99%, 99.9%
Depends on external factors like telco service level, but minimize internal problems too
Rebates policy

## Slide 83: Maximizing Uptime and Performance
Is the goal of designing a good Architecture
Build on this one first, before moving on to...

## Slide 84: Developing New Services
New Consumer Services
  what are the trends? what do end-users want?
  must watch out for new applications that might harm the network, however popular

## Slide 85: Developing New Services (2)
Corporate Consulting
  Tailoring your service to the customer’s needs, and integrating the solution
Product Development
  Research (on new technologies) and Development (making them work for you)

## Slide 86: Part 5
Your Turn

## Slide 87: Case Studies

## Slide 88: Conclusions

## Slide 89: Synthesis

## Slide 90: Thank you!
If you want to talk about anything, just send mail to: map@iphil.net