## Slide 1
Broadband Remote Access (BRAS) Overview

## Slide 2: Why BRAS?
Traditional Circuit Aggregation Services (E1/T1)
  Con:
    Slow to deploy
    Inflexible approach
    No longer cost effective
  Pro:
    Proven/Stable
    Widely accepted
    Typically faster to repair in case of last mile failure
Dial-up
  Con:
    Slow
    Does not scale well
  Pro:
    Existing

## Slide 3: Implications of a BRAS last mile network
Requires a new type of Network Access equipment
  10x increase in bandwidth requirements
  100x increase in customer density
  Combine routing and RAS technologies
Requires new backbone speeds and new types of traffic engineering
Requires new higher-performance routers/servers/access devices
Requires new levels of redundancy and fault tolerance
Breaks the current provisioning paradigm
  old: 10-100’s of new users/day
  new: 1000’s of new users/day

## Slide 4: Old Last Mile Architecture
10’s to 100’s of connections
Internet
Backbone
OC3/STM1
ATM
Service Provider Network
Business Users
Telco
Network
fT1
T1
Channelized T3
ADM
ADM
ADM
DACS
SONET
Ring
T1
Edge
Core
Tier 2/3
ISP
Network
Notes: <number>
<footer>
<header>
<date/time>
This application shows the Router in use for aggregation of private lines into an IP backbone network. In this example, the Router is displacing or augmenting FR (or ATM) private line services to offer native IP service.
The service provider can offer a large range of line rates to the customer, from a single DS0, multiple T1/E1s, or T3/E3s. The lines are typically fed into ADM (Add Drop Multiplexers) on a SONET ring and then fed into the Router.
The Router then handles the de-encapsulation to get to the native IP packet, classifies the packet, applies the service profile, marks the packet if necessary and routes it out the OC3/STM1or OC12/STM4 interface via ATM or POS or via Gigabit Ethernet.
The Router can also use a virtual router configuration to route the packets to different locations, allowing the service provider to sell wholesale or secure IP VPN solutions.
Using the Router for private line aggregation offers a number of key benefits:
  The ability for a service provider to offer a native IP service (with QoS) to subscribers
  Major savings in power and co-location space due to the Router density over current solutions
  Easy migration from Layer2 to Layer3 service offerings; the Router support both from a single platform

## Slide 5: First Generation DSL deployments
Apricot BRAS Presentation - <number>
<footer>
<date/time>
Consumer &
Business
Users (xDSL)
Access
Network
Provider
Service
Network
Provider
IP/PPP/FR
IP/PPPoE/ATM
RADIUS
IP/PPPoE/FR
DHCP
Internet
IP/PPP/ATM
DSLAM
ATM/FR
Switch
Adjunct
Systems
IP
Router
IP/ATM

## Slide 6: Next Generation Aggregation Technology
Service
Network
Provider
DS3 FR/ATM
OC3 ATM
RADIUS
DHCP
OC3/STM1
OC12/STM4
Gig Eth
POS/ATM
CLEC
ISP
VPN
Internet
Consumer &
Business
Users (xDSL)
Access
Network
Provider
IP/PPP/FR
IP/PPPoE/ATM
IP/PPPoE/FR
IP/PPP/ATM
DSLAM
ATM/FR
Switch
IP/ATM

## Slide 7: Target - Integrated Network Platforms
Service
Network
Provider
DS3 FR/ATM
OC3 ATM
RADIUS
DHCP
OC3/STM1
OC12/STM4
Gig Eth
POS/ATM
CLEC
ISP
VPN
Internet
IP/PPP/FR
IP/PPPoE/ATM
DSLAM
ATM/FR
Switch
E1
E3
TDM - Network
CMTS
ATM/Enet
Switch
100BaseT
OC-3 ATM
ADM
DACS
Chan STM-1
E3/DS-3
HFC Network
ATM Network

## Slide 8
1483 Routed Overview

## Slide 9: Remote Access… in the ‘Old Days’
Relatively slow access rates using dedicated POTS line
Point to point session between PC and RAS
RAS terminated the PPP session
Packets sent to appropriate routers
Modem
Modem
RAS
tyler@isp1.com
Routers
paul@isp2.com
ISP1
ISP2
PPP Session
RADIUS
RADIUS
Notes: In the remote access world of yesterday, relatively slow speed connections were made using a dedicated POTS line. These narrowband connections, with speeds from 28.8 kbps to 56 kbps, were one to one in nature. One PC, one phone line. This scenario worked relatively well for the home environment when most families were lucky to have one PC. In this scenario, the phone lines were terminated in a Remote Access Server (RAS), which also terminated the PPP session and handled, in conjunction with RADIUS, all the authentication work. From the RAS, the packets were sent on to the appropriate routers.
However, times have changed and needs have changed. More and more often, families have more than one PC, yet only have one additional phone line to use for connectivity. In addition, more and more users are demanding higher access rates. There must be a better solution.

## Slide 10: xDSL Basics
Digital Subscriber Line where x=
  Asymmetric, Symmetric, Rate-Adaptive, High-bit-rate, Very high bit rate
High Speed Connection Using Existing Phone Lines
  Voice, FAX, Data over the same phone line
  Always on!
  Speed dependent on flavor of DSL, Line Quality, Distance, etc.
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
DHCP
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
Notes: Broadband connections, such as x Digital Subscriber Lines (DSL), are becoming more and more prevalent. xDSL is a family of access technologies that utilize high transmission frequencies (up to 1 MHz) to convert existing phone lines into high speed data connections. Using DSL, a single phone line can be used for voice or FAX and data, at the same time. This is accomplished by dividing the phone line into three separate bandwidths or frequencies. Voice or FAX traffic is carried over the lower frequencies (20 hz to 40 khz), leaving the higher frequencies open for data traffic. Different frequencies are reserved for upstream or transmit traffic (300 khz - 700 khz) and downstream or receive traffic (1000 khz and above). Another benefit of an xDSL internet connection is that the connection is always on. There is no need to ‘dial-up’ your Internet Service Provider. xDSL speeds range from 128 Kbps to 8 Mbps, depending of the type of DSL, the line quality, and the distance from the central office. There are different types of DSL connections, where the ‘x’ indicates the type or flavor:
ADSL - Asymmetric DSL is the most common type of service, providing more bandwidth downstream (from the Internet to the PC) than upstream (from the PC to the Internet). Since Internet requests are typically small and Internet downloads are large, having a smaller transmit rate and a larger receive rate works out fine. ADSL upstream rate range from 16 Kbps - 640 Kbps and downstream speeds are 384 Kbps - 8 Mbps, though lower rates are more common.
SDSL - Symmetric Digital Subscriber Line provides the same bandwidth in both directions. SDSL rates range from 144 Kbps - 2.048 Mbps in both directions.
RADSL - Rate Adaptive Asymmetric DSL is similar to ADSL but the rate adjusts or can be configured based on the quality and length of the local phone line.
HDSL - High bit rate DSL - A symmetric T1/E1 line using standard copper phone wire without the use of repeaters. HDSL is the oldest and most heavily deployed DSL service. Unlike the other DSL types, HDSL uses 2 (T1) or 3 (E1) twisted pairs of copper phone wire.
VDSL - Very High Bit Rate DSL is a shorter distance, higher speed version of DSL.

## Slide 11: xDSL Customer Premise Equipment (CPE)
Business or Enterprise Customer
  Connect LANs to a xDSL router or bridge
  Connect LANs to a router or bridge plus an xDSL modem
Residential or SOHO Customer
  Workstation with integrated xDSL modem
  Workstation with an Ethernet or ATM NIC connected to a standalone xDSL modem
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
DHCP
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
Notes: DSL networks require new equipment to be installed at both the customer’s location as well as the providers location. A DSL modem is installed at the customer premise. It carries the data across existing copper wires to a similar DSL modem at the provider’s central office.
Business or Enterprise customers will often connect their LANs to DSL capable routers or Bridge, such as a Flowpoint. These devices have both a LAN connection such as Ethernet, an ATM component and a DSL modem. Another option is to connect their LANs to a router which in turn connects to an external DSL modem.
Residential or Small Office Home Office (SOHO) users will either have a workstation or a PC with an integrated DSL modem, an Ethernet NIC that connects to an external DSL modem, or an ATM NIC connected to an external DSL modem. The most common approach is the Ethernet NIC connecting to an external DSL modem.

## Slide 12: xDSL POP Equipment
Local POP
  One or more DSLAMs - Digital Subscriber Line Access Multiplexer
Central Office
  ATM Switch
  xDSL Concentrator
  RADIUS, DHCP Servers
PVC Established from the xDSL Concentrator to the CPE Device
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
DHCP
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
Notes: In the providers local point of presence (POP), one or more Digital Subscriber Line Access Multiplexer (DSLAM) are installed. This device contains DSL modems which are aggregated on to a high speed ATM or Frame Relay connection. These connections are potentially aggregated by an ATM switch and ultimately terminated on a DSL concentrator located at a central office. RADIUS and DHCP servers might also be located at the central office. They may be used for user authentication and IP Address assignment.
In a DSL environment, a Permanent Virtual Circuit is established from the DSL concentrator to the CPE device. One or more users can use this PVC, depending on the configuration.

## Slide 13: To Authenticate or not...
Always on, No Authentication
  Bridged 1483
  Routed 1483
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
DHCP
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
Bridged 1483
Routed 1483
Notes: Currently, there are two general approaches to DSL access. With the first approach, the DSL users are always on and no user authentication takes place. This approach is often referred to as Bridged 1483 or Routed 1483. It is the simplest of configurations. The user’s IP addresses can either be statically assigned or obtained via DHCP.

## Slide 14: To Authenticate or not...
To maintain current dial-up model, complete with RADIUS Authentication and Accounting Services
  PPP over ATM
  PPP over Ethernet over ATM
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
PPP over
Ethernet
PPP over
ATM
Notes: The second approach attempts to maintain the current dial-up model, complete with centralized user authentication and authorization. The DSL users are still always on, but initially the users must authenticate through a RADIUS server. They will also obtain their IP address from RADIUS or DHCP. This approach is often referred to as PPP over ATM for a single user environment or PPP over Ethernet for a multi-user environment.

## Slide 15: Routed 1483 - Life of a Packet
PC generates an IP datagram encapsulated in an Ethernet frame
DSL router receives the frame, strips off the Ethernet frame and determines next hop
DSL router encapsulates the IP datagram in an ATM cell using Routed 1483 IP encapsulation
Router receives the frame, strips off the Routed 1483 encapsulation and determines next hop
Router encapsulates the IP datagram in the appropriate next hop frame format
Internet
DSL Router
DSL Router
IP Datagram
Ethernet
IP Datagram
Routed 1483
IP Datagram
New Encap
Notes: In the Routed 1483 environment, a DSL capable router or a router and a DSL modem are installed at the customer’s location. This router provides connectivity to the Internet for one or more networks at the customer’s location. The router or modem is connected over a phone line to a DSLAM, which is in turn connected via ATM to the Router. An ATM PVC is provisioned from the Router to the customer’s CPE device.
If a user at the customer’s location desires access to the Internet, the basic packet flow is as follows. For this example, the customer uses Ethernet.
The user’s PC generates an IP packet that is encapsulated in an Ethernet frame addressed to the router.
The DSL router receives the Ethernet frame, sees that it is addressed to the router, and strips off the Ethernet Frame.
The router looks at the destination IP address, consults its routing table and determines that the next hop is off the DSL interface.
The router encapsulates the IP datagram into an ATM cell. A n RFC 1483 header is added at the beginning of the cell, indicating that the cell contains an IP datagram, hence the name Routed 1483.
The cell is then transmitted across PVC to the Router.
The Router receives the cell, strips off the RFC 1483 header, looks at the destination IP address, and determines the next hop interface.
The router encapsulates the IP datagram in the appropriate layer 2 frame and transmits the data into the Internet.
If a router receives a layer 2 frame addressed to itself, it will strip off the layer 2 encapsulation, determine the next hop address based on the destination IP address, and encapsulate the IP datagram in a new layer 2 frame for the next leg of its journey. We will see that this behavior is very different in a Bridged 1483 environment.

## Slide 16: Routed 1483 - Router Configuration
Think Layers!
Encapsulation, Encapsulation, Encapsulation!
Sonet
SDH
ATM
IP
UT3A/UE3A
OC3c
Physical
Layer
Data Link
Layer
Network
Layer
Slot/Port
Clocking
Shutdown
Framing
PVC VPI/VCI
Encapsulation
ATM Framing
IP Address
Subnet Mask
Loopback Reference
Internet
DSL Router
DSL Router
ATM
IP
Notes: When one is configuring the Router, one must remember to think in layers! Interface columns on the Router must be configured from the bottom up.
Physical Layer parameters must be configured first. In an ATM environment, physical parameters include slot and port, clock source, no shutdown for UT3 or UE3 interfaces, and framing (Sonet or SDH).
Data Link Layer parameters include ATM PVC information, encapsulation method, and ATM framing.
Network Layer parameters include IP addresses, subnet masks, and routing protocols or static routes.
Note that each layer is dependant on one another. An IP address can not be configured on an ATM interface unless an ATM PVC has been configured.
It is also important to remember the type of encapsulation that is occurring on both ends of a link. They must match! If the Router is configured for IP over ATM, otherwise known as Routed 1483, and the other end of the link is a bridge, not a router, things will NOT work!

## Slide 17: ATM Basics
1 Physical Interface, Multiple Logical Connections
  Router supports PVCs
  1 PVC per xDSL CPE
Each PVC identified by a Virtual Path Identifier (VPI)/Virtual Circuit Identifier (VCI) pair
  Router also uses a Virtual Circuit Descriptor (VCD)
  Unique number that identifies a virtual circuit
VPI 0
VCI 33
VCI 34
VCI 35
Customer
Network
Customer
Network
DSLAM
DSL Router
DSL Router
xDSL
Bridge
Notes: In an ATM environment, one physical connection can support multiple logical interfaces. These logical connections are known as Permanent Virtual Circuits or PVCs. They are statically configured and always available. No call setup occurs to establish connectivity. A PVC is identified by a Virtual Path Identifier (VPI) and a Virtual Circuit Identifier (VCI). A Virtual Path (VP) can contain many Virtual Circuits (VCs). In this example, VP 0 contains 3 VCs. The combination of VPI/VCI uniquely identifies a connection on a physical interface. In this example, the following logical connections exist: 0/33, 0/34 and 0/35.
The Router also adds an extra identifier to each VC known as the Virtual Circuit Descriptor (VCD). The VCD must be unique on an interface. It is used to obtain statistics about a particular VPI/VCI on the Router.
In a DSL environment, 1 PVC will be configured for each xDSL CPE device. Therefore, one physical port on the Router can support thousands of DSL users.

## Slide 18: ATM Traffic Management
OC3c (2 port)
  Unspecified Bit Rate (UBR) only
UT3/UE3
  UBR
  UBR with Peak Cell Rate (PCR)
  Non-realtime (nrt) Variable Bit Rate (VBR)
  Shaping done on an individual VC
  Outbound traffic shaping
VPI 0
VCI 33
VCI 34
VCI 35
Customer
Network
Customer
Network
DSLAM
DSL Router
DSL Router
xDSL
Bridge
Notes: The Router supports limited ATM traffic management capabilities, otherwise known as traffic shaping. Traffic shaping is only relevant to outbound traffic. Different Router line cards support different capabilities, depending on the configuration.
The 2 port OC3 line module only supports Unspecified Bit Rate (UBR). UBR traffic is not rate limited in any way. The physical line rate is the only limiting factor.
The UT3A and UE3A supports UBR as well as UBR with Peak Cell Rate (PCR) and Non-Real-Time (nrt) Variable Bit Rate (VBR).
Using UBR with PCR, traffic is never allowed to exceed the configured PCR.
With nrt VBR, the following parameters are configured: Peak Cell Rate, Average (sustained) cell rate, and burst size. Traffic should not exceed the average or sustained cell rate, but traffic can burst to the configured burst size. In addition, traffic can never exceed the peak cell rate.

## Slide 19: ATM Configuration
interface atm slot/port.subinterface
  interface atm 5/0.33
atm pvc vcd vpi vci encapsulation peak average burst
  encapsulation
    aal5snap or aal5mux ip
  Peak, Average in 1 Kbps chunks, burst in cells
    UBR No peak, average or burst configured
    UBR with PCR Peak Configured
    nrt-VBR Peak, Average, and Burst Configured
  atm pvc 33 0 33 aal5snap 256 128 100
Slot 5
Port 0
VCI 33
VCI 34
VCI 35
Customer
Network
Customer
Network
DSLAM
DSL Router
DSL Router
xDSL
Bridge
VPI 0
Notes: To configure ATM PVCs on the Router, it is necessary to configure a slot, port and subinterface. The subinterface refers to the logical connection or PVC. Often administrators will use the same number for ATM Subinterface, Virtual Circuit Descriptor, and Virtual Circuit Identifier, as is the case with this example.
In older software versions (<1.2.x), the peak and average cell rate were configured in 64K chunks. Now, the peak and average can be configure in 1K chunks. The burst size is in terms of cells, not a traffic rate.
Remember that VC traffic shaping can NOT be used on the 2 port OC3 card.

## Slide 20: ATM Traffic Shaping - VP Tunnels
Customers
ISP B
ISP A
Allocate bandwidth to a Virtual Path
All PVCs within VP contend for tunnel bandwidth
Traffic shaping relevant to outbound traffic only
VP Tunnels supported on all ATM line modules
  2 port OC3
  UT3A
  UE3A
VPI 0 5 Mbps
VPI 2 30 Mbps
VPI 1 10 Mbps
Notes: It is also possible to configure traffic shaping at the Virtual Path level using ATM VP Tunnels. This allows the segregation of traffic for different customers. In this example, the carrier is providing service to multiple ISPs and they all share the same ATM link. Assigning a VP tunnel to each ISP allows each to have its own virtually separate pipe. In this example, the carrier is offering services to other ISPs over the UT3A interface. ISP A has been allocated 5 Mbps and ISP B has been allocated 10 Mbps. The remaining 30 Mbps is being used by the carrier.
With ATM VP Tunnels, bandwidth is allocated in a round-robin fashion to all PVCs within a Virtual Path for traffic shaping purposes. Remember that traffic shaping is only relevant to outbound traffic. If a VP Tunnel has been configured, it is not possible to traffic shape at the VC level. In other words, one can shape at the VC level or shape at the VP level, not both.
ATM VP Tunnels are supported on all ATM line modules, including the 2 port OC3 and UT3A/UE3A cards.

## Slide 21: Configuring VP Tunnels
Configure ATM vc-per-vp to allow additional VPs
  Configurable only on UT3A or UE3A
Configure the ATM interface
  interface atm 5/0
Configure the ATM VP tunnels
  Configurable in Kbps
  atm vp-tunnel 0 5000
Configure ATM PVCs
  Traffic shaping not permitted at the VC level
  interface atm 5/0.33
  atm pvc 33 0 33 aal5snap
Customers
ISP B
ISP A
VPI 0 5 Mbps
VPI 2 30 Mbps
VPI 1 10 Mbps
Notes: When using UT3A or UE3A interfaces, first configure the number of VCs per VP to allow additional VPs. By default, UT3/UE3 cards allow 1 VP (VPI 0) with 65,536 VCs (older cards support fewer VCs). If additional VPs are required, fewer VCs are supported per VP. To increase the number of VPs, use the the vc-per-vp command and the following information: #VPs vc-per-vp 1 65536 2 32768 4 16384 8 8192 16 4096 32 2048 64 1024 128 512 256 256 NOTE: Carefully plan how many VPs will be required in your network. If additional VPs are needed later, one must first delete any PVC and VP tunnel configurations BEFORE the vc-per-vp can be executed.
To configure VP Tunnels, perform the following steps:
Configure the VCs-per-VPs, if necessary
Configure the ATM interface
Configure the ATM VP tunnel, specifying the VPI and the tunnel’s traffic rate in 1Kbps chunks.
Configure the PVCs in the VP Tunnel. It is not possible to traffic shape at the VC level if traffic shaping is occurring at the VP level.

## Slide 22: IP Addressing - Option 1
View each ATM PVC as a unique point-to-point network
Assign a single subnet to each ATM PVC
Burns IP addresses
Internet
DSL Router
DSL Router
172.10.1.0/30
172.10.1.4/30
.6
.2
.1
.5
Notes: The Router views all ATM PVCs as simple point-to-point IP interfaces. Each PVC is an interface, and each interface is assigned an IP address.
In a Routed 1483 environment, IP addressing can be approach two ways. The first way is to view each ATM PVC as a unique, point-to-point network. With this approach, each PVC would be assigned a unique subnet. This approach is very straight-forward, easy to manage, but it burns or uses up IP addresses quickly.

## Slide 23: IP Addressing - Option 2
View the group of DSL users as one large LAN
Assign a single subnet to the group
Use Unnumbered Interfaces on the Router’s PVCs
  Reference a Loopback Interface on the Router in the same subnet
Use numbered interfaces on the DSL router from the same subnet
Conserves IP addresses
Internet
DSL Router
DSL Router
172.10.1.0/24
172.10.1.3
172.10.1.2
Loopback 1
172.10.1.1/24
unnumbered IP
Loopback 1
unnumbered IP
Loopback 1
Notes: With the second approach to IP address assignment in a Routed 1483 environment, the ATM cloud is viewed as a large LAN. From the Router’s perspective, a single subnet is assigned to the group of xDSL routers. Each CPE xDSL router is assigned a numbered IP address from the subnet. On the Router, a loopback interface is created and assigned an IP address from the same subnet. The ATM PVCs on the Router are not assigned numbered IP addresses. Instead, the PVCs are configured as unnumbered IP interfaces, and reference the loopback interface created with the IP address from the same subnet. This approach conserves valuable IP address space.

## Slide 24: Routing Configuration
CPE DSL Router
  Create a default route pointing to the Router
  Next hop address is the Loopback Interfaces IP address
On the Router
  Create static routes for each viable customer network
  Create a static host route for each DSL router
  Next hop interface must be the appropriate ATM subinterface
  Redistribute directly connected networks to advertise the DSL group
  Redistribute static routes to advertise the customer’s networks
172.10.1.0
20.20.0.0
30.30.0.0
Destination Next Hop Metric Protocol
10.10.0.0/16 5/1.33 1 Static
20.20.0.0/16 5/1.34 1 Static
172.10.1.0/24 Connected
172.10.1.2 5/1.33 1 Static
172.10.1.3 5/1.34 1 Static
Internet
DSL Router
DSL Router
172.10.1.3
172.10.1.2
Loopback 1
172.10.1.1/24
unnumbered IP
int atm 5/1.34
unnumbered IP
int atm 5/1.33
10.10.0.0
0.0.0.0
0.0.0.0
Redistribute Connected
172.10.1.0/24
Redistribute Static
10.10.0.0/16
20.20.0.0/16
Notes: The routing configuration in a Routed 1483 is fairly straightforward:
The CPE DSL router must have a default route(0.0.0.0) configured, with the Router’s loopback interface as the next hop address. Any traffic not destined for local networks will be forwarded to the Router.
The Router will need a static route configured for each via customer network. In this example, the following networks need to be reachable from the Internet: 10.10.0.0 and 20.20.0.0. Notice that network 30.30.0.0 should not be advertised or reachable from the Internet. Static routes have been configured for each network, with the appropriate ATM subinterface configured as the next hop interface. In addition, static host routes must be configured on the Router for each of the DSL router interfaces, again specifying the appropriate ATM Subinterface for the next hop.
To advertise these networks into the Internet, a redistribution of directly connected networks as well as static routes must be initiated in the appropriate routing protocol.

## Slide 25: Configuring Routed 1483 Interface Columns
IP Address
Loopback for Unnumbered IP OR
Subnet Mask for Numbered IP
OC3
UT3A/E3A
5/0
ATM Interface
5/0
ATM Subinterface
5/0.33
pvc 33 0/33
ATM Subinterface
5/0.34
pvc 34 0/34
IP Unnumbered
Loopback 1
IP Unnumbered
Loopback 1
Clocking
Framing
Slot/Port
Framing # VC per VP
(UT3A/UE3A only)
Slot / Port . Subinterface
PVC VCD VPI/VCI
ATM Subinterface
5/0.35
pvc 35 0/35
IP Interface
172.10.35.1/30
Notes: When one is configuring the Router, one must remember to think in layers! Interface columns on the Router must be configured from the bottom up.
Physical Layer parameters must be configured first. In an ATM environment, physical parameters include slot and port, clock source, no shutdown for UT3 or UE3 interfaces, and framing (Sonet or SDH).
Data Link Layer parameters include ATM PVC information, encapsulation method, and ATM framing.
Network Layer parameters include IP addresses, subnet masks, and routing protocols or static routes. If a numbered interface is configured, a subnet mask must also be configured. If an unnumbered interface is configured, no subnet mask is specified. Instead, the unnumbered interface must reference some IP interface on the Router, typically a loopback interface.
Note that each layer is dependant on one another. An IP address can not be configured on an ATM interface unless an ATM PVC has been configured.
It is also important to remember the type of encapsulation that is occurring on both ends of a link. They must match! If the Router is configured for IP over ATM, otherwise known as Routed 1483, and the other end of the link is a bridge, not a router, things will NOT work!

## Slide 26: Routed 1483 Configuration Steps
Configure Loopback Interface
Configure UT3/U3E Controller
  Clocking, Framing, Shutdown
Configure ATM interface
  # VCs per VP, Framing
Configure the following per DSL router:
  Configure ATM Subinterface
  Configure PVC, PVC encapsulation
  Configure IP Interface
    Numbered IP and Subnet Mask OR
    Unnumbered IP and Loopback reference
  Configure IP Static Routes
UT3 / UE3
OC3c
ATM
Subinterface
ATM
Subinterface
IP Interface
IP Interface
ATM Interface
Notes: The configuration steps for the first DSL router :
Router1(config)#interface loopback 2
Router1(config-if)#ip address 172.10.1.1 255.255.255.0
Router1(config)#controller t3 5/0
Router1(config-controll)#clock source internal chassis
Router1(config-controll)#no shutdown
Router1(config-controll)#exit
Router1(config)#interface atm 5/0
Router1(config-if)#interface atm 5/0.33
Router1(config-if)#atm pvc 33 0 33 aal5snap
Router1(config-if)#ip unnumbered loopback 2
Router1(config-if)#exit
Router1(config)#exit
Router1(config)#ip route 172.10.1.2 255.255.255.255 atm 5/0.33
Router1(config)#ip route 10.10.0.0 255.255.0.0 atm 5/0.33
Router1(config)#^Z

## Slide 27
1483 Bridged Overview

## Slide 28: Bridged 1483 - Life of a Packet
PC generates an IP datagram encapsulated in an Ethernet frame
DSL bridge receives the frame and encapsulates the frame in an ATM cell using Bridged 1483 ATM encapsulation
Router receives the frame, strips off the Bridged 1483 encapsulation and Ethernet Frame and determines next hop
Router encapsulates the IP datagram in the appropriate next hop frame format
Internet
DSL Bridge
DSL Bridge
IP Datagram
Ethernet
IP Datagram
New Encap
IP Datagram
Ethernet
Bridged 1483
Notes: In the Bridged 1483 environment, a DSL capable bridge or modem is installed at the customer’s location. This bridge provides connectivity to the Internet for the customer’s networks. The bridge is connected over a phone line to a DSLAM, which is in turn connected via ATM to the Router. An ATM PVC is provisioned from the Router to the customer’s CPE device.
If a user at the customer’s location desires access to the Internet, the basic packet flow is as follows. For this example, the customer uses Ethernet.
The user’s PC generates an IP packet that is encapsulated in an Ethernet frame addressed to the Router (VERIFY!!!!).
The DSL bridge receives the Ethernet frame and encapsulates the entire frame into an ATM cell. An RFC 1483 header is added at the beginning of the cell, indicating that the cell contains an bridged Ethernet frame hence the name Bridged 1483.
The cell is then transmitted across PVC to the Router.
The Router receives the cell, strips off the Bridged RFC 1483 header, strips off the Ethernet frame, looks at the destination IP address, and determines the next hop interface.
The router encapsulates the IP datagram in the appropriate layer 2 frame and transmits the data into the Internet.

## Slide 29: Bridged 1483 - Router Configuration
Think Layers!
Encapsulation, Encapsulation, Encapsulation!
Sonet
SDH
ATM
IP
UT3A/UE3A
OC3c
Physical
Layer
Data Link
Layer
Network
Layer
Slot/Port
Clocking
Shutdown
Framing
PVC VPI/VCI
Encapsulation
ATM Framing
IP Address
Subnet Mask
Loopback Reference
Internet
DSL Bridge
DSL Bridge
Bridged 1483
ATM
IP
Bridged 1483
Notes: When one is configuring the Router, one must remember to think in layers! Interface columns on the Router must be configured from the bottom up.
Physical Layer parameters must be configured first. In an ATM environment, physical parameters include slot and port, clock source, no shutdown for UT3 or UE3 interfaces, and framing (Sonet or SDH).
Data Link Layer parameters include ATM PVC information, encapsulation method, and ATM framing. Note that the Router must be configured to expect a ‘different’ type of encapsulation on a PVC connected to a bridge. By default, the Router expects to see an ATM header followed by a Routed 1483 header, followed by an IP datagram. In a bridged environment, the Router must be configured to expect an ATM header, a Bridged 1483 header, an Ethernet frame, and then the IP datagram. This encapsulation method is known as Bridged 1483 on the Router.
Network Layer parameters include IP addresses, subnet masks, and routing protocols or static routes.
Note that each layer is dependant on one another. An IP address can not be configured on an ATM interface unless an ATM PVC has been configured.

## Slide 30: IP Addressing - Static IP Addresses
View each ATM PVC as a unique point-to-point network
Assign a single subnet to each ATM PVC
Assign a static, numbered IP address to the client and the Router
Burns IP addresses
Internet
182.10.1.0/24
182.10.2.0/24
.1
.1
182.10.1.2/24
DSL Bridge
DSL Bridge
182.10.2.2/24
182.10.2.3/24
Static Addresses
Notes: Recall that the Router views all ATM PVCs as simple point-to-point IP interfaces. Each PVC is an interface, and each interface is assigned an IP address.
In a Bridged 1483 environment, IP addressing can be approach two ways. The first way is to view each ATM PVC as a unique, point-to-point network. With this approach, each PVC would be assigned a unique subnet. This approach is very straight-forward, easy to manage, but it burns or uses up IP addresses quickly.

## Slide 31: IP Addressing - Static and Unnumbered IP
View the group of DSL users as one large LAN
Assign a single subnet to the group
Use Unnumbered Interfaces on the Router’s PVCs
  Reference a Loopback Interface on the Router in the same subnet
Use statically assigned numbered interfaces on the workstations from the same subnet
Conserves IP addresses
Internet
182.10.1.2
DSL Bridge
DSL Bridge
182.10.1.3
182.10.1.4
Loopback 1
182.10.1.1/24
unnumbered IP
Loopback 1
unnumbered IP
Loopback 1
182.10.1.0
Static Addresses
Notes: With the second approach to IP address assignment in a Bridged 1483 environment, the ATM cloud is viewed as a large LAN. From the Router’s perspective, a single subnet is assigned to the group of xDSL users. Each CPE workstation is assigned a numbered IP address from the subnet. On the Router, a loopback interface is created and assigned an IP address from the same subnet. The ATM PVCs on the Router are not assigned numbered IP addresses. Instead, the PVCs are configured as unnumbered IP interfaces, and reference the loopback interface created with the IP address from the same subnet. This approach conserves valuable IP address space.

## Slide 32: Routing Configuration - Static and Unnumbered
CPE Workstations
  Create a default route pointing to the Router
On the Router
  Create static routes to each workstation
  Next hop interface must be the appropriate ATM subinterface
  Redistribute directly connected networks to appropriate routing protocol
Internet
182.10.1.2
DSL Bridge
DSL Bridge
182.10.1.3
182.10.1.4
Loopback 1
182.10.1.1/24
182.10.1.0
unnumbered IP
int atm 5/1.37
unnumbered IP
int atm 5/1.36
Destination Next Hop Metric Protocol
182.10.1.1/24 Loopback1 1 Connect
182.10.1.2/32 5/1.36 1 Static
182.10.1.3/32 5/1.37 1 Static
182.10.1.4/32 5/1.37 1 Static
0.0.0.0
0.0.0.0
0.0.0.0
Redistribute Connected
182.10.1.0/24
Notes: The routing configuration in a Routed 1483 is fairly straightforward:
The CPE workstations must have a default route(0.0.0.0) configured, with the Router’s loopback interface as the next hop address. Any traffic not destined for local networks will be forwarded to the Router.
The Router will need static host routes for each of the workstations, specifying the appropriate ATM Subinterface for the next hop.
To advertise the group of DSL users into the Internet, a redistribution of directly connected networks must be initiated in the appropriate routing protocol.

## Slide 33: IP Addressing - DHCP
182.10.1.14
Workstation Configuration
  Configured for DHCP
  Obtain IP address dynamically from DHCP server
Router Configuration
  Use Unnumbered Interfaces on the Router’s PVCs
    Reference a Loopback Interface on the Router in the same subnet
  DHCP Relay Agent
    Configure Router as a DHCP Relay Agent
    Configure IP address of DHCP server
    Per virtual router
Internet
182.10.1.12
DSL Bridge
DSL Bridge
182.10.1.13
Loopback 1
182.10.1.1/24
unnumbered IP
Loopback 1
unnumbered IP
Loopback 1
182.10.1.0
Dynamic Addresses
via DHCP
DHCP
Server
Address Range
182.10.1.2 - 182.10.1.255
DHCP Relay Agent
DHCP Server = 1.1.1.1
1.1.1.1
Notes: Another way a PC can obtain its IP address is using the Dynamic Host Control Protocol (DHCP). In this environment, the PC will have DHCP configured for its IP Address assignment and expect to receive their IP address from a centralized DHCP server.
In a Bridged 1483 environment, the Router can be configured as a DHCP relay agent. Any DHCP request packets the Router receives on bridged 1483 interfaces will be forwarded to the DHCP server configured on the Router. Any DHCP server originated responses will be forwarded back to the appropriate DHCP client.
The Router can communicate with up to 5 DHCP servers.

## Slide 34: Routing Configuration - DHCP
CPE Workstations
  Default Route pointing to the Router
Router
  Static routes not necessary
  Automatically insert host route into routing table based on DHCP reply
  Redistribute directly connected networks to appropriate routing protocol
Internet
182.10.1.12
DSL Bridge
DSL Bridge
182.10.1.13
182.10.1.14
Loopback 1
182.10.1.1/24
182.10.1.0
unnumbered IP
int atm 5/1.37
unnumbered IP
int atm 5/1.36
Destination Next Hop Metric Protocol
182.10.1.1/24 Loopback1 1 Connect
182.10.1.12/32 5/1.36 1 AccIntern
182.10.1.13/32 5/1.37 1 AccIntern
182.10.1.14/32 5/1.37 1 AccIntern
0.0.0.0
0.0.0.0
0.0.0.0
Redistribute Connected
182.10.0.0/24
DHCP
Server
Notes: Using DHCP eases configuration on the Router. Static host routes are no longer necessary. The Router will automatically examine the DHCP server response for the IP address being assigned to the client and update its routing tables accordingly.

## Slide 35: Configuring Bridged 1483 Interface Columns
OC3
UT3A/E3A
5/1
ATM Interface
5/1
ATM Subinterface
5/1.36
pvc 36 0/36
ATM Subinterface
5/1.37
pvc 37 0/37
Bridged 1483
Bridged 1483
Clocking
Framing
Slot/Port
Framing # VC per VP
(UT3A/UE3A only)
Slot / Port . Subinterface
PVC VCD VPI/VCI
Encapsulation Method
ATM Subinterface
5/1.38
pvc 38 0/38
Bridged 1483
IP Unnumbered
Loopback 1
IP Unnumbered
Loopback 1
IP Interface
182.10.38.1/30
IP Address
Loopback for Unnumbered IP
Subnet Mask for Numbered IP
Notes: When one is configuring the Router, one must remember to think in layers! Interface columns on the Router must be configured from the bottom up.
Physical Layer parameters must be configured first. In an ATM environment, physical parameters include slot and port, clock source, no shutdown for UT3 or UE3 interfaces, and framing (Sonet or SDH).
Data Link Layer parameters include ATM PVC information, encapsulation method, and ATM framing. In a Bridged 1483 environment, the encapsulation method of Bridged 1483 must be explicitly configured for each PVC terminating on a DSL bridge.
Network Layer parameters include IP addresses, subnet masks, and routing protocols or static routes. If a numbered interface is configured, a subnet mask must also be configured. If an unnumbered interface is configured, no subnet mask is specified. Instead, the unnumbered interface must reference some IP interface on the Router, typically a loopback interface.
By default, proxy ARP in enabled on Bridged 1483 interfaces. The Router will ARP for every device off of a Bridged 1483 interface.
Note that each layer is dependant on one another. An IP address can not be configured on an ATM interface unless an ATM PVC has been configured.

## Slide 36: Bridged 1483 Configuration Steps
Configure Loopback Interface
Configure DHCP for address assignment, if appropriate
Configure UT3/U3E Controller
  Clocking, Framing, Shutdown
Configure ATM interface
  # VCs per VP, Framing
Configure the following per DSL Bridge:
  Configure ATM Subinterface
  Configure PVC, PVC encapsulation
  Configure Encapsulation Bridged 1483
  Configure IP Interface
    Numbered IP and Subnet Mask OR
    Unnumbered IP and Loopback reference
  If not using DHCP, configure Static IP Host Route
UT3 / UE3
OC3c
ATM Interface
ATM
Subinterface
ATM
Subinterface
Bridged 1483
Bridged 1483
IP Interface
IP Interface
Notes: The configuration steps for the first DSL Bridge:
Router2:server(config)#interface loopback 1
Router2:server(config-if)#ip address 182.10.1.1 255.255.255.0
Router2:server(config-if)#exit
Router2:server(config)#interface atm 5/0.34
Router2:server(config-if)#atm pvc 34 0 34 aal5snap
Router2:server(config-if)#encapsulation bridged-1483
Router2:server(config-if)#ip unnumbered loopback 1
Router2:server(config-if)#exit
Router2:server(config)#ip route 182.10.1.2 255.255.255.255 atm 5/0.34
Router2:server(config)#^Z

## Slide 37
PPP over ATM Overview

## Slide 38: Remote Access… in the ‘Old Days’
Relatively slow access rates using dedicated POTS line
Point to point session between PC and RAS
RAS terminated the PPP session
Packets sent to appropriate routers
Modem
Modem
RAS
tyler@isp1.com
Routers
paul@isp2.com
ISP1
ISP2
PPP Session
RADIUS
RADIUS
Notes: In the remote access world of yesterday, relatively slow speed connections were made using a dedicated POTS line. These connections, with speeds from 28.8 kbps to 56 kbps, were one to one in nature. One PC, one phone line. This scenario worked relatively well for the home environment when most families were lucky to have one PC. In this scenario, the phone lines were terminated in a Remote Access Server (RAS), which also terminated the PPP session and handled, in conjunction with RADIUS, all the authentication work. From the RAS, the packets were sent on to the appropriate routers.
However, times have changed and needs have changed. More and more often, families have more than one PC, yet only have one additional phone line to use for connectivity. In addition, more and more users are demanding higher access rates. There must be a better solution.

## Slide 39: Authentication in a xDSL Environment
To maintain current dial-up model, complete with RADIUS Authentication and Accounting Services
  PPP over ATM
  PPPoE over ATM
Customer
Network
Customer
Network
DSLAM
PC w/xDSL
Modem
ATM
Switch
ATM
xDSL
Concentrator
Internet
DSLAM
xDSL
Modem
PC w/ATM NIC
xDSL
Modem
PC w/Ethernet
NIC
DSL Modem
RADIUS
DHCP
Network
of PCs
DSL Router
xDSL
Bridge
DSL Router
Bridged 1483
Routed 1483
PPP over
Ethernet
PPP over ATM

## Slide 40: PPP over ATM - Single User per ATM PVC
Single high speed interface supporting thousands of ATM PVCs
An ATM PVC or subinterface per modem supporting a single PPP session
PPP session between the user and the Router
DSL Modem
DSL Modem
DSLAM
ATM
Switch
tyler@isp1.com
ATM
paul@isp2.com
ISP1
ISP2
Router
PPP Session
RADIUS
RADIUS
PVC
per Modem
Notes: In our scenario, the Router is servicing 2 ISPs - ISP1 and ISP2.
These ISPs have two types of customer connections to service using the Router. The first type is a single user connecting to a xDSL modem. This user’s PC will have an ATM NIC installed which connects to the xDSL modem.
The Router will support a single client on a single ATM subinterface. In other words, a one-to-one relationship is formed.
This scenario uses IP/PPP/ATM.
An ATM PVC is configured for each user.
A PPP session will be established across this PVC between the user and the Router. The Router will terminate this PPP session and act as a liaison or middle-man or client for the authentication, authorization, accounting, and address assignment associated with the user’s PPP client.
Over a single, high speed interface, hundreds of ATM Permanent Virtual Circuits can be configured to support hundreds of remote DSL users.
To support this configuration, each ATM PVC will be configured with a single PPP encapsulation to support this single user.

## Slide 41: IP Addressing Scheme - ISP1
Think of the DSL users as one large LAN
Assign a single subnet to the DSL users
Use Unnumbered Interfaces on the Router’s PVCs
  Reference a Loopback Interface on the Router in the same subnet
DSL user host routes cached dynamically into the IP routing table
  ip access-routes command
Redistribute Directly Connected Networks
  Advertises the entire group of DSL users
DSL Modem
tyler@isp1.com
Internet
Router
DSL Modem
DSL Modem
rich@isp2.com
gary@isp1.com
192.168.1.0
192.168.1.2
192.168.1.3
192.168.1.4
Loopback 1=
192.168.1.1/24
Redistribute Connected
192.168.1.0/24

## Slide 42: Life of a Packet Begins...
User generates PPP frames
PPP frames are fragmented into ATM cells on the PC
ATM cells sent to the Router
Router reassembles the ATM cells into PPP frames
DSL Modem
DSL Modem
DSLAM
ATM
Switch
tyler@isp1.com
PPP Client
ATM
paul@isp2.com
PPP Client
ISP1
ISP2
IP Data
PPP
ATM
Cell
ATM
Cell
ATM
Cell
ATM
Cell
ATM
Cell
ATM
Cell
IP Data
PPP
RADIUS
RADIUS
PPP
over
ATM
Router
Notes: Remember that the PC is initially a PPP client. When the PC wants to send IP data, that data is encapsulated into a PPP frame.
The PC has an ATM NIC card which then connects to the xDSL modem.
The PPP frame is then fragmented into 53 byte ATM cells and sent over the ATM NIC.
These frames are transmitted across the POTS connection, to the DSLAM, across the ATM switch (if necessary) and are received by the Router.
The Router reassembles the PPP frame and routes the packet out the appropriate interface.
From this point on, we will focus our attention on the PPP side of the connection, remembering that this PPP session is carried over in an ATM PVC.

## Slide 43: Life of a Packet - Session Initiation
User initiates PPP connection via LCP
PPP client and Router agree on PPP authentication protocol (CHAP or PAP)
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
PPP
over
ATM
PVC
per Modem
Paul@isp2.com
ISP1
ISP2
1-PPP LCP
Request
2 -PPP LCP
Request - Chap
RADIUS
RADIUS
default
VR2
Router
AAAA
Process
Notes: Let’s take a look at the details of the configuration as well as how a user’s session will be established using this configuration.
The Router has been configured for 2 Virtual routers. ISP1 is using the default virtual router and ISP2 is using the Virtual router VR2.
Tyler@isp1.com (the PPP client) initiates a network connection via PPP LCP to the Router.
LCP Negotiation occurs. The Router can negotiate the following LCP options: MRU, Magic Number (for loopback detection), and authentication protocol (PAP or CHAP).

## Slide 44: Determine Authentication Server
User sends login: Tyler@isp1.com
Router examines login for realm or domain name “@isp1.com”
Router searches the domain to virtual router table for user’s domain name
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
ISP1
ISP2
Tyler@isp1.com
RADIUS
RADIUS
GLOBAL DOMAIN MAP DOMAIN VR
aaa domain-map isp1.com default
aaa domain-map isp2.com VR2
default
VR2
Router
AAAA
Process
Notes: During authentication, the user will send his login, Tyler@isp1.com.
On the Router, the AAAA process handles all of the Authentication, Authorization, Accounting and Address Assignment
The AAAA process on the Router will parse this login for the user’s realm or domain name. The Router will use the string after the @ sign as the domain name. This process receives the request, searches the domain-to-virtual router table, determines which virtual router the user will authenticate through, and forwards the request to the appropriate virtual router
The domain-to -virtual router table is manually configured on the Router. This global or box-wide table simply lists the valid domains and which virtual router they are associated with. This table is used initially to determine which Authentication server to use.
Based on a match, the Router will use the RADIUS Authentication server configured in this virtual router.
In this example, the Router searches the domain to virtual router table for isp1.com. The Router determines that isp1.com uses the RADIUS server configured in the default virtual router.
If no entries were in the domain-to-virtual router table, all requests would be sent to the RADIUS Authentication server configured in the default virtual router.
If there is no match in the domain-to-virtual router table, the request is sent to the RADIUS Authentication server listed in the default virtual router. For example, Diane@isp3.com tries to login using this configuration. What would happen? Since there is no match in the domain-to-virtual router table, the request is sent to the RADIUS server listed in the default virtual router. One can override this behavior using a domain name of “default” in the domain-to-virtual router table.
If there is no domain in the login, tyler, without a domain name, the Router will also use the RADIUS server listed in the default virtual router. One can override this behavior using a domain name of “NONE” in the domain-to-virtual router table.
Entries in the aaa domain to virtual router table are case sensitive.

## Slide 45: RADIUS Authentication and Authorization
Based on the virtual router, authentication request forwarded to appropriate RADIUS server
Configure RADIUS Server IP Address, UDP Port, Key
RADIUS server returns a deny or grant, including user/session attributes
RADIUS
ISP1
ISP2
Tyler@isp1.com
RADIUS
1.1.1.1
2.2.2.1
Tyler@isp1.com
IP=192.168.1.10
GLOBAL DOMAIN MAP DOMAIN VR
aaa domain-map isp1.com default
aaa domain-map isp2.com VR2
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
UDP=1645
key=training
RADIUS=2.2.2.1
UDP=1645
key=training
Notes: The Router looks at the default router configuration and determines the IP address of the RADIUS server used for authentication and authorization.
Note that the RADIUS server configuration is per virtual router, whereas the domain map information is global or “box-wide” and not tied to a virtual router.
By default, the Router uses UDP port 1812 for the RADIUS authentication server per the RFC. If your RADIUS server is using a different UDP port, explicitly configure the Router to use that port, i.e. UDP port 1645.
It may be necessary to configure the radius key, depending on the RADIUS server configuration. This is used to encrypt the password sent from the Router to the RADIUS server.
The Router is a RADIUS client and forwards the authentication request or Access-Request to the RADIUS server, 1.1.1.1. This access-request may include checklist attributes: user name, PAP user password or CHAP Password / Challenge, framed protocol, and the Router IP Address.
The RADIUS server will issue a deny or Access-Reject if Tyler@isp1.com is not found on the server or the passwords are incorrect, respectively.
The RADIUS server will issue a grant or Access-Accept if Tyler@isp1.com is found on the server and the password or challenge response is correct, respectively.
In addition, the grant may include return list attributes which the Router will apply to the user’s session. These attributes may include the IP address, subnet mask, IP routes for security purposes, session timeout, and idle timeout. In the above diagram, the RADIUS server has returned an IP address from a pool configured on the server.
The RADIUS server can also be configured with Redstone Communications Vendor Specific Attributes. We will expand on these attributes and how they are used later in the unit.
Note that at this time, the Router RADIUS client does not support the Access-Challenge.

## Slide 46: Additional RADIUS Parameters
Retransmit Value
Timeout Value
Deadtime
Max-sessions
RADIUS
ISP1
ISP2
Tyler@isp1.com
RADIUS
1.1.1.1
2.2.2.1
Tyler@isp1.com
IP=192.168.1.10
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
UDP=1645
key=training
RADIUS=2.2.2.1
UDP=1645
key=training
Notes: By default, unacknowledged RADIUS requests will be retransmitted to the RADIUS server every 3 seconds. This time interval can be adjusted on the Router using the Retransmit parameter.
By default, the Router will retransmit unacknowledged RADIUS Requests 3 times. This value can be changed using the Timeout parameter.
If the RADIUS server does not respond after 12 seconds (retransmit * timeout), by default the Router will stop sending requests to this RADIUS server for 5 minutes. The RADIUS server is actually taken off the active RADIUS server list. This period of time is known as the Deadtime, another configurable parameter.
You can use the show radius authentication server command to view RADIUS servers.
If you only have 1 RADIUS server on your network, you may want to consider setting the Deadtime to 0 and turn off the Deadtime mechanism.
By default, the Router can have 255 outstanding RADIUS requests, based on the 8 bit transaction ID field. This value is known as the max-sessions. One can limit the number of outstanding request to a specific server by lowering the max-sessions value, so as not to overwhelm a slower RADIUS server.

## Slide 47: Multiple RADIUS Servers
Direct Mode
Round Robin
RADIUS
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
RADIUS=1.1.1.2
RADIUS=1.1.1.3
RADIUS=2.2.2.1
RADIUS=2.2.2.2
RADIUS
1.1.1.2
RADIUS
1.1.1.3
2.2.2.2
Notes: Multiple RADIUS servers can be configured on the Router. The RADIUS servers will be used in the order in which they are configured.
Use the show radius authentication server command to view the order being used by the Router at any point in time.
The RADIUS servers can be configured in two different modes:
Direct Mode (default) - This mode essentially implements a primary/backup scenario for multiple RADIUS servers. Using this mode, requests are only sent to the first RADIUS server listed in the configuration. If this RADIUS server does not respond to requests (based on the timeout value and the retransmit interval), start sending requests to the second RADIUS server listed in the configuration file. The first server will not be used for the configured deadtime.
After the deadtime timer expires, the RADIUS server is reinstated on the active server list.
Round Robin - This mode will send out RADIUS requests to all active RADIUS servers, in the order listed in the configuration file. In the above diagram, the first request is sent to the first server, the second request to the second server, the third request is sent to the first server, and so on. In this case, the primary server changes with each request. This mode will effectively use all configured RADIUS servers equally, in a round robin fashion.

## Slide 48: IP Address Assignment
RADIUS Server
Local IP Address Pool on the Router
DHCP Proxy Client
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
GLOBAL DOMAIN MAP DOMAIN VR
aaa domain-map isp1.com default
aaa domain-map isp2.com VR2
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
UDP=1645
key=training
RADIUS=2.2.2.1
UDP=1645
key=training
Access Accept
Tyler@isp1.com
192.168.1.10
DHCP
1.1.2.1
Notes: The user can obtain an IP address in three different ways. As we saw in the previous slide, the RADIUS server can return both the user IP address and subnet mask.
If the RADIUS server returns a value or 255.255.255.254, 0.0.0.0 or no address, the Router will obtain an IP address for the remote user using the local address pools defined on the Router.
As of release 1.3, the Router can also provide DHCP proxy services for the workstation and obtain the workstation’s IP address from a DHCP server.
In this example, the RADIUS server returned an IP address from a pool configured on the RADIUS server. This IP address will be assigned to Tyler’s PC during the IP NCP negotiation process.

## Slide 49: Local Address Pools
ip address pool local
ip local pool isp1pool
1.1.100.2-1.1.100.254
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
UDP=1645
key=training
RADIUS=2.2.2.1
UDP=1645
key=training
Access Accept
Tyler@isp1.com
255.255.255.254
Notes: Local Address Pools can also be configured on the Router. Local address pools are configured on the Router by issuing the ip address-pool local command. Next, an IP address range would be configured by issuing the command ip local pool <poolname> <ip address start range> <ip address end range>.
Local Address Pools are configured per virtual router.
If the RADIUS server returns an IP address of 255.255.255.254, 0.0.0.0 or no address, as is the case here, the Router determine if any ip address pool information has been configured. In this case, the a local address pool has been configured and the Router will obtain an IP address for the user from the available addresses in that virtual router’s address pool.
The Router will associate this user with this IP address until the session is disconnected and the address is released.
If there are no addresses available, the Router will fail the request.
There is no concept of ‘leasing’ an address as with DHCP. The address is allocated to that user until the user’s session disconnects.

## Slide 50: DHCP Proxy Client
ISP1
ISP2
DHCP
RADIUS
1.1.2.1
2.2.2.1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
ip address-pool
dhcp
ip dhcp-server
1.1.2.1
RADIUS=2.2.2.1
UDP=1645
key=training
Tyler@isp1.com
255.255.255.254
Notes: DHCP Proxy provides the ability to dynamically assign IP addresses to clients even though the clients are PPP clients, not DHCP clients. The Router acts as a DHCP client on behalf of the PPP client and negotiates the allocation of an IP address with one or more DHCP servers on the network. The Router maintains the address for the client by renewing the lease on the address until the client terminates the connection and releases the address back to the server that provided it.
The DHCP proxy client is configured on the Router by issuing the ip address-pool dhcp command. Next, the IP addresses of the DHCP servers would be configured using the command ip dhcp-server <ip address of dhcp server>.
The Router DHCP Proxy client is configured and operates per virtual router.
If the RADIUS server returns an IP address of 0.0.0.0, no address or 255.255.255.254, as is the case here, the Router determines if any IP address pool information has been configured. In this case, DHCP has been configured for the local address pool. The Router will obtain an IP address for the user from one of the DHCP servers configured.
Up to 5 DHCP servers can be configured. The DHCP servers can be the same ones used with Bridged 1483 or they can be completely different DHCP server. Therefore, Bridged 1483 can support 5 DHCP servers and DHCP proxy can support an additional 5 DHCP servers. If multiple DHCP servers are configured, the address request will be sent to all configured servers.

## Slide 51: Determine Virtual Router
Unnumbered interfaces associated with a loopback interface
Loopbacks are IP Interfaces configured per virtual router
Which Virtual Router should be used?
  Domain to Virtual Router Map
  RADIUS Vendor Specific Attribute
  IP Template
RADIUS
IPConf Req 0.0.0.0
IPConf Req ?.?.?.?
ISP1
ISP2
RADIUS
1.1.1.1
2.2.2.1
GLOBAL DOMAIN MAP DOMAIN VR Interface
aaa domain-map isp1.com default Loopback 1
aaa domain-map isp2.com VR2 Loopback 1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
Loopback 1 =
192.168.1.1/24
Loopback 2
172.16.1.1/16
Notes: Once the Router has obtained an IP address for the remote user, the next step is to perform PPP IP NCP negotiations. Typically, the Router will use an unnumbered interface for this PPP session. Each unnumbered interface has an associated loopback interface. If the Router is using an unnumbered interface, the IP address supplied to the user during IPCP negotiation will be the IP address of the associated loopback interface configured on the Router.
This presents a challenge: Which loopback address should be used? Remember that all layer 1 and layer 2 information is global or “box-wide” in nature and is not tied to a specific virtual router. Layer 3 information, specifically IP interfaces, is directly tied to a specific virtual router. Therefore, at this point in time, the Router must determine to which virtual router this IP interface will belong. The Router will then use the IP address of the loopback interface in that particular virtual router for IPCP negotiation.
Which virtual router is this IP interface going to use? The virtual router can be determined by three methods
  The Domain to Virtual Router Map can specify which virtual router and which Loopback interface to use.
  Using the Redstone Communications RADIUS Vendor Specific Attributes (VSA), the RADIUS server can return the user’s virtual router in the Access-accept message and the loopback interface.
  An IP Template can also specify which Virtual Router this interface is going to use. More on Templates later in this unit.

## Slide 52: IPCP Negotiation
IPConf Req 0.0.0.0
IPConf Nak 192.168.1.10
IPConf Req 192.168.1.1
IPConf Req 192.168.1.10
IPConf Ack 192.168.1.10
IPConf Ack 192.168.1.1
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
GLOBAL DOMAIN MAP DOMAIN VR Interface
aaa domain-map isp1.com default Loopback 1
aaa domain-map isp2.com VR2 Loopback 1
default
VR2
Router
DSL Modem
Tyler@isp1.com
Loopback 1 =
192.168.1.1/24
Loopback 2
172.16.1.1/16
Default Virtual Router’s IP Routing Table
Prefix/Length Next Hop Dist/Met Interface
192.168.1.0/24 192.168.1.1 0/1 Loopback1
192.168.1.10/32 0.0.0.0 2/1 serial 513
Notes: Now the Router knows the IP address of the user (either from RADIUS or from a local address pool), the virtual router this IP interface is going to use, and the appropriate IP address to use during IPCP negotiation. The Router and the user will now perform standard IPCP negotiations.
In the above diagram, RADIUS did not return the VSA virtual router, and the template defined on that interface. did not specify the virtual router, so based on the information found in the domain to virtual router table, Tyler@isp1.com is going to belong to the default virtual router. The Router will use 192.168.1.1, the IP address of Loopback 1 found in the default virtual router, during IPCP negotiations.
Optionally, the Router will install the user’s IP host route into the appropriate virtual router’s routing table. In this case, Tyler’s IP Address, 192.168.1.10, will be installed in the default router’s IP routing table as a 32-bit host route.

## Slide 53: Name Servers
aaa dns primary 1.1.1.10
aaa dns secondary 1.1.1.11
aaa wins primary 1.1.1.10
aaa wins secondary 1.1.1.11
DNS/WINS
Obtained two different ways:
  RADIUS
  Configured on Router per virtual router
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
RADIUS=2.2.2.1
DNS/WINS
1.1.1.10
DNS/WINS
1.1.1.11
Notes: The name server configuration operates similar to the IP address configuration. The user can obtain the IP addresses of the name servers (DNS and WINS) two different ways.
1) RADIUS can return the IP addresses of the name servers using VSA.
2) The name servers can be configured on the Router.
Name servers are configured per virtual router.
In this example, RADIUS did not return the IP address of the name servers. The Router will supply the addresses of the name server based on the configuration in the default virtual router.

## Slide 54: Accounting
RADIUS Accounting Start Record Sent
ISP1
ISP2
RADIUS
RADIUS
1.1.1.1
2.2.2.1
default
VR2
Router
DSL Modem
DSL Modem
DSLAM
Tyler@isp1.com
Paul@isp2.com
RADIUS=1.1.1.1
UDP=1646
key=training
RADIUS=2.2.2.1
UDP=1646
key=training
Notes: As with RADIUS authentication servers, RADIUS accounting servers are also configured per virtual router. At this point in time, the Router will determine the IP address of the RADIUS Accounting server for the default virtual router and send a RADIUS accounting start record for Tyler@isp1.com. Accounting is maintained per user.
Recall that there are two basic RADIUS accounting records: RADIUS accounting start and RADIUS accounting stop records.
Remember that ISP1 is wholesaling services to ISP2 using this Router. If Paul@isp2.com logged on, a RADIUS accounting start record would normally be sent to the RADIUS accounting server in VR2. The RADIUS accounting server for ISP2 might be located in ISP2’s domain. However, ISP1 may want to know some of the details of ISP2’s traffic. To accomplish this task, it is possible to configure the Router to send duplicate accounting start and stop messages. Messages would be sent to the RADIUS accounting server at ISP2 as well as the RADIUS accounting server at ISP1. This option is configured using the aaa accounting duplication configuration command.
At this point, Tyler has successfully established a PPP over ATM session with the RX and is ready to ‘surf the web!’

## Slide 55: PPP over ATM Interface Columns
UT3 / UE3
OC3c
ATM Interface
ATM Subinterface
1 per Client
ATM Subinterface
1 per Client
PPP Interface
1 per Client
PPP Interface
1 per Client
IP Interface
IP Interface
Clocking
Framing
Slot/Port
Framing # VC per VP (UT3 or UE3)
Slot/Port.Subinterface
PVC
Authentication Type
Which Virtual Router?
Which IP address to cache?
Notes: The UT3/UE3 controller, ATM Interface, ATM Subinterface, and PPP interface are statically defined on the Router. Recall that in a PPP over ATM environment, each modem supports just one user. Therefore, on the Router, an ATM subinterface or PVC and PPP interface will be statically created for each user.
In a B-RAS environment, IP Interfaces must be dynamically created and assigned to the appropriate virtual router when the user logs on. The user could obtain a different IP address each time he logs on to the Router. After successful completion of IPCP negotiation, the users IP address must be installed as a 32-bit host route in the routing table of the appropriate virtual router. When the user logs off, the route must be deleted and the IP Interface dynamically removed from the configuration.
To facilitate this dynamic creation and deletion of IP interfaces, the Router uses a mechanism called IP templates. The ip interface command ip access-routes automatically inserts and deletes the host route in the Router’s routing table.
If the IP interface is NOT going to be in the default virtual router, it is NOT possible to statically configure the IP interface, assign it an address (numbered or unnumbered) and specify the ip access-route command. In order to dynamically create IP interfaces in non-default virtual routers, it is necessary to use IP Templates.
If the IP Interface is going to be in the default virtual router, it is possible to statically define the IP interface (numbered or unnumbered) and specify the ip access-routes command for each interface. The ip access-routes command instructs the Router to automatically cache the assigned host route in the routing table. It is also possible to use IP templates for default virtual router IP interfaces, but not necessary.

## Slide 56: IP Templates
Placeholder or Trigger to dynamically create an IP interface in the appropriate virtual router using a common set of IP attributes
UT3 / UE3
OC3c
ATM Interface
ATM Subinterface
ATM Subinterface
PPP Interface
PPP Interface
Template
IP Interface
Template
IP Interface
Virtual
Router
Dynamically
Created
Global
Configuration
Static
Configuration
Notes: Remember that all layer 1 and layer 2 information (UT3/UE3/OC3c, ATM Interfaces and Subinterfaces, PPP Interfaces) are global in nature or independent of the VR configuration. The only part of the protocol stack or interface column that is specific to a virtual router is the IP Interface.
A template defines properties or behaviors of an IP interface, such as the MTU size, the option to cache the host route in the routing table, or assigning the IP interface to specific virtual router. A template is created or defined once globally on the Router, and then applied to as many interfaces as desired.
For example, assume ISP2 wants to support 2,000 users or 2,000 IP Interfaces. The ISP wants all of these IP interfaces to have the same behavior and characteristics, specifically that each host route will be cached in the VR2 routing table and that each interface will have an MTU of 1500 bytes.
An IP template will be created globally in the Router. For example:
host8(config)#template isp2
host8(config-template)#ip ?
access-routes Enable the creation of host access routes on this interface address Configure an IP address on an interface directed-broadcast Enable directed broadcast forwarding mtu Configure the maximum transmission unit for this network redirects Enable transmission of ICMP redirect messages unnumbered Configure IP on this interface without a specific address virtual-router Specify a virtual router for the ip template
host8(config-template)#ip access-routes host8(config-template)#ip mtu 1500
This template will then be assigned to all PPP interfaces configured for this ISP. The template is also the mechanism or trigger to dynamically create the IP interface in the appropriate virtual router and must be used to dynamically create and place IP interfaces in any router other than the default virtual router.

## Slide 57: B-RAS Configuration Steps - Initial Setup
Configure a B-RAS License
Configure Virtual Routers
Configure Loopback Interfaces
  Per Virtual Router
Configure the Domain to Virtual Router Map
  Global Table
Configure the RADIUS Authentication and Accounting Servers and Parameters
  Per Virtual Router
Configure Name Servers
  Per Virtual Router
Configure Local IP Address Pools
  Per Virtual Router
Configure IP Templates
  Specify common parameters
  Required to create IP interfaces in a non-default virtual router
default
VR2
RADIUS=1.1.1.1
UDP = 1645
key=training
RADIUS =2.2.2.1
UDP = 1645
key=training
Loopback1=192.168.1.1
Loopback1=172.16.1.1
GLOBAL DOMAIN MAP DOMAIN VR Interface
aaa domain-map isp1.com default Loopback 1
aaa domain-map isp2.com VR2 Loopback 1
Notes: RX-0-9-D0(config-if)#lic b-ras INSERT KEY HERE
NOTICE: By executing this command, you agree to be bound by the terms and conditions of Redstone Communication's RX700/1400 Software License. Please review these terms and conditions found in the Redstone Communication's RX700/1400 Product Overview Guide before continuing.
Proceed with 'license b-ras' command? [confirm]
RX-0-9-D0(config)#int loop 1
RX-0-9-D0(config-if)#ip address 192.168.1.1 255.255.255.0
RX-0-9-D0(config)#aaa domain-map isp1.com default loop 1
RX-0-9-D0(config)#radius authentication server 10.3.0.53
RX-0-9-D0(radius-server)#
RX-0-9-D0(radius-server)#udp-port 1645
RX-0-9-D0(radius-server)#key training
RX-0-9-D0(radius-server)#deadtime 0
RX-0-9-D0(radius-server)#exit
RX-0-9-D0(config)#radius accounting server 10.3.0.53
RX-0-9-D0(radius-server)#udp-port 1646
RX-0-9-D0(radius-server)#key training
RX-0-9-D0(radius-server)#dead 0
RX-0-9-D0(radius-server)#exit
RX-0-9-D0(config)#template isp1
RX-0-9-D0(config-template)#ip access-routes
RX-0-9-D0(config-template)#exit
RX-0-9-D0(config-controll)#virtual vr2
Proceed with new virtual-router creation? [confirm]
RX-0-9-D0:vr2(config)#int loop 1
RX-0-9-D0:vr2(config-if)#ip address 172.16.1.1 255.255.0.0
RX-0-9-D0:vr2(config)#aaa domain-map isp2.com vr2 loopback 1
RX-0-9-D0:vr2(config)#radius authentication server 10.3.0.53
RX-0-9-D0:vr2(radius-server)#udp-port 1645
RX-0-9-D0:vr2(radius-server)#key training
RX-0-9-D0:vr2(radius-server)#deadtime 0
RX-0-9-D0:vr2(radius-server)#exit
RX-0-9-D0:vr2(config)#radius accounting server 10.3.0.53
RX-0-9-D0:vr2(radius-server)#udp-port 1646
RX-0-9-D0:vr2(radius-server)#key training
RX-0-9-D0:vr2(radius-server)#deadtime 0
RX-0-9-D0:vr2(radius-server)#exit
RX-0-9-D0:vr2(config)#template isp2
RX-0-9-D0:vr2(config-template)#ip access-routes
RX-0-9-D0:vr2(config-template)#exit

## Slide 58: PPP/ATM Configuration Steps
Configure UT3/U3E Controller
  Clocking, Framing, Shutdown
Configure ATM interface
  # VCs per VP, Framing
Configure the following per user:
  Configure ATM Subinterface
  Configure PVC, PVC encapsulation
  Configure Encapsulation PPP
  Specify PPP Authentication CHAP/PAP
  Apply an IP Template
UT3 / UE3
OC3c
ATM Interface
ATM Subinterface
ATM Subinterface
PPP Interface
PPP Interface
Dynamic
IP Interface
via Template
Dynamic
IP Interface
via Template
Notes: The configuration steps for Tyler@isp1.com:
RX-0-9-D0(config)#controller t3 5/1
RX-0-9-D0(config-controll)#no shutdown
RX-0-9-D0(config)#int atm 5/1
RX-0-9-D0(config-if)#int atm 5/1.1
RX-0-9-D0(config-if)#atm pvc 1 0 101 aal5snap
RX-0-9-D0(config-if)#encap ppp
RX-0-9-D0(config-if)#ppp auth chap
RX-0-9-D0(config-if)#template isp1
NOTE: Templates are required when the IP Interface will be created in a non-default virtual router.
Templates are NOT required when the IP interface will be created in the default virtual router. If the IP interface will reside in the default virtual router, use the following commands INSTEAD of the template command:
RX-0-9-D0(config)#int atm 5/1
RX-0-9-D0(config-if)#int atm 5/1.1
RX-0-9-D0(config-if)#atm pvc 1 0 101 aal5snap
RX-0-9-D0(config-if)#encap ppp
RX-0-9-D0(config-if)#ppp auth chap
RX-0-9-D0(config-if)#ip unnumbered loopback 1
RX-0-9-D0(config-if)#ip access-routes
The configuration steps for Paul@isp2.com:
RX-0-9-D0:vr2(config)#int atm 5/1.2
RX-0-9-D0:vr2(config-if)#atm pvc 2 0 102 aal5snap
RX-0-9-D0:vr2(config-if)#encap ppp
RX-0-9-D0:vr2(config-if)#ppp auth chap
RX-0-9-D0:vr2(config-if)#template isp2
RX-0-9-D0:vr2(config-if)#int atm 5/1.3
RX-0-9-D0:vr2(config-if)#atm pvc 3 0 103 aal5snap
RX-0-9-D0:vr2(config-if)#encap ppp
RX-0-9-D0:vr2(config-if)#ppp auth
RX-0-9-D0:vr2(config-if)#ppp authentication chap
RX-0-9-D0:vr2(config-if)#template isp2
RX-0-9-D0:vr2(config-if)#exit
NOTE: Since Paul’s IP interface will be located in virtual router VR2, templates are required.

## Slide 59
PPP over Ethernet over ATM (PPPoE) Overview

## Slide 60: Remember the ‘Old Days’
Relatively slow access rates using dedicated POTS line
Point to point session between the PC and the RAS
RAS terminated the PPP session
Packets sent to appropriate routers
Modem
Modem
RAS
tyler@isp1.com
Routers
paul@isp2.com
ISP1
ISP2
PPP Session
RADIUS
RADIUS
Notes: Recall that in the ‘Old Days’, a single remote user would have a single phone line to establish a point to point connection with a remote access server. A strict peer to peer or one to one relationship was established.
When a PC initiated a PPP session, the PC would send out PPP LCP packets across the link. Only one other device was on this dedicated, point to point connection: the RAS. Consequently, the only device capable of receiving these packets and thus responding to these packets was the RAS. Establishing a connection, authenticating the connection, and managing the connection was a fairly straightforward process, given this point-to-point scenario.

## Slide 61: Multiple Clients per ATM PVC - PPP/PPPoE/ATM
High speed access using shared POTS line
Multiple users per DSL modem
ATM PVC per modem, PPP Session per User
How do I setup a connection and perform authentication without a dedicated connection?
DSL Modem
DSL Modem
DSLAM
ATM
Switch
diane@isp1.com
tim@isp1.com
ATM
ken@isp2.com
ralph@isp2.com
ISP2
ISP1
ISP2
pam@isp1.com
Notes: The second environment we will address is a small office or home with multiple PCs on an Ethernet which is connected to the xDSL modem.
Unlike the traditional RAS environment, or even the PPP over ATM environment, no dedicated, point-to-point connection exists in a PPP.E environment. In the old days, if a PC transmitted a LCP request, only one other device on the network could possibly receive it, the RAS. Now, using a shared LAN, the PC has no way of knowing where the RAS server is. In addition, the PC must know the specific MAC address of the RAS server since it is sitting on a LAN. It can no longer indiscriminately transmit PPP LCP requests. Before PPP negotiations can occur, the PC must determine where the B-RAS server is, what its MAC address is, and establish a session with it. Then and only then can the PC initiate a PPP session. Additionally, we need a means to support multiple PPP sessions across the same shared media. The solution to this problem is PPP over Ethernet.
The Router will support multiple clients on a single ATM subinterface. In other words, a one-to-many relationship is formed, 1 PVC, many clients.
The above diagram uses IP/PPP/PPPoE/ATM.
To support this configuration, each xDSL modem or group of users one the Router will use a single ATM PVC. PPP over Ethernet (PPPoE) will then be configured to support multiple users across this PVC. Finally, a PPP interface per user will be configured.
In this scenario, two ATM PVCs would be configured on the Router for the two xDSL modems. PPPoE would be configured as the encapsulation method on each of these PVCs. Finally, two PPP subinterfaces would be configured on the first PVC to support the two users at that location and three PPP subinterfaces would be configured on the second PVC to support the three users at that location. If additional users were added at either location, additional PPP subinterfaces would need to be configured.

## Slide 62: PPP over Ethernet (PPPoE) - RFC 2516
General Frame Format
PC Requirements
Two Stages of PPPoE
  Discovery Stage
  PPP Session Stage
DSL Modem
DSL Modem
DSLAM
ATM
Switch
diane@isp1.com
tim@isp1.com
ATM
ken@isp2.com
ralph@isp2.com
ISP2
ISP1
ISP2
pam@isp1.com
DA=X
SA=A
Type=PPP
PPP
Session ID
IP Data
MAC=X
MAC=A
Notes: When the user PC is transmitting IP data, the PC will create an IP datagram, encapsulate the IP datagram in PPP, and finally insert this data into a Ethernet frame addressed to the Router. Hence the name PPP over Ethernet.
To accomplish this task, the user PC requires special PPPoE software that installs a ‘shim’ between the existing Windows 95/98 dial-up networking PPP stack and the Ethernet driver enabling PPP sessions to be carried directly in standard Ethernet frames. RouterWare’s WinPoET and NTS EnterNet PPPoE Client for Windows 95/98/NT are examples.
Though the PC is using PPPoE, the actual user experience mirrors Dial-Up Networking; a familiar experience to most current remote access users.
Since the PPP frames are encapsulated in Ethernet Frames, multiple users can share the same xDSL line.
PPPoE has two distinct stages:
Discovery stage: When a PC initiates a PPPoE session, it performs the Discovery stage to determine which B-RAS to use, the Ethernet MAC address of the B-RAS and a unique session ID. This discovery stage is a client-server relationship, where the PC is the client and the Router is the PPPoE server.
PPP Session Stage: Once the PC determines which B-RAS to use, the B-RAS MAC address, and the session ID the connection will transition into a peer-to-peer relationship and initiate a standard PPP session using LCP.

## Slide 63: Life of a Packet - PPPoE Discovery Stage
DSL Modem
DSLAM
ATM
Switch
diane@isp1.com
tim@isp1.com
ATM
ISP2
ISP1
ISP2
MAC=X
MAC=A
DA=FF
SA=A
Type=Disc
PPP
Services
PPPoE Active
Discovery Initiation
PADI
PPPoE Active
Discovery Offer
PADO
DA=A
SA=X
Type=Disc
PPP
SessionID=
0000
PPPoE Active
Discovery Request
PADR
DA=X
SA=A
Type=Disc
PPP
SessionID=
0000
PPPoE Active
Discovery Session Confirmation
PADS
DA=A
SA=X
Type=Disc
PPP
SessionID=
1234
Notes: There are four steps in the discovery stage. When this stage completes, both peers know the PPPoE SessionID and the peer’s MAC Address. Collectively, these attributes uniquely define the PPPoE session.
1. Initially the PC broadcasts a PPPoE Active Discovery Initiation (PADI), searching for any and all B-RAS servers that can provide the services the PC is requesting. In our network, only the Router will process the PADI.
2. The Router will respond to the discovery packet with a unicast PPPoE Active Discovery Offer (PADO). At this point the session ID will be all zeros.
3. If multiple B-RAS received the PADI, the PC could receive multiple PADOs. In this case the PC must choose one. In the above diagram, the PC will receive just one PADO from the Router. The PC will respond with a unicast PPPoE Active Discovery Request (PADR) to the server it has chosen to use. In this case, the PC responds to the only PADO received. At this point, the PC knows the MAC address of the B-RAS and now needs the unique session ID.
4. Finally, the B-RAS responds with a PPPoE Active Discovery Session-confirmation (PADS). This packet contains the unique session ID for the PPPoE session.
At any time, a PPPoE Active Discovery Terminate (PADT) packet can be sent by either the client or the server to indicate that a PPPoE session has been terminated.
The Ethertype field for the discovery stage is 0x8863.

## Slide 64: Life of a Packet - PPPoE PPP Session Stage
DSL Modem
DSLAM
ATM
Switch
diane@isp1.com
tim@isp1.com
ATM
ISP2
ISP1
ISP2
MAC=X
MAC=A
PPP LCP
DA=X
SA=A
Type=PPP
PPP
SessionID=
1234
PPP LCP
DA=A
SA=X
Type=PPP
PPP
SessionID=
1234
PPP data sent like any other PPP session
Notes: Once the PPPoE session has been established, the PPP Session stage begins. The PPP session stage is just like any other standard PPP session, starting with LCP negotiations, IPCP negotiations, etc.
All Ethernet frames are unicast between the PC and the Router.
The Ethertype field for PPP sessions is 0x8864.

## Slide 65: A Different Way of Viewing Things - PPP/PPPoE/ATM
UT3 / UE3
ATM Interface
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
ATM Subinterface
1 per Modem
PPPoE Interface
1 per Modem
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
ATM Subinterface
1 per Modem
PPPoE Interface
1 per Modem
Notes: Again, the UT3/UE3 controller, ATM Interface, ATM Subinterface, PPPoE Interface, PPPoE Subinterface and PPP Interface are all statically defined on the ER. Recall that in a PPP/PPPoE/ATM environment, each modem can support multiple users. Therefore, for each modem, an ATM subinterface and PPPoE Interface are defined. For each user connected to that modem, a PPPoE subinterface and PPP interface is defined.
As was the case with PPP/ATM, the IP Interface can not be statically defined since this interface will be dynamically created and assigned to the appropriate virtual router. An IP template must be assigned to the PPP interface to facilitate the dynamic creation of the IP interface and its placement in the appropriate virtual router.
Remember that IP Interfaces are assigned to a specific virtual router in one of three different ways:
  Domain Map Entry
  RADIUS VSA
  IP Template

## Slide 66: PPP/PPPoE/ATM Configuration Steps
Configure UT3/U3E Controller
  Clocking, Framing, Shutdown
Configure ATM interface
  # VCs per VP, Framing
Configure the following per modem:
  Configure ATM Subinterface
  Configure PVC, PVC encapsulation
  Specify PPPoE Encapsulation
Configure the following per user:
  Configure the PPPoE Subinterface
  Specify encapsulation PPP
  Configure PPP Authentication
  Specify an IP Template
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
PPP Interface
1 per User
IP Interface
PPPoE Subinterface
1 per User
ATM Subinterface
1 per Modem
PPPoE Interface
1 per Modem
UT3 / UE3
ATM Interface
Notes: Configuration for the first modem with 2 users:
RX-0-70-D0(config)#int atm 5/1
RX-0-70-D0(config-if)#int atm 5/1.11
RX-0-70-D0(config-if)#atm pvc 11 0 111 aal5snap
RX-0-70-D0(config-if)#encap pppoe
RX-0-70-D0(config-if)#int atm 5/1.11.1
RX-0-70-D0(config-if)#encap ppp
RX-0-70-D0(config-if)#ppp auth chap
RX-0-70-D0(config-if)#template isp1
RX-0-70-D0(config)#int atm 5/1.11.2
RX-0-70-D0(config-if)#encaps ppp
RX-0-70-D0(config-if)#ppp auth chap
RX-0-70-D0(config-if)#template isp1
RX-0-70-D0(config-if)#exit
Configuration for the second modem with 3 users:
RX-0-70-D0(config)#int atm 5/1.12
RX-0-70-D0(config-if)#atm pvc 12 0 112 aal5snap
RX-0-70-D0(config-if)#encaps pppoe
RX-0-70-D0(config-if)#int atm 5/1.12.1
RX-0-70-D0(config-if)#encaps ppp
RX-0-70-D0(config-if)#ppp auth chap
RX-0-70-D0(config-if)#temp isp1
RX-0-70-D0(config-if)#int atm 5/1.12.2
RX-0-70-D0(config-if)#encaps ppp
RX-0-70-D0(config-if)#ppp auth chap
RX-0-70-D0(config-if)#temp isp1
RX-0-70-D0(config-if)#int atm 5/1.12.3
RX-0-70-D0(config-if)#encaps ppp
RX-0-70-D0(config-if)#ppp auth chap
RX-0-70-D0(config-if)#template isp1
RX-0-70-D0(config-if)#exit
RX-0-70-D0(config)#exit
RX-0-70-D0#

## Slide 67
Authentication and Service Activation

## Slide 68
BRAS Service Activation w/ Service Portal
5. Router Configures the connection to allow access to Portal only (or Portal+Internet Only)
Content
Provider A
DSLAMCMTS
RADIUS
Server
Repository
Service Provider Back-office
Registration
Rating &
Billing
Server
1
3
4
6
1. User initiates PPP session and provides identification and password
2. Router detects PPP initiation and formulates RADIUS query
3. RADIUS queries directory to validate userid and password. If valid, RADIUS queries directory for the RADIUS profile which will contain a Portal profile.
4. The RADIUS profile is returned to the Router to configure the connection.
7. The user can only access services granted (in this example - Portal Only)
6. The RADIUS server starts an accounting usage record for the xDSL BRAS session
5
Internet
Content
Provider B
7
2
Portal
Notes: 1. User initiates PPP session and provides identification and password
2. Router detects PPP initiation and formulates RADIUS query
3. RADIUS queries directory to validate user-id and password. If valid, RADIUS also queries the directory for the user’s RADIUS profile. User’s service contains SSC profile.
4. The RADIUS profile is returned to the Router to configure the connection
5. Router Configures the connection to allow access to SSC only (or SSC+Internet Only)
6. The RADIUS server starts an accounting usage record for the xDSL BRAS session
7. The user can only access services granted (in this example - SSC Only)

## Slide 69
BRAS Dynamic Service Selection w/ Portal
5. Portal server uses COPS to configure the Router to allow connection to the selected service (Content Provider B)
Content
Provider A
DSLAM/CMTS
RADIUS
Server
Repository
Service Provider Back-office
Registration
Rating &
Billing
Server
1. Subscriber accesses the Service Selection Portal URL with a web browser
2. Portal server queries repository for list of services available to subscriber using LDAP. Each service and its corresponding COPS “commands” are cached.
3. Portal server builds a web page with the relevant service choices and returns this to the subscriber
4. Subscriber selects a service from the portal by clicking on the service in the browser. In this example, Content Provider B
7. RADIUS writes accounting start record into the repository
6. Portal server notifies RADIUS accounting to generate a start record for the selected service
Internet
Portal
3
Portal
1
2
4
5
Content
Provider B
6
7
Notes: 1. User initiates PPP session and provides identification and password
2. Router detects PPP initiation and formulates RADIUS query
3. RADIUS queries directory to validate user-id and password. If valid, RADIUS also queries the directory for the user’s RADIUS profile. User’s service contains SSC profile.
4. The RADIUS profile is returned to the Router to configure the connection
5. Router Configures the connection to allow access to SSC only (or SSC+Internet Only)
6. The RADIUS server starts an accounting usage record for the xDSL BRAS session
7. The user can only access services granted (in this example - SSC Only)

## Slide 70
Business Models

## Slide 71: Application 1: Standard Acess
DS3/E3
OC3
Access Network
Provider
Service Network
Provider
DSLAM
ATM
FR
DSLAM
ATM/FR End-to-End
High-speed xDSL Internet access for consumer and business subscribers...
Service Provider terminates circuits (ATM or FR) from the access network provider (ILEC, CLEC) and manages PPP sessions. Uses industry standard remote-access protocols such as PAP, CHAP and RADIUS
Consumer &
Business
Users (xDSL)
Internet
Notes: <number>
<footer>
<header>
<date/time>

## Slide 72: Application 2: Different Services
Access Network
Provider
Service Network
Provider
DSLAM
ATM
DSLAM
ATM/FR End-to-End
Support for multiple service offerings for competitive differentiation
Consumer &
Business
Users (xDSL)
The service provider creates and sells multiple services over the same high speed connection, e.g. a VPN service for telecommuting and an Internet access service for personal use.
Internet
VPN
Notes: <number>
<footer>
<header>
<date/time>

## Slide 73: Application 3: Outsourcing
ISP 1
Access Network
Provider
Service Network
Provider
DSLAM
ATM
DSLAM
ATM/FR End-to-End
Wholesaling application to support outsourced network access for smaller ISPs
The service provider uses Virtual Router capability for each ISP that it resells service to. All subscriber information is sent via proxy to the "retail" ISP, who manages its own RADIUS database.
Consumer &
Business
Users (xDSL)
ISP 2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 74: Application 4: Content Hosting
Internet
Access Network
Provider
Service Network
Provider
DSLAM
ATM
DSLAM
ATM/FR End-to-End
Wholesaling application to support outsourced network access for smaller ISPs
The service provider uses Virtual Router capability for each ISP that it resells service to. All subscriber information is sent via proxy to the "retail" ISP, who manages its own RADIUS database.
Consumer &
Business
Users (xDSL)
ASP/
Games
Portal
Notes: <number>
<footer>
<header>
<date/time>