## Slide 1: Introduction To VoIP
Anthony Kirkham
tkirkham@cisco.com

## Slide 2: Agenda
VoIP Applications
VoIP Introduction
Packet Networking Challenges
Cisco QoS Toolkit
Dial Plans, Dial Peers, Gatekeepers and configuration

## Slide 3: Enterprise Voice Example
Typical Building
PSTN
Data Center
T1,E1
QoS
WAN
(Intranet/Internet)
V
V
Telco
Switch
PBX
PBX
3600/
2600
AS5300
PSTN
PSTN
V
V
PSTN
V
Phoenix
Philadelphia
Call Comes In
Bypass
PSTN
AS5300
AS5300
AS5300
Notes: Works with exsisting telephony architecture
Passes office to office telephone and fax calls across data network significantly reducing toll’s.

## Slide 4: ITSP - Internet Telephony Service Provider
PSTN
V
Los
Angeles
QoS IP Backbone
PSTN
V
Denver
PSTN
V
Houston
PSTN
V
Chicago
PSTN
V
Atlanta
PSTN
V
Philadelphia
PSTN
V
NY
AS5300’s
Calling
Party
Called
Party

## Slide 5: ITSP - Internet Telephony Service Provider
LEC
SP TCP/IP
Backbone
V
V
V
V
V
V
V
V
V
V
V
V
IXC (Offnet Access)
5E
5E
5E
5E
5E
5E
LEC
HSRP
Cluster
GK
GK
415
POP
408
POP
213
POP
212
POP
Radius
HSRP
Cluster
GK
GK
Radius
Local Dialing
Two Stage
CLID/PIN Auth
1+ POP/area code
H.323 Network

## Slide 6: VoIP - Enable New Applications
PC based Telephony Applications
  Microsoft Net Meeting, Virtual Phones, VoIP Telephones (handsets)
Computer Telephony Applications
Distributed Call Centre Applications
VoIP Based ‘Web Tone’
VoIP Based Voice Mail
IVR Applications

## Slide 7: Cisco’s ‘Router Based’ VoIP Products
AS5300 Router
2600 Router
3620 Router
3640 Router

## Slide 8: AS5300
Services Supported
  VoIP (direct and two-stage dialing)
  Fax relay
  Fax store and forward (soon)
  Modem and ISDN Internet access
Performance
  150-MHz R4700 RISC CPU
  High-performance, low-latency architecture
Carrier class
  Voice quality
  AccessPath-VS3/DASA
  NEBS
  SS7
Connectivity
  Four CT1/CE1/PRI
  One 10-MB and one 10/100-MB Ethernet interface
Voice/data on same platform

## Slide 9: Voice on AccessPath-VS3: Carrier-Class Integrated System
Carrier-class VoIP system
  Scalability
    CT1/PRI VoIP port capacity: 96 to 1008
    CE1/PRI VoIP port capacity: 120 to 1260
    Engineered to support over 5000 VoIP ports
    Integrated gatekeeper (optional)
  High availability
    VoIP feature shelves: hot swap and RPS
    Gatekeepers: HSRP
    DASA: No single point of failure
  NEBS compliant
Internet Telephony™ Editor’s Choice Award, 1998

## Slide 10: Cisco’s VoIP Products
11.3T and 12.0/12.0T Release
Must have the IOS “Plus” images
  IP Plus, Desktop Plus, Enterprise
Features added in the “T” train of 11.3
11.3(x)NA Train for SP’s
More features in 12.0T

## Slide 11: Agenda
Intended VoIP Applications
VoIP Introduction
Packet Networking Challenges
Cisco QoS Toolkit
Dial Plans, Dial Peers, Gatekeepers and configuration

## Slide 12: VoIP and MultiService—Why Now?
Digital Signal
Processor Advances
Bigger, Cheaper Bandwidth
IP Precedence, RSVP
802.1p, CiscoAssure
H.323/MGCP
FRF.11/12
AAL1/2/5
Voice
Data
Voice
Data Exceeds Voice Over Voice Net
Cost Savings
Network Consolidation
Usage Charges
Toll Charges
DSP
DSP
QoS Advances
Open Standards
Data

## Slide 13: Network Convergence
Service
Adaptation
L1
L2
F-T1
DS1 DS3
Sonet
OC3 - OCn
Campus
802.N
Frame
Relay
ATM
L3
IP
Applications
PPP
WAN
IP

## Slide 14: Comment
Voice Is “Just” Another
Latency-Sensitive
IP Application
“
”

## Slide 15: Voice over IP Protocols VoIP is not bound to H.323
Presentation
Session
Transport
Network
Link
Physical
G.729(A)/G.723(.1)/G.711
H.323/SIP/SGCP/MGCP
RTP/UDP
IP
MLPPP/FR/ATM AAL1
– – –
Constant - Voice Packets ride on UDP/RTP
Variable - Several Signaling Protocols

## Slide 16: ITU H.323 Infrastructure
Intranet
Gatekeeper
Gateway
e
H.323 Terminals
V
- User Interface
- Gateway
- Video
Terminal
Telephone Network
H.320 (Over ISDN)
H.324 (Over POTs)
Speech Only
(PSTN)
Proxy
Real-Time Network

## Slide 17: ITU H.323 for VoIP
System Control
H.245 Control
Call Control H.225.0
RAS Control H.225.0
Video Codec
H.261, H263
User Data
Applications
T.120
H.225.0 Layer
Audio
I/O
Equipment
Audio Codec
G.711, G.722, G.723, G.723.1, G.728, G.729
Receive Path Delay
System Control and
User Interface
Video
I/O
Equipment
Session Layer
and Above
<number>
LAN Stack
309-E
1171_04F8_c1

## Slide 18: H.323 End Pt to End Pt Signaling
Media (UDP)
Cisco Implementation Note:
UDP ports 16384 thru
16384 + (4 x the number
of channels on the device)
RTP Stream
RTCP Stream
H.323
Gateway
H.245 (TCP)
Open Logical Channel
H.225 (TCP)
(Q.931)
Setup
Connect
Open Logical Channel Acknowledge
Capabilities Exchange
RTP Stream
H.323
Gateway
V
V
Assumes Endpoints(Clients)
know each others IP addresses

## Slide 19: Gatekeepers (RAS)
Policy Component for H.323 terminals, proxies, and gateways
Address translation and/or redirection
Call admission, authorization, accounting
Used with proxies to establish best QoS paths

## Slide 20: H.323 Gatekeeper Call Control/Signaling Gatekeeper Registration
Gatekeeper A
Gatekeeper B
Terminal A
Terminal B
RRQ
RCF
Hello: I am registering my
Name or E.164 address
(Terminal A)
RAS - Registration Admission and Status
UDP Transport Port 1719
  RRQ - Registration Request
  RRJ - Registration Reject
  RCF - Registration Confirm
Hello: I am registering my
Name or E.164 address
(Terminal B)
RRQ
RCF
IP QoS
WAN
Zone A
Zone B

## Slide 21: H.323 Gatekeeper Call Control/Signaling Call Placement
IP QoS
WAN
Gatekeeper A
Gatekeeper B
Terminal A
Terminal B
ARQ
ACF
ARQ (Admission Request):
I would like to call
Terminal B
LRQ
LCF
Call
Setup
LRQ (Locate Request):
Do you know Terminal B’s
IP address?
LCF (Locate Confirm):
Yes I do, here it is
X.X.X.X
ACF (Admission Confirm):
Yes you can, here it’s IP
Address X.X.X.X
1
2
3
4
5
Zone A
Zone B

## Slide 22: RTP/RTCP—RFCs 1889/1890
End-to-end network transport function
  Payload type identification - Voice, Video, Compression Type
  Sequence numbering
  Time Stamping
  Delivery monitoring
RTCP (Real-Time Control Protocol) provides feedback on the quality of the distribution
RTP Timestamp
Synchronization Source (SSRC) ID
4bytes
4bytes
4bytes
Sequence Number
Payload
Type
M
CC
V
E
R
Notes: RTP Services
  Payload Type ID
  Sequence Numbering
  Timestamp
  Delivery Monitoring
  Synch. Source ID (end point ID not dependent on Net ID.)
RTCP
  Quality Monitoring
Header Compression is used to keep payload to header ratio high for efficiency
  20ms @ 8kbs = 20byte payload
  RTP + UDP + IP = 12 + 8 + 20 (bytes) = 40byte Header 2x Payload!
Fragmentation and Interleave of large packets reduces residency on slow links
  1500 Byte MTU Takes 215Ms to Transmit on 56Kb Link
  MLPPP on single interface at frag level
  IETF Draft memo - draft-ietf-issll-isslow-mcml-01.txt

## Slide 23: Analog to Digital
= Sample
8 kHz (8,000 Samples/Sec)
Sampling Stage
Analog Audio Source
= 0010110101
Voice Bandwidth 300-3400 Hz
Nyquist Theorem - Sample at twice the highest frequency

## Slide 24: Bandwidth Requirements
Encoding/
Compression
Result
Bit Rate
G.711 PCM
A-Law/u-Law
64 kbps (DS0)
G.726 ADPCM
16, 24, 32, 40 kbps
G.727 E-ADPCM
G.729 CS-ACELP
8 kbps
G.728 LD-CELP
16 kbps
G.723.1 CELP
6.3/5.3 kbps
Variable
16, 24, 32, 40 kbps
Notes: Dick Tracy Decoder Ring so you look smart:
PCM = Pulse Code Modulation
ADPCM = Adaptive Delta PCM
CS-ACELP = Conjugate-Structure Linear-Predictive Coding
LD-CELP = Low Delay CELP
CELP = Code Excited Linear Prediction
ACELP = Algebraic CELP

## Slide 25: G.729 CS-ACELP
20byte packet every 20ms (50pps)
8kb/s data rate
Note - This 8bkps for “Voice Payload” only!!
Add on 40 bytes of IP/UDP/RTP and you now have 24kbps!
The “IP Tax”
RTP Header Compression will take this down to 11.2kbps

## Slide 26: G.711
160 Byte Packet
50 packets per sec (every 20 msec)
64 Kbit/s Data rate
Data Rate with Framing Overhead - apx 82 Kbit/sec

## Slide 27: Silence Suppression / VAD
Essential Components
22%
Pauses
56%
Repetitive
22%
Over half of the typical voice call is silence!
VAD removes silence from data stream.
Comfort noise during silent periods.

## Slide 28: Voice CODEC Cheat Sheet
Encoding
Compression
G.711
PCM
4.1
64
Mean
Opinion
Score
Native
Bit Rate
Kbps
G.729
CS-ACELP
3.92
8
G.729a
CS-ACELP
3.7
8
G.723.1
ACELP
3.65
5.3
G.726
ADPCM
3.85
32
G.728
LD-CELP
3.61
16
A
Voice
Quality
A
B
C
B
C
D
BW
A
A
A
C
B
A
DTMF
B
C
C
B
B
A
Dual
Comp
B
C
D
B
C
A
CPU
C
B
C
B
C
A
Music
on
Hold
C
D
D
B
C

## Slide 29: Agenda
Intended VoIP Applications
VoIP Introduction
Packet Networking Challenges
Cisco QoS Toolkit
Dial Plans, Dial Peers and Gatekeepers

## Slide 30: Voice Transport Requirements
Background noise
Silence suppression
  Comfort noise
Language sensitivity
Subjective quality (MOS)
  MOS
Delay and delay variation
Echo cancellation
Loss
Bandwidth
Delay
VoIP Challenges in the WAN
<number>
309-E
1171_04F8_c1

## Slide 31: VoIP (G.729) Is Tolerant of “Occasional” Packet Loss
missing packet
G.729 vocoder algorithm
The friendly “retransmission” is of no use in the Voice world… late is as good as never
Complex “concealment strategy” in algorithm interpolates lost packets based on context

## Slide 32: How Does Echo Happen?
Echo is due to a reflection
Impedance mismatch at the 2w-4w hybrid
is the most common reason for echo
2 Wire Local Loop
Central Office
2w-4w
Hybrid
Receive
Direction
Transmit
Direction
Rx & Tx
Superimposed
Echo is always present and as a problem is a function of the echo delay, and the magnitude of
the echo

## Slide 33: Delay—How Much Is Too Much?
Cumulative Transmission Path Delay
Time (msec)
0
100
200
300
400
CB Zone
Satellite Quality
Fax Relay, Broadcast
High Quality
Delay Target
500
600
700
800
ITU’s G.114 Recommendation = 0 – 150msec 1-way delay

## Slide 34: Delay Budgeting— Networked End Points
Input queuing
Jitter buffer
CODEC
Access (up) link transmission
Backbone network transmission
Access (down) link transmission
CODEC
Packetization
Output queuing
26
309-E
1171_04F8_c1
Voice Path
Loss
+
Delay
Notes: It is important to note that this might be only part of a circuit should the connection be going out to the PSTN, further delay could be encountered. Echo cancellers in VoPACKET end points should help with echo along with cancellers in PSTN.

## Slide 35: Fixed Delay Components
Propagation—six microseconds per kilometer
Serialization
Processing
  Coding/compression/decompression/decoding
  Packetization
Processing Delay
Propagation Delay
Serialization Delay— Buffer to Serial Link

## Slide 36: Fixed Frame Size Serialisation Delay matrix
Frame Size
Link
Speed
56kbps
64kbps
128kbps
256kbps
512kbps
768kbps
1536kbs
1
Byte
143us
125us
62.5us
31us
15.5us
10us
5us
64
Bytes
9ms
8ms
4ms
2ms
1ms
640us
320us
18ms
128
Bytes
16ms
8ms
4ms
2ms
1.28ms
640us
36ms
256
Bytes
32ms
16ms
8ms
4ms
2.56ms
1.28ms
72ms
512
Bytes
64ms
32ms
16ms
8ms
5.12ms
2.56ms
144ms
1024
Bytes
128ms
64ms
32ms
16ms
10.24ms
5.12ms
1500
Bytes
46ms
214ms
187ms
93ms
23ms
15mss
7.5ms

## Slide 37: Variable Delay Components
Queuing delay
Dejitter buffers
Variable packet sizes
Dejitter Buffer
Queuing Delay
Queuing Delay
Queuing Delay

## Slide 38: Delay Variation—“Jitter”
t
t
Sender Transmits
Sink Receives
A
B
C
A
B
C
D1
D2 = D1
Sender
Receiver
Network
D3 = D2

## Slide 39: Calculate Delay Budget
Coder Delay 25 ms
Serialization Delay 3 ms
Dejitter Buffer
50 ms
Queuing Delay 6 ms
Los
Angeles
Munich
Propagation
Delay—32 ms
(Private Line Network)
<number>
309-E
1171_04F8_c1
Total
110 msec
Dejitter Buffer
50 msec
32 msec
Network Delay (e.g.,Public Frame Relay Svc)
Serialization Delay 64 kbps Trunk
3 msec
6 msec
Queuing Delay 64 kbps Trunk
5 msec
Packetization Delay—Included in Coder Delay
Coder Delay G.729 (5 msec look ahead)
Propagation Delay (Private Lines)
Fixed Delay
Variable Delay
Coder Delay G.729 (10 msec per frame)
20 msec

## Slide 40: Design Planning/Challenge Considerations
Frame Relay
PBX
Router Egress
1. Contention/Loss
2. Delay - Serialization
3. Delay - Jitter
4. BW Consumption
5. CPU Utilization
Transport
1. Contention/Loss
2. Delay - Absolute
3. Delay - Jitter
4. Remote to Central site over subscription
5. Central to Remote Speed Mismatch
Dial Plan
1. Call Plan Intelligence
2. Failure/Busy/No Answer
3. Hunt Groups
4. Fax + Modem
WAN QoS
Router QoS
Administration
Cisco’s QoS Toolkit can help here!

## Slide 41: Agenda
Intended VoIP Applications
VoIP Introduction
Packet Networking Challenges
Cisco QoS Toolkit
Dial Plans, Dial Peers and Gatekeepers

## Slide 42: Earlier Comment Again
Voice Is “Just” Another
Latency-Sensitive
IP Application
“
”

## Slide 43: QoS Mechanisms for WAN
CAR Committed Access Rate
WFQ Weighted Fair Queuing
PQ Priority Queuing
Admission Control
Congestion Management
Congestion Avoidance
WRED Weighted Random Early Detection
Traffic Shaping
GTS Generic Traffic Shaping
FTS Frame Relay Traffic Shaping
Notes: <number>
13
Network managers are concerned with tailoring their network to support a mix of different applications. It’s important to have a range of QoS mechanisms available in the network infrastructure, to help in deploying new applications quickly and successfully.
Cisco IOS has a very rich set of QoS queuing and priority mechanisms to support different network and application scenarios.
QoS mechanisms can be divided into four types: - Admission control: ensuring that traffic is admitted to a link, at an agreed rate. Such a mechanism is CAR - Congestion management: Providing prioritization and queuing of outgoing traffic onto a slow link - so that high priority traffic is not delayed behind less time-sensitive traffic. Such mechanisms, which include priority queuing, custom queuing and weighted fair queuing, enable routers to provide varying levels of service to different traffic flows or types. This allows preferential treatment to applications that require an assured quality of service, such as SNA or Oracle SQL*net, when there is bandwidth contention due to congestion. - Congestion avoidance: is used to prevents congestion from occurring in the first place. This is achieved by associating specific priorities to packets and discarding low priority packets, when buffers surpass a predetermined utilization. Such a mechanism is Weighted RED or Random Early Detection - Finally, Traffic Shaping: these are feedback mechanisms provided by Frame Relay or ATM, to ensure that congestion doesn’t occur within the network, by controlling flow into the network to only what can be supported. Such mechanisms include Generic Traffic Shaping.

## Slide 44: Weighted Fair Queuing (WFQ)
One 200 Byte Data
Packet
Interface Buffer
Resources
Transmit
Scheduling
Two 100 Byte
Voice Packets
Classify
1
1
De-
queue
1
2
Configurable Queues
2
1
Two 100 Byte Packets Transmitted for Every One 200 Byte Packet
Therefore = “Fair”
Flow Classification/Sorting
Source and destination address
Protocol
Session identifier (Port/Socket)
Weighted Fair Scheduling
Requested Qos (IP Precedence, RSVP)
Frame Relay FECN, BECN, DE
Flow throughput (Weighted-Fair)
38
1086_03F8_c1
NW98_US_309
1
1
2
Notes: Fair Queue sorted to emulate TDM:
  Messages arrive in emission order
  Queue order by simulated last bit delivery
Fair queue sorted to emulate TDM
Real time traffic streams get timely service—as much as they need
Elastic traffic streams are interleaved and shared
  Cooperatively share BW

## Slide 45: Configuring WFQ
!
midge(config-if)#fair-queue ?
<1-4096> Congestive Discard Threshold
<16-4096> Number Dynamic Conversation Queues
<0-1000> Number Reservable Conversation Queues
<cr>
interface Serial0/0
ip address 10.1.0.1 255.255.0.0
bandwidth 64
fair-queue 64 256 1000
The following example requests a fair queue with 256 dynamic queues,
1000 RSVP queues, and a congestive discard threshold of 64 messages:
(On by Default on Links 2 Meg or Less)

## Slide 46: Displaying WFQ
bottom#sho queu se 0
Input queue: 0/75/0 (size/max/drops); Total output drops: 0
Queuing strategy: weighted fair
Output queue: 31/64/0 (size/threshold/drops)
Conversations 2/4 (active/max active)
Reserved Conversations 0/0 (allocated/max allocated)
(depth/weight/discards/interleaves) 24/4096/0/0
Conversation 184, linktype: ip, length: 1504
source: 10.1.2.2, destination: 171.68.56.138, id: 0x04CF, ttl: 31,
TOS: 0 prot: 6, source port 1503, destination port 1034
(depth/weight/discards/interleaves) 7/4096/0/0
Conversation 227, linktype: ip, length: 68
source: 10.1.2.2, destination: 171.68.56.138, id: 0xFCCF, ttl: 31,
TOS: 0 prot: 17, source port 49608, destination port 49608
High BW Flow
vs
Telnet, VoIP Etc.
Emphasizing the “Fair” in Weighted Fair Queuing
Notes: Note the equal weights per
flow. Each queue will be
serviced EQUALLY in terms
of total BPS,,,,,,,,,,but small
packet flows will get more
packets.

## Slide 47: IP Precedence
Set IP Precedence higher on VoIP
  Result = Isolated WFQ queue from Best Effort traffic
  Set at: Endpoint, proxy, or statically through router
May scale better than RSVP in SOME networks
  Bulk QoS by customer or network
Warning: No admission control
Version
Length
ToS
1 Byte
TTL
Proto
IP-DA
Len
ID
offset
FCS
IP-SA
Data
3 bits called IP Precedence for
differentiated services
IPV4

## Slide 48: Setting IP Precedence
!
interface Serial0/0
ip address 10.1.0.1 255.255.0.0
ip policy route-map testprec
!
!
access-list 101 permit udp any any range 16384 16400
route-map testprec permit 10
match ip address 101
set ip precedence critical
midge(config-route-map)#set ip precedence ?
<0-7> Precedence value
critical Set critical precedence (5)
flash Set flash precedence (3)
flash-override Set flash override precedence (4)
immediate Set immediate precedence (2)
internet Set internetwork control precedence (6)
network Set network control precedence (7)
priority Set priority precedence (1)
routine Set routine precedence (0)
Option 1
42
1086_03F8_c1
NW98_US_309

## Slide 49: Setting IP Precedence
midge(config)#dial-peer voice 25 voip
midge(config-dial-peer)#ip precedence ?
<0-7> Packet IP precedence value
!
dial-peer voice 25 voip
destination-pattern 5011
req-qos guaranteed-delay
ip precedence 5
session target ipv4:10.5.0.1
!
Option 2
Notes: can set IP precedence at the network dial-peer this config example sets precedence at 5 = critical

## Slide 50: Setting IP Precedence - CAR
VoIP
FTP
HTTP
FTP
HTTP
VoIP
Gold Class
Silver Class
Bronze Class
Separate “Conform” and “Exceed” Actions
CAR Engine
‘Rule Based’ Engine
CoS Packet Classification (Set-ToS) Based on Flexible Rules
  IP Precedence / IP Access List / Incoming Interface / MAC Address
Rate Limiting Functionality
Generally Deployed at the Network Edge
VoIP
HTTP
FTP

## Slide 51: Displaying Effects of IP Precedence
bottom#show queue serial 0
Input queue: 0/75/0 (size/max/drops); Total output drops: 0
Queuing strategy: weighted fair
Output queue: 5/64/0 (size/threshold/drops)
Conversations 2/7 (active/max active)
Reserved Conversations 0/0 (allocated/max allocated)
(depth/weight/discards/interleaves) 1/585/0/0
Conversation 90, linktype: ip, length: 46
source: 10.1.1.1, destination: 10.1.1.2, id: 0x0064, ttl: 255,
TOS: 192 prot: 6, source port 23, destination port 11000
(depth/weight/discards/interleaves) 3/4096/0/0
Conversation 219, linktype: ip, length: 68
source: 10.1.2.2, destination: 171.68.56.138, id: 0x1C7E, ttl: 31,
TOS: 0 prot: 17, source port 49604, destination port 49604
This Is Using the “Weight” in Weighted Fair Queuing
44
1086_03F8_c1
NW98_US_309
Notes: Note the lower weight
due to the TOS/IP
Precedence change
(This was a telnet with
the IP Precedence changed)

## Slide 52: Priority Queuing
One 400 Byte Data
Packet
Interface Buffer
Resources
Transmit
Scheduling
Two 100 Byte
Voice Packets
Classify
1
1
De-
queue
1
2
Configurable Queues
2
1
1
1
2
Higher order
packets ALWAYS
sent ahead of
lower queued
packets

## Slide 53: Configuring Priority Queuing
interface Serial0/0
ip address 10.1.0.1 255.255.0.0
bandwidth 64
priority-group 1
!
access-list 100 permit ip any host 192.168.100.1
access-list 101 permit udp any any precedence critical
priority-list 1 protocol ip high list 101
priority-list 1 default low
priority-list 1 queue-limit 60 60 60 20
4 Queues
High
Medium
Normal
Low
Create Priority Queue in global config mode
Assign Priority Group to interface
Higher queues ALWAYS emptied before lower queues
Can result in port starvation for lower priority traffic

## Slide 54: Monitoring Priority Queuing
    Perth3640#sh int s1
    Serial1 is up, line protocol is up
    Hardware is HD64570
    MTU 1500 bytes, BW 1544 Kbit, DLY 20000 usec, rely 255/255, load 1/255
    Encapsulation HDLC, loopback not set, keepalive set (10 sec)
    Last input never, output never, output hang never
    Last clearing of "show interface" counters never
    Input queue: 0/75/0 (size/max/drops); Total output drops: 0
    Queueing strategy: priority-list 1
    Output queue (queue priority: size/max/drops):
    high: 2/20/0, medium: 5/40/0, normal: 21/60/0, low: 0/80/15
Packets in
Queue
Size of
Queue
Dropped
Packets

## Slide 55: Resource reSerVation Protocol
46
1086_03F8_c1
NW98_US_309
IETF signalling protocol
- Reservation of bandwidth and delay
Dynamic end-to-end “access lists”
- Programs queuing policy
Flow can be signalled by end station or by router (static reservation)
Notes: RSVP used by an application to request a specific QoS of the IP network
In practice it is used to “program” the access lists that drive WFQ in the routers
Could be mapped to traffic management services of ATM link layer network.
  Guaranteed - CBR
  Controlled Load - VBR-RT
Choose the right link layer to solve the problem
What is reserved?
  Minimum bandwidth
  End to end delay
  What isn’t addressed ?
    Policy
      Who can
      Who can’t
      When
Path Messages propagate from sender to rcvr
  Sender_Template defines format of data packet
  Sender_TSPEC specifies traffic characteristics of flow

## Slide 56: Resource Reservation Protocol (RSVP)
Large
Volume/Size
Packet
Interface Buffer
Resources
Transmit
Scheduling
Small
Volume/Size Packet
Classify
1
2
2
1
Flow Classification
Source and destination address
Protocol
Session identifier (Port/Socket)
Reserved Flow Scheduling
Works in conjunction with WFQ
Reserved queue for RSVP flow
Queues serviced by “Weight”
De-
queue
1
2
Configurable Queues
Reserved
Packet
Reserved Queue
for Flow, Lower
Weight applied
to Queue
Works in Conjunction with Weighted Fair Queuing
49
1086_03F8_c1
NW98_US_309

## Slide 57: Configuring RSVP
!
interface Serial0/0
ip address 10.1.0.1 255.255.0.0
ip rsvp bandwidth 24 12
ip policy route-map testprec
bandwidth 64
fair-queue 64 256 1000
!
ip rsvp bandwidth [interface-kbps] [single-flow-kbps]

## Slide 58: Verifying Reservation Accepted
bottom#show ip rsvp installed
BPS To From Protoc DPort Sport Weight Conversation
18K 171.68.56.138 10.1.2.2 UDP 49608 49608 4 264
bottom#show ip rsvp reservation
To From Proto DPort Sport Next Hop I/F Fi Serv BPS Byts
171.68.56.138 10.1.2.2 UDP 49608 49608 10.1.1 .2 Se0 FF RATE 18K 3K

## Slide 59: Overcoming Serialization Delay
Session
1
Session 2
Session 3
Session 4
Fragmentation Methods
- Fixed MTU Size
- PPP Fragmentation and Interleaving (RFC 1717)
- FRF.12 (Fragmentation on Frame Relay)
Question: How do we reduce serialization delay?
Answer: Increase bandwidth
or reduce MTU

## Slide 60: Fixing MTU Size
Perth3640#Interface serial 0
Perth3640(config-if)#mtu 150
Perth3640# show interface s0
Serial0 is up, line protocol is up
Hardware is HD64570
MTU 150 bytes, BW 64 Kbit, DLY 20000 usec, rely 255/255, load 1/255
Encapsulation FRAME-RELAY, loopback not set, keepalive set (10 sec)
LMI enq sent 459, LMI stat recvd 0, LMI upd recvd 0, DTE LMI up
LMI enq recvd 65, LMI stat sent 67, LMI upd sent 32
LMI DLCI 0 LMI type is ANSI Annex D frame relay DTE
Be careful when hard-coding MTU
Voice works well over low MTU
Some protocols not so tolerant of low MTU

## Slide 61: RFC1717 - Multilink PPP with Fragmentation and Interleave
Elastic Traffic MTU
Real-Time MTU
64 kbps Line
Elastic MTU
Real-Time MTU
Elastic MTU
Elastic MTU
Addendum to PPP Specification
214ms Serialization Delay
for 1500 byte Frame at 64 kbps
64 kbps Line
Reduces Serialization delay for real
time traffic

## Slide 62: PPP Fragmentation Frame Size Formula
“Real Time Packet Interval / Time per byte for BW = Fragment Size”
Example
20ms / 143us = 140bytes
1 VoIP Frame Every
20ms
Time to Send 1byte
on 64kbps Circuit
Max Byte Size to Allow
Interleaving of “Real Time”
Packets Every 20ms
Calculating Fragment Size
Notes: Note: Fragment Size
must be LARGER than
Real Time Data packet
size

## Slide 63: PPP Fragmentation Frame Size Matrix
Real Time Packet Interval
Link
Speed
56kbps
70
Bytes
140
Bytes
210
Bytes
280
Bytes
700
Bytes
1400
Bytes
10ms
20ms
30ms
40ms
50ms
100ms
200ms
64kbps
80
Bytes
160
Bytes
240
Bytes
320
Bytes
400
Bytes
800
Bytes
1600
Bytes
128kbps
160
Bytes
320
Bytes
480
Bytes
640
Bytes
800
Bytes
1600
Bytes
256kbps
512kbps
768kbps
1536kbs
350
Bytes
3200
Bytes
320
Bytes
640
Bytes
960
Bytes
1280
Bytes
1600
Bytes
3200
Bytes
6400
Bytes
640
Bytes
1280
Bytes
1920
Bytes
2560
Bytes
3200
Bytes
6400
Bytes
12800
Bytes
1000
Bytes
2000
Bytes
3000
Bytes
4000
Bytes
5000
Bytes
10000
Bytes
20000
Bytes
2000
Bytes
4000
Bytes
6000
Bytes
8000
Bytes
10000
Bytes
20000
Bytes
40000
Bytes
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
—Fragmentation not an issue due to BW + Interval Combination
58
1086_03F8_c1
NW98_US_309

## Slide 64: Configuring Multilink PPP Fragmentation and Interleave
interface Virtual-Template1
ip unnumbered Loopback0
ip rtp reserve 49580 100 18
no ip mroute-cache
bandwidth 64
fair-queue 64 256 1000
ppp multilink
ppp multilink fragment-delay 140
ppp multilink interleave
!
interface Serial0
no ip address
encapsulation ppp
bandwidth 64
no fair-queue
ppp multilink
interface Virtual-Template1
ip unnumbered Loopback0
ip rtp reserve 49600 100 18
no ip mroute-cache
bandwidth 64
fair-queue 64 256 1000
ppp multilink
ppp multilink fragment-delay 140
ppp multilink interleave
!
interface Serial0
no ip address
encapsulation ppp
bandwidth 64
no fair-queue
clockrate 64000
ppp multilink
Perth
Brisbane

## Slide 65: Frame Relay - Various Fragmentation and Interleave Mechanisms
Frame Relay
FRF.12 (Also MLPPP for Pt to Pt Links)
Frame Relay
1500 byte Packet
1500 byte Packet
Frag
Frag
Frag
1500 byte Packet
Frag
Frag
Frag
Frag
Frag
Frag
IP/Interface MTU Reduction
Fragment for life of Packet
Cannot fragment non-IP Protocols
or
IP Frames with “do not fragment” bit set
Can be very detrimental to IP Applications

## Slide 66: FRF.12 - Frame Relay Fragmentation
Frame Relay Forum Standard for fragmenting large frames to interleave with real time frames (e.g. voice)
FRF.12
Support for FRF.12 in IOS 12.0(4)T
UNI Fragmentation - DTE to DCE
NNI Fragmentation - DCE to DCE
End to End Fragmentation
DTE to DTE
Frame Relay
Frame Relay
Frame Relay
V
V
V
V
V
V
Fragmentation at interface
level
Fragmentation at interface
level
Fragmentation at PVC level

## Slide 67: FRF.12 for VoIP
Large
Packet
PVC#1
1
1
De-
queue
Router Queuing Structure
PVC #1
1
1
1
Route
Table
Fragmentation Occurs
at De-queue from PVC
WFQ
Frame Relay
1
1
“Non Fragment”
Voice Queue
“Fragment”
Voice Queue
2 Interface Queue’s
1. Non Fragment Queue
2. Fragment Queue
Small
VoIP
Packet
PVC#1
1. FRF.12 + WFQ on PVC Basis
2. Frame Relay Traffic
Shaping turned on when
FRF.12 enabled
4. Fragments Reassembled
at far end (Voice Interleaved)
1
1

## Slide 68: FRF.12 Config
Hub3640#
interface Serial0/0
no ip address
encapsulation frame-relay
bandwidth 1300000
frame-relay traffic-shaping
!
interface Serial0/0.1 point-to-point
ip address 10.1.1.1 255.255.255.0
no ip directed-broadcast
bandwidth 1300000
frame-relay class Test1
map-class frame-relay Test1
frame-relay fragment 70
no frame-relay adaptive-shaping
frame-relay bc 2000
frame-relay mincir 56000
frame-relay fair-queue
Remote3640#
interface Serial0/0
no ip address
encapsulation frame-relay
bandwidth 56000
frame-relay traffic-shaping
!
interface Serial0/0.1 point-to-point
ip address 10.1.1.2 255.255.255.0
no ip directed-broadcast
bandwidth 1300000
frame-relay class Test1
map-class frame-relay Test1
frame-relay fragment 70
no frame-relay adaptive-shaping
frame-relay bc 2000
frame-relay mincir 56000
frame-relay fair-queue
New Commands
with FRF.12
Note: Bc set lower than the default of 1/8th the CIR
(Not mandatory but lower interval better on high speed links with low CIR, can result
in quicker credit exhaustion)

## Slide 69: RTP Header Compression
20ms@8kb/s yields 20 byte payload
IP header 20; UDP header 8; RTP header 12
  40 byte header = 2X payload!!!!!!!!
Header compression 40Bytes to 2-5 Bytes much of the time
Overhead
Version
IHL
Type of Service
Total Length
Identification
Flags
Fragment Offset
Header Checksum
Protocol
Time to Live
Source Address
Destination Address
Padding
Options
Source Port
Destination Port
Checksum
Length
PT
M
CC
X
P
V=2
Sequence Number
Timestamp
Synchronization Source (SSRC) Identifier

## Slide 70: Frame Relay VoIP Issues
V
2Mb Link Access
32K CIR per PVC
PVC to each remote
site
64K Link Access
32K CIR
per site
V
V
V
V
V
  IP
Network
Problem: Head Office has faster link than remote office
Result: Voice quality degrades at remote under load
Solution: Apply traffic shaping at faster end to shape traffic down to speed that remote end can process

## Slide 71: Agenda
Intended VoIP Applications
VoIP Introduction
Packet Networking Challenges
Cisco QoS Toolkit
Dial Plans, Dial Peers, Gatekeepers and configuration

## Slide 72: Network Design Dial Plan Considerations/Design
Traffic engineering (Erlang Calculations)
  http://www.erlang.com - handy calculator
PBX Operation/Interoperation
Transport Method/Tie Line transmission
  Tandem encoding
Translate Method/Virtual switching
  Dial plan integration

## Slide 73: PBX Review/Introduction
PBX
PSTN
Out Bound
Trunk Group
?
ARS

## Slide 74: PBX Route Replacement
Back
Bone
PBX
Out Bound
TG 1
PSTN
QoS
Out Bound
TG 2
ARS
WAN
PBX
V
V

## Slide 75: Transport/Trunking Method
Access
WAN
KTS/
PBX
KTS/
PBX
KTS/
PBX
PBX
Requires a PBX to perform the “Tandem”/Voice call Switching Function
“Dedicated” trunks between PBX’s
KTS/
PBX
KTS/
PBX
KTS/
PBX
PBX
Issue - Beware of multiple Compression/Decompression cycles
that occur when Tandeming AND using Compression
Voice and DTMF quality may suffer
Very common practice using PCM/G.711 Circuits
PCM/64kbps
PCM/64kbps
PCM/64kbps
G.729/11kbps Circuits

## Slide 76: Translate/Virtual Switching Method
Access
WAN
KTS/
PBX
KTS/
PBX
KTS/
PBX
PBX
Uses the Voice transport to make call routing decisions based on dialed
number - One trunk may dial many sites - Much like the PSTN
KTS/
PBX
KTS/
PBX
KTS/
PBX
PBX
Call routing occurs in the PSTN
PCM/64kbps
G.729/11kbps Calls
PSTN
PCM/64kbps
PCM/64kbps
PCM/64kbps
One trunk can call many sites. VoIP infrastructure makes call
routing decisions much like PSTN. Can go anywhere to anywhere
with one Compression/Decompression cycle.
Design Consideration - Traffic Engineering to avoid busies

## Slide 77: Dial Plan Design
IP QoS
WAN
3600A
AS5300
PSTN
V
3600B
V
NXX
555-xxxx
1111
NXX
556-xxxx
1111
1111
Netmeeting
PC
NXX
559-xxxx
NXX
557-xxxx
1111
10.1.5.0
.4
.10
.2
.3
PBX
7 digits for Local PSTN
1 and 10 digits for Long Distance to PSTN
7 digits of “on net” Location
Notes: Works with exsisting telephony architecture
Passes office to office telephone and fax calls across data network significantly reducing toll’s.

## Slide 78: Dial-Peer Concept
  IP
Network
3600A
3600B
FXS 1/1/0
FXS 1/1/0
555-1111
5561111
local-peer
dial-peer voice 100 voip
destination-pattern 556....
session target ipv4:10.1.5.4
!
dial-peer voice 4 pots
destination-pattern 5551111
port 1/1/0
!
num-exp 61111 5561111
<number>
V
V
309-E
1171_04F8_c1
10.1.5.0 255.255.255.0
.4
.3
network-peer
local-peer
dial-peer voice 104 voip
destination-pattern 555....
session target ipv4:10.1.5.3
!
dial-peer voice 1 pots
destination-pattern 5561111
port 1/1/0
!
num-exp 51111 5551111
network-peer

## Slide 79: Router 3600A
dial-peer voice 1 pots
destination-pattern +1..........
port 1/0/0
prefix 1
!
dial-peer voice 2 pots
destination-pattern .......
port 1/0/0
!
dial-peer voice 4 pots
destination-pattern 5551111
port 1/1/0
!
dial-peer voice 100 voip
destination-pattern 556....
session target ipv4:10.1.5.4
!
dial-peer voice 102 voip
destination-pattern 557....
session target ipv4:10.1.5.2
!
dial-peer voice 105 voip
destination-pattern 5591111
codec g711ulaw
session target ipv4:10.1.5.10
FXS 1/1/0
5551111
3600A
V
309-E
1171_04F8_c1
PSTN
FXO 1/0/0
Long Distance
to PSTN
Local Calls
to PSTN
Local
Extension
To
3600B
To
AS5300
To
Netmeeting
PC
Notes: Yellow dial-peer subscriber dials 9 to get PSTN dial tone
Blue dial-peer subscriber dials 8 and any 3 digits to reach an extension on the pictured PBX
Green dial-peer subscriber dials 6 and any 3 digits to reach an extension on the PBX across the tie-line
Grey dial-peer subscriber dials 7 and any 3 digits to reach an extension on the PBX across the tie-line

## Slide 80: AS5300
Voice-Port 0:D
dial-peer voice 100 voip
destination-pattern 1..........
session target ipv4:10.1.5.3
!
dial-peer voice 101 voip
destination-pattern .......
session target ipv4:10.1.5.3
!
dial-peer voice 104 voip
destination-pattern 555....
session target ipv4:10.1.5.3
!
dial-peer voice 105 voip
destination-pattern 5591111
codec g711ulaw
session target ipv4:10.1.5.10
!
dial-peer voice 106 voip
destination-pattern 556....
session target ipv4:10.1.5.4
!
dial-peer voice 1 pots
destination-pattern 557....
port 0:D
prefix 557
309-E
1171_04F8_c1
Long Distance
to PSTN
Local Calls
to PSTN
To
3600A
To
Netmeeting
PC
To
3600B
To
Local PBX
5571111
PBX
Notes: Yellow dial-peer subscriber dials 9 to get PSTN dial tone
Blue dial-peer subscriber dials 8 and any 3 digits to reach an extension on the pictured PBX
Green dial-peer subscriber dials 6 and any 3 digits to reach an extension on the PBX across the tie-line
Grey dial-peer subscriber dials 7 and any 3 digits to reach an extension on the PBX across the tie-line

## Slide 81: Gatekeeper
RAS - Registration, Admission and Status
During Call Setups Gateways ask gatekeeper for destination IP Address
Gatekeeper
RRQ
RCF
IP QoS
WAN
RRQ
RCF
GW B
GW A
CALL
ARQ
ACF
GK

## Slide 82: Gatekeeper Example
IP QoS
WAN
Gatekeeper
AS5300
NXX
07 3238 xxxx
1111
10.1.5.0
.2
.3
AS5300
NXX
02 8448 xxxx
1111
.1
Zone
brisbane.XYZcorp.com
2500, 2600
or 3600
PBX
PBX
Zone
sydney.XYZcorp.com
Zone
melbourne.XYZcorp.com

## Slide 83: Using Gatekeepers - 1 Brisbane AS5300 Config
!
dial-peer voice 100 pots
destination-pattern 02….....
direct-inward-dial
port 0D
prefix 02
!
dial-peer voice 110 pots
destination-pattern 073238....
port 0D
prefix 073238
!
dial-peer voice 120 voip
max-conn 10
destination-pattern 028448....
ip precedence 5
session target ras
!

## Slide 84: Using Gatekeepers - 2 Brisbane AS5300 Config
!
gateway
!
Interface ethernet 0
ip address 10.1.5.1 255.255.255.0
h323-gateway voip interface
h323-gateway voip id gk.brisbane.XYZ_corp.com ipaddr 10.1.5.3 1719
h323-gateway voip h323-id AS5300-1.brisbane.XYZ_corp.com
h323-gateway voip tech-prefix 1#
!

## Slide 85: Using Gatekeepers - 3 Gatekeeper Config
int ethernet 0
ip address 10.1.5.3 255.255.255.0
!
gatekeeper
zone local gk.brisbane.XYZ_corp.com XYZ_corp.com
zone local gk.sydney.XYZ_corp.com XYZ_corp.com
zone remote gk.melbourne.XYZ_corp.com XYZ_corp.com 10.1.5.10 1719
zone access gk.brisbane.XYZ_corp.com default direct
zone access gk.sydney.XYZ_corp.com default direct
zone bw gk.brisbane.XYZ_corp.com 640
zone bw gk.sydney.XYZ_corp.com 640
zone prefix gk.brisbane.XYZ_corp.com 073238.....
zone prefix gk.sydney.XYZ_corp.com 028448......
zone prefix gk.melbourne.XYZ_corp.com *
gw-type-prefix 1#* default-technology
no shutdown
!

## Slide 86
<number>
Presentation_ID
© 1999, Cisco Systems, Inc.