## Slide 1
Optical Networking
Driving the Evolution of the Public Network
Wade Rubinstein
Director of Network Services
Sycamore Networks

## Slide 2: Agenda
Evolution of the Public Network
DWDM Fundamentals
Intelligent Optical Networking
9:00 - 10:30
(10:30 - 11:00 break)
11:00 - 12:30
(12:30 - 2:00 lunch)
2:00 - 5:00
(3:30 - 4:00 break)

## Slide 3
Evolution of the
Public Network

## Slide 4: Evolution of the Public Network A Changing World
The New
Public Network
Rapid pace of optical technology and new traffic demands are reshaping...
  Service delivery requirements and possibilities
  Network elements and functions
  Network architectures

## Slide 5: Evolution of the Public Network What is Optical Networking?
Sonet - - - - - > > Fiber (transport)
Sonet - - - - - > > WDM (2 lambdas)
Sonet - - - - - > > DWDM (fiber multiplication)
- - - - - > > DWDM (fiber multiplication)
- - - - > > Intelligent Optical Network
(switching, protection,
APS, CNM)
SONET/SDH
ATM
IP
Private Line
SONET/SDH
ATM
IP
All-optical network (routed lambdas)

## Slide 6: Evolution of the Public Network Transmission Architectures
Copper, electronic
Analogue Transmission
1970
1980
1990
2000
2010
WDM/DWDM
PDH/Asynchronous (TDM-based)
Sonet/SDH (TDM-based)
Fiber, Photonic
Source: Ovum
Intelligent
Optical
Networking

## Slide 7: Evolution of the Public Network Multiplexing Technology
Time Division Multiplexing (TDM)
  Underlying multiplex structure of PDH and SONET/SDH transmission architectures based on electronic TDM
  Combines traffic from multiple lower-speed inputs streams onto a single common high-capacity output stream

## Slide 8: Evolution of the Public Network Multiplexing Evolution in the Public Network
Asynchronous TDM
Synchronous TDM
Wave Division Multiplexing (WDM)
Dense Wave Division Multiplexing (DWDM)
Optical Time Division Multiplexing (OTDM)

## Slide 9: Evolution of the Public Network PDH/Asynchronous Digital Hierarchy
Designed for 64 kbps voice
DS-3
(28 DS-1s)
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-1
DS-0 = 64 kbps
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-1
(24 DS-0S)

## Slide 10: Evolution of the Public Network From Asynchronous to SONET/SDH
What is SONET/SDH?
  Set of standards for high capacity optical communications:
    Synchronous Optical NETwork (North American ANSI standard)
    Synchronous Digital Hierarchy (ITU standard)
STS Electrical
Signal
SONET
MUX
EQUIPMENT
(based on TDM)
Optical
Signal
Line
Interfaces
(1) Short reach
(2) Intermediate reach
(3) Long reach
fiber plant
1310 nm
1550 nm
(WDM standards
emerging)

## Slide 11: Evolution of the Public Network From Asynchronous to SONET/SDH
Drivers behind SONET/SDH:
  Standards-based: allows multi-vendor interworking
  Cost: leveraged emerging fiber optic transport technologies
  Synchronous transmission: addresses timing variations
  Reduces manual operations: automation of OAM&P
    Lack of reliability and management capability of PDH/asynchronous network systems
  Network scalability: Simple to multiplex lower-speed streams onto single high-speed transport

## Slide 12: Evolution of the Public Network SONET/SDH Overview
STS-1, payloads and virtual tributaries
Packet over SONET (PoS)
Multiplexing and frame format
Line rates
Network layers
Physical characteristics
Network elements and topologies
Protection
Applications
Summary of benefits

## Slide 13: SONET/SDH Overview STS-1 Frame
90 Columns
9 Rows
87 Columns of Payload
STS-1 Synchronous
Payload Envelope
(STS-1 SPE)
A1
A2
JO/Z0
B1
E1
F1
D1
D2
D3
H1
H2
H3
B2
K1
K2
D4
D5
D6
D7
D8
D9
D10
D11
D12
S/Z1
M0/M1
Z2
E2
J1
B3
C2
G1
F2
H4
Z3
Z4
Z5
Section Trace/Growth
BIP-8/BI: Parity Checking
BIP-8/B2: Error Monitoring

## Slide 14: SONET/SDH Overview Virtual Tributaries (VT)
Transports and switches payloads smaller than STS-1 rate
  e.g., DSO, DS-2, PCM30
Maps these channels onto the STS frame
  e.g., VT 1.5, VT 2, VT 3, VT 6
STS-1
(28 VT1.5s multiplexed
onto the STS-1 signal)
VT1.5
DS-1
(24 DS-0s)
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
DS-0
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
VT1.5
V
VT1.5
VT1.5
VT1.5
VT PDH Signal Rate
VT1.5 DS-1 1.544 Mbps
VT2 E-1 2048 Mbps
VT3 DS-1c 3.152 Mbps
VT6 DS-2 6312 Mpbs

## Slide 15: SONET/SDH Overview STS-1 Multiplexing
STS-1 Signal A
STS-1 Signal B
STS-1 Signal C
STS-3 Combined Signal
SONET
MUX
EQUIPMENT
3 x 51.840 Mb/s = 3 x STS1 = STS-3 = 155.520 Mb/s (OC-3)
Time Slots

## Slide 16: SONET/SDH Overview Packet over SONET
Method to pack IP into SONET SPEs
RCF 1619, 1661, 1662
Greater than 10,000 PoS interfaces deployed
OC-48c now shipping
OC-192c shipping next year

## Slide 17: SONET/SDH Overview Multiplexing Frame Format
3 columns of
transport overhead:
Section overhead
Line overhead
Path overhead
OH PAYLOAD
OH PAYLOAD
OH PAYLOAD
9 rows
90 columns (87 columns of payload)
STS-1
Synchronous
Payload
Envelope
810 bytes x 8000 frame/sec x 8 bits + 51,840,000 bits

## Slide 18: SONET/SDH Overview Line Rates
Fiber
Optic
Signal
OC Level
Synchronous
Transport
Signal
STS Level
Synchronous
Transport
Mode
STM Level
Line Rate
DS0
DS1
DS3
OC1
STS-1
51.84 Mbps
672
28
1
OC3
STS-3
STM-1
155.52 Mbps
2016
84
3
OC12
STS-12
STM-4
622.08 Mbps
8064
336
12
OC48
STS-48
STM-16
2488.320 Mbps
32256
1344
48
OC-192
STS-192
9953.280 Mbps
129024
5376
192
Equivalent Channels
1995
1999
Backbone
Speeds
STM-64
OC-768
STS-768
STM-256
39813.12 Mbps
516096
21504
768

## Slide 19: SONET/SDH Overview Layers
Section
Line
Path
Physical
STS-1 Frame Structure:
3 columns of transport overhead:
Path overhead
Line overhead
Section overhead
90 columns (87 columns of payload)
STS-1
Synchronous
Payload
Envelope
9 rows
Four layers of overhead and transport functions

## Slide 20: SONET/SDH Overview Layers
Repeater
Repeater
LW
LW
Section
Line
Path

## Slide 21: SONET/SDH Overview Layers
Line
Section
Physical
Section
Physical
Section
Physical
Line
Section
Physical
Path
Line
Section
Physical
Path
Line
Section
Physical
Payload
Mux
STS-1
Mux
Regenerator
Regenerator
STS-1
Mux
Payload
Mux
B3
B1
B2

## Slide 22: SONET/SDH Overview Physical Characteristics
Line interfaces
  Short reach
  Intermediate reach
  Long reach
    1550 nm vs 1310 nm optics
STE regenerators to extend distance
    1310 nm
    1550 nm
Amplifiers
    1550 nm amps

## Slide 23: SONET/SDH Overview Low Loss Windows
0.1
0.2
0.3
0.4
0.5
1100
1300
1500
1700
Wavelength ()
1550
window
Attenuation (dB/km)
1310 nm
1550 nm

## Slide 24: SONET/SDH Overview Network Elements and Topologies
Ring #1
Ring #2
Cross Connect
Central Office
Ring
ADM
ADM
ADM
Linear
Work
Protect
Terminals
Add/drops
Cross-connects

## Slide 25: SONET/SDH Overview Protection Schemes
Linear
Rings
Client

## Slide 26: SONET/SDH Overview Protection Schemes: 1 + 1
(Source)
(Destination)
Working Facility
Protection Facility
1 + 1 Protection Switching
(50% bandwidth utilization)
Network Protection

## Slide 27: SONET/SDH Overview Protection Schemes: 1:n
(Source)
(Destination)
Working Facility
Protection Facility
1:n Protection Switching
(Bandwidth Efficiencies)
.
.
.
1
2
3
Network Protection

## Slide 28: SONET/SDH Overview Protection and Restoration
D1
S
D2
1 + 1
D1
S
D2
1:n
Path Protection
Line Protection (Loopback)

## Slide 29: SONET/SDH Overview Protection Schemes: UPSR
Unidirection/Path Switched Ring (UPSR)
Work
Protect
Rx
Rx
Tx
Rx
Tx

## Slide 30: SONET/SDH Overview Protection Schemes: BLSR
Bidirection/Line Switched Ring (BLSR)
2 fiber, 4 fiber
Work
Protect

## Slide 31: SONET/SDH Overview Protection Schemes: Client
(Source)
(Destination)
Working Facility
Protection Facility
.
.
.
Network Protection
Client Protection
1 + 1
1:1
1:n

## Slide 32: Evolution of the Public Network SONET/SDH Benefits
Mature technology
Standards enable interoperability (vendor-independence, reduced costs)
Multiplexing, switching and grooming
Self-healing capability
High availability
Extensive management capability built into the protocol
Simplification (vs PDH)

## Slide 33: Evolution to SONET/SDH over WDM
D
W
D
M
D
W
D
M
Sonet
SDH
Sonet
SDH
Sonet
SDH
Sonet
SDH
services
services
services
services

## Slide 34: SONET/SDH over WDM Traditional SONET/SDH Architecture
DSO-based
services
DCS
DCS
DCS
Working Fiber Pair
Protect Fiber Pair
Sonet
ADM
Sonet
ADM
Sonet
ADM
Sonet
ADM
OC-48
DCS
DS1/DS3
OC-3/OC12
4-Fiber
BLSR

## Slide 35: SONET/SDH over WDM SONET/SDH Face Growth of Data
Trunk Bandwidth Required to Support Growth in Data
Source: RHK 1999
0
200
400
600
800
1000
1200
1400
1998
1999
2000
2001
2002
Voice
Traffic relative to 1998
Internet
Other Data

## Slide 36: SONET/SDH over WDM Scaling Options
Option 2:
Upgrade SONET
Option 3:
Introduce DWDM
λ1λ2
λ8
•••
λ8
OADM
OC-12
OC-48
OC-192
Option 1:
Overbuild Fiber

## Slide 37: SONET/SDH over WDM Limitations of TDM
0.01
0.1
1
10
100
1,000
1985
1990
1995
2000
2005
2.5 Gpbs
10 Gpbs
100 Gpbs
400 Gpbs
TDM Only
WDM + TDM
ATM
Switches
Ethernet
IP routers
Ovum

## Slide 38: Introduction to Wave Division Multiplexing (WDM)

## Slide 39: WDM Introduction Low Loss Regions of Optical Fiber
Wavelength (nanometers)
1300
1200
1400
1700
1500
1600
18,000
GHz
1310 Window
Loss dB/Km
0.6
0.4
0.2
0.1
λ
1
λ
2
λ
3
λ
n
..…....
1310 nm
apprx 200 nm < 0.5 dB/km
1550 nm
apprx 200 nm < 0.2 dB/km
12,500
GHz
1550 Window
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: WDM Introduction Wavelengths
850 nm
Low Loss Windows:
1310 nm
1550 nm
Ultra
Violet (UV)
Infrared (IR)
The Visible Spectrum
-80
-70
-60
-50
-40
-30
-20
1500
1520
1540
1560
1580
1600
dBm
4,000 GHz
EDFA

## Slide 41: WDM Introduction Evolution of WDM
First phase WDM
  1310 nm, 1550 nm windows
Second phase WDM
  2 - > 4 channels; 1550 nm window
  Spacing: 400+ GHz
Current DWDM systems
  16, 32, 40 channel; 1550 nm window
  Spacing: 100 GHz
Next-generation systems:
  40 - 80 channels; 1550 nm window
  Spacing: 50 to 100 GHz

## Slide 42: WDM Introduciton Wavelengths
0.1
0.2
0.3
0.4
0.5
0.6
Attenuation (dB/km)
1600
1700
1400
1300
1200
1500
1100
Wavelength (nm)
Sparse
Dense
WDM
Mux
.
.
.
OC-3/OC-12
1
2
n
.
.
.





n

n
. . .
TE
TE
TE
Tx
Tx
Tx
OC-48

## Slide 43: WDM Introduction Basic System Elements


. . .

n
.
.
.



n
.
.
.
1
2
n
TE
TE
TE
Tx
Tx
Tx
WDM
Mux
.
.
.



n
.
.
.
1
2
n
TE
TE
TE
Rx
Rx
Rx
WDM
De-Mux
Terminal equipment (TE)
WDM transmitter/transponder (Tx)
Wavelength multiplexer/demultiplexer
Optical amplifier
Optical fiber

## Slide 44
SONET/SDH and DWDM Application
1310nm
repeater
1310nm
repeater
1310nm
repeater
1310nm
repeater
< - 40 km - >
< - 40 km - >
< - 40 km - >
< - 40 km - >
< - 40 km - >
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Before

## Slide 45
SONET/SDH and DWDM Application
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
Sonet
Mux
After


n


n

## Slide 46: WDM Introduction Erbium-Doped Fiber Amplifiers (EDFA)
Regen
40 km
TE
40 km
40 km
40 km
TE
40 km
Before Optical Amplifiers
Regen
Regen
Regen
B1, J0
B1, J0
B1, J0
B1, J0
B1, J0
After Optical Amplifiers
TE
TE
65 - 100 km
65 - 100 km
65 - 100 km
B1, J0

## Slide 47: WDM Introduction Summary of WDM Benefits
Increases bandwidth capacity of fiber
Addresses fiber exhaust in long-haul routes
Reduces transmission costs
Improves performance
Enhances protection (virtual and physical)
Enables rapid service deployment
Reduces network elements

## Slide 48: Emerging Trends: IP over DWDM

## Slide 49: Advances in Router Port Speeds
0.01
0.1
1
10
100
1,000
1985
1990
1995
2000
2005
2.5 Gpbs
10 Gpbs
100 Gpbs
400 Gpbs
TDM Only
WDM + TDM
ATM
Switches
Ethernet
IP routers
Ovum

## Slide 50: Emerging Trends: IP over DWDM Practical Implications
DSO-based
services
DCS
SONET/SDH
Protected Ring
DCS
Sonet
ADM
Sonet
ADM
OC-48
DCS
DCS
DS1/DS3
OC-3/OC12
Sonet
ADM
Sonet
ADM
IP/ATM/SONET
IP/SONET

## Slide 51: Emerging Trends: IP over DWDM Limitations of SONET/SDH Ring-Based Network Architecture
National
Interoffice
Access
Regional
Interoffice
Regional
Access
Numerous O/E/O conversions
Core rings must carry the aggregate traffic of all rings feeding them
50% of bandwidth reserved for protection
Designed to scale voice
LA
NY

## Slide 52: IP over DWDM
Sonet
SDH
Sonet
SDH
Voice, low-speed
data services
Voice, low-speed
data services
High speed
data services
High speed
data services
DWDM
Sonet
SDH
Sonet
SDH
IP
IP
Packet over SONET
OC-n

## Slide 53: Emerging Trends: IP over DWDM Motivations
Tremendous growth in data traffic
  OC-48c, OC-192c router interfaces
  High-speed and terabit routers
Elimination of SONET/SDH equipment
Access to protection bandwidth
Mesh vs rings

## Slide 54: Emerging Trends: IP over DWDM Issues
Restoration and protection
Performance monitoring
Fault isolation
Network engineering and bandwidth distribution
Wavelength management
Network scalability
Adopting new transmission technologies

## Slide 55: Intelligent Optical Networking

## Slide 56: Intelligent Optical Networking Evolution from Fiber Multiplication to Intelligent Optical Networking
DWDM Fiber Multiplication
  Move waves over distance
Intelligent Optical Networking
  Lightpath networking
  System for delivering services over waves
    Move waves over distance
    Map services onto waves
    Provision, switch, and manage lightpaths
  DWDM is only the physical layer of the Intelligent Optical Network

## Slide 57: Intelligent Optical Networking Benefits
Transforms the optical layer by combining --
  Functionality of SONET/SDH
  Capacity creation of DWDM
  All-optical networking technology
Intelligent optical network
  A flexible, scalable network
  Foundation to easily introduce new services and technologies
Services are delivered over networked lightpaths
Redefines the service provider economic model
  “Just in time” infrastructure

## Slide 58: The Intelligent Optical Network Drivers
Now
15%
90%
OC-3
70%
OC-12
60%
OC-48
OC-192
In Two Years
90%
OC-3
70%
OC-12
OC-48
70%
60%
OC-192
Forrester Research
What access speeds do you plan to offer?

## Slide 59
miles
Number
of calls
Voice traffic
miles
Number
of flows
IP Traffic
The Intelligent Optical Network Drivers: A Changing Traffic World
Voice
  Slow steady growth
  Predictable growth pattern
  Low bandwidth consumption
  Most calls terminate within the local area
Data
  Rapid, unpredictable growth
  Huge bandwidth consumption
  Distance insensitive

## Slide 60: The Intelligent Optical Network Emergence of the Carrier’s Carrier
Dallas
New
Jersey
L.A.
Boston
Private Network
Customer A
Ingress
ISP B
Ingress
ISP A
Egress
Private Network
Customer A
Egress
ISP B
Ingress
ISP A
Egress
Internal OC-48 Service - Wave #1
OC-48 Wave Service - Wave #2
OC-48 Wave Service - Wave #3
OC-48 Wave Service - Wave #4
Backbone existing data networks
ISP connectivity
Alternative platform for “bandwidth barons”/”carrier’s carrier”