## Slide 1: Agenda
Evolution of the Public Network
DWDM in the Public Network
Intelligent Optical Networking
9:00 - 10:30
(10:30 - 11:00 break)
11:00 - 12:30
(12:30 - 2:00 lunch)
2:00 - 5:00
(3:30 - 4:00 break)

## Slide 2
Intelligent Optical Networking

## Slide 3: Intelligent Optical Networking Agenda
The public network challenge
Intelligent optical networking technologies and network elements
Intelligent optical networking architectures
Internetworking
Future trends

## Slide 4: Intelligent Optical Networking The Public Network Challenge
Service delivery requirements changing
  Growing demand to interconnect OC-48c/OC-192c routers
  OC-N private line
  Competitive pressures force re-evaluation of traditional service platforms and network cost structures
Limitations of existing architecture
  Existing SONET/SDH ring-based architecture failing
  Optimized for voice
  Can’t scale fast enough for data
Problem is bandwidth creation and distribution

## Slide 5: The Public Network Challenge Limitations of SONET RING Architecture
IP and private line requirements approaching OC-48c and OC-192c
Rings inefficient for large pipes
Interconnection of rings does not allow end-to-end provisioning and management
Upgrading requires upgrading of many rings
IP does not always need the protection BW of rings
Meshes are more efficient
  Access to protection bandwidth
  Shared protection
  BW can be added where and when needed

## Slide 6: The Public Network Challenge The Intelligent Optical Network
SONET/SDH
ATM
Frame Relay
IP
Fiber
SONET/SDH
ATM
Fiber
Frame Relay
IP
SONET/SDH
ATM
DWDM
Fiber
IP
SONET/SDH
ATM
DWDM
Fiber
IP
SONET/SDH
Fiber
IP
OC-N
Private
Line
ATM
The Intelligent
Optical Network
Notes: Move private line one frame earlier as it’s one of the motivations for ION

## Slide 7: Intelligent Optical Networking From Fiber Multiplication to Lightpath Networking
DWDM fiber multiplication
  Move waves over distance
Intelligent optical networking
  System for delivering services over waves
    Move waves over distance
    Map services onto waves
    Provision, switch and manage lightpaths
  DWDM is only the physical layer of the Intelligent Optical Network

## Slide 8: Intelligent Optical Networking Motivations
Cost and efficiencies
  Switching waves cheaper than switching packets
  Eliminates costly O/E/O conversions
  Eliminates and consolidates equipment and simplifies network infrastructure
Flexibility and Management
  “Just-in-time” point-and-click service provisioning
  Traffic engineering at the wave level
Revenue Opportunities
  Fast provisioned Wave services
  OC-N private line services
  IP services through backbone
  Scaled services: protected, unprotected, ...

## Slide 9: Intelligent Optical Networking Motivations (cont.)
Scalable, evolutionary path to all-optical networking
Allows gradual and seamless adoption of new technologies into network
Supports migration to mesh networks
Provides access to protection bandwidth

## Slide 10: Intelligent Optical Networking Alternative: IP over DWDM
IP
IP
IP
IP
DWDM

## Slide 11
Asynchronous Packet TDM
Asynchronous Cell TDM
Synchronous TDM
DWDM
SDM
Packets
Cells
Circuits
Waves
Fibers
Conduits
Network Layer
Multiplexing
Method
Available Switching
Technology
Opto-mechanical Switches
Optical Mux / Demux
Opto-mechanical Switches
Interferometric Wavelength Converters
Pointer Processing
Asynchronous Electrical Switches
Synchronous Reconfigurable Switches
Cell Buffering
Asynchronous Reconfigurable Switches
Label Lookup
Packet Buffering
Asynchronous Reconfigurable Switches
Packet Header Lookup
None Today
Increasing Bandwidth
Increasing Complexity

## Slide 12: Intelligent Optical Networking Drivers
Industry shift from fiber multiplication to optical networking
Revenue opportunities change the role of the optical layer
Shorter service contracts --> faster depreciation --> faster network technology adoption
Commoditization of optical components enable powerful and economical network designs
Network simplification and equipment consolidation

## Slide 13: Intelligent Optical Networking Agenda
The public network challenge
Intelligent optical networking technologies and network elements
Intelligent optical networking architectures
Internetworking
Future trends

## Slide 14: Intelligent Optical Networking Requirements for Intelligent Optical Networks
Cost effective
Rapid easy service provisioning
Scalability of system, optics, HW, SW, and NMS
Network element and topology auto-discovery
Gradual and seamless introduction of new technology
Grooming of sub-rate circuits
Protection and restoration
Fault isolation and performance monitoring

## Slide 15: Layering the Intelligent Optical Network
FIBER
WAVE
LIGHTPATH
NETWORK
MANAGEMENT
AND CONTROL
SERVICE
SERVICE
SERVICE
Transport and switching of WDM signals
Wavelength Networking
End-to-End Electro-optic Lightpath Networking
ADAPTATION LAYER

## Slide 16: Layering the Intelligent Optical Network Network Elements
Fiber Layer
  In-line optical amplifiers
  Optical protection switches
  Optical fiber cross-connects
Wave Layer
  Open terminals
  Open OADNs
  Wavelength selective switches
Lightpath Layer
  Adaptation Sub-layer
  Closed terminals
  Closed OADNs
  Regeneration nodes
  Lightpath switching node

## Slide 17: Layering the Intelligent Optical Network Point-to-Point Example

## Slide 18: Layering the Intelligent Optical Network Fiber Layer
Functions
  Transport and monitoring of wavelength multiplexed signals
Network elements
  In-line optical amplifiers
  Optical switches for 1+1, loopback and 1:N protection
  Optical cross-connects

## Slide 19: Layering the Intelligent Optical Network Fiber Layer
Optical switches for 1+1, 1:N, and loopback protection

## Slide 20: Layering the Intelligent Optical Network Fiber Layer
Optical cross-connects
  Micro-electrical machines (MEMs)
  Thermo-optic
  Opto-mechanical

## Slide 21: Layering the Intelligent Optical Network Wave Layer
Functions
  Routing and switching of wavelengths
  Monitoring of wavelengths
  Protection switching at the wave layer
Network elements
  Open terminals
  Open optical add-drop nodes
  Wavelength selective switches

## Slide 22: Layering the Intelligent Optical Network Wave Layer: Open Terminal
“Open Architecture”
  Eliminates two 1310 nm O/E/O’s per link
WDM
Mux
.
.
.





n

n
. . .
Client
Client
Client

## Slide 23: Layering the Intelligent Optical Network Fixed Open Optical Add-Drop Nodes
~
~
Wavelength
Demultiplexer
Wavelength
Multiplexer

4*

1

2

3

4

4
Client

1

2

3

4*
Technologies / Architectures
  Mux/demux + patch panel
  Thin film add/drop filters
  Fiber bragg gratings (FBG) + circulator
  Mach-Zehnder + FBG

## Slide 24: Layering the Intelligent Optical Network Configurable Open OADNs
Technologies/architectures
  Fixed add/drop (mux/demux, thin film, FBG...) + switches (opto-mechanical, thermo-optic, MEMs,…)
  Thermally tunable fiber bragg gratings
  Acousto-optic switches
  Liquid crystal switching
  Planar lightwave circuits
…..
Client
Client
Client

## Slide 25: Layering the Intelligent Optical Network Wavelength Selective Switch
Switching architectures/technologies
  Mux/demux + switching (opto-mechanical, MEMs, …)
  Arrayed Waveguide mux/demux w/ integrated thermo-optic switches
  Arrays of semi-conductor amplifiers
  Acousto-optic switches
  Liquid crystal switches
  Electro-optic (LiNbO3)

## Slide 26: Layering the Intelligent Optical Network Wavelength Selective Switch w/ Wavelength Changers
Wavelength Changing Technologies
  Electro-optic
  Semi-conductor amplifier gain switching
  Phase conjugation

## Slide 27: Layering the Intelligent Optical Network Lightpath Layer
Functions
  End-to-end networking of circuits
  Routing
  Protection and restoration
  Management of circuits
Network elements
  Adaptation sub-layer
  Closed terminals
  Closed OADNs
  Regeneration nodes
  Lightpath switch

## Slide 28: Layering the Intelligent Optical Network Lightpath Layer
Adaptation technologies: optics
  Lasers
  Receivers
  Dispersion compensation
  Polarization manipulation
  Amplifiers
  VOAs
  Trends to smaller size, lower cost, better performance, and integration

## Slide 29: Layering the Intelligent Optical Network Lightpath Layer
Adaptation technologies: electronics
  SONET/SDH processing ASICs
  Packet over SONET/SDH
  Packet over ATM
  Forward Error Correction (FEC) and digital wrappers

## Slide 30
Layering the Intelligent Optical Network Digital Wrappers
FEC + overhead
OPTICAL TRANSPORT UNIT
(OTU)
OVERHEAD
+ PARITY CHECKS
OPTICAL TRANSPORT UNIT
(OTU)
BENEFITS
FEC for greater distances
Overhead for management
Conceptually works for any client signal
No disruption of any client overhead
CURRENT SHORT COMINGS
Not yet standardized
No provisions yet for muxing wrappers
Issues with legacy equipment
Issues with future proofing
May require reinvention of SONET functions: timing, performance management, …

## Slide 31: Layering the Intelligent Optical Network Digital Wrappers: Future Issues
OTN
OTN
OTN
Wrapped (OC-768) capable
Wrapped (OC-48) capable
No provisions yet included for multiplexing multiple lower rate wrapped signals into a higher rate signal.

## Slide 32: Layering the Intelligent Optical Network Digital Wrappers: Legacy Issues
OTN w/ Transponder Interfaces
OTN
OTN
Unwrapped OC-48 capable
~2.5 Gb/s
Wrapped (OC-48) capable (~2.6 Gb/s)
Not a near term solution.
Not an end-to-end solution.
Signals have to be unwrapped to be transmitted through legacy DWDM equipment.

## Slide 33: Layering the Intelligent Optical Network Closed Terminals and OADNs
WDM
Mux
.
.
.
OC-N
1
2
n
.
.
.





n

n
. . .
Client
Client
Client
Tx
Tx
Tx
“Closed Architecture”
  No wavelength specific sparing of router PHY cards
  Fault isolation and performance monitoring end-to-end
  Transmitter / Receiver technology matches link
  LTE transponders can perform electronic grooming

## Slide 34: Layering the Intelligent Optical Network Regeneration Nodes
WDM
Mux
.
.
.





n

n
. . .
WDM
Mux


Rx
Rx
Rx



n
. . .

n
Tx
Tx
Tx
3R regeneration of signals
Performance monitoring
Optional add/drop and grooming
.
.
.

## Slide 35: Layering the Intelligent Optical Network Lightpath Switching
ONE
ONE
ONE
ONE
Electrical
Switch
Sonet
SDH
OXC

## Slide 36: Layering the Intelligent Optical Network Lightpath Routing and Wavelength Assignment
ONE
ONE
ONE
ONE
Electrical
Switch
Sonet
SDH
OXC

## Slide 37: Layering the Intelligent Optical Network Protection and Restoration
Client
ONE
ONE
ONE
ONE
Network Protection
1 + 1
1 + 1
Client
ONE
Local Protection

## Slide 38: Layering the Intelligent Optical Network Important Technologies
Adaptation optics and electronics
    Transceivers, optics
    SONET ASICs, PoS, FEC, and wrappers
Switching
    High-speed electronic switching
    Grooming ASICs
    VCSEL and other low cost high speed interfaces
Trends to
    Higher speeds and port counts
    More integration
    Better density
    More functionality

## Slide 39: Layering the Intelligent Optical Network Key Software
Routing, signaling, and wavelength assignment
  Efficient, scalable, and facilitate internetworking
  Coordination of multiple layers
Grooming algorithms and resource allocations
End-to-end performance monitoring
Protection and restoration
  Coordination of multiple layers
Hardware and network abstractions to allow new technologies to be incrementally absorbed into infrastructure

## Slide 40: Layering the Intelligent Optical Network Services
Basic transport services
Advanced transport services
Network and service management

## Slide 41: Layering the Intelligent Optical Network Basic Transport Services
ADM
ADM
Bit Pipe or STE
(protected or unprotected)
Bit Pipe, STE, LTE
(protected or unprotected)
IP
IP
1 + 1
Optical Clear Channel
Client
Client
Wrapper
Wrapper

## Slide 42: Layering the Intelligent Optical Network Advanced Services
Customer Network Management (CNM)
Optical Virtual Private Networks (OVPNs)
Service Level Agreements (SLAs)
Intelligent
Optical
Network

## Slide 43: Layering the Intelligent Optical Network Network and Service Management
Optical network visibility and control - CNM
Performance monitoring
Ease of service provisioning
Fault management
  Historical/live
  Correlation
  Context sensitive

## Slide 44: Tying it All Together All-Optical Islands

## Slide 45: Tying it All Together All-Optical Islands

## Slide 46
Optics, not electronics, is now the cost effective method to utilize the large BW of optical fibers
  “The Electronic Bottleneck”
Transparency allows multiple protocols/bit rates to co-exist on fibers, as well as future proofing infrastructure
Optical amplifiers enable large islands
Tying it All Together All-Optical Islands: Motivations

## Slide 47
Physical impairments still limit scalability of all-optical networks
Segmentation allows carriers to adopt new technology incrementally
  50 GHz --> 25 GHz
  OC-48 --> OC-192 --> OC-768
  L-band
Multi-vendor environment
Subnetworks are easier to monitor and manage
Tying it All Together Why Not End-to-End All-Optical?

## Slide 48: Intelligent Optical Networking Agenda
The public network challenge
Intelligent optical networking technologies and network elements
Intelligent optical networking architectures
Internetworking
Future trends

## Slide 49: Intelligent Optical Networking Lightpath Networking: Architectures and Topologies
Super capacity & distances
IP, ATM, SONET/SDH backbones
Bandwidth:
  OC-192
  OC-768
Point-to-point, mesh
Need to regen
Multi-vendor environment
Backbone
Metro, Interoffice
Access and Enterprise
Traffic mix
Access to BB
  Rings prevalant
  Fiber rich in areas, poor in others
Shorter distances
Lower speed services
  OC-3/12/48
Low cost points
Larger variety of traffic types
  Gigabit Ethernet
  ESCON
  FDDI
Uncontrolled environment
Security issues

## Slide 50: Intelligent Optical Networking Architectures and Topologies
Collection and
Distribution Network
CO
Business
Access
Ring
Collection and
Distribution Network
Long-
Distance
Backbone
- International
- National
- Regional
Metro,
InterOffice
Access
and
Enterprise
Gigabit LAN
Feeder
Network
ESCON, FDDI, Fiber Channel, Gigabit Ethernet
OC-3, 12
OC-48
OC-48/192/768
MESH
COLLAPSED RING
RINGS
TREE
Notes: Subscriber access equipment converts services into bandwidth
Access Sonet/SDH transport rings deliver bandwidth to carrier network
Switching/routing equipment is an overlay on fiber transmission
Voice and data are sepearate networks

## Slide 51: Intelligent Optical Networking Network Architectures and Topologies
Linear with OADM
Backbone mesh
Collapsed ring
Interoffice ring
Access rings
Dual homed ring
Trees

## Slide 52: Intelligent Optical Network Architectures and Topologies Linear with OADM
OADM
ADM
ADM
OADM
ADM
ADM
West
East
Fixed wavelength (static)
Wavelength selectable (configurable)

## Slide 53: Intelligent Optical Network Architectures and Topologies Backbone Mesh
ONE
ONE
ONE
ONE
Electrical
Switch
Sonet
SDH
OXC

## Slide 54: Intelligent Optical Network Architectures and Topologies Collapsed Ring with Integrated Work and Protect
Backbone Optical
Network
Backbone
Spur
Work
Protect
ONE
ONE

## Slide 55: Intelligent Optical Network Architectures and Topologies Interoffice Ring
OADN
Backbone Optical
Network
OADN
OADN
OADN
Path and line protection
Optical and electrical
Groom to share lambdas

## Slide 56: Intelligent Optical Network Architectures and Topologies Access Rings
OADN
OADN
OADN
OADN
Gibabit
Ethernet
FDDI
ESCON

## Slide 57: Intelligent Optical Network Architectures and Topologies Access Trees
Gibabit
Ethernet
FDDI
ESCON
OADN
OADN
OADN
OADN

## Slide 58: Intelligent Optical Network Architectures and Topologies Dual Homed Ring
OXC
OXC

## Slide 59: Intelligent Optical Network Architectures and Topologies All-Optical Evolution
LINEAR
RINGS
MESHES
400 GHz
200 GHz
100 GHz
50 GHz
Fixed add/drops
Configurable add/drops
Configurable switches
Wavelength changers
Early-Mid ‘90s
Late ‘90s - Early ‘00s
Early ‘00s
Early ‘90s
Mid ‘90s
Late ‘90s
Late ‘90s
Late ‘90s
Early ‘00s
Early ‘00s
?

## Slide 60: Intelligent Optical Networking Agenda
The public network challenge
Intelligent optical networking technologies and network elements
Intelligent optical networking architectures
Internetworking
Future trends

## Slide 61: Internetworking
Sonet
SDH
Sonet
SDH
Intelligent Optical Network
Linear
Ring
Collapsed Ring
Mesh
ION

## Slide 62: Intelligent Optical Networking Internetworking Topics
ION* to ION
  Same vendor, different carriers
  Same vendor, same carrier, different domains
  Different vendors
Clients to ION
  IP to ION
  ATM to ION
  SONET to ION
  Other (GE, FC, ESCON, PDH, …) to ION
Network element to network element
All-optical and electro-optic
*ION here refers to “Intelligent Optical Network”

## Slide 63
ITU -- “within cloud”
  Wavelength grid, fiber specifications, ...
  Optical transport network reference model
  All-optical hand-offs between all-optical islands
  ONE - ONE interfaces
  Transport service definitions
Optical Internetworking Forum (OIF) -- “between clouds”
  Client - ION interface
  ION - ION interface
  Emphasis on IP and data networking
  Issues:
    Signaling, Routing, and Addressing
    Transport Service Agreements
    Low cost interfaces
Intelligent Optical Networking Intenetworking
*ION here refers to “Intelligent Optical Network”

## Slide 64: Intelligent Optical Networking ITU OTN Layering
Optical channel layer network
  End-to-end networking of optical channels
  Optical channel connection, overhead, and supervisory
Optical multiplex section layer network
  Networking multi-wavelength signals
  Supervisory and overhead functions
Optical transmission section layer network
  Transmitting multi-wavelength signals
  Supervisory and overhead functions
Physical media layer network
  The fiber

## Slide 65: Intelligent Optical Networking Agenda
The public network challenge
Intelligent optical networking technologies and network elements
Intelligent optical networking architectures
Internetworking
Future trends

## Slide 66: Intelligent Optical Networking Future Trends in Optical Networking
Increasing capacity and distance
All-optical switching and routing
Architectures

## Slide 67: Future Trends Increasing Capacity and Distance
Faster transmission speeds
More waves in the C-band
Opening up more wavelength bands
Bidirectional interleaved transmission
Distributed amplification
Wavelength power equalization

## Slide 68: Future Trends OC-768 and Beyond
40-160 Gb/s transmission
Very sensitive to polarization mode dispersion
  Newer fibers have reduced PMD
  Components within system can be specified with low PMD
  Polarization mode dispersion compensation likely required
Very sensitive to chromatic dispersion
  New transmission formats (solitons) help combat chromatic dispersion and PMD
Very sensitive to noise accumulation
  Raman gain and FEC can help
M-ary signaling can alleviate impairments

## Slide 69: Future Trends More Waves in the C-Band
Spacing # of Waves
400 GHz 10
200 GHz 20
100 GHz 40
50 GHz 80
25 GHz 160
10 GHz 400

## Slide 70: Future Trends Opening Up New Wavelength Bands
350
80
460
80
water-peak
1260-1360
850
1530-1562
Loss
(nm)
1365-1525
1570-1604
1st
2nd
3rd
4th
5th
C-band
L-band
EDFAs
# of waves
@ 50 GHz
C-band (conventional)
80 channels
1530 - 1562 nm
L-band (long wavelength)
80 channels
1570 - 1620 nm

## Slide 71: Future Trends Bidirectional Interleaved Transmission
Uni-directional Transmission: 80x80, 50 GHz spacing
Conventional Bi-directional Transmission: 32x32, 50 GHz spacing
Bi-directional Interleaved Transmission: 160x160, 50 GHz spacing

## Slide 72: Future Trends Lumped Amplification
Distributed Raman Amplification
Pump
Pump
Pump
Makes link “look” 5-7 dB shorter --> better OSNR
Requires very high power pumps (~1-2W)
- Reliability concerns
- Eye safety concerns
- Connectorization concerns -- new outside plant management
- Harder to do C- and L-band systems

## Slide 73: Future Trends Wavelength Power Equalization
EQN

## Slide 74: Approximate Evolution and Speculation of OC-48 DWDM
1 8 300-400km 200 GHz
2 16 500-600km 100 GHz
3 32-40 500-600km 100 GHz, GFF
4 64-100 500-600km 50 GHz, C+L
5 160 500-600km L-Band
6 160 ~1200km FEC
7 160 ~3000km Raman
8 320 ~3000km 25 GHz
Generation Waves Distance Technology

## Slide 75
1 4 300-400km 400 GHz, Bi-Dir.
2 8 300-400km 200 GHz, Bi-Dir.
3 16 400-500km 100 GHz, Bi-Dir.
4 32-40 500-600km 100 GHz, Uni-Dir.
5 64-80 500-600km L-Band
6 160 500-600km 50 GHz, Bi-Dir.
7 160 ~1200km FEC
8 160 ~3000km Raman
Generation Waves Distance Technology
Approximate Evolution and Speculation of OC-192 DWDM

## Slide 76: Future Trends Evolution of DWDM Capacity
Tb/s*km
Generation
OC-48
OC-192

## Slide 77: Future Trends Evolution of Capacity
BW*Distance ~doubles each generation
Today: ~120-160 Tb/s*km
  80xOC-48: 200 Gb/s over 600km
  40xOC-192: 400 Gb/s over 400km
Trend to OC-192
FEC, Raman will provide x5-10 gain
OC-192 systems can exceed 2000 Tb/s*km
Trend to OC-768?

## Slide 78: Intelligent Optical Networking Future Trends in Optical Networking
Increasing capacity and distance
All-optical switching and routing
Architectures

## Slide 79: Future Trends Wavelength Routing Network
n
m
Wavelength Routing Node
Broadcast Star
Wavelength Router
Frequency Selective Switch
Wavelength Changers
...
ON-USER
LINK
- SINGLE FIBER
- FIBER BUNDLE
*Electro-optic control and management not shown.
User-Network Interface
Notes: <number>
<footer>
<header>
<date/time>

## Slide 80: Future Trends Common All-Optical Nodes
WAVELENGTH ROUTER
(PASSIVE)
BROADCAST STAR
(PASSIVE)
FREQUENCY SELECTIVE SWITCH
(CONFIGURABLE)
FREQUENCY SELECTIVE SWITCH
WITH WAVELENGTH CHANGERS
(CONFIGURABLE)

## Slide 81
Network-Network Interfaces Between Subnets
  Re-use of wavelengths
  Independent management and design
Resolving Wavelength Conflicts
Studies have shown not much difference in rings, (none in some architectures)
30-40% reduction in capacity in common backbone mesh networks
Traffic uncertainty exacerbates conflicts
Good algorithms can reduce conflicts
x
n
m
i
k
y
x
y
Future Trends Wavelength Changers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 82: Intelligent Optical Networking Future Trends in Optical Networking
Increasing capacity and distance
All-optical switching and routing
Architectures

## Slide 83: Future Trends Architectures
AON and MONET: All-optical end-to-end
  AON: LAN, MAN, and WAN
  MONET: WAN, MAN
ON-RAMP: Jointly designed electro-optic access network
Fiber to the mome and PONs
  Various architectures based on trees
  Drive for low cost optics
All-optical BW Sharing
  Synchronous and statistical multiplexing of wavelengths
  MAC protocols
  Useful for LANs (e.g. RAINBOW) and access networks

## Slide 84: Future Trends And One Day…..
Optical Time Division Multiplexing (OTDM) Networks
All-Optical
Processing