## Slide 1: APRICOT 2000 VPN and Network Security Tutorial Dean Hamilton CoSine Communications Feb 1, 2000

## Slide 2: Agenda
What Are VPNs?
Why Are VPNs So Confusing?
How Have VPNs Evolved?
VPNs And The Next Generation Networks
Questions
Lunch
VPN Technologies - In Depth
VPN Management Systems
VPN Service Strategies
Questions

## Slide 3: Virtual Private Networks: A High Level View

## Slide 4: What Is A VPN?
VPN:
  A Network That Provides The Characteristics And Security Of A Dedicated Private Network Using A Shared Public Network Infrastructure

## Slide 5: The Typical Private Network
TDM Network
Providence, RI
HQ - NYC, NY
Fife, WA
Wala Wala, WA
Aurora, IL
Oberlin, OH
Dedicated
Private
Leased
Circuits
Router
Router
Router
Router
Router
Router

## Slide 6: Private Network Characteristics
Positives:
  Secure Dedicated Connections (Circuits)
  Bandwidth Always Available
  Privacy Guaranteed
Negatives:
  Extremely Expensive
  Almost Impossible To Fully Mesh Large Network
  Hub and Spoke Topologies Impair Performance

## Slide 7: The Typical “Shared” Public Network
Router
Router
Router
Router
Router
Router
Router
Router
Router
Router
Routers
or
Switches
Statistically
Multiplexed
Trunks

## Slide 8: Public Network Characteristics
Positives:
  Very Inexpensive
  Can Support Meshed Topologies Easily
  Available Everywhere (especially the Internet)
Negatives:
  No Privacy
  No Bandwidth Guarantees (without QOS)

## Slide 9: How Can A Public “Shared” Network Be Used Securely And Where Must The Security Be Applied?

## Slide 10: Three Possible Locations For Security
The Clients Of The Network Must Provide Security
  Necessary When Even The Internal Network (LAN) Is Not A “Trusted Network”
A Customer Premises Gateway Must Provide Security Before Getting To The Public Network
  Possible When Trusted Networks Must Be Interconnected Using An Un-Trusted “Public” Network
A Service Provider Gateway Must Provide Security At The Edge Of The Public Network
  Possible When Trusted Networks Must Be Interconnected Using An Un-Trusted VALUE-ADDED PUBLIC NETWORK (VAPN)

## Slide 11: Clients Provide Security
Router
Router
Router
Statistically
Multiplexed
Trunks
Router
Public
Network
Not Trusted
Trusted

## Slide 12: Customer Premises Network Gateways Provide Security
Router
Router
Router
Statistically
Multiplexed
Trunks
Router
Public
Network
Not Trusted
Trusted

## Slide 13: Service Provider VAPN Gateways Provide Security
Router
Router
Router
Statistically
Multiplexed
Trunks
Router
VAPN
Not Trusted
Trusted

## Slide 14: Why Are VPNs So Confusing?

## Slide 15: …Because VPNs Can Exist At Many Layers Of The Network Model
PHYSICAL LAYER
LINK LAYER
NETWORK LAYER
TRANSPORT LAYER
SESSION LAYER
PRESENTATION LAYER
APPLICATON LAYER
1
2
3
4
5
6
7
Frame Relay, ATM, L2TP
IPSec
SSL
PGP

## Slide 16: …Because VPNs Can Exist At Many Layers Of The Network Model
PHYSICAL LAYER
LINK LAYER
NETWORK LAYER
TRANSPORT LAYER
SESSION LAYER
PRESENTATION LAYER
APPLICATON LAYER
1
2
3
4
5
6
7
Frame Relay, ATM, L2TP
IPSec
SSL, TLS
PGP

## Slide 17: …Because VPN Technology Can Be Used For Several Different Reasons
Intranets
  Site-to-Site Communications Within A Single Organization
Mobile Access
  Telecommuters and Mobile Users Access To The Organization
Extranets
  Partnership Site-to-Site Communications Between Organizations (With Suppliers, Customers, Etc.)

## Slide 18: …Because VPNs Application Don’t Always Need The Same Characteristics
Varying Degrees Of The Following Characteristics May Be Needed For A VPN Application
  Isolation / Virtualization
  Privacy
  Authenticity
  Policy
  Quality Of Service

## Slide 19: VPN Evolutionary Steps Layer 2 VPNs Frame Relay and ATM

## Slide 20: The First VPNs Used Layer 2 Networks
Frame Relay:
  The Most Common VPN Technology In The World
ATM:
  The Second Most Common VPN Technology In The World
Both Are Statistically Multiplexed Public Network Technologies Used For Private Site-To-Site Communications

## Slide 21: The Typical “Shared” Public Network
Router
Router
Router
Router
Router
Router
Router
Router
Router
Router
Statistically
Multiplexed
Trunks
FR or ATM
Switches

## Slide 22: Layer 2 VPNs - Frame Relay and ATM Isolation and Privacy Assured
Isolation Provided By Switching Based On Link Layer ID (DLCI or VPI / VCI)
Security Assured Because Connections Are Privately (Not Publicly) Administered
  Addressing Is Privately Controlled
  Routing Is Privately Controlled
  Management System Is Privately Controlled
The Result: A “Virtual Circuit”

## Slide 23: Layer 2 VPNs - Frame Relay and ATM No Authentication Of End Points
Virtual Circuit “Connections” Are Provisioned Statically or “Dialed-Up” (SVCs)
No Authentication Is Provided
  If You Connect To The Wrong Address You Have No Way Of Knowing
This Will NOT Work For Extranets
  Dynamic Business-to-Business Network Connections Need Strong Authentication

## Slide 24: Layer 2 VPNs - Frame Relay and ATM Policy Enforcement Not Provided By SP
If Site-to-Site Connection Within A Single Organization, No Policy Enforcement May Be Needed
If Site-to-Site Extranet Connection Policy Enforcement Is Extremely Important
  Subscriber Must Provide His Own Policy Enforcement Infrastructure (Firewall, NAT)

## Slide 25: Layer 2 VPNs - Frame Relay and ATM Quality Of Service
Excellent QOS Can Be Provided Using The Following Techniques:
  Policing
  Queuing
  Rate Allocation
  Metering
  Connection Admission Control
  Traffic Management

## Slide 26: Layer 2 VPNs - Frame Relay and ATM Poor Dial / Mobile Service Integration
Integration With Dial Services Can Be Done Two Ways:
  Securely - At The Customer Premises
    This Is Very Expensive, But The Preferred Solution
  Less Securely - In The Service Provider’s Network
    Poor Implementation Will Compromise The Security Of The Frame Relay Network
    Dial Platform Must Map Directly To Layer 2 Without Routing
    If Routing Is Done, Require Virtual / Isolated Routers (Not Available From Dial Platform Vendors)

## Slide 27: VPN Evolutionary Steps Layer 3 (IP / Internet) VPNs The First Generation

## Slide 28: The Internet “Changes Everything” IP - The Protocol That Matters
Not Long Ago People Thought That ATM Would Extend All The Way To The Desktop
Today, ATM Is A Core Technology And IP Reigns Supreme In The LAN
Interconnecting Networks Almost Always Means Interconnecting IP Network

## Slide 29: The Internet / IP WAN Advantages
Ubiquity - The Internet Is The Same, Available Everywhere
  Dynamic Extranet Relationships Become Possible
Cost - The Internet Is The Least Expensive WAN Solution
Resiliency - The Internet Is An Inherently Resilient Network

## Slide 30: The Internet / IP WAN Disadvantages
An Inherent Lack Of Security
  No Isolation / Virtualization
  No Data Privacy
  No Address Privacy
  No Endpoint Or Message Authenticity
  No Data Integrity Guarantee
A Pervasive Lack Of Mission Criticality
  No Connection Admission Control
  No QOS
  Poor / No Traffic Engineering

## Slide 31: The Internet / IP VPNs
Must Use An Array Of Security And QOS Technologies To Overcome The Disadvantages.
These Technologies Are:
  New / Not Stable
  Expensive To Purchase
  Even More Expensive To Administer
  Not Tightly Integrated Together
  Not Tightly Integrated With The IP Backbone Network

## Slide 32: The First Generation Internet / IP VPNs
Use Single Purpose Appliances To Overcome IP Weaknesses
Security Appliances Are Deployed At Each Subscriber Site - Behind The IP Router
Appliances Provide Security Capabilities Only For That Site

## Slide 33: IP VPN Security Appliances / System
Encryption Appliance
  Provides For Data Privacy And Sometimes Data Integrity And Authenticity
Public Key Infrastructure / Certificate Authority
  Provide Digital Certificates Used For Authenticity

## Slide 34: IP VPN Security Appliances / System
Firewall Appliance
  Provides For Perimeter Privacy And Denial Of Service Attack Protection
Intrusion Detection Appliance
  Provides Active Monitoring Of Intrusion Attempts, Automated Protective Reactions And Sometimes Active Countermeasures

## Slide 35: IP VPN Security Appliances / System
Dial Tunnel Server Appliance
  Provides Tunnel Termination Resources For Mobile Users
AAA Server
  Provides Authentication Services For Mobile Users

## Slide 36: IP VPN Security Appliances / System
Bandwidth Manager
  Enforces Traffic Prioritization Policies
Perimeter Virus Scanner
  Eradicates Viruses Before They Reach Internal Host Computers

## Slide 37: Scaling First Gen. Internet / IP VPNs

## Slide 38: Barriers to Scale IP VPNs
Affordability
Security
Performance
Reliability
Management
Interworking

## Slide 39: Managed First Generation VPN Implementation Models
Managed CPE Appliances
Managed Network-based Appliance Farms

## Slide 40
Managed CPE Appliances
IP Backbone
Subscriber
Service Provider
Server
IP Router
Router Management
System
User
User
Application
Firewall
Encryption
Appliance
Tunnel
Termination
Bandwidth
Manager
Router
User
Public Frame Relay
and Private
Line Services
Authentication
Server
Intrusion
Detection
Certificate
Authority

## Slide 41: Managed CPE Appliances Scalability Ratings
Affordability – Low
  Very high operational cost
  High capital cost
  Upgrades require equipment obsolescence
Security – Medium-High
  As long as policies are managed effectively
Performance - Medium
  Encryption CPE needs hardware assistance
  Multi-box environment increases latency
  Encapsulation overhead reduces WAN link efficiency
Manageability– Low
  No scalable, centralized service management tools
  Often requires an on-site expert
  No visibility into total end-to-end behavior
Reliability – Low
  CPE devices more susceptible to failure than CO equipment
  Required on-site staging of spares for reasonably available SLAs
  Multivendor environment prone to interoperability problems
Interworking Capabilities - Difficult
  No interworking for sites on Frame Relay/ATM
  No migration strategy for Frame Relay and ATM
High
Med
Low
Affordability
Security
Performance
Manageability
Reliability
Interworking

## Slide 42: Managed Routers and Farms of Small Boxes The Current POP-based “Hybrid” Approach
Service Provider
Service Management System
IP Backbone
Firewall
Farm
Encryption
Farm
Bandwidth
Management
Large
Edge
Router
Small Routers
Public Frame Relay
and Private
Line Services
Subscribers

## Slide 43: Managed Routers and Farms of Small Boxes Scalability Ratings
Affordability – Medium
  Improved operational cost – across locations
  Space inefficient
  Upgrades require equipment obsolescence
Security – Medium-High
  As long as policies are managed effectively
Performance - Medium
  Encryption appliances needs hardware assistance
  latency still poor
  Improved use of WAN link (no encapsulation)
Manageability– Low
  Very little improvement
  No visibility
Reliability – Medium
  Appliances prone to failure
  Multivendor interoperability
  Many cables and discrete devices
  Faults difficult to isolate
Interworking Capabilities - Low-Medium
  Only provided through a complex mix of LAN and router equipment
High
Med
Low
Affordability
Security
Performance
Manageability
Reliability
Interworking

## Slide 44: VPN Evolutionary Steps Layer 3 (IP / Internet) VPNs The Next Generation

## Slide 45: What Comes After Broadband Connectivity? Elements For Success and Profitability for Next-Gen Carrier
IP
(Ubiquitous
Low-Cost
Commoditized Connectivity)
“Open”
Platform
Value-Added
Services
(Differentiation
and Revenue)
Out-Sourcing
(Delivery and Management
for Profit)

## Slide 46: Why Are These Elements Needed ? Service Profitability: The PSTN / AIN Lesson
Phone Service - Ubiquitous Commodity
Value-Added Services - Very Profitable
Network Intelligence
Centrex
800 WATS
Messaging
Value Added Call Handling
Basic
Connectivity
Service
Profitability
$$$
Out-Sourced “Intelligent Network”
Delivered Via Open “Service Creation” Platforms

## Slide 47: Network Service Pyramid Sources Of Service Provider Revenues Increased Processing Need
BEST EFFORT CONNECTIVITY
CLASS / QUALITY OF SERVICE
NETWORK-BASED BUSINESS DIAL
SLA MANAGEMENT
IP ACCOUNTING
IP SECURITY
(Proxy Firewall
NAT, Key Mgmt, Intrusion Detection, Virtual Routing, Etc.)
Hosted
Applications
$$
E-Commerce / Business
Applications
Gateway/Security
Applications
Connectivity
Applications
300
400
1000
2000
6000
8000
0
MIPS

## Slide 48: An “Open” Computing Platform for the NGN
“Best-of-Breed” Value-Added Applications
Computing
Networking

## Slide 49: Network-Based Integrated Service Delivery Platforms
Provide Edge Access Router Capability
Full Integrates Value-Added Services Such As:
  Encryption
  Firewall
  Virtual Routing
  NAT
  Dial Tunnel Serving
  Layer 2 Interworking

## Slide 50: Managed Network-based Service Delivery A Fully Integrated POP-based “Hybrid” Approach
Subscribers
Service Provider
Service Management System
Customer Network Management
IP
Backbone
Service Processing Switch
Router
Server
User
User
User
Virtual
Router
Firewall
IPSec
Tunnel
Termination
Bandwidth
Management
Subscribers
Router
Server
User
User
User
Public Frame Relay
and Private
Line Services
Customer Network Management

## Slide 51: Managed Network-based Service Delivery Scalability Ratings
Affordability – High
  Attractive operational cost model
  Very space efficient
  No equipment obsolescence on upgrade
Security – Medium-High
  As long as policies are effectively managed
Performance - High
  Hardware-assisted incrementally scalable encryption
  Tight coupling reduces latency
  Improved use of WAN link (no encapsulation)
Management – High
  Centralized service and policy management
  Customer network management available
  End-to-end visibility off services
Reliability – High
  Single carrier-class fault-tolerant device
  Service applications designed to inter-operate
  Sophisticated fault management integrated
Interworking Capabilities - High
  Provided through virtual routing services
  No external equipment required
High
Med
Low
Affordability
Security
Performance
Manageability
Reliability
Interworking

## Slide 52: VPN Evolutionary Steps VPNs Will Overtake Frame Relay “Forrester predicts that in 2003, Internet VPNs, grounded in serving these newer applications, will eclipse frame relay as the dominant WAN in most Global 2,000 corporations. This power shift will be facilitated by: *IP dominance *Global reach *Service interworking"
Forrester Group
Frame Relay's Middle Age
March 1998

## Slide 53: Next Generation VPN Technologies

## Slide 54: Technologies For A “Complete” VPN Solution
Virtualization / Routing
Tunneling
NAT
Privacy / Encryption
Authentication
Perimeter Security

## Slide 55: Virtualization / Routing

## Slide 56: VPNs Need “Private” Routing Services Static Routes Not Scalable
Virtual Routers - Private Instances Of Routers
Must Support:
  RIP V1 / V2, OSPF, BGP-4, Static Routes
  Distributed Route Computation
  Distributed Forwarding Information Base (FIB)

## Slide 57
Virtual Router Example
Subscriber Logical Interfaces
Service Provider Logical Interfaces
Control Net LIs
Virtual Interface
Tunnel Interface
Sub-VR

## Slide 58: Tunneling

## Slide 59: Tunneling - A Message Within A Message
Used To Send A Message Between Networks Through An Intermediate Network
Original Addressing And Payload Are Encapsulated Within A New Addressing Envelope
Address
PAYLOAD
Address
PAYLOAD
Original Message
New Message

## Slide 60: Tunneling Protocols IP-in-IP (GRE)
An IP Packet Is Encapsulated Within Another IP Packet
  No Security (Only Address Domain Isolation)
  Simple / Cheap To Implement
  Only Works For IP Traffic

## Slide 61: Layer 2 Tunneling Protocols
Encapsulates A Layer 2 Protocol Packet Into An IP Packet

## Slide 62: Tunneling Protocols Microsoft PPTP
An PPP Packet Is Encapsulated Within An IP Packet With Moderate Security Applied
  Provides
    Data Privacy and Session Authenticity Options
    Uses MS-CHAP Authentication
    Uses RC-4, DES Ciphers
  Simple To Implement
    Available with Microsoft Windows 95, 98
  Can Tunnel Non-IP Traffic
  Used For Dial VPNs
  RADIUS Supported

## Slide 63: Tunneling Protocols L2TP
An IETF Standard for PPP Packets Encapsulated Within IP - Poor Security
  Provides
    Session Authenticity Options
    CHAP Authentication
    No Cryptographic Ciphers for Data Payload
  Simple To Implement
    Available with Microsoft Windows 2000
  Can Tunnel Non-IP Traffic
  Used For Dial / Broadband Wholesale Aggregation
  RADIUS Supported

## Slide 64: L2TP Session Initiation Example

## Slide 65: Tunneling Protocols IPSec
An IP Packet Is Encapsulated Within Another IP Packet With Strong Security Applied
  Provides
    Data Privacy, Integrity, Authenticity,Replay Detection and Perfect Forward Secrecy (PFS) Options
    Uses DES, 3-DES Ciphers
    Internet Key Exchange (IKE) - ISAKMP/Oakley/Diffie-Hellman
    HMAC SHA-1 and HMAC MD5 Authentication
  Complex / Costly To Implement
  Only Works For IP Traffic
Can Used For Site-Site and Dial
Dial Requires A Dial Client
  PKI-based Authentication (No RADIUS)

## Slide 66: Tunneling Protocols IPSec

## Slide 67: Tunneling Protocols IPSec

## Slide 68: Tunneling Protocols IPSec

## Slide 69: Network Address Translation (NAT)

## Slide 70: Network Address Translation (NAT)
Static Address Translation
  Allows access to an internal IP address from the Internet although the real IP address remains unknown to the outside world. Every internal IP address mapped by Static NAT is converted to a different global IP address.
Dynamic Address Translation
  Enables the administrator to define a pool of global addresses to be shared among local users when there are more users available than global IP addresses. Every address mapped by Dynamic NAT is allowed access to the Internet/Intranet but no request from the outside is allowed access.
Single Address Translation
  Allows all users on the private network to have the one global source. Every address mapped by Single NAT is allowed access out to the Internet, but no access is allowed in.

## Slide 71: Firewalls Packet Filtering (SMTP and Telnet Example)
Excellent Performance
Good Scalability
Moderate Security
No Application Layer Awareness
Packet Filtering Router
Internet
SMTP Traffic Only
TELNET Traffic Only
Other Traffic

## Slide 72: Firewalls Application “Proxy” Gateway
Information Hiding
Robust Authentication and Logging
Cost Effectiveness
Less Complex Filtering Rules

## Slide 73: Firewalls Dual-Homed “Proxy” Gateway
Gateway Serves As Router Between Two Internal Subnets
Email, FTP and Public Web Servers Live Between Router and Firewall DMZ)
Only Gateway Is known Externally
Application Gateway
Info Server
IP Filtering
INTERNET
All Application Traffic
All HTTP/FTP Application Traffic

## Slide 74: Firewalls Stateful Inspection
A stateful inspection firewall examines application-layer data in incoming and outgoing
packets. The firewall substitutes its own IP address for the source address on outgoing packets.

## Slide 75: VPN Service Management Systems (SMS)

## Slide 76: Managed VPN Obstacles
Firewall Policy
Routing Protocol
Frame Relay
Device Configuration
Cards
Ports
Channels
Link Layer Protocols
Logical Interface
Network Components
Virtual Private Networks
Virtual Routers
Virtual Interfaces
Encryption
Certificates
NAT
Tunnels
Scalability of Services
How to reduce provisioning complexity?
Outsourced Services: A Daunting Proposition to the Enterprise Managers
  Need to build customers’ trust
  Can service providers scale its services?
  How are services scaled for end-users?

## Slide 77: Architectural Goals
System Architecture Goals
  Open, distributed architecture that scales
  Ease integration into existing SP Applications by using standard architectures: CORBA, TMN, SNMPv2c.
  Provide a fault tolerant platform as an option for critical, non-stop environments
Application Architecture Goals
  Ability to define new service offerings
  Ease of service roll out and provisioning
  Logical mapping of services to network objects to device objects
  De-mystify the IP Services provisioning: intuitive GUI, service templates provisioning “Wizards”
  Subscriber level visibility at all levels

## Slide 78: SMS - Architecture
Device Management
Network Management
Service Management
F
A
U
L
T
C
O
N
F
I
G
S
E
C
U
R
I
T
Y
P
E
R
F
O
R
M
A
N
C
E
A
C
C
O
U
N
T
I
N
G
Architectural
Layers
(TMN Model)
Application Components
(FCAPS)
SPS Devices
Control Net
NOC
Integrated Java Based GUI
IIOP
IIOP

## Slide 79: SMS - Architectural Layers
Device Management
Network Management
Service Management

## Slide 80: Device Management
Device Management
Manages the following
  Devices
  Cards
  Ports
  Channels
  Link Layer Protocols
  Logical Interfaces
SNMP
NEs Provide All
Services
Device
Managers
Network Management
Service Management

## Slide 81: Network Management
Manages the following
  Network Components
  Virtual Private Networks
  Virtual Routers
  Virtual Interfaces
  Firewall
  Encryption
  Certificates
  NAT
  Tunnels
  Network Versions
SNMP
SPS
Devices
Device
Managers
CORBA IDL
Network
Managers
Device Management
Network Management
Service Management

## Slide 82: Service Management
Manages the following
  Service Definition
  SLAs
  Customer Management
  Security Planning
  Capacity Planning
SPS
Devices
Device
Managers
Network
Managers
CORBA IDL
Service
Managers
CORBA IDL
SNMP
Device Management
Network Management
Service Management

## Slide 83: SMS Architectural Layers
Service Processing Switches
CORBA IDL
CORBA IDL
SNMP
Service Management
Device Management
Network Management

## Slide 84: System Architecture Scalability
Distributes systems based on Client-Server as well as Peer to Peer communication models
Architecture based on the highly scalable CORBA architecture
Ability to move any “object” to any “server” without major changes
Variety of options to “Scale-up”
  Add more machines
  Deploy on larger machines
  Add more processors and more memory to existing machines
No bottlenecks in system architecture

## Slide 85: Service Scalability
Traditional methods require high-powered network admins
SMS allows service operators to easily configure services
  Hundreds of VRs, VIs
SMS allows net admins to provision high number of networks/tunnels in a matter of minutes
Templating allows quick configuration of basic attributes
Configuration Wizard
CLI is a powerful tool for low-level debugging and is done on a device basis
It’s all about mass deployment

## Slide 86: Customer Network Management System
Application Suite for the Subscriber to
  monitor outsourced VPN services
  manage network configurations
  monitor SLAs
  generate network performance reports and trends
  retain the desired level of control
“Brand-able” Management Tool for Service Provider to
  determine which features to make available to which customers
  promote new services to existing customers

## Slide 87: CNMS - Architecture
SMS Servers
CNMS Server
Internet
Control Net
CNM
Clients
WNM
Clients
IIOP
IIOP
Subscriber A
Subscriber B
SSL
SSL

## Slide 88: Managed Security Service CNM Provides Visibility and Control
Subscriber HQ Office
Virtual
Router
IPSec
Remote
Office
Service Management System
Application Service Provider
Firewall
SLA Manager
Web
Add Encrypted Dial User
Modify Firewall Policies
View SLA Performance
Service Provider Network

## Slide 89: Customized Security for Secure Service Creation
Service Management System
CNM Server
Service Profile Database
Browser Based CNM Client
Certificate Authority
Service Processing Switch
Service Processing Switch
Name and Password, Secure
Token and/or Digital Certificate
SSL
IPSec (AH)
SNMP or CORBA
Internet

## Slide 90: Managed Bandwidth Service Example
Subscriber HQ Office
Virtual
Router
Bandwidth
Manager
Remote
Office
Service Management System
SLA Manager
Web
Bandwidth
Default Profile
ASP 128K
Remote
Office 256K
Web 64K
Application Service Provider
128K
256K
64K

## Slide 91: Managed Bandwidth Service Example End of Quarter Application
Subscriber HQ Office
Virtual
Router
Bandwidth
Manager
Remote
Office
Service Management System
SLA Manager
Web
320K
64K
64K
Bandwidth
Default Profile
ASP 320K
Remote
Office 64K
Web 64K
Application Service Provider

## Slide 92: A New Model of Customer Trust
Subscriber HQ Office
Virtual
Router
Remote
Office
Service Management System
SLA Manager
Web
Add Encrypted Dial User
Modify Firewall Policies
Change Application Priority
View SLA Performance
Application Service Provider

## Slide 93: Network-Based Managed Service Offerings

## Slide 94: Why are IP VPNs are compelling?
IP-Based Virtual Private Networks Services Market:
Market Drivers Ranked in Order of Impact (U.S.), 1998-2004
Rank Driver 1-2 Years 3-4 Years 5-7 Years
1 Cost-savings High High High
2 Rapid set up time High High Medium
3 IP-based VPN provider’s expertise High Medium Medium
4 Advancements in security software Low Medium High
5 Improved Tunneling Standards Low Medium High
6 VPN margins for service providers Medium Medium Medium
7 Cost-effectiveness in reaching partners, Medium Medium Medium
customers, and remote employees
8 Rapid growth of data networks High Medium Low
9 Higher competition among end-users Medium Medium Medium
10 Trend towards outsourcing data networks Medium Medium Medium
Source: Frost & Sullivan

## Slide 95: Market Potential for VPN Strategies
Frost&Sullivan VPN market was $3.5 billion in 1998 and will grow to $18.7 billion in 2004
Gartner Group Inc. predicts that by 2003 more than 130 million employees worldwide-including one-third of the U.S. workforce-will use remote access.
Infonetics Research Inc. estimates that network managers can save up to 40% for site-to-site networks domestically (and more,internationally) by replacing leased lines with VPNs

## Slide 96: VPN Service Strategies

## Slide 97: VPN Applications of the CoSine IP Service Delivery Platform
Network Based Managed VPN Services
  Site to Site Intranet
  Managed Firewall
  Dial-Up Remote Access
  Extranets
Frame Relay to IP Services Migration

## Slide 98: Managed VPN: Virtual Private Routed Network Site-to-Site Application
Service Processing Switch
Service Management System
IP or ATM Core
Subscriber
Virtual
Router
Corporate Headquarters
Service Processing Switch
Remote Office
Remote Office
Subscriber
Virtual
Router
FT1
T1
DS3
IPSec
Service Provider
Virtual Router
IPSec
Service Provider
Virtual Router
Customer Network Management System

## Slide 99: Managed VPN: Adding Managed Firewall Services
Service Processing Switch
Service
Provider
Virtual
Router
Subscriber
Virtual
Router
Corporate Headquarters
Service Processing Switch
Service Provider
Virtual Router
Remote Office
Remote Office
Subscriber
Virtual
Router
Firewall
Firewall
IP or ATM Core
Internet
IPSec
IPSec
Service Management System
Customer Network Management System

## Slide 100: Managed VPN: Dial-up Remote Access
Service Processing Switch
Service
Provider
Virtual
Router
Subscriber
Virtual
Router
Corporate Headquarters
Service Processing Switch
Service Provider
Virtual Router
Remote Office
Remote Office
Tunnel
Termination
IP
Core or ATM
Internet
Dial-up Telecommuter
Subscriber
Virtual
Router
IPSec
Service Management System
Customer Network Management System
Firewall
IPSec

## Slide 101: Extranet Application
Headquarters
Service Provider Network
Service Processing Switch
Router
Server
User
User
User
Virtual
Router
Firewall
IPSec
Manufacturer
SPVR
Supplier
SMS
Service Processing Switch
Virtual
Router
Firewall
IPSec
SPVR
SP IP
or ATM Core
T1
T1
DS3

## Slide 102
Secure DSL Aggregation
DSLAMs
LEC/CLEC Network
SPS will have an ISP VR for each “wholesale” customer
Each ISP can have multiple subscriber VRs, one or more for type of service offering.
Value-Added IP Services (NAT, Firewall, Intrusion Detection, Virus Scanning) can be provided for individual or groups of end-users
DSL ATU-R
Subscriber VRs
ISP #1 VR
ISP #12 VR
CO #1
CO #2
CO #3
DSL ATU-R
DSL ATU-R
DSL ATU-R
DSL ATU-R
DSL ATU-R
SP #1
ATM Core
SP #2
IP Core
Firewall
Firewall

## Slide 103: Frame Relay to IPSec Interworking: Integrating Frame Relay and IP Subscribers
Subscriber
Router
Subscriber A Headquarters
Subscriber n Remote Office
Subscriber
Router
Subscriber A Remote Offices
Subscriber
Router
Subscriber n Headquarters
Subscriber
Router
Subscriber A Remote Office
Dial-up Users
w/Client IPSec
Encryption
Subscriber
Router w/IPSec
PVC
IPSec
Internet
Frame Relay
PVC
Virtual
Router A
IPSec
Virtual
Router n
SP VR
Service Processing Switch
SMS
SMS
SPS

## Slide 104: Frame Relay Over IP: SPs Deliver Frame Relay Service Without Frame Relay Switch
Remote Office
IPX
AppleTalk
Router
Router
Virtual Layer 2
Switch
Headquarters
DS3 FR
Virtual Layer 2
Switch
IPSec
Service Provider Network
T1
Frame Relay
SP
VR
IPX FR(IPX)
IP[FR(IPX)]
FR(IPX) IPX
UNI-user
UNI-Network
IPSec
SP
IP Core
IPX
AppleTalk
SP
VR
Service Processing Switch
San Francisco
Service Processing Switch
New York

## Slide 105: Future Applications: MPLS
Remote
Office
Service Processing Switch
Service Processing Switch
Subscriber
Virtual Router
Bandwidth Management
(Diff Serv)
Bandwidth Management
(Diff Serv)
SP
MPLS
Core
Label Switching Router
Label Switching Router
Corporate Headquarters
Service Provider
Virtual Router
Service Provider
Virtual Router
Subscriber
Virtual Router
Remote
Office