## Slide 1: Introduction & Deployment
IPv6 Tutorial:
By:
Che Rohani Ishak
Raja Azlina Raja Mahmood
Monday, February 26th 2001
Kuala Lumpur, MALAYSIA

## Slide 2: Introduction and Deployment of IPv6
This tutorial and reference handbook is designed to help you understand the significance of the new IP protocol and its deployment techniques.
Notes: Che Rohani (roha@mimos.my) and Raja Azlina (ina@mimos.my) are the primary authors of this material. Supporting authors and editors include: Mahizzan Mohd Fadzil and Shaheezul Mazhar.

## Slide 3: Tutorial Outline
Topic 1: IPv4 Concepts
Topic 2: IPv6 Concepts
Topic 3: Migration Process
Topic 4: IPv6 Implementation & Deployment
SESSION 1
Topic 1: IPv6 Hands-on
SESSION 2
Notes: This tutorial consists of 2 sessions; morning and evening. Session 1 will be held from 9:30 a.m to 12:15 p.m. which covers basic IP concepts (both IPv4 and IPv6). Participants will also be guided through the migration process from IPv4 towards IPv6 network. Lastly, some information on current implementation and deployment of IPv6 throughout the world.
Session 2 will be held in the evening which includes hands-on activity on implementing IPv6 network, concentrating on OpenBSD and WinNT operating systems. Together with demonstration on IPv6 configuration network using Cisco router.

## Slide 4: TOPIC 1: IPv4 Concepts
Notes: This topic is meant as an introduction to existing IP or IPv4 network, which is a prerequisite topic in understanding the new version of IP or known as IPv6. It is our hope that all participants will then have the basic understanding of IP, before moving into IPv6 topic.

## Slide 5: Objectives
Understanding IP Network
Header Format
Addressing
Fragmentation
Routing
Limitation
Topic 1: IPv4 Concepts
Notes: Upon completion of this section, participants will be familiar with the IPv4 basic concepts.
The participants will learn:
1- IP header and the function of each field
2- IP addressing and its relation to DNS
3- Fragmentation process
4- Routing in current IP network
5- Limitations imposed by IPv4

## Slide 6: Section 1: IP Network
Understanding IP network
Data transmition
IP / Network layer
Topic 1: IPv4 Concepts
Notes: Upon completion of this section, participants will have basic understanding on what is IP network, how data been transmitted over IP network as well as IP basic functions.

## Slide 7: Internet
Networks
Networks
Networks
Networks
Networks
Networks
Networks
Leased
Line/WAN
Leased
Line/WAN
TCP/IP
TCP/IP
A collection of network of many computers,
through WAN utilizing telecommunication leased lines
Talking with one another using a standard protocol called TCP/IP
Topic 1: IPv4 Concepts
Notes: Basically, Internet is a collection of networks connected via leased circuits using a standard protocol called TCP/IP protocol.

## Slide 8: How Packets are transmitted on a network
Transport
Application
Physical
Data Link
Network
Media (Fiber,UTP,coax)
Ethernet, ATM, FDDI
IP
TCP , UDP , ICMP
Telnet , FTP, SMTP , DNS
Topic 1: IPv4 Concepts
Notes: Standardization is an important aspect to ensure data can travel across network. IP network is a layered approach network as shown in the above diagram.
This Layerr approach will describe how data moves from one host to another.Data will be carried out to the network via physical media which can be fiber or copper connection. Data will pass through either Ethernet, FDDI, token ring or ATM network. From here packets will be routed using a device called router (gateway). Transport protocols like TCP and UDP is used for end to end transmission.For example, TCP is connection oriented. It will ensure that packet will reach its destination. When packet reaches its destination, the host will strip of the header and executes application/message. This is how packets travel through the network.
In this tutorial, we will be concentrating on OSI layer three (Network or IP layer)

## Slide 9: IP
IP robust protocol that connects different kind of hardware platforms using a unique addressing scheme
Current version is IPv4
IP functions:
- Addressing
- Routing
- Fragmentation and Reassembly
Topic 1: IPv4 Concepts
Notes: IP protocol which is used as standard protocols in the internet is important because it provides unique addressing to every host. Uniqueness is important to ensure data can be delivered correctly to every host in the internet.Current version of IP is 4 or known as IPv4or IP version 4.
IP will route packets to their destination host even though it provides unreliable, connectionless datagram delivery service. Unreliable here means that there are no guarantees that packet will successfully be delivered to the destination host. Whereas connectionless means packets are delivered independently. This sometimes can cause packets lost and arrive out of order.
There are some extra works that IP needs to do, such as if network cannot accept large data, then IP needs to fragmentize this data into smaller packets. Later, these packets will be reassembled at the destination host.

## Slide 10: Section 2: IP Header
IPv4 Packet Structure
IPv4 Header
Topic 1: IPv4 Concepts
Notes: Upon completion of this section, participants will be familiar with :
- IPv4 packet structure
- IPv4 header fields and their functions.

## Slide 11: IPv4 packet structure
Upper Layer
PDU
Payload
IPv4 Packet
IPv4
Header
IPv4 packet :
Payload
IPv4 header
+
IPv4 payload :
Upper Layer PDU
+
Topic 2: IPv6 Concepts
Application Data
Application Data
Notes: IPv4 packet comprises of IP header and its payload. The minimum IPv4 header’s size is 20 bytes without options and padding. The total length of IPv4 packet (combination of the IPv4 headers and application data) size can be up to 65,535 bytes long.
IPv4 Header
The maximum size of IPv4 header is 60 bytes.
Upper Layer Protocol Data Unit
The upper layer protocol data unit (PDU) usually consists of an upper layer protocol header and its payload (for example, an ICMP message, a UDP message, or a TCP segment).

## Slide 12: IP- Header (Datagram)
0 15 16 31
Topic 1: IPv4 Concepts
Version = 4
IHL - Internet Header Length = 5 with no header options
[min = 160 bits] [max = 512 bits]
Type of service , desired quality service
0- 2 Precedence
3 Normal delay low delay
4 Normal throughput High throughput
5 Normal Reliability High reliability
6- 7 Reserved
Prec. D T R 0 0
0 1 2 3 4 5 6 7
Identification, Flags, Fragmentation Offset- use to segmentation and reassembly packet
Bit 0 = Reserved; must be 0
Bit 1 = DF ( 0 = May fragment; 1 = do not fragment )
Bit 2 = MF (0 = last fragment; 1 = more fragments )
Option and Padding - additional info to control functions such as routing and security
Notes: Version will show the current version which is version 4 or better known as IPv4.
Internet Header length will show IP header length (including options and padding) excluding payload. Options and padding are used for routing,security and time stamping.The minimum size of IHL is 5 or (5*32=160 bits or 20 bytes). Maximum size for this Header Length is (15*32=480 bits or 60 bytes)
Type of Service will support real-time delivery of data, so called quality of service. This field will assign high priority data, the best route to take, low delay and high reliability data.This field is used by routers to route packets.
Total Length - Inclusive of payload and header length. Maximum is 64K bytes
Identification - Will provife identification number for packets, used during reassemble.
Flags - three bits field. Bit 0 is reserved. The last fragment will have MF = 0.
Fragment offset - will be in 8 octet boundaries.The second fragment shows data position.
TTL - the upper bound time for data to travel in the network. It will be decrement by 1 at every hop (more suitable to be called as Hop Limit). This is because time is measured in macro seconds and is hard to measure, the best solution is to decrement by 1 at every hop. Protocols : TCP and UDP are transport protocols. TCP is more reliable, connection-oriented protocol.ICMP is an error checking protocol. It will send back error messages e.g host unreachable.
Header Checksum : Is a 16 bits field. This is for calculating just the header. Header will be examined when there are changes in the header value (e.g decrement in TTL value), which means packet is examined at every router hop.
Source & Destination Address : The sender and receiver host address.
Options and Padding : This field will be used to impose security or routing

## Slide 13: Issue on header format
Checksum in header format will calculate only the header checksum. Computation will be done if there are changes in header value. TTL value is decrement at every hop. Therefore, computation will be done at every router hop.
Options and Padding Field will be checked at every router hop and this use up router processing time which will degrade router performance.
vers
frag offset
source address
destination address
options and padding
header checksum
TOS
total length
identification
hlen
protocol
flag
TTL
Notes: Checksum decreases router performance. Since at Transport and Link layer already have their own checksum, so imposing another checksum at IP Layer is redundant.
These options are rarely used and not all hosts and routers support this option. Options field is always end on a 32-bit boundary.

## Slide 14: Section 3: IPv4 Addressing
IPv4 Address Architecture
IPv4 Address Type
IPv4 Address Class
Limitation
Domain Name Service
Topic 1: IPv4 Concepts
Notes: Every host in the Internet must have a unique Internet Address (IP addresses) which is globally routable in the Internet. Allocation of IP addresses are done by IANA (Internet Assigned Number Authority) and delegate the authority to regional registries such as APNIC (Asia Pacific Region), ARIN (North America) and RIPE-NCC (European Region).

## Slide 15
IPv4 addressing
32 bits address
Divided into Classes
Class A 0.0.0.0-127.255.255.255
Class B 128.0.0.0-191.255.255.255
Class C 192.0.0.0-223.255.255.255
Represent Network & Host Address
Network Address
Host Address
192.228.0.0/16 or 192.228.0.0/20 …..
Features
Presentation
Where you are connected
Who you are
Later adopt CIDR
Topic 1: IPv4 Concepts
202.188.125.67
Notes: IPv4 is a 32 bits address which will give 232 addresses ~ approximately 4 billions of Internet addresses
IPv4 address is separated by dots.It represents network and host address.
IPv4 is a classful address representation.To differentiate one class from another is to look at the first four bits of IP address. The range is shown as above
CIDR use Subnetting to reduce the size of Internet routing table and also to conserve IP addresses. CIDR is also hierarchical routing method.

## Slide 16: IPv4 address type
“Unicast” Address : Specified for a single recipient, i.e. interface.
Multicast Address : 244.0.0.0/4
Broadcast Address : e.g 192.228.128.255
Unspecified Address : 0.0.0.0
Loopback Address : 127.0.0.1
Topic 1: IPv4 Concepts
Notes: Unicast address is assigned for a single interface. Unicast can be a public or private IP. Private IP : 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16. Private IP is not routable via Internet, usually used for private network or intranet.
Multicast address is a point to multi-point destinations (destined for host in multicast group) which is frequently used for video streaming and video conferencing.
Broadcasting is used in IPv4 to send messages to every other hosts on the network. It will get information from other hosts and update its routing table.
Unspecified address : Is never used as destination address.
Loopback address : Host send message to itself. Router will never forward this packet.

## Slide 17
IP address classes
“ Classful” IP addresses are identified by the first byte of the address
Each class fixes the boundary between the network-prefix and the host-number at a different point within the 32-bit address
Class A (or /8)
Class B (or /16)
Class C (or /24)
0
1 0
1 1 0
Bit #
0 1 78 1516 2324 31
Highest
order
Lowest order
Topic 1: IPv4 Concepts
Notes: As defined before, IPv4 address is a classful address (Class A, B, C, D and E ). The bits order in the diagram will show how IP classes are determined.

## Slide 18
Ranges of different IP addresses
255.255.255.0
C
192.0.0.0 to 223.255.255.255
255.255.0.0
B
128.0.0.0 to 191.255.255.255
255.0.0.0
A
0.0.0.0 to 127.255.255.255
Network mask
Class
Range
Topic 1: IPv4 Concepts
Notes: Decimal Representation of the Classful network and network mask that represents each network.Network mask The network mask will indicate number of hosts in the network.

## Slide 19
Class A network (/8 Prefixes)
8-bit network prefix with the highest order bit set to 0
Host-number is 24-bit
This means max. 127 or (27-1 ) networks with 16,777,214 or (224 –2) hosts per network
Also known as “slash eight” or “eights”
Subnet mask for this network is 255.0.0.0
Class A (or /8)
0
Bit #
0 1 78 1516 2324 31
Network
prefix
Host prefix
Topic 1: IPv4 Concepts
Notes: We take a look at one example : IPv4 class A network or CIDR terms as /8 network.
We can predetermine how many networks and number of host per network.

## Slide 20
Other classes
Class D ( 224.0.0.0 to 239.255.255.255 )
which is reserved for IP Multicasting have their four leading four-bits set to 1-1-1-0
Class E ( 240.0.0.0 to 255.255.255.255 )
which is reserved for experimental use have their four-bits set to 1-1-1-1
Topic 1: IPv4 Concepts
Notes: IP multicast as explained earlier is used for video conferencing and video streaming. Class E is reserved for future used or for experimental use. Router will not forward any of class E packets.

## Slide 21: Quiz: IP address classes
1. Let us look at network 202.187.35.0/24. ( Note that :this is a class C network ). Compute how many host in this network. (Remember that 202.187.35.0 is reserved for network address and 202.187.35.255 as a broadcast address) ?
2. If you decide to do subnetting for your class C network (CIDR) using 202.187.35.0/27. Calculate how many network can you have? How many host per network ? What is the broadcast address for each network?
Topic 1: IPv4 Concepts
Notes: Answer :
1. 28 - 2 = 254 hosts on the network.
2a) 23-1 = 7 networks (b) 25-2 = 30 hosts
c) 255.255.255.31, 255.255.255.63, 255.255.255.95, 255.255.255.127 255.255.255.159, 255.255.255.191, 255.255.255.223

## Slide 22
Limitation to IPv4 addressing
Decision to stick with 32-bit address space meant that there were only 232 (4,294,967,296) IPv4 addresses available
Classful A, B, and C octet boundaries are easy to understand but inefficient to deploy in the real world. A /24 is too small for an average organization, while a /16 is too big!
Topic 1: IPv4 Concepts
Internet gowth
IP
4
Notes: Current IPv4 address space cannot accommodate enough addresses to the increasing internet demands.From statistic quoted from the Next Generation Internet NGI.ORG September2000
The Internet is now expanding at the rate of 79 new hosts and 19 new domains per minute worldwide.
A lot of address have been wasted , one of the factors that cause address depletion.To preserve IPv4 currently use CIDR and NAT as a solution.

## Slide 23: Domain Name System(DNS)
Used by TCP/IP applications to map IP addresses to hostname and vice versa
Organised in hierachical
com
edu
gov
ae
int
net
mil
Generic domains
Country Domains
arpa
org
my
..
..
in-addr
net
manis
Unnamed root
65.22.187.202.in-addr.arpa
www.manis.net.my
Topic 1: IPv4 Concepts
Arpa domains
Notes: For human usually names are a lot easier to remember than addresses.Therefore, DNS is used to map IP address with names and vise versa.
DNS is a distributed database because the entire address table is not stored on a single host, rather it is distributed across many servers.
The top-level domains are divided into three areas :
1. Arpa is a special domain used for address-to-name mappings.
2. The seven 3 -character domains are called generic domains
3. All 2-character domains for country codes as defined in ISO 3166
Yahoo.com is the example of domains within this generic domain..gov and .mil are the only generic domains that are restricted to the United States.

## Slide 24: Section 4: Fragmentation
Fragmentation
Fragmentation Problems
Avoiding Fragmentation
Topic 1: IPv4 Concepts
Notes: This section, will show extra work that IP need to do when sending data to its destination. If the destination host is in the same network then fragmentation will be done at the source host else fragmentation is done by router.

## Slide 25: Fragmentation
MTU limited
datagrams
fragments
receiving computer’s
fragment reassembly buffer
A process used by IP to reduce the size of packets (will be acceptable to MTU size)
Fragments will be reassembled at the final destination (based on identification field, segment offset and flags)
How ?
Topic 1: IPv4 Concepts
Notes: Before sending packets, host and destination host will negotiate on the size of packets that they agree to accept. The smaller size will be agreed between them. These agreement is just between the host. But when packet travels, it needs to pass through several networks in between. For example through network x,y,z .If it happens that the MTU size of network y is smaller than the packet, router will need to fragment the packet before sending to y. Packet can be fragmented a few times before it reaches its destination.
Fragmented packets are routed independently.But each of them will have their own header with the same identification number that will be used during reassemble at destination host.

## Slide 26: Fragmentation flag
Identification Number
16 bits integer value used to identify all fragments. This id is not a sequence number!
Flags - 3 bits control fragmentation
R
DF
MF
Fragment offset - indicate the distance of fragment data
from the start of the original datagram, measure in 8 octets unit
reserved, must be 0
0=may fragment 1=don’t fragment
0=last fragment 1=more fragment
Topic 1: IPv4 Concepts
vers
frag offset
source address
destination address
options and padding
header checksum
TOS
total length
identification
hlen
protocol
flag
TTL
Notes: Identification number - will be used during reassembly.The same packet will have the same identification.This is unique during the lifetime of the packets.
If 2nd bit of flags is 1.The packets will not be fragmented.If the packets size is larger than MTU, the packets will be discarded from the network.
The 3rd bit will show whether this is the last segment or there are more.
Fragment offset will show the position of data in each fragment so that data can be reassembled accordingly.

## Slide 27: Fragmentation sample
UDP Data (2000 bytes)
0 ..1472 bytes
1472….2000
Ethernet with MTU 1500
IP packets
IP Header
UDP
IP Header
UDP
IP Header
Identification=26304 MF = 1 Fragment Offset= 0
Identification=26304 MF = 0 Fragment Offset = ( 184* 8)1472
Topic 1: IPv4 Concepts
Fragment #1
Fragment #2
Notes: Every fragment will carry its own header. Fragment will be in 8 octet boundary.

## Slide 28: Problems in fragmentation
The end node has no way to know how many fragments there be.
Every node will travel independently.If any fragment lost, all datagram must be discarded
If any fragments fail to arrived (timer) all datagrams must be discarded
IP will make no attempt to recover these situations (connectionless). Only give ICMP error e.g “Packet too big”
Topic 1: IPv4 Concepts
Notes: There will be no way of keeping track on how many fragments there is. If one of the fragment is lost or does not arrive on time packets will be discarded. Fragmentation will take up router processing time which will cause degradation in routing performance.

## Slide 29: Avoiding fragmentation
Set DF=1 and the message will not be fragmented.But if message is larger than the link is able to accept, message will be discarded from the network
Standard recommend that all networks supporting TCP/IP should have an MTU of at least 576 bytes (guaranteed packets will never be fragmented)
Topic 1: IPv4 Concepts
Notes: The steps above is to avoid fragmentation. However, the first step will not guarantee that packets will be send to the destination host.

## Slide 30: Section 5: Routing
IP forward packet from source to destination host based on routing info (consult from routing table)
Routing are done by routers or gateways
Routing protocols used RIP, OSPF, BGP ,ISIS
IP routing is a combination of flat and hierarchical routing. Flat using the legacy IPv4 and hierarchical routing when CIDR has been adopted.
Topic 1: IPv4 Concepts

## Slide 31: Section 6: Limitation
Address Space
Routing
Security
Auto-configuration
Topic 1: IPv4 Concepts
Notes: IPv4 is a huge success story. A lot of devices had already been connected to the Internet. But there are still rooms for improvement.
This section will highlight IPv4 limitation which will bring about to the deployment of new Internet Protocol.

## Slide 32: Address space
- Communications appliances (e.g. phone, pager)
- Information appliances(e.g. electronic books)
- Entertainment appliances (e.g. set-top boxes)
More connected devices
More management costs
More demanding applications
IPv4 with only 32 bits gave approximately 4.3 x109
Topic 1: IPv4 Concepts
LARGE ADDRESS SPACE NEEDED Facts : With current world populations 2 persons need to share an IP address
Notes: The most obvious factor is the depletion of IPv4 address space .
Even though approximately half of IPv4 address space is still unassigned , we have effectively run out of IP addresses :
- in a way, dial-up users are denied permanent IP addresses
- and many sites are forced to use NAT or other address-sharing tricks (loss globally addressibility has seriously harmed the flexibility, robustness and managability of Internet.

## Slide 33: Routing problems
Large Backbone Routing Table backbone routing table explosion ~ 90K routes . Problem with legacy IPv4
Routing Performance At every hop router will need to check and verify header checksum.This will increase processing time and degrade routing performance.
Fragmentation of packets are also done by router.Might need to be fragmented several times. This will also effect routing performance.
Topic 1: IPv4 Concepts
Hierarchical addressing scheme should be adopted and simplified header field can ease router burden.
Notes: Routing in IPv4 is a flat and hierarchical routing that had caused explosion of backbone routing table.
Example :
Assume that an ISP has been assigned the address block 206.0.64.0/18. This block represents16,384 (214) IP addresses which can be interpreted as 64 /24s. If a client requires 800 host addresses, rather than assigning a Class B (and wasting ~64,700 addresses) or four individual Class Cs (and introducing 4 new routes into the global Internet routing tables), the ISP could assign the client the address block 206.0.68.0/22, a block of 1,024 (210) IP addresses (4 contiguous /24s).
Header checksum in IP header is checked at every router hop and this take up router processing time. Fragmentation is also done by router. This cause degradation of routing performance.

## Slide 34
Internet security
Long Messages
ges
L
n
M
s
a
s
e
g
o
Internet
Eavesdropping
Spoofing
Forgery
Packet drops
Denial of service
Topic 1: IPv4 Concepts
Notes: Internet is an amazing opportunities but not without some risks. The Internet is known for several attacks such as Loss of data privacy , Loss of data integrity, Spoofing and Denial of service.
Loss of data privacy : without end-to-end encryption, message send across the network can be read by unauthorised party (e.g intruders install packet sniffer to collect account names and passwords)
Loss of data Integrity : Even if the data is not confidential but we do not want anyone to tamper with the data. We must make sure that data is not changed along the way.
Identity spoofing : Many security systems rely on IP address to uniquely identify users. There are many tools can fool this. Intruders may be able to impersonate your identity and have access to your data confidentiality
Denial of Service : When providing a service you always want yourself to be available. Intruders might send packets or overflow data to crash the system.

## Slide 35: IP layer security
Security at Network Layer.
Confidentiality, Integrity, and Authentication are key services used to protect against these threats
If data is encrypted while in transit, it is impossible for a perpetrator to observe or modify.
Security in IPv4 is not mandated. We have to run IPSec on top of IP.
Topic 1: IPv4 Concepts
Strong Network-Layer authentication, identity spoofing and denial-of service can be prevented
Notes: Currently in IPv4, IPsec is used for IP-Layer security. IPSec is used to provide confidentiality, integrity and authenticity of data. In the current situation we have to run IPsec on top of IP to ensure ip-security. This requires extra work.

## Slide 36: Host auto-configuration
Stateful Server Mode
Via DHCP
DHCP Server
DHCP request
DHCP respond
host
Topic 1: IPv4 Concepts
Stateless Server mode will be a better solution and can save cost
Notes: In IPv4, in order to allow for host auto-configuration, we need to setup DHCP server. Without DHCP server we cannot do auto-configuration.This is called Stateful Auto-configuration. Host will send request to DHCP Server and DHCP will reply and assigned IP address to the host.

## Slide 37: Quality of Service
Quality of Service in IPv4 is using best effort delivery services , for data to arrive its destination as soon as possible.
No reservation for bandwidth. This is adequate for traditional applications such as Telnet and FTP. But nowadays, multimedia applications need real-time and sensitive data transfer to the network. Therefore, better QOS is needed.
An improved Quality of service need to be implemented.
Topic 1: IPv4 Concepts

## Slide 38: TOPIC 2: IPv6 Concepts
Topic 2: IPv6 Concepts
Notes: Participants are to be introduced to basic concepts of IPv6 together with its features and advantages.

## Slide 39: Objectives
Background
Header Format
Fragmentation
Addressing
Routing
Improved Features(security, QoS, auto-configuration)
Topic 2: IPv6 Concepts
Notes: At the completion of this section, the participants will be familiar with these core concepts of IPv6. The participants will learn:
1- How IPv6 gets its name
2- How IPv6 header differs from current IP
3- How IPv6 fragmentation process is done
4- How IPv6 address looks like
5- How routing is done in IPv6
6- How security, quality of service and auto configuration features have been improved
in IPv6

## Slide 40: Section 1: Background
Some History
Some IPv4 Problems(Recap)
Some IPv6 Advantages
Topic 2: IPv6 Concepts

## Slide 41: Before IPv6…
0-3 unassigned
4 Internet Protocol, IP (current version)
5 Stream Protocol, ST (not a new version of IP)
6 IPv6 (formerly SIP, SIPP)
7 CATNIP (formerly IPv7, TP/IX; deprecated)
8 Pip (deprecated)
9 TUBA (deprecated)
10-15 unassigned
Topic 2: IPv6 Concepts
Note:
IPv6 working group was formed and being chaired by Steve Deering
(Cisco Systems, Inc) and Robert Hinden (Nokia)
Notes: History of the IPv6 Effort
1990: IETF defined a new version of IP, generally known as IP Next Generation(IPng)
Feb 1992: 4 proposals to IPng(CNAT, IP Encaps, Nimrod, Simple CLNP)
March 1992: evolving
- IP Encaps to IPAE(IP Address Encapsulation)
- Simple CLNP to TUBA (TCP & UDP with bigger address)
Dec 1992: 3 more proposal for IPng(PIP- P Internet Protocol, SIP - Simple IP and TP/IX)
Fall 11993: resolution to 3 possibilities:
- TUBA
- TP/IX=CATNIP(Common Architecture for the Next Generation Internet Protocol)
- SP+IPAE+PIP=SIPP(Simple Internet Protocol Plus)
Jul 1994: SIPP was chosen, known as IPv6

## Slide 42: IPv4 problems
depletion of addresses + inefficient temporary solutions
explosion of backbone routing table size (>90K routes)
lack of support for multimedia
lack of address auto configuration facility
no security feature(inherently)
Topic 2: IPv6 Concepts
Notes: To recap some of the problems in IPv4, which includes:
- running out of IP addresses
- backbone routing table growing too large
- no much support for real-time traffic
- not plug-n-play environment
- no security on IP layer

## Slide 43: What are IPv6 advantages?
scalable IP address with streamlined IP header
optimized routing table size (<10K routes)
better real time support
self-configuration of workstations
security features
Topic 2: IPv6 Concepts
Note:
IPv6 was designed to re-build and re-engineer IPv4; thus
still inherit some IPv4’s characteristics but rejects its flaws
Notes: Some overview of IPv6 advantages, such as:
- bigger IP addressing space
- better header format; less fields and fixed size
- optimized backbone routing table size whereby only those of the “highest” hierarchy are considered; of this new hierarchical addressing structure
- a flow-label mechanism was introduced to support real-time traffic, i.e. multimedia
- auto configuration is introduced; fabricate own host’s address
- security is a must; through authentication and encryption implementation

## Slide 44: Section 2: IPv6 Header
Structure of IPv6 Packet
Comparison of Two Headers
Major Simplifications
Extension Headers
Topic 2: IPv6 Concepts

## Slide 45: IPv6 packet structure
Extension
Headers
Higher-level protocol header
+ application content
payload
IPv6 packet
IPv6
Header
Definitions:
IP header provides addressing and control
IP payload carries information and error/control protocols
Extension headers(optional):
hop-by-hop, routing, fragment, authentication, encryption & destination header
Higher-level protocol header:
ICMPv6, UDP & TCP
Topic 2: IPv6 Concepts
header
Notes: IPv6 packet comprises of IP header and its payload. The IPv6 header’s size is fixed to 40 bytes, meanwhile the IPv6 packet payload’s (combination of the IPv6 extension headers, higher-level protocol header & application content) size can be up to 2^16 (65,535) bytes long.
IPv6 Header
The IPv6 header is always present and is a fixed size of 40 bytes.
Extension Headers
Zero or more extension headers can be present and are of varying lengths. These headers are placed between the IPv6 header and the transport-layer header in a packet. IPv6 extension headers have no maximum size and can expand to accommodate all the extension data needed for IPv6 communication. Extension headers includes hop-by-hop, routing, fragment, authentication, encryption and destination options.
Higher-level Protocol Header
Consists of an upper layer protocol header; for example, ICMPv6, UDP or TCP header.
Application Content
Consists of application(user level) content such as an ICMPv6 message, a UDP message, or a TCP segment.

## Slide 46: Header comparison
vers
0
15
16
31
hlen
TOS
total length
identification
flags
frag offset
TTL
protocol
header checksum
source address
destination address
options and padding
20
bytes
vers
traffic class
flow label
payload length
next header
hop limit
source address
destination address
40
bytes
Removed (6)
ID, flags, frag offset
TOS, hlen
header checksum
Changed (3)
total length=> payload
protocol=>next header
TTL=>hop limit
Added (2)
traffic class
flow label
Expanded
address 32 to 128 bits
IPv4
IPv6
Topic 2: IPv6 Concepts
Notes: IPv6 header is only about TWICE bigger than IPv4 header. Given no options, IPv4 header will have the size of 160 bits(20 bytes), while IPv6 header has the size of 320 bits(40 bytes).
IPv6 header is much simpler than that of IPv4. There are only 6 fields and two addresses in IPv6, meanwhile in IPv4, there are 10 fixed header fields, two addresses and some options.
IPv6 header fields are as the followings:
Version: Indicates the version of IP and set to 6[4 bits].
Traffic Class : Indicates the class/priority of the IPv6 packet. It has similar functionality to the Type of Service(TOS) of IPv4[8 bits].
Flow Label: Indicates that this packet belongs to a specific sequence of packets between a source and destination, requiring special handling by intermediate IPv6 routers[20 bits].
Payload Length: Indicates the length of the IP payload(anything after the IPv6 header). The max IPv6 payload is 65,535 bytes[16 bits] .
Next Header: Indicates either the first extension header (if present) or the protocol in the upper layer PDU (such as TCP, UDP, or ICMPv6)[8 bits].
Hop Limit: Indicates the maximum number of links over which the IPv6 packet can travel before being discarded[8 bits].
Source Address: Stores the IPv6 address of the originating host[128 bits].
Destination Address: Stores the IPv6 address of the current destination host[128 bits].

## Slide 47: Major improvement
1- No Options. Options field is replaced with extension header. The removal of the options results in a fixed length, 40 byte IP header.
2- No header checksum. Transport and data link layer have already performed checksumming.The removal of this feature leads to fast IP packet’s processing.
3- No segmentation procedure by routers. With path MTU discovery in IPv6, only source host performs fragmentation process. Removal of this procedure will speed up IP forwarding in routers.
Topic 2: IPv6 Concepts
vers
0
15
16
31
hlen
TOS
total length
identification
flags
frag offset
TTL
protocol
source address
destination address
options and padding
header checksum
Notes: Since IPv4 header includes all options, each intermediate router must check for their existence and process them when present. This causes performance degradation in the forwarding of IPv4 packets. In IPv6, these options are moved to extension headers, appended after the main header and not being processed at each intermediate router(except Hop-by-Hop Options extension header). This increases IPv6 header processing speed and improves forwarding process performance.
Because the transport layer (e.g, TCP and UDP) and data link (e.g., Ethernet) protocols in the Internet layers have already perform checksumming, it is agreed that it is redundant to do it at the network layer that it was then removed. Moreover, this has reduced the cost of header processing is for there is no need to check and update the checksum at each relay. However, the risk of it is that errors will not be detected by intermediate routers but only by the destined host.
No fragmentation is done by the IPv6 header. Instead, the hosts should learn the maximum acceptable segment size through its path MTU discovery mechanism. If host tries to send larger packets, they will be rejected by the network and this process continue until the smallest MTU is found. Fragmentation and reassembly is a time-consuming operating; removing this functionality from the routers and placing it in the end systems considerably speeds up IP forwarding within the network. Besides, taking out fragmentation from IPv6 has saved the header from the segmentation control fields (identification, flags and fragmentation offset).

## Slide 48: Extension headers
IPv6 header
next header=TCP
TCP header + data
IP header
IP Payload
Extension headers include hop-by-hop, destination,
routing, fragment, authentication and encapsulating
security payload
Extension header
IPv6 header
next header=routing
IP header
Routing header
next header=TCP
TCP header + data
IP Payload
Extension headers
IPv6 header
next header=routing
IP header
Routing header
next header=fragment
fragment of
TCP header + data
IP Payload
Fragment header
next header=TCP
Topic 2: IPv6 Concepts
Extension Headers
Higher-level protocol header
+ application content
IPv6 Header
IPv6 packet
Notes: IPv6 extension headers will only be added by the source node when special handling is required by the intermediate routers or the destination. These extension headers are not processed by every routers on the path EXCEPT for hop-by-hop option, and therefore if present, it must be placed in front of other extension headers.
Hop-by-Hop: Carries options that are examined by intermediate nodes along the forwarding path. Since this header is read by all routers along the path, it is useful for transmitting management information or debugging commands to routers.
Destination: Specifies packet delivery parameters for intermediate destinations or final destination.
Routing: Specify a source route; a list of intermediate destinations for the packet to travel to on its path to the final destination(similar to option function in IPv4).
Fragmentation: Source node uses this option if the packets sent to a particular destination are too large to fit in the maximum size allowed by the links along the path; this is known as Maximum Transmitted Unit(MTU).
Authentication: Provides data authentication and integrity assurance for IPv6 packets. It also provides protection against replay but not confidentiality.
Encapsulating Security Payload: Provides data confidentiality, data authentication, and data integrity services to the encrypted payload; not including the header.

## Slide 49: Quiz : IPv6 header
1- Payload includes IPv6 header, extension header & PDU (T/F)
2- Extension headers come after PDU (T/F)
3- Extension headers is part of the IPv6 main header (T/F)
4- IPv6 header has a fixed size (T/F)
5- IPv6 header size is TRIPLE the min IPv4 header size (T/F)
6- TOS is replaced by flow label in IPv6 (T/F)
7- Extension header is equivalent to padding in IPv4 (T/F)
8- All extension headers are not examined by the intermediate routers (T/F)
9- Only AH is the only extension header available to enforce IP security (T/F)
Topic 2: IPv6 Concepts
Notes: Answer:
1- False, payload shouldn’t include IPv6 header
2- False, the extension headers should come before PDU
3- False, extension header is part of payload and not IPv6 main header
4- True, IPv6 header has a fixed size of 20 bytes
5- False, IPv6 header is DOUBLE the min IPv4 header size
6- True, flow label replaces the TOS
7- False, extension header is equivalent to option
8- False, only hop-by-hop extension header is examined by the intermediate routers
9- False, ESP is the other extension header used for IPsec implementation

## Slide 50: Section 3: Fragmentation
IPv6 fragmentation & reassembly is an end-to-end function
Routers do not fragment packets BUT only send the ICMP “message too big”(with the new MTU size) using the Path MTU Discovery feature
Advantage:
- better router performance; that is intermediate routers don’t have to check for the fragmentation fields (identification + flags + fragment offset fields) every time the packets pass through them
Topic 2: IPv6 Concepts
Notes: IPv4 allows fragmentation to be done at any point in the path, both intermediate routers and host. However, in IPv6, only source node is allow to fragmentize. By removing the fragmentation field(identification, flag and fragment offset), IPv6 has more streamlined packet header and allows better router performance. Today's networks generally support frame sizes that are large enough to carry typical IP packets without fragmentation. However if required, an optional extension header can be used by source nodes to divide packets into an arbitrary number of smaller units.
The source will fragment and eventually transmit the minimum MTU along the path from source to the destination(recall path MTU discovery process). For instance, if two FDDI networks with 4500-byte MTUs are connected by an Ethernet with an MTU of 1500, then the source station must send packets that are no larger than 1500.
If higher level applications are using larger payloads, the source node can make use of the IPv6 fragmentation extension header to divide large packets into 1500-byte units for network transmission. The IPv6 destination node will reassemble these fragments in a manner that is transparent to upper layer protocols and applications.End nodes performing fragmentation can determine the smallest MTU of a path with the MTU path discovery process

## Slide 51: Path MTU discovery
For packets bigger than 1280 bytes, path MTU discovery is expected:
start by assuming MTU of the first-hop link
if a packet reaches a link which couldn’t fit, an ICMP “packet too big” is generated and sent back to the source
then the source will fragmentize the packet into smaller chunks (following this new MTU size) and start this process all over again
FDDI
MTU=4500
Ethernet
MTU=1500
Source
Destination
FDDI
MTU=4500
FDDI
MTU=4500
ICMP “packet too big”
Topic 2: IPv6 Concepts
A
B
Notes: Link MTU is a link’s maximum transmission unit, that is the biggest IP packet size that can be transmitted over a specific link. Path MTU is the minimum MTU for all the links in a path between a source and a destination
IPv6 requires that the link layer support a minimum IPv6 packet size of 1280 bytes(68 bytes in IPv4). Link layers that do not support this must provide a link layer fragmentation and reassembly scheme that is transparent to IPv6. For link layers that can support a configurable MTU size, it is recommended that they be configured with an MTU size of at least 1500 bytes (the Ethernet II encapsulation IPv6 MTU). IPv6 source hosts can fragment payloads of upper layer protocols that are larger than the path MTU by using the Fragment header. However, the use of IPv6 fragmentation is highly discouraged. An IPv6 node must be able to reassemble a fragmented packet that is at least 1500 bytes in size.
In Path MTU Discovery, the source node sends out a packet with an MTU as large as the local interface can handle. If this MTU is too large for some link along the path, an ICMP "Datagram too big" message will be sent back to the source. This message will contain a packet-too-big indicator and the MTU of the affected link. The source can then chops the packet to smaller chunks(fragment) and retransmit this chunk. This process is repeated until a packet gets all the way to the destination node. The discovered MTU is then used for fragmentation purposes. Although source-based fragmentation is fully supported in IPv6, it is recommended that network applications adjust packet size to accommodate the smallest MTU of the path. This will avoid the overhead associated with fragmentation and reassembly on source and destination nodes.

## Slide 52: Quiz: MTU/Fragmentation
1- In path MTU discovery process:
a) Router with smaller MTU(than the transmitted packets), chops this
packet into smaller chunks (T/F)
b) Router with smaller MTU replies with error & new MTU size info
to destination host(T/F)
c) Upon sending the packet for the 1st time, source host uses the
MTU of the destination(T/F)
d) Source host fragments the packets based on the destination’s link
MTU (T/F)
2- Ethernet MTU size is 4500 (T/F)
3- IPv6 requires min MTU of 1820(T/F)
4- Every packet bigger than 1500 bytes MUST be fragmented (T/F)
5- IPv6 uses its identification, flags and fragment offsets header
fields in the fragmentation and reassembly process (T/F)
Topic 2: IPv6 Concepts
Notes: Answer:
1-a) False, router does not chop the packet into smaller chunks
b) False, the error should be delivered to source host
c) False, the source host uses the MTU of the next hop
d) False, the source host fragments based on the min MTU found
along the path way(no necessarily based on the destination’s MTU)
2- False, Ethernet MTU size is 1500 bytes
3- False, IPv6 requires min MTU of 1280 bytes
4- False, only fragment if there is a MTU size smaller than 1500 bytes along the path
from host to destination
5- False, IPv6 doesn’t have these fragmentation fields in its header

## Slide 53: Section 4: IPv6 Addressing
IPv6 Address Space
IPv6 Address Syntax
Types of IPv6 addresses
Topic 2: IPv6 Concepts

## Slide 54: Address space
128-bit or 16 bytes
2^128=340,282,366,920,938,463,463,374,607,431,768,211,456
4.2 x 10^9 versus 3.4 x 10^38 addresses
Note:
IPv4 allows 1 IP for every 2 persons, but IPv6 offers ~5.6 x
10^28 per person(out of 6 billions population -- 6 x 10^9)
Topic 2: IPv6 Concepts
IPv4
IPv6
IPv4 Address space
192.228.134.34
32-bit
IPv6 Address Space
3FFE:90:AD:23:112:9:56:210
128-bit
Notes: The most obvious distinguishing feature of IPv6 is its use of much larger addresses. The size of an address in IPv6 is 128 bits, which is four times the larger than an address in IPv4. A 32-bit address space allows for 4,294,967,296(4 billions) addresses. Meanwhile a 128-bit address space allows for 340,282,266,920,938,463,463,374,607,431,768,211,465 (or 3.4 x 1038) addresses. In brief, we can say that IPv6 provides 655,570,793,348,866,943,898,599 (6.5 x 1023) addresses for every square meter of the Earth’s surface.
It is important to note that IPv6 address being enlarged to 128-bit not only to provide bigger address space but also designed to be subdivided into hierarchical routing domains that reflect the topology of the modern-day Internet. The use of 128 bits allows for multiple levels of hierarchy and flexibility in designing hierarchical addressing and routing that is currently lacking on the IPv4-based Internet.

## Slide 55: Address syntax: preferred
Hexadecimal values of the eight 16-bit pieces, separated by colon
Example:
FE78:3450:BED8:9542:FEDC:BA09:1236:763C
3FFE:0:0:0:13:45D:432:1A
X:X:X:X:X:X:X:X
Topic 2: IPv6 Concepts
X = 16-bit numbers
e.g. A3BF or FFFE
Notes: In IPv6, the 128-bit address is divided along 16-bit boundaries, and each 16-bit block is converted to a 4-digit hexadecimal number and separated by colons. The following is an example of Pv6 address => 21DA:00D3:0000:0000:02AA:00FF:FE28:9C5A. Zero compression can then be used to compress this expression to => 21DA:00D3::02AA:00FF:FE28:9C5A.

## Slide 56: Address syntax: compressed
Compressed form=> “::” indicates multiple groups of 16-bits of zeros
4A80:0:0:0:5:800:50CA:290D => 4A80::5:800:50CA:290D
FE80:0:0:0:0:0:0:349 => FE80::349
4D0A:0:0:89:0:0:236:8009 => 4D0A::89:0:0:23:8009 or
4D0A:0:0:89::23:8009
0:0:0:0:0:0:0:1 => ::1
Note:
Except 2 types of IPv6 addresses have different representation (IPv4-compatible and IPv4-mapped)
Topic 2: IPv6 Concepts
Notes: To determine how many 0 bits are represented by the “::”, you can count the number of blocks in the compressed address, subtract this number from 8, and then multiply the result by 16. For example, in the address FF02::2, there are two blocks (the “FF02” block and the “2” block.) The number of bits expressed by the “::” is 96 ((8-2) x 16 = 96).
Zero compression can only be used once in a given address. Otherwise, you could not determine the number of 0 bits represented by each instance of “::”.

## Slide 57: Address type
Anycast : defines a number of recipients
A packet sent to an anycast address is delivered to one of the
interfaces (the working nearest interface)
There are 3 types of addresses:
Unicast : defines a single recipient
A packet sent to a unicast address is delivered to the interface
identified by that address
Multicast : defines a number of recipients
A packet sent to a muticast address is delivered to all of the
interfaces identified by that address
Topic 2: IPv6 Concepts
Notes: Unicast is a name for one-to-one address, that is it identifies exactly one interface. A packet sent to a unicast address will normally be delivered to that interface.
Multicast is a name for one-to-many address, that is it identifies a group of interfaces. A packet sent to a multicast address will normally be delivered to all the members of the group.
Anycast is a name for one-to-nearest address, that is it identifies a group of interfaces. The difference between multicast and anycast is in the transmission process. Instead of being delivered to all members of the group, packet sent to anycast address is normally delivered to only one interface and that is the nearest member in the group.

## Slide 58: Address allocation
Global unicast 001 2xxx or 3xxx
Site-local unicast 1111 1110 11 FECx .... FEFx
IPv4-compatible unicast 000...0(96 zero bits) 0:0:0:0:0:0:n.n.n.n
Multicast 1111 1111 FFxx
Reserved IPX 0000 010 04xx or 05xx
Allocation
Binary prefix
Link-local unicast 1111 1110 10 FE8x ... FEBx
All other binary prefix are reserved for future use
Anycast addresses are allocated from the unicast prefixes
Example
(the first 16-bit)
Topic 2: IPv6 Concepts
Prefix is used to identify type of IPv6 address; normally
the first 16 bits(or first 2 bytes)
IPv4-mapped unicast 000..FFFF(80 zero bits) 0:0:0:0:0:FFFF:n.n.n.n
Notes: Binary prefix or known as Format Prefix(FP), is the set of leading bits indicating specific type of an IPv6 address(i.e. global unicast,multicast). For example, 2001: 89A:97::FFEA is a global unicast type of address for its leading bits is “0010”. The same goes to 3FFE:80D0:900::30 that has “0011” for its first 16-bit address. An address of FF02::1:360:89 belongs to the multicast address since the first two 16-bit of it starts with “1111 1111”.

## Slide 59: Aggregatable global unicast
This hierarchical structure improves backbone routing; it
sorts traffic towards networks attached to the Internet
backbone
Without an address hierarchy, backbone routers have to
store route table information on the reachability of every
network in the world
FP
TLA ID
RES
NLA ID
SLA ID
Interface ID
Public Topology
Topology
Site
Interface ID
13
3
8
24
Topic 2: IPv6 Concepts
FP = Format Prefix
TLA= Top Level Aggregation SLA = Site-Level Aggregation
NLA= Next-Level Aggregation RES= Reserved
Global unicast 001 2xxx or 3xxx
Allocation Binary Prefix Example
Notes: Details of the fields is as followings:
TLA ID [13 bits]– Identifies the highest level in the routing hierarchy which are to be given to large, long haul Internet service providers (ISPs). This 13-bit field allows up to 8,192 different TLAs, which is nice enough(less than 10K routes), for this numbers would determine the backbone routing size.
RES [8 bits]- Reserved for future use, either by TLA or NLA.
NLA ID[24 bits]– Identifies a specific customer site. It allows an ISP to create multiple levels of addressing hierarchy within a network to both organize addressing and routing for downstream ISPs and identify sites.
SLA ID[16 bits] –Identifies subnets within its site. With 16 bits of subnetting flexibility, an aggregatable global unicast prefix assigned to an organization is equivalent to that organization being allocated an IPv4 Class A network.
Interface ID – Indicates the interface on a specific subnet. The size of this field is 64 bits.

## Slide 60: Aggregatable global unicast cont’
Topic 2: IPv6 Concepts
TOP
TOP
Next Level
Next Level
Next Level
Site Level
Interface ID
Public
Topology
( providers/exchanges )
Site
Topology
(LAN)
Interface ID
(link)
Notes: Aggregatable global unicast addresses are equivalent to public IPv4 addresses. They are globally routable and reachable on IPv6 network or known as the 6bone (IPv6 backbone). It is designed to be aggregated(summarized) to produce an efficient routing infrastructure. Unlike the current IPv4-based Internet, which is a mixture of both flat and hierarchical routing, the IPv6-based Internet has been designed from its foundation to support efficient, hierarchical addressing and routing.
In brief, this address consists of:
public topology => a collection of larger and smaller ISPs that provide access to the IPv6 Internet,
site topology => a collection of subnets within an organization’s site and interface
identifier => identifies a specific interface on a subnet within an organization’s site.

## Slide 61: Link-local & Site-local
Link-local addresses are used during auto-configuration
while no router present
Site-local addresses are used within an isolated intranet,
independence from changes of TLA/NLA:
1111111011 0 SLA* interface ID
Topic 2: IPv6 Concepts
1111111010 0 interface ID
link-local unicast 1111 1110 10 FE8x ... FEBx
Allocation Binary Prefix Example
site-local unicast 1111 1110 11 FECx .... FEFx
e.g=>fe80::2d0:b7ff:fe11:5d36
e.g=>fec0::90:234:ffde:1098
Notes: Link-local are used by nodes when communicating with neighboring nodes on the same link. For example, on a single link IPv6 network with no router, link-local addresses are used to communicate between hosts on the link. A link-local address is always automatically configured. It always begin with FE80. With the 64-bit interface identifier, the prefix for link-local addresses is always FE80::/64. An IPv6 router never forwards link-local traffic beyond the link.
Site-local are equivalent to the IPv4 private address space (10.0.0.0/8, 172.16.0.0/12, and 192.168.0.0/16). For example, private intranets that do not have a direct, routed connection to the IPv6 Internet can use site-local addresses without the need of aggregatable global unicast addresses. Site-local addresses are not reachable from other sites, and routers must not forward site-local traffic outside the site. Unlike link-local addresses, site-local addresses are not automatically configured and must be assigned either through stateless or stateful address configuration processes(to be discussed later). It always begin with FEC0.
.

## Slide 62: IPv4-compatible & IPv4-mapped
These addresses have a mixed environment of IPv4 and
IPv6 addresses:
0:0:0:0:0:0:192.226.124.45 => ::192.226.124.45
0:0:0:0:0:FFFF:192.226.124.45 => ::FFFF:192.226.124.45
Topic 2: IPv6 Concepts
1) IPv4-compatible IPv6 address
technique for hosts and routers to dynamically tunnel IPv6 packets
over IPv4 routing infrastructure
2) IPv4-mapped IPv6 address
represent the addresses of IPv4-only nodes(those that do not
support IPv6) as IPv6 addresses
IPv4-compatible 00..(96 bits of zero) 0:0:0:0:0:0:n.n.n.n
Allocation Binary Prefix Example
IPv4-mapped 00..ffff(80 bits of zero) 0:0:0:0:0:ffff:n.n.n.n
Notes: To aid in the migration from IPv4 to IPv6 and the coexistence of both types of hosts, the following addresses are defined:
The IPv4-compatible address, 0:0:0:0:0:0:w.x.y.z or ::w.x.y.z (where w.x.y.z is the dotted decimal representation of an IPv4 address), is used by dual-stack nodes that are communicating with IPv6 over an IPv4 infrastructure. Dual-stack nodes are nodes with both IPv4 and IPv6 protocols. When the IPv4-compatible address is used as an IPv6 destination, the IPv6 traffic is automatically encapsulated with an IPv4 header and sent to the destination using the IPv4 infrastructure.
The IPv4-mapped address, 0:0:0:0:0:FFFF:w.x.y.z or ::FFFF:w.x.y.z, is used to represent an IPv4-only node to an IPv6 node. It is used only for internal representation. The IPv4-mapped address is never used as a source or destination address of an IPv6 packet.

## Slide 63: Special Addresses
0:0:0:0:0:0:0:0 => ::
Unspecified address
used as a source address by a station that has not yet been configured
with other type of addresses
0:0:0:0:0:0:0:1 => ::1
Topic 2: IPv6 Concepts
Loopback address
used by a node to send an IPv6 datagram to itself
Notes: The following are special IPv6 addresses:
The unspecified address (0:0:0:0:0:0:0:0 or ::) is only used to indicate the absence of an address. It is equivalent to the IPv4 unspecified address of 0.0.0.0. The unspecified address is typically used as a source address for packets attempting to verify the uniqueness of a tentative address. The unspecified address is never assigned to an interface or used as a destination address.
The loopback address (0:0:0:0:0:0:0:1 or ::1) is used to identify a loopback interface, enabling node to send packets to itself. It is equivalent to the IPv4 loopback address of 127.0.0.1. Packets addressed to the loopback address must never be sent on a link or forwarded by an IPv6 router.

## Slide 64: Anycast address
Anycast allocated from the unicast address space;
syntactically indistinguishable from unicast address
An unicast address assigned to more than one interfaces
becomes anycast address; the nodes to which the
address is assigned must be explicitly configured to know
that it is an anycast address
It cannot be a source address
Topic 2: IPv6 Concepts
Notes: An anycast address is assigned to multiple interfaces. Packets addressed to an anycast address are forwarded by the routing protocol to the nearest interface to which the anycast address is assigned. In order to facilitate delivery, the routing protocol must be aware of the interfaces assigned anycast addresses and their “distance” in terms of routing metrics. At present, anycast addresses are only used as destination addresses and are only assigned to routers. Anycast addresses are assigned out of the unicast address space and the scope of an anycast address is the scope of the type of unicast address from which the anycast address is assigned.

## Slide 65: Multicast address
Multicast identifies a group of nodes; specifically identifies
a set of interfaces that usually belong to different nodes.
11111111 flags scope group ID
Low-order flag: indicates permanent(well-known) or non-permanent
(transient) group
Scope value: limits the scope of multicast group, i.e. node-local,link-
local,site-local, community-local, organization-local,
global etc
Topic 2: IPv6 Concepts
Multicast 1111 1111 FFxx
Allocation Binary Prefix Example
Notes: In IPv6, multicast traffic operates in the same way as it does in IPv4. Arbitrarily located IPv6 nodes can listen for multicast traffic on an arbitrary IPv6 multicast address. IPv6 nodes can listen to multiple multicast addresses at the same time. Nodes can join or leave a multicast group at any time.
An IPv6 address is easy to classify as multicast because it always begins with “FF”. Multicast addresses cannot be used as source addresses or as intermediate destinations in a Routing header.

## Slide 66: Section 5: Routing
No new structure being introduced in IPv6 routing
Uses the IPv4 CIDR method; which relies on the IPv6
address architecture(hierarchical)
Changes the existing IPv4 routing protocols to handle bigger address e.g. OSPF, RIP, BGP4+
Topic 2: IPv6 Concepts
TOP
TOP
Next Level
Next Level
Next Level
Site
Host
link
Top Level 2^13 = 8,192
Notes: IPv6 routing does not differ much from existing routing.

## Slide 67: Section 6: Outstanding Features
Security
Quality of Service (QoS)
Auto-configuration
Topic 2: IPv6 Concepts

## Slide 68: Security
All implementation are expected to support authentication and encryption headers (IPsec)
IPsec protects the network layer, that provides:
- authenticity
- integrity
- confidentiality
IPsec uses the Encapsulating Security Payload(ESP)
and Authentication Header(AH); part of extension headers
The security can cover communications between two
host, two networks or between a host and a network
Topic 2: IPv6 Concepts
Extension Headers
(ESP and/or AH)
Higher-level protocol header
+ application content
IPv6 Header
IPv6 packet
Notes: IPsec is a combination of protocols that offers security over IP networks. It works at the IP layer, protecting all the upper layer protocol, i.e. UDP, TCP, ICMP. The protocols that makes up this IPsec suite are the Internet Key Exchange(IKE), the Authentication Header(AH) and the Encapsulating Security Payload(ESP). It also uses the concept of Security Associations (SA). The security services that IPsec offers include confidentiality, authentication, integrity, access control and partial against traffic flow analysis.
AH is designed to protect the integrity of the whole datagram and to check that its content has not been modified in transit. However, AH does not transform data; whereby data remain unsave or vulnerable to sniffers’ attacks. ESP is used when confidentiality is desired; data been scrambled up using certain algorithm.
IPsec can be implemented between host-to-host, security gateway-to-security gateway or host-to-security gateway environment. A host can be any of network device such as a computer or router or firewall. A firewall however can also be a security gateway. The difference between a host and security gateway is defined on how IPsec is used by the network device. If the device is used to secure communication between itself and another IPsec node, then it is considered as host. If the device is used to secure communications coming from and going to a network segment, that is is a security gateway.

## Slide 69: How IPSec work?
Security
Gateway B
Security Gateway A
Public IP
Network
Gateway A
Secret: abcdefg
Policies:
Local 192.228.140.0 ESP,3DES,MD5
Remote 10.0.0.0, tunnel security gateway B
192.228.140.0
10.0.0.0
10.0.0.2
10.0.0.1
Gateway B
Secret: abcdefg
Policies:
Local 10.0.0.0 ESP,3DES,MD5
Remote 192.228.140.0, tunnel security gateway B
Topic 2: IPv6 Concepts
Note:
This IPsec tunnel is built between network and network
scenario
Notes: Step-by-step:
1- Security gateway A and B exchange the secrets information, in this case abcdefg.
2- Then, the policies is created, through the key distribution protocol; the Internet Key Exchange(IKE) protocol.
3- Then a secure negotiation channel is established, in which secrets of the gateways are compared to verify each other’s identities.
4- Using this secure channel, the association is created, in which the two security gateways decide which authentication and/or encryption algorithm to use, which key(s) to use and for how long before they exchange a new key. As shown in the above slide, the gateways will use 3DE for encryption and MD5 for authentication.
5- Lastly, we have an active session between both gateways; whereby IPv6 packets will be secured by ESP for encryption and AH for for authentication.

## Slide 70: Authentication header
destination address + SPI identifies Security Association(key, lifetime,
algorithm, etc)
provides authentication and data integrity for IPv6 packets that do not change en-route(source and destination are not allowed to change during the transit)
default algorithm is keyed MD5; computing the hash code of combination of message & the secret key
Authenticated
IP
Header
Data
TCP
AH
0
7
15
23
31
Next
header
Payload
Length
Reserved
Security Parameters Index (SPI)
Sequence number
Authentication data
Topic 2: IPv6 Concepts
Notes: AH provides:
- data origin authentication(authentication data is the digital signature for the packets)
- connectionless integrity(authentication data contains the Integrity Check Value(ICV) mechanism)
- protection against replay attacks(sequence numbering protects against replay attacks)
AH is the simplest of the two protocols, offering the above-mentioned security services. The use of AH is determined by the Security Associations negotiated between the two IPsec nodes (during policy setup). In the security descriptors, there will be a section that defines which parameters to be used with AH, i.e. the authentication algorithm. These two nodes will then initiate the IKE session and when this session is completed, the two nodes will use AH. During this active duration(within the defined lifetime), AH header is to be added in every IP packet transmitting across these nodes. This header will authenticate the packet, assuring the receiver of the legitimate source of the packet.

## Slide 71: ESP header
Authenticated
IP
Header
ESP
Trailer
TCP
Data
ESP
Auth
data
Encrypted
0
7
15
23
31
Next header
Payload Data
Padding
Security Parameters Index (SPI)
Sequence number
Authentication data
Pad length
Topic 2: IPv6 Concepts
ESP encrypts the payload data & hides the traffic between the two nodes
ESP provides authentication as well(but exclude IP header)
default algorithm is DES-CBS
Notes: The encapsulating security payload is the second of the two security protocols offered by the IPsec suite. It provides:
- confidentiality
-data origin authentication
-connectionless integrity
- protection against replay attacks(option)
-limited traffic flow confidentiality
ESP offers more security services than AH. Like AH, it does provide authentication, but it doesn’t cover the IP header. The authentication is provided through one-way hash functions or manual key exchanges. The confidentiality is provide through encryption. The connectionless integrity is provided through the authentication service. Sequence numbering of each packet protects against the replay attacks. The encryption of the payload data and therefore hides the amount of traffic exchanged between two IPsec nodes.

## Slide 72: Real time support
Applications reserve resources in advance via Flow Label.
Flow 1
Flow 2
Workstation
PC
File
Server
Multimedia
Server
All packets belongs to the same flow must be sent with the
same source/destination address, traffic class and flow label
Topic 2: IPv6 Concepts
Notes: New fields in the IPv6 header define how traffic is handled and identified. Traffic identification using a Flow Label field in the IPv6 header allows routers to identify and provide special handling for packets belonging to a flow, a series of packets between a source and destination. Because the traffic is identified in the IPv6 header, support for QoS can be achieved even when the packet payload is encrypted through IPsec
.

## Slide 73: Auto configuration
Auto configuration allows hosts to fabricate their own addresses,
with or without DHCP server.
It is part of the the Neighbor Discovery(ND; messages and
processes that determine relationships between neighboring
nodes.
Message types(ICMP):
- router solicitation
- router advertisement: periodically announces the prefix info(among others)
- neighbor solicitation
- neighbor advertisement
- redirected
Processes:
- router discovery(similar to ICMPv4 Router Discovery)
- prefix discovery (similar to ICMPv4 Address Mask Request/Reply)
- autoconfiguration of address & other parameters
- duplicate address detection
- neighbor unreachability detection
- link-layer address resoultion (similar to ARP in IPv4)
- first hop redirect(similar to the IPv4 ICMP Redirect message)
Topic 2: IPv6 Concepts
Notes: router advertisement: router periodically advertises its prefix and other info to all-nodes
router solicitation: sent only at host start-up, to solicit immediate router advert.
neighbor solicitation: for address resolution, sent to “solicited node”
neighbor advertisement: for address resolution, sent to unicast address of solicitor
Router discovery; a host discovers the local routers on an attached link
Prefix discovery; hosts discover the network prefixes for local link destinations
Parameter discovery; hosts discover additional operating parameters, including the link MTU and the default hop limit for outgoing packets.
Address auto configuration; the process for configuring IP addresses for interfaces in either the presence or absence of a stateful address configuration server such as DHCPv6.
Address resolution; nodes resolve a neighbor’s IPv6 address to its link-layer address,
Next-hop determination; node determines the IPv6 address of the neighbor to which a packet is being forwarded based on the destination address. The forwarding or next-hop address is either the destination address or the address of an on-link default router.
Neighbor unreachability detection; a node determines that the IPv6 layer of a neighbor is no longer receiving packets.
Duplicate address detection; node determines that an address considered for use is not already in use by a neighboring node, similar to using gratuitous ARP frames in IPv4.
Redirect function; process of informing a host of a better first-hop IPv6 address to reach a destination.

## Slide 74: Auto configuration ‘cont
“Plug and play” feature
Stateless mode :
Stateful server mode :
via ICMP (no server required)
via DHCP
Prefix
3ffe:89::/64
+
Link Address
00:A87:C09:1BE:CC7:BA
=
IPv6 Address
3ffe:89::A87:C09:1BE:CC7:BA
DHCP
server
00:A87:C09:1BE:CC7:BA
DHCP request
router advertisement
3ffe:89::A87:C09:1BE:CC7:BA
DHCP response
Topic 2: IPv6 Concepts
Notes: Stateless auto configuration allows host to automatically learn the subnet prefix from the nearest router(through router advertisement) and fabricate its own address by adding to its interface ID(refer above). Automatic renumbering is also supported, whereby with new subnet prefixes added, the old address will be replaced by the new one; the one with new prefix but with same interface ID.
Stateful auto configuration can be overridden by the use of DHCP. Hosts will send out the DHCP request to the available DHCP server and only then be allocated with IPv6 address. This mode of operation is provided to those who are not keen of the “plug-n-play” idea.
Things to ponder
Current implementation of auto configuration is lacking of security, whereby anybody who plugs in his/her laptop is given the right to access the network, without any authentication process. There is a need to improve this phenomenon and there are few areas that need to be looked into, including:
1- How can we assure that the router advertisements come from an authorized router?
2- How can we assure that the neighbor advertisements come from an authorized
host?

## Slide 75: TOPIC 3: Migration Technique
Topic 3: Migration Technique
Notes: Migrating of IPv4 to IPv6 is a gradual implementation. This is to avoid from totally scraping out huge IPv4 network which will be costly to organisations. Step by step transition techniques will be listed in next slide. IPv4 network IPv6 will be deployed in parallel to the existing IPv4 network , possibly by borrowing some of its infrastructure.

## Slide 76: Objectives
Migration Step
Migration Techniques
Topic 3: Migration Technique
Notes: The Objective is to get participant to understand every step of the transition process.
The objective of this transition is :
- to allow IPv6 and IPv4 hosts to inter-operate.
- to allow incremental deployment of hosts and routers
- to make transition as easy as possible for end-users, other network and system administrators and network operators.

## Slide 77: Section 1: Migration Steps
Topic 3: Migration Technique
1. Upgrade DNS to support IPv6 stack
2. Install host with dual stack to support both IPv6 and IPv4 host
3. Configure router to support IPv6/IPv4 Tunnel
4. Rely on IPv4 Header Translation only
5. Remove IPv4 Support
Notes: Migration Steps will show the step-by step procedure to move from IPv4 to IPv6 network.

## Slide 78: Section 2: Migration Techniques
Dual Stack Host
Tunneling
Translation
Topic 3: Migration Technique
Notes: Tunneling is the next step in order to connect IPv6 island through IPv4 oceans. Tunneling works by encapsulating/wrapping the IPv6 packet
into the IPv4 packets and send this packet through the IPv4
network.
Automatic Tunnelling
Configured Tunneling

## Slide 79: Dual stack host
Support both IPv4 and IPv6
Determine stack via DNS
Application
TCP
IPv4
IPv6
Ethernet
Dual Stack Host
IPv4
IPv6
Topic 3: Migration Technique
Notes: The dual-stack strategy relies heavily on the Domain Name Service (DNS). Dual stack host will have both Ipv4 and IPv6 stack co-exist on the same machine. DNS will check the record type either A type (for IPv4) or AAAA for IPv6 stack, then it will decide to use IPv4 or IPv6 stack.
Critical Point here is that dual-stack transition assumes that name service already updated to support AAAA records.

## Slide 80: Automatic tunneling
……
IPv4
IPv6
IPv4
IPv6
src = ::1.2.3.4 (IPv4-compatible IPv6 adr)
dst = ::2.3.4.5 (IPv4-compatible IPv6 adr)
6
traffic
flow label
payload len
next
hops
payload
flow label
6
traffic
payload len
next
hops
payload
4
frag
off
ident
src = ::1.2.3.4
dst = ::2.3.4.5
TTL
prot
checksum
src = ::1.2.3.4 (IPv4-compatible IPv6 adr)
dst = ::2.3.4.5 (IPv4-compatible IPv6 adr)
flow label
6
traffic
payload len
next
hops
payload
4
frag
off
ident
src = ::1.2.3.4
dst = ::2.3.4.5
TTL
prot
checksum
src = ::1.2.3.4 (IPv4-compatible IPv6 adr)
dst = ::2.3.4.5 (IPv4-compatible IPv6 adr)
2.3.4.5
2.3.4.5
2.3.4.5
IPv6 host ::1.2.3.4
IPv4 network
IPv4/6 host
2.3.4.5
Encapsulate IPv6 packet in Ipv4
rely on IPv4-compatible IPv6 address
hl
TOS
len
hl
TOS
len
Topic 3: Migration Technique
Notes: Automatic Tunneling - (host to host or host to router) IPv6 packet is encapsulated in an IPv4 header that is address to an IPv6 destination. The encapsulated packet is transmitted across the IPv4 router to the IPv6 destination node. Example you have tunnel broker (Freenet)

## Slide 81: Configured tunneling
……
IPv4
IPv6
IPv4
IPv6
src = 2001::A:A:B (IPv6 adr)
dst = 2001::B:B:C (IPv6 adr)
6
traffic
flow label
payload len
next
hops
payload
flow label
6
traffic
payload len
next
hops
payload
4
frag
off
ident
src = R1
dst = R2
TTL
prot
checksum
src = 2001::A:A:B (IPv6 adr)
dst = 2001::B:B:C (IPv6 adr)
2001::B:B:C
IPv6 host 2001::A:A:B
IPv4 network
IPv6 host
2001::B:B:C
Encapsulate IPv6 packet in Ipv4
IPv6 only address
hl
TOS
len
2001::B:B:C
R1
R2
src = 2001::A:A:B (IPv6 adr)
dst = 2001::B:B:C (IPv6 adr)
6
traffic
flow label
payload len
next
hops
payload
Topic 3: Migration Technique
Notes: Configured Tunneling - Connection between router to router or host to router. Router will encapsulate IPv6 packets into IPv4 format and transmit it across the router. And router at the other end will decapsulate the packets and send Ipv6 packets to destination host, IPv6 nodes.

## Slide 82
Translation
IPv6-IPv4 Translation
Translating both the network address and protocol from IPv6 to IPv4 and vice versa
IPv6-only
devices
IPv4-only and dual-
stack devices
NAT-PT
Topic 3: Migration Technique
Notes: This is a simple NAT techniques which will translate IPv6 to IPv4 and vice versa. In this scenario you can have IPv6 only devices talking to IPv4 only devices.

## Slide 83: TOPIC 4: Implementation & Deployment
Topic 4: Implementation & Deployment

## Slide 84: Objectives
IPv6 Initiative
Topic 4: Implementation & Deployment

## Slide 85: Section 1: IPv6 Initiative
IPv6 Specification
IPv6 Implementation
IPV6 Deployment
Miscellaneous
Topic 4: Implementation & Deployment

## Slide 86: Specification
the development is coordinated by IETF, specifically by IPv6/IPng Working Group
a number of IPv6 specifications have already become IETF Draft Standards; well-tested and proven stable
Visit: http://playground.sun.com/ipng/specs/standards.html
others are proposals; with more new standards coming along
Visit: http://playground.sun.com/ipng/specs/specifications.html
discussion on specifications are carried out in mailing lists such as: ipng@sunroof.eng.sun.com or users@ipv6.org
Topic 4: Implementation & Deployment

## Slide 87: Implementation
most IP stack vendors are actively working towards
fully supporting IPv6
router: 3com, Nortel, CISCO, Hitachi, Telebit, Zebra
host : IBM, HP, Kame, BSDI, Sun, Microsoft, Linux,
OpenBSD
beta releases are common to be found and testers are
always welcome
details, visit:
“http://playground.sun.com/pub/ipng/html/ipng-implementations.html”
Topic 4: Implementation & Deployment

## Slide 88: Deployment
experimental infrastructure: 6bone
- for testing and debugging IPv6 protocols/operations
- mostly IPv6-over-IPv4 tunnels
- anybody can join : www.6bone.net
production infrastructure in support of education and
research -- www.6ren.net, www.6tap.net
commercial infrastructure -- NTT, SURFnet, IIJ, Trumpet
mailing list 6bone@isi.edu carries out discussion on IPv6 deployment
Topic 4: Implementation & Deployment

## Slide 89: 6bone
660 sites in 50 countries worldwide running IPv6 on 6bone
80 of these sites are the IPv6 backbone nodes, including
MIMOS
358
183
21
81
4
China 11
India 1
Korea 16
Malaysia 1
Taiwan 6
New Zealand 3
Kazakhstan 1
13
Topic 4: Implementation & Deployment
Note: Statistics are as of February 9,2001
Singapore 4
Hong Kong 1
Japan 40
Australia 10
Notes: 6bone is an IPv6 test bed, that supports the routing of IPv6 packets over IPv4 network, through IPv6-over-IPv4 tunnel.

## Slide 90: MANIS (Malaysian Advanced Network Integrated System)
Topic 4: Implementation & Deployment
Notes: History
May 2000 - IPv6 LAN
Jun 2000 - IPv6-over-IPv4 tunnel to freenet6.net(tunnel broker)
July 2000 - IPv6-over-IPv4 tunnel to singAREN (NLA)
Aug 2000 - IPv6-over-IPv4 tunnel to DTI, Japan (NLA)
Sep 2000 - IPv6-over-IPv4 tunnel to Viagenie, Canada (NLA)
Oct 2000 - Allocated with TLA; become an IPv6 backbone node
- IPv6-over-IPv4 tunnel to Stealth, USA
Dec 2000 - MANIS set-up
Jan 2001 - Provided IPv6 connection to local universities(University of Malaya and National University of Malaysia)

## Slide 91: TOPIC 1: IPv6 Hands-on
Topic 1: Demonstration
Notes: In this evening session, the participants will have the opportunity to do some hands-on activity. This includes, learn how to patch the hosts to support IPv6 and configuring the IPv6 network. Plus, we will show you the router configuration in doing IPv6-over-IPv4 tunneling and the feature of AAAA record(quad A) that supports IPv6 address for name server.

## Slide 92: Objectives
Step-by-step implementation
Topic 1: IPv6 Hands-on
Notes: At the completion of this section, participants will have the hands-on experience in setting up IPv6 network. The participants will have the ability to:
1- install dual stack machine(IPv4/IPv6)
2- configure IPv6 network(host and router)
3- configure IPv6 zone and reverse file(AAAA record)

## Slide 93: Section 1: Step-by-step Instructions
Host to host connectivity (LAN & WAN)
Host to router connectivity
Router to router connectivity
DNS connectivity
Topic 1: IPv6 Hands-on

## Slide 94: Some information
We will use the following OS:
OpenBSD 2.7 (IPv6 ready)
WinNT4 (not IPv6 ready)
6 PCs are allocated with OpenBSD OS and another 6 with WinNT
These machines are IPv4/IPv6 supported, refer the how to in the notes
Topic 1: IPv6 Hands-on
Notes: WinNT4
Download IPv6 stack from: http://research.microsoft.com/msripv6/license.htm
-Go to your Control Panel,->Network settings->Protocols-> Add->Select Have
DiskChoose the path where you unpacked the archive.The system will install msripv6
protocol.Reboot your system. --
-Then, check the interface by issuing command: “ipv6 if” at DOS command.
-Ping the available addresses (ping6 ::1 and fe80…)
OPENBSD(IPv6-ready)
Check your NIC, do ifconfig and check “fxp0” addresses:
Ping that IPv4 and IPv6 addresses
1) ping “ipv4”
2) ping6 “ipv6”
Loopback address->::1 equivalent to 127.0.0.1
Link Local address ->Fe80… equivalent to the MAC address(48-bit)
Exercise: Check the routing table of the machine. How?

## Slide 95
OPTION 1: Host-to-host via site local address
Go to dos prompt and type the following : C:/ ipv6 if - verify at interface fec0:: address exist
C:/ ping6 <your neighbor’s site local add>
Type the following:
%/sbin/ifconfig - verify at interface fec0:: address exist
%ping6 <your neighbor’s site local add>
Topic 1: IPv6 Hands-on
Notes: Site local address is not routable via internet. This is similar to ipv4 private address. Packets with site local address will not be forwarded by router.If we are able to ping6 our neighbor on the network, this means that the host is already up and alive.
Windows NT :
To run ipv6 command is just by using ipv6.exe file. Ipv6 if command will list out all intefaces and their configurations.
OpenBSD :
Run /sbin/ifconfig to see all interfaces and their configurations.

## Slide 96: OPTION 2: Host-to-Host via tunnel broker (freenet6)
go to www.freenet6.net , choose your OS and register
run the given script(refer to note)
ping6 your ipv6 tunnel address and end-tunnel
ping6 ipv6 site such as www.6bone.net
Topic 1: IPv6 Hands-on
A network script will be
downloaded to the host
(contains tunnel addresses,etc)
Notes: Register and choose your OS. What you need to fill is your host IPv4 address in the registration form and which country you are from. Fill the form and register.
A network script will then be downloaded to your PC. Once the script was saved in specific directory, you need to open it and check if the configuration is correct. Here, you have to check for your IPv4 address etc. In this script also, you will be given your IPv6 tunnel addresses (for your site and end tunnel).
Then run the script by double-clicking it in WindowsNT or enter command “perl <given filename>” in OpenBSD . After you have run the script, make sure that you are already connected, i.e. the tunnel is established. To ensure this :
- ping6 your tunnel address (make sure it works)
c:\ping6 <your site’s tunnel add>
%ping6 <your site’s tunnel add>
-ping6 your end-tunnel (if it works you are already connected)
c:\ping6 <your end-tunnel’s add>
%ping6 <your end-tunnel’s add>
-ping6 to ipv6 site for example www.6bone.net
c:\ping6 www.6bone.net
%ping6 -n www.6bone.net

## Slide 97: OPTION 3: Host-to-Router via global address
……
IPv4
IPv6
IPv4
IPv6
R1
R2
202.187.22.2 3ffe:80d0:fffe:17::1
202.187.22.3 3ffe:80d0:fffe:17::2
(tunnel address)
(tunnel address)
LAN
assign global address to interface on NT & OpenBSD
assign IPv6 default gateway to NT & OpenBSD
ping6 to ipv6 sites, i.e. www.6bone.net
Topic 1: IPv6 Hands-on
Notes: OpenBSD :
Configure your network configuration by executing these commands:
%/sbin/ifconfig fxp0 3ffe:80d0:60:2::2 - assign global address to the interface(i.e. fxp0)
%/sbin/route add -inet6 default 3ffe:80d0:60:2::1 - assign your IPv6 gateway,i.e. router address
(Note: Once reboot, this information is gone)
WinNT:
Go to dos command prompt and do the followings :
C:/ ipv6 adu 4/3ffe:80d0:60:2::2
C:/ ipv6 rtu ::/0 3ffe:80d0:60:2::1
(Note: This information will be lost once you reboot your machine)
After this is done, ping6 to few IPv6 sites e.g www.6bone.net
OpenBSD=> %ping6 -n www.6bone.net
WinNT => C:/ping6 www.6bone.net

## Slide 98: OPTION 4: Router-to-Router: Cisco configuration
interface Tunnel3
description Tunnel to R2
no ip address
no ip directed-broadcast
ip accounting output-packets
ipv6 enable
ipv6 address 3FFE:80D0:FFFE:17::1/64
tunnel source 202.187.22.2
tunnel destination 202.187.22.3
tunnel mode ipv6ip
interface Tunnel1
description Tunnel to R1
no ip address
no ip directed-broadcast
ip accounting output-packets
ipv6 enable
ipv6 address 3FFE:80D0:FFFE:17::2/64
tunnel source 202.187.22.3
tunnel destination 202.187.22.2
tunnel mode ipv6ip
……
IPv4
IPv6
IPv4
IPv6
R1
R2
202.187.22.2 3ffe:80d0:fffe:17::1
202.187.22.3 3ffe:80d0:fffe:17::2
(tunnel address)
(tunnel address)
ping6 both tunnel addresses to check if tunnel has been established
ping6 to other IPv6 sites e.g. www.6bone.net
Topic 1: IPv6 Hands-on
Notes: We are using Cisco router tunnel to other Cisco router with IOS 12.0(B). Above is the example of configuration commands for establishing the tunnel, in both routers. We can check if the tunnel has been established or not by entering this command:
r1# sh ipv6 tunnel
Tun Route LastInp Packets Description
0 - 00:00:10 168786 Tunneling to singAREN
1 - 00:00:11 260285 Tunnel to DTI Japan
2 - 00:00:19 394340 Tunnel to Viagene's
3 - 00:00:19 196695 Tunnel to NEL-MIMOS-ZEBRA
4 - 00:00:08 303837 Tunnel to STEALTH
After this has been established, ping6 tunnel address for both tunnel. If alive then ping6 to ipv6 site such as www.6bone.net

## Slide 99: DNS configuration
IPv6 name server uses the A6 or AAAA(quad A) record
Bind v9 supports A6 while bind v8.2.2-P5 supports AAAA
Given this scenario: Domain : apricot-ipv6.my IP meg : 204.33.14.36 3ffe:400:107:2::36 IP ryan : 204.33.14.37 3ffe:400:107:2::37
Configuration files involved:
/etc/named.conf, /var/named/”mydomain”,/var/named/”reversefile”
Topic 1: IPv6 Hands-on
Testing:
% nslookup
> britney.manis.net.my
> set q=any
> britney.manis.net.my
Notes: 1- add in /etc/named.conf
zone "1.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.ip6.int"
{ type master; file "localhost"; };
zone ”apricot-ipv6.my”
{ type master; file ”apricot-ipv6.my"; };
zone "4.0.e.f.f.3.ip6.int"
{ type master; file "3ffe:04"; };
2- add in /var/named/apricot-ipv6.my(zone file)
meg IN A 204.33.14.36
IN AAAA 3FFE:400:107:2::36
ryan IN A 204.33.14.37
IN AAAA 3FFE:400:107:2::37
3- add in /var/named/3ffe:400(reverse file)
$ORIGIN 4.0.e.f.f.3.ip6.int.
6.3.0.0.0.0.0.0.0.0.0.0.0.0.0.0.2.0.0.0.7.0.1.0.0.0 IN PTR meg.apricot-ipv6.my.
7.3.0.0.0.0.0.0.0.0.0.0.0.0.0.0.2.0.0.0.7.0.1.0.0.0 IN PTR ryan.apricot-ipv6.my.

## Slide 100: Conclusion
All in all, IPv6 improves existing IP in many ways. Hopefully, by attending this tutorial, every participant would find the significance of IPv6 and therefore, does not hesitate to move towards this new much improved network.
Dead End
IPv4 is coming to its end and the way forward is IPv6

## Slide 101: References
Books TCP/IP Illustrated Volume 1, The Protocols, Richard Stevens, Addison-Wesley 2000 IPv6: The new Internet Protocol , Christian Huitema, Prentice Hall, 1997 IPv6 Networks: Marcus Goncalves & Kitty Niles, McGraw Hill, 1998 IPv6: The New Version of the Internet Protocol, Steve Deering, APRICOT2000
WWW www.6bone.net www.microsoft.com www.playground.sun.com www.manis.net.my www.cbe.ku.ac.th/~nguan/resource/slide/network.html
RFCs RFC 2373: Internet Version 6 Addressing Architecture, July 1998 RFC 2460: Internet Protocol Version 6(IPv6) Specification, Dec 1998 RFC 2461: Neighbor Discovery for IP Version 6 (IPv6), Dec 1998 RFC 2462: IPv6 Stateless Address Autoconfiguration, Dec 1998 RFC 2471: IPv6 Testing Address Allocation, Dec 1998