## Slide 1: Diff-Serv-aware Traffic Engineering and its Applications

## Slide 2
Author
Francois Le Faucheur
Cisco Systems
flefauch@cisco.com
Presenter
Darren Patterson
Cisco Systems
dapatter@cisco.com

## Slide 3: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class TE
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 4: Diff-Serv support over MPLS
Diff-Serv is supported over MPLS <draft-ietf-mpls-diff-ext-07.txt>
Example above illustrates support of EF and AF1 on single E-LSP
  EF and AF1 packets travel on single LSP (single label) but are enqueued in different queues (different EXP values)
E-LSP
LSR
LDP/RSVP
LDP/RSVP
EF
AF1
Notes: <number>

## Slide 5: MPLS Traffic Engineering
Find route & set-up tunnel for 20 Mb/s from POP1 to POP4
Find route & set-up tunnel for 10 Mb/s from POP2 to POP4
POP4
POP
POP
POP
POP2
POP1
WAN area
Notes: <number>

## Slide 6: Relationship between MPLS TE and QoS
MPLS TE designed as tool to improve backbone efficiency independently of QoS:
  MPLS TE compute routes for aggregates across all PHBs
  MPLS TE performs admission control over “global” bandwidth pool for all COS/PHBs (i.e., unaware of bandwidth allocated to each queue)
MPLS TE and MPLS Diff-Serv:
  can run simultaneously
  can provide their own benefit (ie TE distributes aggregate load, Diff-Serv provides differentiation)
  are unaware of each other (TE cannot provide its benefit on a per class basis such as CAC and constraint based routing)

## Slide 7: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class TE
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 8: Delay/Load Trade-Off
Percentage
Priority
Traffic
Delay
0%
100%
 %
Voice
Target
Data
Premium
Target
Good
Best-Effort
Target
If I can keep EF traffic <  % , I will keep EF delay under M1 ms
If I can keep AF1 traffic <  % , I will keep AF1 delay under M2 ms
 %

## Slide 9: Motivation for DS-aware TE
Thus, with Diffserv, there are additional constraints to ensure the QoS of each class:
  Good EF behavior requires that aggregate EF traffic is less than small  % of link
  Good AF behaviors requires that aggregate AF traffic is less than reasonable  % of link
=>Can not be enforced by current aggregate TE
=> Requires Diff-Serv aware TE
- Constraint Based Routing per Class with different bandwidth constraints
- Admission Control per Class over different bandwidth pools (ie bandwidth allocated to class queue)

## Slide 10: Motivation for DS-aware TE
In networks which are largely over-provisioned everywhere, DS-aware TE is not useful
  because aggregate load is small percentage of link anyway, EF traffic will be less than  % of link and AF1 traffic will be less than  % of link
In networks where some parts are not over-provisioned, DS-aware TE is useful
  ensures(*) (through CBR and CAC) that EF traffic will be less than  % of link and AF1 traffic will be less than  % of link
  example: Global (transcontinental) ISPs
(*) DS aware TE does not “create” bandwidth, but it can first use resources on non SPF-path and then reject establishment of excess tunnels

## Slide 11: Diff-Serv aware TE: protocol Components
Current IGP(*) extensions for TE:
  advertise “unreserved TE bandwidth” (at each preemption level)
Proposed IGP(*) extensions for DS aware TE:
  Class-Types= group of Diff-Serv classes sharing the same bandwidth constraint (eg AF1x and AF2x)
  advertise “unreserved TE bandwidth” (at each preemption level) for each Class-Type
(*) OSPF and ISIS

## Slide 12: Diff-Serv aware TE: protocol Components
Current LSP-signalling (*) extensions for TE:
  at LSP establishment signal TE tunnel parameters (label, explicit route, affinity , preemption,…)
Proposed LSP-signalling (*) extensions for DS aware TE:
  also signal the Class-Type
  perform Class-Type aware CAC
(*) RSVP-TE and CRLDP

## Slide 13: Diff-Serv aware TE: protocol Components
Current Constraint Based Routing for TE:
  compute a path such that on every link :
  - there is sufficient “unreserved TE bandwidth”
Proposed Constraint Based Routing for DS aware TE:
  same CBR algorithm but satisfy bandwidth constraint over the “unreserved bandwidth for the relevant Class-Type” (instead of aggregate TE bandwidth)

## Slide 14: DS-TE Standardisation
standardization effort initiated 2 IETFs ago
see I-Ds submitted at Dec 2000 IETF:
  draft-ietf-mpls-diff-te-reqts-00.txt
  draft-ietf-mpls-diff-te-ext-00.txt
  draft-lefaucheur-diff-te-ospf-00.txt
  draft-lefaucheur-diff-te-isis-00.txt

## Slide 15: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class Traffic Engineering
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 16: Aggregate TE in Best Effort Network
Find route & set-up tunnel for 20 Mb/s from POP1 to POP4
Find route & set-up tunnel for 10 Mb/s from POP2 to POP4
POP4
POP
POP
POP
POP2
POP1
WAN area
Notes: <number>

## Slide 17: Aggregate TE in Diff-Serv NW
Find route & set-up tunnel for 20 Mb/s (aggregate) from POP1 to POP4
Find route & set-up tunnel for 10 Mb/s (aggregate) from POP2 to POP4
POP4
POP
POP
POP
POP2
POP1
WAN area
Notes: <number>

## Slide 18: per COS Traffic Engineering
Find route & set-up tunnel for 5 Mb/s of EF from POP1 to POP4
Find route & set-up tunnel for 3 Mb/s of EF from POP2 to POP4
POP4
POP
POP
POP
POP2
POP1
WAN area
Find route & set-up tunnel for 15 Mb/s of BE from POP1 to POP4
Find route & set-up tunnel for 7 Mb/s of BE from POP2 to POP4
Notes: <number>

## Slide 19: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class TE
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 20: The Trouble With Diffserv
As currently formulated, Diffserv is strong on simplicity and weak on guarantees
Virtual leased line using EF is quite firm, but how much can be deployed?
  No topology-aware admission control mechanism
Example: How do I reject the “last straw” VOIP call that will degrade service of calls in progress?

## Slide 21: MPLS Guaranteed Bandwidth
Combining MPLS Diff-Serv & Diff-Serv-TE to achieve strict point-to-point QoS guarantees
A new “sweet-spot” on QoS spectrum
No state
Best effort
Per-flow state
RSVP v1/ Intserv
Aggregated state
Diffserv
MPLS Diffserv + MPLS DS-TE
Aggregated State (DS)
Aggregate Admission Control (DSTE)
Aggregate Constraint Based Routing (DSTE)
MPLS
Guaranteed
Bandwidth

## Slide 22: MPLS Guaranteed Bandwidth
“Guaranteed QoS” is a unidirectional point-to-point bandwidth guarantee from Site-Sx to Site-Sy : “The Pipe Model”
“Site” may include a single host, a “pooling point”, etc.
10.2
10.1
11.5
11.6
CE
CE
CE
CE
N1 Mb/s Guarantee
N2 Mb/s
Guarantee

## Slide 23: MPLS Guaranteed Bandwidth
“Guaranteed QoS” is a unidirectional point-to-point bandwidth guarantee from Site-Sx to Site-Sy : “The Pipe Model”
“Site” may include a single host, a “pooling point”, etc.
10.2
10.1
11.5
11.6
CE
CE
CE
CE
N1 Mb/s Guarantee
N2 Mb/s
Guarantee
DS-TE LSP for AF or EF,
used to transport Guaranteed Bandwidth traffic edge-to-edge

## Slide 24: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class TE
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 25: VoMPLS over Diff-Serv EF
GW
PSTN
PSTN
Call
Agent
GW
GW
SS7
EF/PQ
BE
Data
Voice
If EF load obviously very small compared to every link capacity (eg DWDM everywhere), then just works fine. That’s it!

## Slide 26: DS aware TE Applications: Voice Trunks
MPLS TE Tunnel for EF
GW
PSTN
PSTN
Call
Agent
GW
GW
SS7
EF/PQ
BE
MPLS Voice Trunks

## Slide 27: Voice over MPLS DS-aware TE Tunnels
Will use emerging “Diff-Serv aware MPLS TE” in order to perform:
  Explicit Admission Control of “EF Traffic/Voice Trunks”
  EF-aware Constraint Based Routing
in combination with “Diff-Serv over MPLS”, this provides hard QoS for Voice without relying on over-engineering
maximises the amount of Voice Traffic that can be transported on given set of resources
allows Fast Reroute of Voice

## Slide 28: VoMPLS: DS-aware TE Tunnels with RSVP Aggregation
GWb
PSTN
PSTN
Call
Agent
GWa
GWc
SS7
Site A
Per call e2e RSVP
Per call e2e RSVP
RSVP Aggregation:
-per call RSVP reservations aggregated into EF DS-TE Tunnel
-EF DS-TE Tunnel size dynamically adjusted to current load
-EF DS-TE Tunnel routed/rerouted/split (make-before-break) to fit size
-new per call RSVP reservation rejected if EF DS-TE Tunnel can’t be increased

## Slide 29: Agenda
MPLS Diff-Serv and MPLS TE today
Diff-Serv-aware-TE (DS-TE)
DS-TE for per Class TE
DS-TE for Guaranteed Bandwidth services
DS-TE for VoMPLS
Conclusions

## Slide 30: Diff-Serv-aware TE: Conclusions
New work in IETF, emerging implementations
extensions over existing MPLS TE, to do CBR and CAC on a per Class(-Type) basis
allows tighter control of QoS performance for each class (helps solve Diff-Serv’s provisioning challenge)
enables support of applications with tight QoS requirements such as “Guaranteed Bandwidth services”, Voice Trunks, Bandwidth Trading,… ==> further step towards enabling IP/MPLS as the Multiservice Transport Infrastructure
useful in networks which cannot be assumed to be over-engineered everywhere all the time

## Slide 31
<number>
© 2000, Cisco Systems, Inc.
Apricot 2001